## Slide 1
Plasma electron acceleration
driven by a long-wave infrared (LWIR)* laser
Mike Downer, University of Texas at Austin
Laser-Plasma Acceleration Workshop,
Ischia, 15 April 2025
University of Texas at Austin:
Faculty: M. C. Downer
Research Scientist: R. Zgadzaj
PhD students: Y. Cao, J. Welch
Stony Brook University:
Faculty: Navid Vafaei-Najafabadi
Roman Samulyak
V. N. Litvinenko
Postdocs: L. D. Amorin, I. Petrushina
PhD Students: A. Cheng, A. Gaikwad,
P. Iapozzutto, P. Kumar
Brookhaven ATF*:
ATF Director: M. A. Palmer
Research Scientists: M. Babzien,
M. Fedurin, R. Kupfer, K. Kusche,
W. Li, I. V. Pogorelsky,
M. N. Polyanskiy, C. Swinson
UCLA:
Faculty: C. Joshi
Research Scientist: C. Zhang
1
*ATF = Accelerator Test Facility
* 8 < 𝜆 < 15 µm
LWFA driven my MWIR laser (3.9 µm):
Woodbury et al., Opt. Lett. 43, 1131 (2018)
LWIR lasers (and ATF) are poised to drive a new generation of laser-plasma accelerators
that deliver spin-polarized e-bunches with the ultra-low emittance and energy spread
required to drive free-electron lasers.

## Slide 2
Drive pulses with a0 ≈ 4, τ ≈ ωp-1 , w0 ≈ λp
generate
ne ≈ 5 × 1018 cm-3
ne ≈ 2 × 1016 cm-3
Plasma electrons self-inject into a
region of strong EM field gradients.
Plasma electrons do not self-inject.
External injection is necessary.
λ [µm]:
1
τ [fs]:
30
w0 [µm]:
8
Laser Energy [J]:
0.7
10
30
8
0.007
1
500
120
1250
0
5
10
electron density (1018 cm-3)
x = 0 mm
x = 0.3 mm
x = 0.6 mm
(τ ≈ 1 cycle)
(w0 < λ)
(inefficient, impractical)
Max e- energy gain [GeV]:
0.6
λ [µm]:
τ [fs]:
w0 [µm]:
Energy [J]:
Max e- energy gain [GeV]:
10
500
120
12.5
1.6
Pogorelsky et al., PPCF 58, 034003 (2016).
...that preserve the low ℇn, low ∆Ee/Ee, spin polarization of linac-injected e-bunches.
Externally-
injected
e-bunches
within reach
at ATF
Polyanskiy et al.,
Photonics 8,
101 (2021)
LWIR
efficiently
plasma “bubbles”.
super-sized
plasma “bubbles”...
Externally-
injected
e-bunches

## Slide 3
TW CO2 laser technology & LWFA science advance hand-in-hand
PBWA
Plasma Beat-
Wave Accelerator
Clayton, PRL 70, 37 (1993)
ne = 8.6 x 1015 cm-3
60J, 300 ps, 0.2 TW
λ1 = 10.59 µm;
λ2 = 10.29 µm
CO2 laser technology
LWFA regime
2-color
(MARS)
CPA (ATF) →
2J, 4 ps, 0.5 TW
CO2: natural, 10R branch,
𝜆 = 10.3 µm
CPA: 25 ps stretch; 75 l/mm,
50% T compressor
Polyanskiy, Optica 2, 675 (2015)
linear
SM*-LWFA
(*Self-Modulated)
AE-71 (2018-20)
3-10J, 2 ps, 1.5-5 TW
CO2: isotopically enriched,
9R branch, 𝜆 = 9.2 µm
CPA: 140 ps stretch; 100 l/mm,
75% T compressor
Polyanskiy, OSA Cont. 3, 459 (2020)
nonlinear
SM-LWFA,
forced LWFA
AE-95 (2022-24)
electrons
0.5 < ne < 2 x 1018 cm-3
0.4 > Pcr > 0.1 TW
collective Thomson scatter
1 < ne < 4 x 1017 cm-3
1.7 > Pcr > 0.5 TW
electron spectrometer
10-15J, 0.5 ps, 20-30 TW
CO2: isotopically enriched,
9R + 9P branches
CPA: augmented by nonlinear
post-compression
Polyanskiy, Opt. Expr. 29, 31714 (2021)
bubble
regime
AE-?? (2024-26)
NONE
1 < ne ≲ 4 × 1016 cm-3
Q ≈ 5 fC
Ee ≈ 9 MeV
wake structure
linear wake
laser
electron radiography,
Faraday rotation
external injection
• linac (synched, compressed)
• 2-color ionization
exponential & peaked
electron spectra
Q ≈ 1-500 pC
Ee ≈ 5-25 MeV
Kumar, Phys. Plasmas 28, 013102 (2021)
P = 20 TW, ne0 = 2x1016 cm-3, a0 = 3.8
z [mm]
x [µm]
0
-100
100
𝛿n/ne0
ATF
pulse
nonlinear wake
linear wake
3
plasma parameters
& diagnostics

## Slide 4
SPACE* simulations predicted detectable SM wakes,
but no accelerated electrons for PL = 0.5 TW (2 J, 4 ps) CO2 pulses
Yu et al., Comp. Phys. Commun. 277, 108396 (2022).
*
simulations by...
4
3D, parallel, relativistic PIC
*
z [mm]
*
ion motion and atomic physics included
Prof. Roman Samulyak
Aiqi Cheng
Only pz attributable to
wake itself are observed.

## Slide 5
0
10
-10
-20
-30
20
30
Notch filtered
collective Thomson shift [nm]
ne [1018 cm-3]
0.57
0.75
0.98
1.11
1.45
1.69
Stokes
sum-
frequency
difference-
frequency
0.63
anti-
Stokes
Collective Thomson Scatter (CTS)*
experiments to observe wakes
Slusher, Phys. Fluids 23, 472 (1980)
Villenueve, JOSA B 8, 895 (1991)
*
120 cycles,
~30 𝜈p-1
rms jitter:
1 ps
(data for ∆t = 0, P = 0.5 TW, ne variable)
∆t
Dr. Rafal
Zgadzaj
(UT-Austin)
experiments led by...
5

## Slide 6
(data for ∆t = 0, ne = 1.3 × 1018 cm-3)
6
CTS data: variable CO2 laser power P
Stokes/anti-Stokes sidebands appear for P > Pcr

## Slide 7
CTS data: variable time delay ∆t
(ne = 1.5 × 1018 cm-3 , PL = 0.5 TW = 3.75 Pcr)
7
Averaged & normalized
sideband amplitude
0
1
0.5
pu-pr
x-corrn
PIC
EXP
epw decays by converting into
• transverse wakes
• plasma channel
• ion acoustic waves
For further details, see:
Zgadzaj et al., Nat. Commun. 15, 4037 (2024)

## Slide 8
TW CO2 laser technology & LWFA science advance hand-in-hand
PBWA
Plasma Beat-
Wave Accelerator
Clayton, PRL 70, 37 (1993)
ne = 8.6 x 1015 cm-3
60J, 300 ps, 0.2 TW
λ1 = 10.59 µm;
λ2 = 10.29 µm
CO2 laser technology
LWFA regime
2-color
(MARS)
CPA (ATF) →
2J, 4 ps, 0.5 TW
CO2: natural, 10R branch,
𝜆 = 10.3 µm
CPA: 25 ps stretch; 75 l/mm,
50% T compressor
Polyanskiy, Optica 2, 675 (2015)
linear
SM*-LWFA
(*Self-Modulated)
AE-71 (2018-20)
3-6J, 2 ps, 1.5-3 TW
CO2: isotopically enriched,
9R branch, 𝜆 = 9.2 µm
CPA: 140 ps stretch; 100 l/mm,
75% T compressor
Polyanskiy, OSA Cont. 3, 459 (2020)
nonlinear
SM-LWFA,
forced LWFA
AE-95 (2022-24)
electrons
0.5 < ne < 2 x 1018 cm-3
0.4 > Pcr > 0.1 TW
collective Thomson scatter
0.3 < ne < 4 x 1017 cm-3
1.7 > Pcr > 0.5 TW
electron spectrometer
10-15J, 0.5 ps, 20-30 TW
CO2: isotopically enriched,
9R + 9P branches
CPA: augmented by nonlinear
post-compression
Polyanskiy, Opt. Expr. 29, 31714 (2021)
bubble
regime
AE-?? (2024-26)
NONE
1 < ne ≲ 4 × 1016 cm-3
Q ≈ 5 fC
Ee ≈ 9 MeV
wake structure
linear wake
laser
electron radiography,
Faraday rotation
external injection
• linac (synched, compressed)
• 2-color ionization
exponential & peaked
electron spectra
Q ≈ 1-500 pC
Ee ≈ 5-25 MeV
Kumar, Phys. Plasmas 28, 013102 (2021)
P = 20 TW, ne0 = 2x1016 cm-3, a0 = 3.8
z [mm]
x [µm]
0
-100
100
𝛿n/ne0
ATF
pulse
nonlinear wake
linear wake
8
plasma parameters
& diagnostics

## Slide 9
SPACE simulations predicted electron injection
and acceleration for PL = 2 TW (4 J, 2 ps) CO2 pulses
Zgadzaj et al., Nat. Commun. 15, 4037 (2024)
PL = 2 TW (4 J, 2 ps)
MeV
ne = 5 × 1017 cm-3
~ 75 mrad
e- output
Q ≈ 50 pC
9
simulations by A. Cheng & R. Samulyak
pz from trapped,
accelerated e- observed
above e- injection threshold
simulations by...
Prof. Roman Samulyak
Aiqi Cheng
0
2
1
z (mm)

## Slide 10
CO2 pulse
2-5 J, 2ps
H2
jet
Lanex
10
CCD
e-
integrated luminescence
⇒ total charge Q
Detection and Characterization of
relativistic electron beams
P appearance thresholds
⇒ all are sub-Pcr
appearance thresholds
⇒ all are relativistic
Qmax ≈ 500 pC
For 2 TW pulses,
self-focusing no
longer essential
to trigger LWFA.

## Slide 11
Transverse profiles of 90% of
e-beams have 2-components
CO2 pulse
2-5 J, 2ps
H2
jet
Lanex
CCD
e-
Key to lineouts
data
wide
Gaussian
narrow
Gaussian
11
wide (w) Gaussians: 60 < 𝜎w < 120 mrad
narrow (n) Gaussians: 12 < 𝜎n < 18 mrad

## Slide 12
Electron energy spectra have
2 corresponding components
CO2 pulse
2-5 J, 2ps
H2
jet
Lanex
CCD
magnet
12
ne = 4 × 1017 cm-3
*
*
*
SM-LWFA → bubble regime
Collimated quasi-monoenergetic
e-spectral features
*
⇒ transition from

## Slide 13
”Forced” LWFA
*
Malka et al., “Electron acceleration by a wake field forced by an intense ultrashort laser pulse” Science 298, 1596 (2002)
*
13
4 × 1017 cm-3
3 × 1016 cm-3
2 ps
10 wake periods
3 wake periods
4-6 J
2 ps
4-6 J
~1016 cm-3
~ 0.5 ps
~ 10 J
~1/2 wake period
“Bubble”
Regime

## Slide 14
TW CO2 laser technology & LWFA science advance hand-in-hand
PBWA
Plasma Beat-
Wave Accelerator
Clayton, PRL 70, 37 (1993)
ne = 8.6 x 1015 cm-3
60J, 300 ps, 0.2 TW
λ1 = 10.59 µm;
λ2 = 10.29 µm
CO2 laser technology
LWFA regime
2-color
(MARS)
CPA (ATF) →
2J, 4 ps, 0.5 TW
CO2: natural, 10R branch,
𝜆 = 10.3 µm
CPA: 25 ps stretch; 75 l/mm,
50% T compressor
Polyanskiy, Optica 2, 675 (2015)
linear
SM*-LWFA
(*Self-Modulated)
AE-71 (2018-20)
3-10J, 2 ps, 1.5-5 TW
CO2: isotopically enriched,
9R branch, 𝜆 = 9.2 µm
CPA: 140 ps stretch; 100 l/mm,
75% T compressor
Polyanskiy, OSA Cont. 3, 459 (2020)
nonlinear
SM-LWFA,
forced LWFA
AE-95 (2020-24)
electrons
0.5 < ne < 2 x 1018 cm-3
0.4 > Pcr > 0.1 TW
collective Thomson scatter
1 < ne < 4 x 1017 cm-3
1.7 > Pcr > 0.5 TW
electron spectrometer
10-15J, 0.5 ps, 20-30 TW
CO2: isotopically enriched,
9R + 9P branches
CPA: augmented by nonlinear
post-compression
Polyanskiy, Opt. Expr. 29, 31714 (2021)
bubble
regime
AE-?? (2024-26)
NONE
1 < ne ≲ 4 × 1016 cm-3
Q ≈ 5 fC
Ee ≈ 9 MeV
wake structure
linear wake
laser
electron radiography,
Faraday rotation
external injection
• linac (synched, compressed)
• 2-color ionization
exponential & peaked
electron spectra
Q ≈ 1-500 pC
Ee ≈ 5-25 MeV
Kumar, Phys. Plasmas 28, 013102 (2021)
P = 20 TW, ne0 = 2x1016 cm-3, a0 = 3.8
z [mm]
x [µm]
0
-100
100
𝛿n/ne0
ATF
pulse
nonlinear wake
linear wake
14
plasma parameters
& diagnostics

## Slide 15
Next-generation ATF experiments will inject
~ 70 MeV electrons from linac into large LWFA
Dream parameters:
1) 10 fs laser-e-beam rms jitter
2) e-bunch compression to 10 fs
3) 20-25 TW CO2 pulse
Actual parameters will depend
on status of laser and linac
development.
Simulations are in progress to define experimental parameters
15

## Slide 16
Simulations validated by experiments in SM regime
can be trusted to predict bubble regime accurately
matched
unmatched
unmatched
P = 20 TW, τ = 0.5 ps
w0 = 117 µm, a0 = 2.4
δn/n
P = 20 TW, τ = 0.5 ps
w0 = 74 µm, a0 = 3.8
P = 20 TW, τ = 1 ps
w0 = 74 µm, a0 = 3.8
ne = 2 x 1016 cm-3
ne = 2 x 1016 cm-3
ne = 2.3 x 1016 cm-3
• Multiple ways to reach bubble regime
• no e-laser overlap for τ ≲ 0.5 ps
longitudinal distance z [mm]
incomplete blowout
complete blowout
laser
complete blowout
• no self-injection for z < 2.5 mm
16
Kumar, Phys. Plasmas 28, 013102 (2021)

## Slide 17
Simulations of growth of ∆Ee/Ee and emittance
of externally injected e-bunches in large bubbles.
(a) ne = 1016 cm-3
0.5 ps CO2 pulse
(b)
(c) Electron Energy
(d)
Evolution of
Energy Spread (%)
2 externally
injected
e-bunches
See Tu WG1 poster Y. Cao, “Simulations of externally-injected CO2-driven LWFA”
7
17

## Slide 18
OSIRIS* quasi-3D simulations show that large bubbles preserve energy spread
& spin polarization of strategically injected e-bunches during acceleration
Simulations by Z. Nie, F. Li and W. B. Mori (UCLA)
• Depolarization due to spin precession is ~ few %
• Depends on coordinates of injection point
spin-polarized
injected e-bunch
slightly depolarized
accelerated e-bunch
sz
sz
sx
sy
sx
sy
• Occurs predominantly from γ = 1 10, constant thereafter
sz
1.0
0.8
0.6
1
0.3
0
2
50
100
z [mm]
1.0
0.8
injection point
after acceleration
Fonseca et al., PPCF 55, 124011 (2013)
*
E = 65 MeV,
∆E = 0.5 MeV
injected e-bunch
E = 330 MeV,
∆E = 0.8 MeV
accelerated e-bunch
0.32
0.33
0.34
0.07
0.06
-6.0
-7.0
-6.5
longitudinal distance
z – ct [c/ωp]
electron energy
[GeV]
-6.0
-7.0
-6.5
longitudinal distance
z – ct [c/ωp]
electron energy
[GeV]
Simulation
parameters:
∆E/E ≈ 0.25%
∆E

## Slide 19
New compact TW-scale MIR/LWIR
CPA laser technologies are emerging ...
Gain medium | 𝜆 [µm] | anticipated fs/mJ/TW | references
Cr: ZnSe | 2.5 | 100/100/1 | Y. Wu et al., Sci. Rpts. 10, 7775 (2020)
Fe: ZnSe | 4 - 5 | 100/100/1 | Y. Wu et al., in Emerging Laser Technol. for High-Power Ultrafast Science, ed. F. Légaré (IOP, 2021)
optically-pumped CO2 | ~10 | 500/500/1 | D. Tovey et al., Opt. Express 29, 31455 (2021)
discharge-pumped CO2 | 9.2 | 500/10000/20 | Polyanskiy et al., Photonics 8, 101 (2021)
...to drive future LWFAs in the super-bubble regime.
18
But for now, this is the only game in town!
A bird in the hand...

## Slide 20
SUMMARY
• Plasma e- acceleration driven by LWIR laser demonstrated at ATF
• Peak laser power: 2-3 TW
• Plasma density: 3e16 ≲ ne ≲ 4e17 cm-3
• Accelerated electrons: 5-10 MeV, plasma-injected,
quasi-monoenergetic features ⇒ “forced” LWFA
Zgadzaj et al., Nat Comms 15, 4037 (2024)
• An upgraded ATF laser is poised to demonstrate low-∆Ee/Ee, low-
emittance acceleration of electrons injected from the ATF linac.
• Injected e-: synchronized, compressed to fs scale
• Plasma: ne ≲ 1016 cm-3
• CO2 laser: 0.5 ≲ 𝜏L ≲ 2 ps; ℇL ~ 10 J
• Plasma physicists need not re-invent the cathode. Use plasma
for what God intended: compact particle acceleration.
record
19

## Slide 21
Nat Comms 15, 4037 (2024)
• DoE grant DE-SC0014043 (Stony Brook U., N. Vafaei-Najafabadi, PI)
• DoE grant DE-SC0011617 (U. Texas-Austin, M. C. Downer, PI)
• DoE grant DE-SC0012704 (Brookhaven NL, M. A. Palmer, PI)
Financial Support
Thanks to all
of these co-
workers!

## Slide 22
Centimeter-long LWFAs have progressed
steadily toward multi-GeV electron energy...
...but are stuck at 10% energy spread,
5
0
10
Ee (GeV)
2000
2010
2020
Year
∆Ee/Ee
100
10-1
10-2
10-3
quasi-monoenergetic
Πspin
1.0
0.5
0
ATF
oppor-
tunity
unpolarized spins
conventional RF
accelerator capability
E-beam quality*, not energy,
is the concern of the HEP
research community.
*energy spread, spin poln, emittance
preservation, beam stability & control,
high rep-rate, peak current, staging,...
Report of Accelerator R&D Subpanel
2015
HEPAP
“bubble”
regime
discovery
electron
energy
, tens pC charge
Q (nC)
100
10-1
10-2
10-3
drive FELs,
probe reso-
nant particle
interactions
probe nuclear
spin states,
parity
violation
high
luminosity
at collider
IP
most RF
accelerators
all
research
acceler-
ators

## Slide 23
ne = 1016 cm-3
ne = 1014 cm-3
CO2 laser parameters: 10 J, 2 ps, 5 TW, w0 = 40 µm, a0(vac) = 3.56
There are near-term scientific opportunities
even for currently available 2 ps pulses
OSIRIS* simulations courtesy N. Vafaei-Najafabadi
* Fonseca et al., PPCF 55, 124011 (2013)