## Slide 1
Johannes Zirkelbach
LMU/CALA (Karsch group)
Laser Wavefront-based Classification of successful Injection in LWFA

## Slide 2
ATLAS-3000 (Garching/LMU/Centre for Advanced Laser Applications)
~100 m
Wavelength: 800 nm (Ti:Sa)
Pulse duration: 27 fs
Pulse energy: ~70 J (curr.: ~20 J)
Repetition rate: 1 Hz
Applications:
Electron acceleration
X-ray generation
Ion acceleration
Fundamental research
Remember:
- Don’t use “Gaias”, instead “Pump Lasers”

## Slide 3
ATLAS-3000 (Garching/LMU/CALA)
Frontend (-> 2 J)
Main Amplifier (-> 20-30 J)
Beamline & Labs
Laser parameters:
18 cm beam (bypassing AMP2)
LWFA with slit nozzle and optical injection
Hydrogen
20 mm
~8 J on target
26 fs pulse duration
f/56
From: PhD thesis of M. Förster
From: PhD thesis of K. von Grafenstein
Data discussed today:

## Slide 4
Electrons from LWFA driven by ATLAS-3000
Shot
Electron Energy (MeV)
Shots without injection into the first bubble
Shot-to-shot fluctuations
Drift
Why?
Laser output appears more stable than LWFA electrons:

## Slide 5
Laser Parameters are more stable than Electron Energy
Shot
Electron Energy (MeV)
Shots without injection into the first bubble
Shot-to-shot fluctuations
Drift
Laser output appears more stable than LWFA electrons:
Why?

## Slide 6
Laser Parameters are more stable than Electron Energy
Shot
Electron Energy (MeV)
Shots without injection into the first bubble
Shot-to-shot fluctuations
Drift
Laser output appears more stable than LWFA electrons:
Why?

## Slide 7
Laser Parameters are more stable than Electron Energy
Shot
Electron Energy (MeV)
Shots without injection into the first bubble
Shot-to-shot fluctuations
Drift
Laser output appears more stable than LWFA electrons:
Norm. Intensity
6 cm
Indicate scale
Why?

## Slide 8
Laser Parameters are more stable than Electron Energy
Shot
Electron Energy (MeV)
Shots without injection into the first bubble
Shot-to-shot fluctuations
Drift
Laser output appears more stable than LWFA electrons:
Change to
Pulse Duration (Probe)
~6%
~0.5%
Why?

## Slide 9
~2000 Shot Data Set for Statistical Analysis
Shot
Electron Energy (MeV)
~2000 shot series at 0.25 Hz repetition rate
Recorded without actively changing any parameters
‘Successful’ injection only in 2/3 of the cases:
63%
37%
Injection into the first bubble
No/little injection into the first bubble
Why does this vary?

## Slide 10
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield

## Slide 11
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield
Laser beam pointing

## Slide 12
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield
Laser beam pointing
Laser output wavefront

## Slide 13
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield
Laser beam pointing
Laser output wavefront
Laser pulse spectrum (probe)
Laser pulse duration (probe)
Laser beam pointing (probe)
Laser probe pulse energy

## Slide 14
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield
Laser beam pointing
Laser output wavefront
Laser pulse spectrum (probe)
Laser pulse duration (probe)
Laser beam pointing (probe)
Laser probe pulse energy
Plasma density (interferometer)
Shock position
Gas pressure

## Slide 15
Diagnostics at ATLAS-3000 and in LWFA Lab
Record in sync with the electron spectra:
Laser pulse energy
Laser pulse spectrum
Laser beam nearfield
Laser beam pointing
Laser output wavefront
Laser pulse spectrum (probe)
Laser pulse duration (probe)
Laser beam pointing (probe)
Laser probe pulse energy
Plasma density (interferometer)
Shock position
Gas pressure
Electron beam pointing
Electron energy spectrum
Accelerated charge
Correlation matrix

## Slide 16
Correlation between LWFA Electrons and Laser Parameters
Laser energy
Frontend output pointing
Laser output wavefront
Probe beam
Gas pressure
Electron pointing
Electron energy & charge
Laser energy
Frontend output
pointing
Laser output
wavefront
Probe beam
Gas pressure
Electron pointing
Electron energy
& charge
High correlation between electron energy and wavefront coefficients
Mention:
In squares: non-independent measurements
Tend to be correlated

## Slide 17
Correlation between LWFA Electrons and Laser Parameters
Defocus Zernike coefficient at the laser output
vs. maximum electron energy
Laser energy
Frontend output
pointing
Laser output
wavefront
Probe beam
Gas pressure
Electron pointing
Electron energy
& charge
Injection into the first bubble
No/little injection into the first bubble

## Slide 18
Classification of Injection based on Wavefront
Can predict based on the laser wavefront whether ?
63%
37%
Average wavefront at the laser output:
difference
Add Zernike decomp
And quantify defocus and astig contributions
Mention:
Fluctuations as subtle as a small fraction of the wavelength can have profound effects
Add reference to classification based on full wavefront.

## Slide 19
Classification of Injection based on Wavefront
Can predict based on the laser wavefront whether ?
63%
37%
Average wavefront at the laser output:
difference
Add Zernike decomp
And quantify defocus and astig contributions
Mention:
Fluctuations as subtle as a small fraction of the wavelength can have profound effects
Add reference to classification based on full wavefront.
AUC = 0.87
Mention:
Diagonal -> completely random
‘Square’ -> perfect classification

## Slide 20
AUC = 0.87
Classification of Injection based on Defocus
Can predict based on the defocus parameter whether ?
63%
37%
AUC = 0.81
How to improve classification?
More information on target parameters (?)
Pulse front tilt/curvature (?)
… (?)
How to move on from here?
Understand physics/run simulations.
Reduce defocus fluctuations.

## Slide 21
Fluctuations in Focus Position
Reference to DESY
Defocus fluctuations during the experiment:
RMS = 1.2%
Wavefront video?
To demonstrate that not statistical noise?
Focal shift :
Look up exact Phasics model and check repeatability
Sensor repeatability:
Check: could the laser focus have fluctuated from slightly upstream of the shock to on the shock?
30 min

## Slide 22
Fluctuations in Focus Position
Defocus fluctuations during the experiment:
RMS = 1.2%
Focal shift :
Sensor repeatability:
4 min

## Slide 23
Fluctuations in Focus Position
What causes these defocus fluctuations? Candidates:
Fluctuations in the amplifier crystal temperature
Air humidity fluctuations
Air turbulence
Defocus fluctuations during the experiment:
RMS = 1.2%
Focal shift :
Sensor repeatability:
Upstream of target/shock
Downstream of target/shock
Work in progress

## Slide 24
9 cm
IR-image of AMP1 laser crystal while pumped with 4 Gaias
Where do the Defocus Fluctuations come from?
Cooling from the side via index-matched liquid
Mention that temperature profile is shifted and moves up after turning on the pump lasers.
Temperature distribution in laser crystals, in particular at the main AMP:
Ti:Sa
Pump lasers
Seed
Pump lasers
Seed
IR camera

## Slide 25
9 cm
Temperature distribution in laser crystals, in particular at the main AMP:
IR-image of AMP1 laser crystal while pumped with 4 Gaias
Pump lasers on
Pump lasers off
Does the Thermal Lens induce Defocus Fluctuations?

## Slide 26
9 cm
Thermal lenses in laser crystals, in particular at the main amplifier:
IR-image of AMP1 laser crystal while pumped with 4 Gaias
Correlation between and defocus coefficient fluctuations?
Does the Thermal Lens induce Defocus Fluctuations?
Pump lasers on
Pump lasers off
Thermal lensing
Expected defocus RMS:
Measured defocus RMS: 1.2%
Might be measuring additional thermal dynamics that is not relevant for the defocus at the laser shots.

## Slide 27
9 cm
Thermal lenses in laser crystals, in particular at the main amplifier:
IR-image of AMP1 laser crystal while pumped with 4 Gaias
Correlation between and defocus coefficient fluctuations?
Based on our current measurement, we can not directly explain the defocus fluctuations based on thermal lens fluctuations in the main AMP crystal.
Does the Thermal Lens induce Defocus Fluctuations?
Pump lasers on
Pump lasers off
Expected defocus RMS:
Thermal lensing

## Slide 28
Do Air Humidity Fluctuations induce Defocus Fluctuations?
The air humidity control in the ATLAS-3000 lab sometimes creates spikes (during the winter time…):

## Slide 29
Do Air Humidity Fluctuations induce Defocus Fluctuations?
Measurement with cw-diode; only using part of the full laser chain.
The air humidity control in the ATLAS-3000 lab sometimes creates spikes (during the winter time…):

## Slide 30
Do Air Humidity Fluctuations induce Defocus Fluctuations?
Measurement with cw-diode; only using part of the full laser chain.
For operation of the full laser chain:
Typical defocus RMS:
sub-percent-level humidity fluctuations could influence the defocus in the laser output notably.
The air humidity control in the ATLAS-3000 lab sometimes creates spikes (during the winter time…):
How does air humidity affect the laser wavefront?

## Slide 31
Do Air Humidity Fluctuations induce Defocus Fluctuations?
Test with humidifier close to adaptive mirror (“DM1”):
Hypothesis:
Water accumulates in (porous E-beam) coatings and creates stress.
The flexible substrates of the adaptive mirrors deform more readily than thicker, regular substrates.
Main deformation: curvature -> introduces defocus.
For operation of the full laser chain:
sub-percent-level humidity fluctuations could influence the defocus in the laser output notably.
The air humidity control in the ATLAS-3000 lab sometimes creates spikes (during the winter time…):
Typical defocus RMS:

## Slide 32
Reducing Crystal Temperature in the Main Amplifier
Crystal mount
Pump lasers
Seed
9 cm
Ti:Sa
Cooling liquid
Pump lasers
Seed
Temperature profile of the AMP1 crystal:

## Slide 33
Reducing Crystal Temperature in the Main Amplifier
Crystal mount
40°C
20°C
Air flow/
turbulence
9 cm
Ti:Sa
Cooling liquid
Temperature profile of the AMP1 crystal:
Pump lasers
Seed
Upgrade heat exchanger
Flow speed -> 2x
Chiller temperature 18°C-> 15°C
Seeing indications that wavefront overall becomes more stable by cooling the crystal.
Needs confirmation!
30°C
36°C
Frontend output
Main AMP output

## Slide 34
Conclusions
Subtle fluctuations in the laser wavefront can induce substantial fluctuations in the energy of LWFA electrons and determine to a good extent whether injection takes place or not.
Among all Zernike coefficients, defocus (and astigmatism) have the strongest impact on electron energy and injection probability.
The defocus fluctuations might be caused by a combination of temperature fluctuations in the main amplifier crystal, humidity fluctuations, and air turbulence. Will look into this in more detail.
Reducing the temperature of the main amplifier crystal appears to reduce (higher-order) wavefront fluctuations.

## Slide 36
Conclusions
Subtle fluctuations in the laser wavefront can induce substantial fluctuations in the energy of LWFA electrons and determine to a good extent whether injection takes place or not.
Among all Zernike coefficients, defocus (and astigmatism) have the strongest impact on electron energy and injection probability.
The defocus fluctuations might be caused by a combination of temperature fluctuations in the main amplifier crystal, humidity fluctuations, and air turbulence. Will look into this in more detail.
Reducing the temperature of the main amplifier crystal appears to reduce (higher-order) wavefront fluctuations.

## Slide 37
Correlation between LWFA Electrons and Laser Parameters
Defocus Zernike coefficient vs. average electron energy
Defocus at Laser Output (
Mean Electron Energy (MeV)
Laser energy
Frontend output
pointing
Laser output
wavefront
Probe beam
Gas pressure
Electron pointing
Electron energy
& charge

## Slide 38
Correlation between LWFA Electrons and Laser Parameters
Defocus @ Laser Output
Shot Number (Rep. rate: 0.25 Hz)
Standardized time series
Electron Max. Energy
Smoothed Time Series
Origin of defocus drifts?
Some: originates in front-end
Most of it: Thermal lensing in the main amplifier (?)
Currently exploring in more detail…
30 min
Defocus and the maximum electron energy fluctuate in sync on a timescale of minutes.

## Slide 39
Correlation between LWFA Electrons and Laser Parameters
Defocus @ Laser Output
Shot Number (Rep. rate: 0.25 Hz)
Standardized time series
Electron Mean Energy
Smoothed Time Series
Origin of defocus drifts?
Some: originates in front-end
Most of it: Thermal lensing in the main amplifier (?)
Currently exploring in more detail…
30 min
Defocus and mean electron energy fluctuate in sync on a timescale of minutes.