## Slide 1: New designs of helical coil targets for laser-driven proton, carbon and alpha acceleration
M. Bardon1, C.L.C. Lacoste1,2, A. Hirsch-Passicos1,3, K. Aliane1, T. Carrière1, E. Catrix2, S. Vallières2,
S. Fourmaux2, P. Nicolaï1, D. Raffestin1, P. Antici2, V.T. Tikhonchuk1,4 and E. d’Humières1
1) CELIA, Université de Bordeaux-CNRS-CEA, UMR 5107, Talence F-33405, France
2) INRS EMT, Varennes J3X 1P7, Canada
3) Helmholtz-Zentrum Dresden-Rossendorf, Bautzner Landstraße 400, Dresden 01328, Germany (currently)
4) Extreme Light Infrastructure ERIC, ELI-Beamlines Facility, Dolní Brežany 25241, Czech Republic

## Slide 2: Motivations
Development of a new tunable proton source for different applications
D. Raffestin et al. Matter Radiat. Extremes 6, 056901 (2021)
±20°
Proton isochoric heating
Radioisotope production
ICF fast ignition scheme
TNSA beam features are not suitable for various applications  We need to shape this proton beam
TNSA proton energy distribution
TNSA proton half-angular divergence
Most robust laser-driven ion acceleration process: the TNSA
TNSA beam features
M. Roth et al, CERN Yellow Reports (2016)
laser
Proton target
p+
Heated target
WDM studies
laser
Proton target
p+
Calcium
target
Sc isotopes
PET scan

## Slide 3: Helical coil target (HC)
Proton and current pulse propagations must be synchronized
Current pulse must spread over, at least, one turn
Radius a
Length L
Pitch h
(0.3-0.8mm)
(0.4-1mm)
(5-20mm)
Rules to design a helical-coil
Discharge current pulse
Laser
Target
Helix
Protons
S. Kar et al., Nature Com. 7 10792 (2016)
is not strong enough to act on protons
Proton beam is focused, collimated, post-accelerated & bunched by the helical-coil
Only one single laser beam is needed to generate the protons and the discharge current
PIC simulation (Sophie)
Current
Protons
Helix acts as a EM wave-guide & also as a delay line

## Slide 4: Results of the Pacman 1 experiment on LULI2000 (2019)
M. Bardon et al., PPCF 62, 125019 (2020)
50J, 1ps
Bunching
Acceleration
Focusing
Fluence multiplied by 10 (E>12MeV)
30% increase in the cut-off energy
Limited bunching
Limited yield (~10%)
RCF without HC
RCF with HC

## Slide 5: Results of the Pacman 2 experiment on LULI2000 (2020)
Cut-off energy does not increase with the coil length
Post-acceleration is not efficient all along the coil length
Variations on the helical coil length
Why?

## Slide 6: Current dispersion
Current pulse propagation along the helical coil is dispersed
M. Bardon et al., PPCF 62 125019 (2020)
PIC simulation (Sophie)
Bunching
Splitting
HC parameters: a=0.5mm h=0.35mm
Acceleration
Deceleration
Acceleration
Deceleration
A series of small bunches is produced. Bunching & acceleration are not efficient all along the HC
Current pulse (~10ps) has a broadband frequency spectrum
Frequencies do not propagate at the same speed
This will modulate the current pulse intensity

## Slide 7: New helical coil design with a tube (HCT)
LASER
Tube
Holder
Holder
Target
Tube limits the current dispersion along the helix
E [MeV]
TNSA
HC without tube
HC with tube
With tube
Without tube
We are able to predict the energy of the bunches depending on the HCT geometry
A. Hirsch-Passicos et al., Phys. Rev. E 109, 025211 (2024)
Helix
and increases the proton bunching

## Slide 8: Experiment at the ALLS facility (INRS-EMT – Canada - June 2024)
ALLS parameters
Elaser= 3J (on target)
t = 30fs
Spot size (FWHM) = 5µm
I = 1020 W/cm2
Target : Ta (2µm)
First time that a Thomson Parabola was used as main diagnostic in a HC experiment

## Slide 9: ALLS experiment: Results on the proton spectrum
We had some issues with:
The target assembly with tubes,
The current intensity in the coil was weaker than expected.
C.L.C. Lacoste et al., Matter Radiat. Extremes 10, 037602 (2025)
But, with the helical coil, we observed:
A good focusing & collimation of the proton beam (2° divergence),
An increase in the proton temperature,
An increase in the proton cut-off energy.
We successfully identified the appropriate input parameters for our simulations to achieve a good agreement with the measurement on the proton spectrum.
RCF

## Slide 10: ALLS experiment: Results on the carbon spectrum
Carbons are suppressed by the HC in this geometry
 First experimental evidence that the HC can act on carbons
Results also confirmed by PIC simulations
HC geometry can be optimized for carbons
Same inputs for both simulations
C.L.C. Lacoste et al., Matter Radiat. Extremes 10, 037602 (2025)
protons
carbons
Proton beam at the HC exit is quite pure
3 MCP images of the TPS
Same inputs parameter as the ones we used to reproduce the proton spectrum

## Slide 11: Bunching of alpha particles with HCT for radioisotopes production
PIC simulations (Sophie) – Alpha particles bunching with HCT
Nuclear cross-section reaction of a Ca target
Based on simulated alpha spectra for LFEX laser (ILE-Japan)
We can strongly increase the Sc44 production (confirmed by Fluka simulations)  need to be validated by an experiment
C.L.C Lacoste et al., Submitted to Phys. Rev. & Part. Beams (2025)
3 HCT geometries

## Slide 12: Conclusion
New designs of HC with tube (HCT) were developped to mitigate current dispersion & increase proton bunching
Need to improve the target assembly with tube
ALLS experiment is the first evidence that HC can act, not only on protons, but also on carbons
PIC simulations show that HCT can also bunch, focus & accelerate alpha particles for radioisotopes production
Next steps
  Experimental validation of HCT at high energy & high intensity with the LFEX laser (ILE-Japan)
  Towards high repetition rate: firts step is to dissociate the proton generation from the current pulse production  This will be performed with the use of 2 laser beams at DRACO facility (HZDR-Germany)

## Slide 13: Acknowledgements
CELIA
C. Lacoste, K. Aliane, T. Carrière, H. Larreur, M. Ben Tayeb, M. Huault, T. Guilberteau, M. Lafargue, J. Lopez, L. Merzeau, F. Blais,
R. Bouillaud, N. Fedorov, I. Manek-Hönninger, J.L. Feugeas, D. Batani, P. Nicolaï, D. Raffestin, V.T. Tikhonchuk and E. d’Humières
INRS
E. Catrix, S. Vallières, J. Maltais, S. Fourmaux and P. Antici
CEA
J. Moreau, I. Lantuéjoul, R. Nuter and O. Cessenat
HZDR
A. Hirsch-Passicos
This study was granted access to the HPC resources of IRENE under allocation Grant
No. A0170512899 made by GENCI.

## Slide 14: Backup

## Slide 15: Optimization of the proton post-acceleration: principle
Protons are accelerated during their propagation inside the HC
Current pulse propagation must also be accelerated in order to be synchronized with the protons
Use of HC with variable pitch or diameter along their axis
1 radius a, 1 pitch h  Infinity of degrees of freedom
We need an efficient model to perform an optimization of the HC geometry

## Slide 16: The DoPPLIGHT code
Coil geometry
Particles
Helix fields
Space charge fields
Boris pusher
For each particle species
,
Electric current
,
, ,
, ,
,
DoPPLIGHT (Dynamics of Particles Produced by Laser Interaction in Grounded Helical Targets)
a
A hellically conducting cylindrical sheet
Radius a
Length L
Pitch h
The helix
The Sheath helix model J. R. Pierce (1950)
DoPPLIGHT
2D axi-symmetric
Time resolved
Not self-consistent
Runs in few minutes on a laptop
Valid for helixes with constant pitch & diameter along their axis
Inputs

## Slide 17: Development of an electromagnetic model for HCT with varying pitch & diameter
pitch=0.35mm
tube
radius a =0.5mm
radius b =0.7mm
pitch=0.525mm
pitch=0.7mm
Modelling of helixes with varying pitch & diameter is validated  We can begin optimization process using ANN (in progress)
C.L.C. Lacoste et al., Matter Radiat. Extremes 9, 067201 (2024)

## Slide 18: Bunching of alpha particles with HCT for radioisotopes production
PIC simulations (Sophie) – Alpha particles bunching with HCT
Setup proposal
Nuclear cross-section reaction
Based on simulated alpha spectra for LFEX laser (ILE-Japan)
We can strongly increase the Sc44 production (confirmed by Fluka simulations)
Submitted to Phys. Rev. & Part. Beams (2025)
3 HCT geometries

## Slide 19: New helical coil design with a tube (HCT)
LASER
Tube
Holder
Holder
Target
Tube limits the current dispersion along the helix & increases the proton bunching
E [MeV]
TNSA
HC without tube
HC with tube
With tube
Without tube
Scaling laws:
We are able to predict the energy of the bunches depending on the HCT geometry
A. Hirsch-Passicos et al., Phys. Rev. E 109, 025211 (2024)
Helix