## Slide 1: Plasma density shaping for beam control and brilliant X-rays
Olle Lundh, Lund University, Sweden
Laser Plasma Accelerator Workshop April 14-18, 2025

## Slide 2: Acknowledgement
Julien Ferri
Chalmers
Laszlo Veisz
Umeå Univ.
Cornelia Gustafsson
Erik Löfquist
Andrea Angella
Flanish D’Souza
Kristoffer
Svendsen
Jonas Björklund Svensson
Diego Guenot
Isabel Gallardo Gonzalez
Anders Persson
Chen Guo
Henrik Ekerfelt
Claes-Göran Wahlström

## Slide 3: Motivation: Divergence and Dephasing
+ + + +
+ + + + + + + +
+ + + + + + + + +
+ + + + + + + + + +
+ + + + + + + + + +
+ + + + + + + + +
+ + + + + + + +
+ + + +
Electron
Ion cavity
Electric field
Laser pulse
+ + + +
+ + + + + + + +
+ + + + + + + + +
+ + + + + + + + + +
+ + + + + + + + + +
+ + + + + + + + +
+ + + + + + + +
+ + + +
Betatron orbit
Ion cavity
Laser pulse
X-rays
Electrons
Betatron motion leads to divergent beams
Inefficient beam transport
Electrons outrunning wake
Limits beam energy

## Slide 4: Density shaping by combining two gas jets
Jet 1: Controlled injection via shock + ionization
Jet 2: Independent control of density and position → energy boost, focusing, X-rays
Goal: Control of beam quality and radiation
or
N2

## Slide 5: Experimental setup
Laser: 1 J | 35 fs | focused to 12 µm FWHM
Jet 1 | 1.5 mm | He+1%N2| 2–8･1018 e-/cm3
Jet 2 | 1.0 mm | He or N2 | 2–16･1019 e-/cm3
Notes: Experimental setup

## Slide 6: Shock-assisted ionization injection
Shock-assisted ionization injection: electrons are ionized and trapped at a sharp density transition.
Expanded plasma cavity at the shock front allows prolonged acceleration and easier trapping.
Localized injection achieved when laser intensity and plasma density are sufficiently low.
Razor blade
1.5 mm jet 99% He 1% N2
0.8 T dipole magnet
Scintillator screen
Thaury et al, Sci. Rep. 5, 16310 (2015)

## Slide 7: Beam quality and tunability
Gustafsson et al, Sci. Rep. 14, 26286 (2024)

## Slide 8: Energy boost via density jump
Typical beam
One gas jet
Jet 1
Energy boost
Two gas jets
Jet 2
Jet 1
Rephasing
Schematic
24 MeV

## Slide 9: Rephasing – Energy boost via density jump
Jet separation
Plasma density (jet 2)
Gustafsson et al, Sci. Rep. 14, 26286 (2024)

## Slide 10: Divergence reduction – Plasma lens
Typical beam
One gas jet
Energy boost
Two gas jets
Jet 2
Jet 1
Jet 1
Beam focusing
Two gas jets
Jet 2
Jet 1

## Slide 11: Overdense plasma lens
Laser pulse diffracts – ionizes Jet 2 – drives weak wake ()
In vacuum: space charge repulsion cancelled by attractive force of the self-magnetic field
Overdense plasma lens (): neutralizes space-charge → magnetic focusing remains
Focusing strength scales with bunch charge and bunch radius:
Kuschel et al, Phys Rev AB 2016
Su, Katsouleas, Dawson & Fedele, Phys Rev A 1990

## Slide 12: Plasma lensing – Divergence reduction
Jet separation
Plasma density (jet 2)

## Slide 13: Monte-Carlo simulation
Propagation
Deflection
Focusing

## Slide 14: Tunable chromaticity
Increased jet separation
→ Lower at jet 2
→ Smaller
→ Focusing lower energies
Divergence reduction ()

## Slide 15: Effect on the high-charge electron beam
Jet 2 on
Jet 2 off
22 consecutive shots, with Jet 2 on/off
Björklund Svensson et al, Nat. Phys. 17, 639-645 (2021)
Divergence of below 120 MeV is greatly increased (from 8.5 to 47 mrad FWHM)
Divergence above 120 MeV is decreased (from 4.5 to 3 mrad)

## Slide 16
Jet 2 off
Typical betatron X-rays
15 mrad
30 mrad
Björklund Svensson et al, Nat. Phys. 17, 639-645 (2021)
Jet 2 on
Narrow X-ray beams
5 mrad
5 mrad
X-ray spectrum
Jet 2 on

## Slide 17: Narrow X-ray beams
Density Jet 2
Jet separation
∆s = 2.7 mm
∆s = 2.7 mm
∆s = 2.7 mm
∆s = 2.7 mm
0.0
∆s = 2.7 mm
∆s = 3.2 mm
∆s = 3.7 mm
∆s = 4.2 mm

## Slide 18: Summary
Plasma density shaping enables simultaneous control of electron beam energy and divergence in LWFA.
Overdense plasma lensing yields stable, few-mrad X-ray divergence through magnetic focusing.
Flexible two-stage design allows tuning between energy gain and collimation.