## Slide 1: Diagnosing a metre-scale plasma discharge for plasma wakefield acceleration
Claudia Cobo, Louis Forrester, Bingxue Wu, Nuo Xu and Zulfikar Najmudin
17th April 2025
Laser-Plasma Accelerators Workshop

## Slide 2: Scalable Plasma Sources
AWAKE requirements
  0.1 Hz operation
  High reproducibility
  Plasma density: ne = 7 × 1020 m−3
  Transverse profile: constant ne over 3 mm
  Axial uniformity: ∆ne < 0.2 % over 10 m
Large energy content of proton drivers allows single stage electron acceleration to TeV level
AWAKE proof of principle demonstrations in 10 m rubidium vapour source (laser ionised)
Need to scale up to > 100 m for particle physics applications
Claudia Cobo c.cobo@imperial.ac.uk
P. Tuev, K. Lotov, PPCF (2021)
A. Caldwell and K. Lotov, PoP (2011)
This talk
Notes: Beam radius = 0.2 mm

## Slide 3: Discharge Plasma Source at AWAKE
Discharge used in AWAKE tunnel C. Amoedo talk, Wed 09:30
Multiple gases, pressures, lengths
Enabled interesting physics measurements
Filamentation of a relativistic proton bunch in plasma L. Verra et al. PRE (2024)
Ion motion in a resonantly driven PWFA M. Turner et al. PRL (2025)
Light diagnostics for wakefields at AWAKE J. Mezger et al. NIMA (2025)
Claudia Cobo c.cobo@imperial.ac.uk

## Slide 4: Discharge Plasma Source at ICL
Claudia Cobo c.cobo@imperial.ac.uk
Parameter | ICL Value | CERN Value | Unit
Tube length | 1 | 10 | m
Diameter | 19.5 | 26 | mm
Discharge gap | 15 | 25 | cm
Gas pressure | 0.01 – 1.5 | 0.01 – 1 | mbar
Discharge current | 100 – 500 | 100 – 500 | A
Discharge time | 0.5 – 100 | ~25 | μs

## Slide 5: Plasma Formation
Gas + vacuum
Cathode
Return cage
Virtual anode
Anode
Discharge gap
Claudia Cobo c.cobo@imperial.ac.uk
HV switch
R
2 kΩ
HV Supply
C
Pulse Generator
Voltage leak (~1 kV) produces glow discharge (~ mA)
    Weakly ionised plasma
Pulse generator (8 kV) drives ~100 A through plasma
Transition from glow to arc discharge plasma regime
    High ionisation level  high uniformity
Notes: Power consumption, I say 1 kA * 10 kV = 10^7 W. Operating for 25 µs = 250 J per shot. At 1 Hz, 250 W, at kHz, 250 kW per metre (but probably similar for 10 metre) - so for 100 m of acceleration need 25 MW (a lot of energy!)

## Slide 6: High Voltage Pulse Generator
Semiconductor-based pulse generator
Multi-stage optically isolated trigger
Controllable pulse duration 0.5 – 100 μs
Claudia Cobo c.cobo@imperial.ac.uk
High repetition rate operation tested on resistive-inductive dummy load
630 A peak at 500 kHz
500 A peak at 1 MHz
< ns jitter

## Slide 7: Discharge Reproducibility
Argon, 8 kV
Claudia Cobo c.cobo@imperial.ac.uk
Microsecond-level jitter of 330 A discharge
    Jitter worsens at lower pressures
Reduced jitter by increasing discharge current
    5× decrease with 500 A discharge
330 A (R = 22 Ω)
500 A (R = 15 Ω)

## Slide 8: Longitudinal Interferometry
CMOS sensor
Plasma tube
Mach-Zehnder interferometer
Longitudinally-integrated density measurement
Transversely resolved
Time scan possible by varying laser – discharge timing
Fibre laser
500 μJ
100 ns
1064 nm
Claudia Cobo c.cobo@imperial.ac.uk
Photodiode

## Slide 9: Plasma Current Scan
Claudia Cobo c.cobo@imperial.ac.uk
Peak densities ~ 1021 m–3  30% ionisation
Plasma density (ionisation fraction) increases with current
Gas | Argon
Pressure | 0.2 mbar
Laser timing | 3.5 μs

## Slide 10: Plasma Channel Evolution
Argon, 0.2 mbar, 8 kV, 330 A (R = 22 Ω)
Claudia Cobo c.cobo@imperial.ac.uk
Low Current

## Slide 11: Plasma Channel Evolution
Argon, 0.2 mbar, 8 kV, 500 A (R = 15 Ω)
Claudia Cobo c.cobo@imperial.ac.uk
High Current

## Slide 12: Plasma Density Evolution
Claudia Cobo c.cobo@imperial.ac.uk
Rapid expansion early in the 500 A discharge counteracts faster ionisation by higher current
Similar peak densities achieved with 330 A and 500 A
Gas | Argon
Pressure | 0.2 mbar
Voltage | 8 kV

## Slide 13: Plasma Density Evolution
Claudia Cobo c.cobo@imperial.ac.uk
Ambipolar diffusion in weakly ionised plasma
Exponential fits imply Te = 2.6 eV for 330 A discharge and Te = 10.5 eV for 500 A discharge
Gas | Argon
Pressure | 0.2 mbar
Voltage | 8 kV
Notes: 66 ns propagation time over 10 m. Rate of change of density relative to this propagation time?
2.6 eV for 330 A, 5.5 eV (from 1 us), 10.5 eV (from 2 us) for 500 A

## Slide 14: Plasma Emission Spectroscopy
Bentham M300 Czerny-Turner spectrometer used to measure spectrum of plasma emission.
Integrated over discharge pulse
Claudia Cobo c.cobo@imperial.ac.uk
Spectrometer
CMOS camera
Plasma tube
Gas | Argon
Voltage | 8 kV
Current | 500 A
Plasma spectrum dominated by Ar II (singly ionised argon)

## Slide 15: Plasma Emission Spectroscopy
Collisional-radiative spectral analysis code
Low temperature spectroscopy
Zero width geometry
Non-LTE
Spectra suggest Te ≈ 1.5 – 2 eV
Result from ambipolar diffusion (Te ~ 2 – 10 eV) likely overestimated
Claudia Cobo c.cobo@imperial.ac.uk
PrismSPECT Simulations
Gas | Argon
Pressure | 0.06 mbar
∆λ | 2 nm

## Slide 16: Conclusions
1 m argon arc discharge using 8 kV pulse generator
Higher current leads to more reproducible discharge
Longitudinal interferometry reveals radial expansion of plasma during discharge pulse
ne ~ 1020 – 1021 m-3 densities reached
Complex ionisation and diffusion dynamics to be investigated further with PIC simulations
Plasma emission spectroscopy provides information about the plasma temperature
Acknowledgements
AWAKE scalable plasma sources R&D team
Claudia Cobo c.cobo@imperial.ac.uk