## Slide 1
ELI NP status and challenges
for the LPAW community
Victor Malka ELI-NP, Magurele, Romania Weizmann Institute of Science, Rehovot, Israel
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 2: Extreme Light Infrastructure
Attosecond Light Pulse Source, offering unique time-resolved investigation possibilities for both nonrelativistic and relativistic interaction of light with all the four states of matter” (ELI ALPS, Szeged, HU)
High-Energy Beamlines Facility, developing and applying short pulses of ultra-intense radiation to explore extreme conditions or produce high-energy particles and radiation (ELI Beamlines, Prague, CZ)
Nuclear Physics Facility with ultra-intense lasers and brilliant gamma beams to produce and explore new nuclear states or generate neutron beams (ELI NP, Magurele, RO)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 3: Extreme Light Infrastructure: The laser road
ELI Beamlines
ELI ALPS
ELI-NP
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 4: ELI-NP in a nutshell
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
Geothermal system
Laboratories and workshops
9 Experimental areas
Clean rooms ISO6 - ISO7
120,000 tons antivibration platform
2 x 10 PW Laser System
Laser Beam Transport System
Over 32.000 sqm of built area and 270.000 cubic meter of air to condition

## Slide 5
ELI-NP: Where do we stand today
Overall implementation status: more than 85%
Major Components:
High power laser system (HPLS) + Laser beam transport system (LBTS)
  100% – fully implemented and operational (2019 HPLS, 2020 LBTS)
Gamma beam system
  45% – completion delayed
Experimental setups and laboratories
  100% – fully implemented and operatonal
Civil constructions
  100% – fully implemented and operational (since 2016)
2 x 10 PW High Power Laser System
Laser Beam Transport System
Gamma Beam System
Laboratories and Workshops
Experimental Rooms
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 6: Combined Experimental Areas
E7: 10 PW + 1 PW + 𝛾/e–
High Field QED
E3: X rays
Test/develop instrumentation and technology
E6: 10 PW @ 1/min
High Field QED
E1: 10 PW @ 1/min
High Field Physics
Laser driven
Nuclear Physics
E4: 0.1PW@10 Hz
Photon-photon int., LWFA, betatron
E5: 1 PW @ 1 Hz
E8 & E9: 𝛾 beams
Photonuclear Reactions
ERA: positrons Material Studies
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 7: High Power Laser System operation
2021 – Delivered beam time – Total of 36 weeks
  16 weeks @ 100 TW output
  20 weeks @ 1 PW output
2022 – Delivered beam time – Total of 59 weeks
  20 weeks @ 100 TW output
  28 weeks @ 1 PW output
  11 weeks @ 10 PW output
2023 – Delivered beam time – Total of 52 weeks
  7.5 weeks @ 100 TW output
  20 weeks @ 1 PW output
  24.5 weeks @ 10 PW output
Commissioning experiments
  Experiments approved by ELI-NP ISAB
  Performed with expert users from Italy, Germany, Czech Republic, Israel, Japan, UK, US,
April 13th 2023 – a landmark in the history of plasma physics
  the most powerful laser system in the world, at ELI–NP, has focused for the first time in the world 10 PW laser pulses on solid targets marking an important milestone in laser plasma physics
Parabola
Microscope
objective
Inside E1 10 PW interaction chamber
First tests at 10 PW show focal spot below 3 µm
⟹ ≲ 1023 W/cm2
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 8: High Power Laser System operation
2021 – Delivered beam time – Total of 36 weeks
  16 weeks @ 100 TW output
  20 weeks @ 1 PW output
2022 – Delivered beam time – Total of 59 weeks
  20 weeks @ 100 TW output
  28 weeks @ 1 PW output
  11 weeks @ 10 PW output
2023 – Delivered beam time – Total of 52 weeks
  7.5 weeks @ 100 TW output
  20 weeks @ 1 PW output
  24.5 weeks @ 10 PW output
Commissioning experiments
  Experiments approved by ELI-NP ISAB
  Performed with expert users from Italy, Germany, Israel, UK, US, Czech Republic, Japan
April 13th 2023 – a landmark in the history of plasma physics
  the most powerful laser system in the world, at ELI–NP, has focused for the first time in the world 10 PW laser pulses on solid targets marking an important milestone in laser plasma physics
Parabola
Microscope
objective
Inside E1 10 PW interaction chamber
First tests at 10 PW show focal spot below 3 µm
⟹ ≲ 1023 W/cm2
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 9: ELI-NP Infrastructure
Laser bay
HPLS architecture
Output type | 100 TW | 1 PW | 10 PW
Pulse energy (J) | 2.7 | 25 | 242
Pulse duration (fs) | < 25 | < 24 | <23
Repetition rate (Hz) | 10 | 1 | 1/60
Calculated Strehl ratio from measured wavefront | > 0.9 | > 0.9 | > 0.9
Pointing stability (µrad RMS) | < 3.4 | < 1.78 | < 1.27
Pulse energy stability (rms) | < 2.6 % | < 1.8 % | < 1.8 %
Measured parameters of HPLS
ISO 7 cleanroom
Routine operation with the two laser arms in parallel
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
E7:
Combined laser-gamma experiments
E6:
2x10PW, 1shot/min
QED experiments
E5: 2x1PW, 1Hz experiments
1PW block
Ti:Sapph
Flashlamp based
1PW amplifier
Ti:Sapphire
25J@1Hz/ <25fs
10PW amplifier
Ti:Sapphire
220J@1shot/min
Oscillator+
OPCPA + XPW
10mJ@10Hz <20fs
E4: 2x0.1PW, 10Hz, experiments
1PW compressor
100TW compressor
1PW block
Ti:Sapph
Flashlamp based
100TW amplifier
Ti:Sapphire
2.5J@10Hz/ <25fs
100TW compressor
1PW compressor
1PW block
Ti:Sapph
Flashlamp based
100TW amplifier
Ti:Sapphire
2.5J@10Hz/ <25fs
1PW block
Ti:Sapph
Flashlamp based
1PW amplifier
Ti:Sapphire
25J@1Hz/ <25fs
10PW amplifier
Ti:Sapphire
220J@1shot/min
10PW compressor
10PW compressor
E1:
2x10PW, 1shot/min
Nuclear Physics exp.
L
B
T
S
Oscillator+
OPCPA + XPW
10mJ@10Hz <20fs

## Slide 10: Most Powerful Laser in the World
Chart: Time of the day
| 0.63541666666666663 | 0.63611111111111118 | 0.63680555555555596 | 0.63749999999999996 | 0.63819444444444495 | 0.63888888888888895 | 0.63958333333333395 | 0.64027777777777894 | 0.64097222222222305 | 0.64166666666666805
Energy in main peak | 42.9792 | 66.0264 | 73.128 | 103.0304 | 131.8064 | 167.0768 | 201.3792 | 220.3432 | 221.188 | 218.1608
Peak Power (PW) | 1.9806 | 3.0427 | 3.37 | 4.7479 | 6.074 | 7.6994 | 9.2801 | 10.1541 | 10.193 | 10.0535
Unique system in the world:
power, intensity, number of beams, versatility and flexibility
demonstrated power level 10 PW
combination of 2 high-power lasers
Laser peak power
Spectral characteristics
Time characteristics
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 11: ELI–NP @ 10 PW
Chart: Demonstrated Laser Peak Powers in the world
| 2007 | 2008 | 2009 | 2011 | 2012 | 2012 | 2013 | 2013 | 2017 | 2017 | 2017 | 2017 | 2018 | 2019
 | 0.56 | 0.3 | 0.5 | 1.16 | 0.4 | 0.9 | 0.61 | 2 | 1.3 | 0.85 | 4.2 | 4.9 | 1.3 | 10
LFRC China
GIST S Korea
QST Japan
Berkeley USA
Colorado S. U. USA
SIOM China
Inst Physics China
U Michigan USA
IAP, RAS Russia
Ohio S U USA
ELI-NP Romania
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 12: Transition Implementation ⇒ Operation: 2020-2023
Year
2021
2022
2023
2024
Experiments
Apr.
Jul.
Oct.
Jan.
Apr.
Jul.
Oct.
Jan.
Apr.
Jul.
Oct.
Jan.
Apr.
100 TW Comm. Exp. E4
1 PW Commissioning Exp. E5 1 PW Commissioning Exp. E7
10 PW Commissioning Exp. E1 10 PW Commissioning Exp. E6 Flagship Exp. (IMPULSE)
user 1 PW
2020
Mar.
user 100 TW
user 10 PW
  100 TW (E4): 2022 Four-wave mixing in vacuum, in search of dark matter candidates
    X ray production through betatron emission
  1 PW (E5 - E7): 2022 - 2023 Benchmark TNSA proton acceleration
  Benchmark LWFA electron acceleration
    Optimization of high charge, stable electron acceleration
  10 PW solid target (E1): 2023 Demonstrate extreme focal intensity through laser‐γ conversion (“γ‐flash”)
    Demonstrate over 200 MeV proton acceleration (neutron generation add‐on)
    Dense heavy ion beams for nuclear physics
  10 PW gas target (E6): 2023 10 PW laser wakefield acceleration of multi GeV electron beams
Commissioning experiments
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 13: Recent development: ps Contrast improvement
Chart: Time [ps]
Old Contrast
Improved Contrast
Scientific collaboration with Marvel Fusion and Thales LAS France in the field of ICF
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
101
100
10-1
10-2
10-3
10-4
10-5
10-6
10-7
10-8
10-9
10-10
10-11
10-12
10-13
contrast
-60 -50 -40 -30 -20 -10 0 10
Time (ps)

## Slide 14: Recent development: Stretcher convex mirror
New mirror – RMS roughness - 0.2 nm
Old mirror – RMS roughness - 3.5 nm
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 15: ns contrast on the 10 PW output
Chart: Time [ns]
Chart: 
Improved Contrast
Previous Contrast
101
100
10-1
10-2
10-3
10-4
10-5
10-6
10-7
10-8
10-9
10-10
contrast
-70 -60 -50 -40 -30 -20 -10 0 10
Time (ns)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 16: ns contrast improvement/ pockels cell
Pockels cell:
Leysop LTD
50mm aperture
98% Deuterated KD*P
P1, P2, P3, P4:
Polarizers
Laser Components
72° AOI
Pockels cell for back reflection protection used for ns contrast improvement
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 17: Recent development: 11 fs post-compression at 1 J
1J pulses post-compressed
@11.36 +/- 0.4 fs
Experimental set-up:
1 J, 26 fs input pulses @10 Hz
full aperture metrology
Spectrum: Initial and after 2 mm BK7
SPIDER duration: Initial and after 2 mm BK7
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 18: About 10 fs temporal drift stabilization for 1 PW outputs
scanning time (s)
Relative delay between the pulses (fs)
11 fs rms for 50 min
100 fs drift in 30 min
Temporal fluctuations suppression after 129 pulses
Laser
control room
Figure 3: HPLS layout
Laser source: front-end B
LP-01 – LASER Room
Stretched probe pulse
Compressed ultrashort pulse
Plasma mirror
Laser target
Spectral cut pulse
Optical fiber & spectrometer
A
B
170 m parallel propagation
Running amplifiers
Measurement after 1 PW compressors
Method: Plasma mirror ultrafast optical switch
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 19: Far-field at 1 PW & 10 PW: HPLS focal spot & stability
FWHM ~ 2.8 µm
Gaussian fit
Far-field
40 µJ, 25 fs
Best focal spot
10 PW focal spot and pointing stability
1 PW focal spot and pointing stability
Focal spot RAW image
Focal spot image
5 µm
µm
Laser beam profile
Typical focal spot
Pointing fluctuation (mrad)
  Short focal mirror: 707 mm focal length (F# ~3.7)
  Spot size diameter: ~ ﻿3.6 ± 2 µm at FWHM
  Short focal mirror: 1500 mm focal length (F# ~2.7)
  Spot size diameter: ~ ﻿2.9 ± 2 µm at FWHM
Pointing fluctuation (mrad)
x Pointing (mrad)
y Pointing (mrad)
x Pointing (mrad)
y Pointing (mrad)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 20: 100 TW Experimental area E4
VE1: HV
VE2: UHV
Laser
HV
UHV
Interaction chambers
25 µm
Laser beam profile
Example of focus properties
  Parabolic mirror: 1.5 m focal length (F# ~28)
  Spot size diameter: ~ ﻿22±2 µm at FWHM
  Encircled energy ~ 70% @ 1/e2
100 TW laser beam features
  Energy: < 2.5 J
  Pulse duration: < 25 fs
  Central wavelength: ~ 810 nm
  Beam diameter: ~ 54 mm
  Laser pointing fluctuation on target: ~ ±7 µrad
  Energy stability: <2.5%
  Repetition rate: 10 Hz (single shot possible)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 21
Helical laser beam (Laguerre-Gaussian beam)
Laguerre modes
l=0
l=1
l=2
l=3
Experimental results
(far-field: focal spot at full power with but 25 µJ)
Near-field high power shot 23 J, 900 TW
Helical mirror element
Mid-field
full power with 25 µJ
M. Cernaianu et al., in preparation
Typical Gaussian
Helical wavefront
Lower divergence H+ beam with increased helical order
Helical PM, novel technique
Complex wavefronts generation for ion acceleration
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
1.1 3.2 4.5 5.6. 7.5 9.7 12.3 14.5 16.8
Proton cutoff energy (MeV)
25
20
15
10
5
0
Divergence (degree)

## Slide 22
100 TW LWFA example of results
Experimental setup
LWFA electron acceleration in gas jet
Gas: He
Gas: He + 2% N2
nozzle
2 mm
gas
laser
plasma channel
~0.7 T
Acceleration field of ~ 1 GV/cm
I0 ~ 1019 W/cm2
E4
Electron diagnostics: spectrometer (up to 500 MeV) – 16 cm long dipole magnet
with 3 cm gap and ~0.7 T B-field, and a Lanex screen
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 23
Gas jet target and gas cell from 2mm to 2 cm long
SourceLab variable metal gas cell, fix 3D printed gas cell, 2 mm metal gas jet
Pure He and mixture He +2% N2 were used
F=5000mm parabola
Max. electron energy attained with both Helium gas and admixture of ≈ 2 GeV
Electron diagnostics: spectrometer (up to 3 GeV) – 30 cm long dipole magnet with 3 cm gap and ~1 T B-field, and a Lanex screen
Shadowgraphy and WFS (plasma channel)
Electron Beam Energy Spectra for pure He
zero point
Electron deviation on lanex
Electron Beam Pointing in a typical day from gas admixture
>2 GeV electron beam obtained with 2 cm gas cell
1 PW commissioning with gas targets
Experimental setup
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 24
PM triggered later, estimated intensity contrast < 10-8 @ -15 ps
PM triggered earlier contrast estimated < 10-8 @ -15 ps
Intensity contrast ~10-7 – 10-8 @ -15 ps
Intensity contrast ~10-7 – 10-8 @ -15 ps
Scan of maximum proton energy with target thickness, and laser energy with different temporal contrast
Solid line: w PM
Dashed line: w/o PM
16 J
5.7 J
13 J
14 J
Laser energy on target
Preliminary analysis
Temporal contrast improvement allowed the increasing of the cutoff energy for thin targets
1 PW commissioning with solid targets
target thickness (mm)
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
40
35
30
25
20
15
10
Proton cutoff energy (MeV)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 25
Electron acceleration with longitudinal laser fields
Traditional direct laser acceleration (DLA) uses , making large electron divergence unavoidable.
that is present in a tightly focused laser to accelerate electrons directly forward without transverse oscillations.
Prolonged acceleration is ensured by an empty micro-channel target that guides the laser without allowing it to defocus.
Preliminary experimental results:
I = 4x1021 W/cm2, 200µm length cylinder,
12µm diameter
CsI gamma detector
e- spectrometer trace
Transmitted
laser light
Alexey Arefiev (UC San Diego)
Mihail Cernaianu (ELI-NP)
1 PW electron acceleration in hollow micro-channel
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 26
10 PW proton acceleration
132 MeV
1 MeV
9.5 MeV
20 MeV
31 MeV
IL = 3.6 x 1022 Wcm-2 on 400nm Al foil
121 MeV
Radiochromic and CR39 stack detector
Hole at 6um to show
101 102 103 104 105
Al foil thickness scan
Target thickness (nm)
Proton energy (MeV)
PM anti-ref improved
0.3% -> 0.1%
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 27
10 PW proton acceleration
Laser peak intensity on target (1022W/cm2)
0 1 2 3 4
Proton energy (MeV)
160
140
120
100
80
60
40
20
0
400 nm Al foil thickness
E
Examples of parametric studies
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
140
120
100
80
60
40
20
0
Focus scan on 1.5 mm Al foil (I3.5x1022W/cm2)
Proton energy (MeV)
-60 -40 -20 0 20 40 60
Focus position from the target (mm)

## Slide 28: Perspectives: Studies under Extreme Conditions
Extreme light intensity (10 PW ⟹ 1023 W/cm2)
Nuclear Physics with Lasers
Extreme light pressures (Tbar)
10 PW radiation pressure acceleration of dense ion beams
Strong-field QED
Extreme electric fields (1015 V/m)
10 PW laser + GeV LWFA electrons
Radiation reaction Breit-Wheeler pairs
QED vacuum
Nuclear reactions in plasma
Neutron-rich nuclei
10 PW laser + solid target
PW 𝛾-source
Develop particle beams for nuclear and QED experiments and for Societal Applications (muons imaging, hadrontherapy, Cancer detection, radioisotopes production, security)
Ultra-intense
neutron source
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 29: All optical Compton experiment at Apollon/ELI NP
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
dipole
g lanex
Lyso
e- Lanex
Plasma mirror
g Rays
gas jet
laser
Courtesy of Aimé Matheron

## Slide 30: All optical Compton experiment at Apollon/ELI NP
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
f/60 spherical, 6 cm gaz jet
3-5 GeV, 1 nC (>2 GeV), 1.6 mrad
Successive shots ( signal)
Apollon
ELI-NP
A. Matheron et al., submitted

## Slide 31: All optical Compton experiment at Apollon/ELI NP
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
Critical photon energy of 0.14 GeV
APOLLON
ELI-NP
MAX
MAX
Critical photon energy of 0.55 GeV
Quantum effects may start to play a role
A. Matheron et al., submitted

## Slide 32
It is all about people ...
269 employees
48 foreign researchers and engineers
1 Armenia, 2 Bulgaria, 2 China, 1 Czech Republic, 5 France, 1 Russia, 5 Germany, 1 Greece, 9 India, 1 Israel, 3 Italy, 4 Japan, 2 Malesia, 1 Pakistan, 3 Poland, 1 USA, 1 Sweden,1 Taiwan, 2 Turkey, 1 Uzbekistan
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
more than 120 young researchers below 35
56 Students PhD, master and bachelor
Journal Club & Board of Study

## Slide 33
ELI ERIC is Open to the World: the 3 Access Mode
Excellence-Based Access – Evaluation of proposals by international peer-review panels. Results of experiments published and open.
Mission-Based Access – Thematic research granted on the basis of scientific missions pursuing challenges. Proposals reviewed by international panels. Results published and open.
Proprietary Access – Paid access for industrial or other users. Results are retained by the user, consistent with ELI ERIC’s Data and IPR Policy.
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 34
Conclusion and perspectives
Unique and versatile facility
Commissioning is almost finished
Access capability is validated and may be improved
Attractivity has to be be improved (PhD/Post-Doc/Engineers)
Scientific grand challenges are on the way
Single laser : simple setup
Auto-alignment : 100 % collision rate
-rays in the GeV range
Quantum effects may start to play a role
New opportunities for Collaborations (Japan, Germany, …)
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)

## Slide 35
Conclusion: ELI NP welcomes you !
LPAW, Ischia Island (Naples, Italy), April 14-18 (2025)
200
150
100
0
9:00 11:00 13:00 15:00 17:00
Time
Time
Pulse energy (J)
9:00 11:00
13:00 15:00 17:00
Time of the day