## Slide 1: Design and Prospect of MELODY in China
Yu Bao
IHEP/CSNS
On behalf of MELODY collaboration
2025.5.27
Muon4Future 2025

## Slide 2: Outlines
MAIN CONTENT
1
Muon Physics and Applications
2
Design and Prospect of MELODY
3
Progress and timeline
4
Summary
（1） Surface muon beam
（2） Negative muon beam
（3） Decay muon beam

## Slide 3
Muon Applications:
Muon tomography
Muon Physics
Precision measurements
  g-2
  EDM
cLFV
Muon collider
μSR
MIXE/MuX
Muon – from discovery to application
Carl Anderson
Nobel Price 1936
I. I. Rabi
Nobel Price 1944

## Slide 4
Muon Sources worldwide
MuSIC
CW
40Hz
CW
25Hz
  FNAL：g-2/mu2e
  RAON
Pulsed
~ 100 ns
10s ms
t
CW
< 1ns
10s ns
t

## Slide 5: China Spallation Neutron Source
1
CSNS
Dongguan
Shenzhen
Guangzhou

## Slide 6: China Spallation Neutron Source（CSNS）
1
MELODY
Accelerator: 170kW 25Hz 1.6GeV proton beam
Neutron Spectrometers: 9 built and 2 under construction
Phase I completed in July, 2018
Phase II started in Jan, 2024

## Slide 7: CSNS II Project (Approved on Jan. 11, 2024)
1
300MeV SC
500 kW
500 kW
9 more neutron spectrometers
MELODY
Muon station for sciEnce technoLOgy and inDustrY

## Slide 8: Chinese Muon Community
2
muSR users
Particle Physicists
Element Analysis
USTC
Fudan University
IOP
Zhejiang University
…
Peking University
IHEP
SJTU
SYSU
…
Palace Museum
National Museum
CIAE
IHEP
…

## Slide 9: Architectural Design of MELODY
03
MELODY

## Slide 10: Overview of MELODY
SMT1
SMT2
DMT1 Reserved
NMT
Reserved
DMT2
Reserved
Water Cooling system (underground)
Sampling room
control room
Proton Beam
Waste Target
SMBT
NMBT
DMBT

## Slide 11
Design features
3.1
Target
  Stand-alone target: more freedom to design
  Thick target: 10 cm interaction length
  Copper Target: high production
Beamlines
  Surface Muon: Solenoid focusing; AI optimized; Large acceptance
  Negative Muon: by-product, low cost, dedicated μ- beam
  Decay Muon: Large acceptance; wide applications
muSR spectrometer
  High Asymmetry: 0.3
  Large number of detectors: 3024 units

## Slide 12
Surface Muon Beam
3.1
Coll5
SMSOLX
SMBA
SMSOL1
SMBB
SMSOL2
SMK
SMSOL3
SMSP
SMBC
SMWF
SMSOL4
SMSOL8
SMSOL9
SMSOL5
SMSOL6
SMSOL7
SMT1
SMT2
Coll1
Coll2
Coll3
Coll4
Proton
optical design
Layout of SMBT
Fully focusing solenoids, 3 dipole bending magnet.
SMWF, SMK, 5 collimators
Deflection angle: SMBA @34, SMBB @40.9, SMBC @90, Kicker @8, Septum @15
Optical design by Transport
Features: Fixed energy @4 MeV, higher acceptance, cost-effective
Design parameters
Momentum：28 MeV/c, Polarizability：>95%
Intensity：>105 μ/s, Positron background：<1%
AI optimization
2 terminals:
SMT1 for muSR
SMT2 for R&D

## Slide 13
Science for SMT1
3.2
MuSR：Magnetic material, superconductivity, battery, semiconductor
Dedicated beam for muSR
~1584 detector units in the first stage (~3024 units in total)
Counting Rate：~ 3.8107 e+/hour @1 Hz (~76 MEvent/hour in total)
Asymmetry：> 0.3
Pulse length：~130 ns (consider slicing to 10 ns)
Temperature: 2-300 K with cryostat
LF: 0-5000 G
TF: 0-400 G
Beam spot: Ф10-30 mm
Spectrometer Design

## Slide 14
Science for SMT2
3.2
Muon moderation
Muonium experiments
Muon acceleration
Potential Muon Physics
  MuMuBar
Muon technology development
Muon moderation
Muonium production
Muon PW acceleration

## Slide 15
Muon moderation
3.2
Detector
Muon beam
…
… …
…
30
300
Gas cell
Acc E-field
HV
100 mbar He gas
HIFI B-field
20
15
5
10
Electrodes
Cu collimator
C foil
20
With E-field
Planned Test At ISIS

## Slide 16: Muonium to Anti-muonium conversion
Signals:
Michel Electron
Thermal Positron
Detection Efficiency
Total sensitivity with 108μ/s
Michel Electron detection with LGAD detectors

## Slide 17
Negative Muon Beam
3.2
NMBT: Dedicated μ- beam
5 focusing solenoids
1 dipole magnet
1 wien filter
Beam parameters
Momentum：29 MeV/c @13% (FWHM)
Penetration：~ 50 μm in Fe
Beam size： Φ100 mm
Beam intensity：4.4×105 Hz (Φ100 ratio>90%)

## Slide 18
Science for NMT
3.2
18
Non-destructive elemental analysis:
  Sensitive for almost all elements (including C, N, O)
  No activation for samples
  Archeology:
    Palace Museum
    National Museum
    Guangdong Museum
    FURUKAGE Conservation center
Moon soil
Elemental analysis for Archeology
μ- and μ+ study on Li+ battery anodes
J. Phys. Chem. C 2022, 126, 25, 10506

## Slide 19
Science for DMT
3.2
Momentum: 20 ~ 120 MeV/c
Charge: + or -
Intensity: 105~107 muon/s
Penetration in Cu: 1 ~ 50 mm
Polarization: 50% ~ 99%
Decay muon beamline with 2 terminals
High-energy MuSR
Thick Samples
Depth scan MIXE
Depth scan for archaeology
Single Event Effect
Large capture cross section of μ-
Muon
Imaging
Thick samples
Samples in container
High field
Thick moon rock
Batterries

## Slide 20
Design Parameters
Proton driver | Power | Repetition | Energy | Time Structure |  | σx | σy | 
 | 20 kW | 1 Hz | 1.6 GeV | 120ns/409ns |  | 3.1 mm | 8.5 mm | 
Muon beam | Surface Muon (SMBT) |  | Negative Muon (NMBT) |  |  | Decay Muon (DMBT) |  | 
Momentum | 28 MeV/c |  | 28 MeV/c |  |  | 20~120 MeV/c |  | 
dp/p | 6% |  | 13% |  |  | 8% @ 120 MeV/c |  | 
Beam spot | Φ10mm-Φ100mm |  | Φ100mm |  |  | Φ30mm |  | 
Intensity | 105-107 μ+/s |  | 4×105 μ-/s |  |  | 4×106 μ+/s |  | 
Polarization | > 95% |  | ~ 20 % |  |  | > 70% |  | 
Pulse width | 130 ns (SP) ~ 520ns (DP) |  | 520 ns |  |  | 130 ns (SP) ~ 520ns (DP) |  | 
Spectrometer | Segments | Asymmetry | Count Rate |  | FOM: A2*R | Temperature |  | LF/TF
 | 1584/3024* | ~0.3 | 38/76* MEv/h |  | 2.9/5.8* | 2K ~ 300K |  | 5000 G/ 400 G
* Can be upgraded to

## Slide 21
Physics Design Review
July 1st, 2024

## Slide 22
Timeline of MELODY
4
Chart: 
| Beam test | Spectrometer | Target Station | Muon Beamline | Civil Construction
Technique Design | 2025.6 | 2025.1 | 2025.1 | 2025.1 | 2024.1
Engineering Development | 2.5 | 2 | 1.5 | 2.5 | 2
Installation | 0.5 | 1 | 1.5 | 1 | 0.5
Trial Run | 1.2 | 1.7 | 1.7 | 1.2
Complete of Muon Hall
Start trial run

## Slide 23
Workshops of MELODY

## Slide 24
Construction Progress
2025.2.20
2024.8.20
2025.5.14

## Slide 25
MELODY TEAM
Target： Chen Wu、 Lei Liu、Gang Zhang、Ning He、Zhiduo Li、Nikos Vasiloploss、Jiaxin Chen、Zhixin Tan、Yu Liu、Congju Yao、Yongji Yu、Guangyuan Wang、Junsong Zhang、Huihong Liang、Huayan He、Xiaoyin Mo
Beamlines：You Lv、Cong Chen、 Guangdong Liu 、Changdong Deng、Yuwen Wu、Junhao Wei、Xin Qi、Wenqing Zhang、Pengcheng Wang、Yuliang Zhang、Yongcheng He
Spectrometer：Qiang Li、Ziwen Pan、Yang Li、You Lv、Ruirui Fan、Haiyan Du、Yuhang Guo、Hao Liang、Tianyi Yang、Bangjiao Ye
Coordinator: Yu Bao

## Slide 26: SUMMARY
05
MELODY has been approved and started construction
The surface muon beam will be constructed first. The negative muon beam and the decay muon beam will be built in the future
We will be able to welcome all of you in 4 years!
We Welcome all collaborations!
yubao@ihep.ac.cn