## Slide 1
Basis of ion acceleration and status of the ELIMAIA beamline
11.07.2024
Date:
Lorenzo Giuffrida
Head of department of Ion Acceleration and Application of High Energy Particles
ELI Beamlines Facility. The Extreme Light Infrastructure ERIC Email: Lorenzo.Giuffrida@eli-beams.eu

## Slide 2
Laser-plasma accelerator: an introduction
ELIMAIA beamlines
ELIMED commissioning
Applications
Summary

## Slide 3
The birth of the laser, 1960
Theodore Maiman
What is a laser?
Light Amplification by Stimulated Emission of Radiation
Components of a typical laser system: 1. Gain medium 2. Laser pumping energy 3. High reflector
4. Output coupler
5. Laser beam
Types of lasers: Gas lasers; Chemical lasers; Excimer lasers; Solid-state lasers; Fiber lasers; Photonic crystals lasers; Semiconductor lasers; Dye lasers; FEL
Ruby Laser (solid state) – 694 nm, ~1 ms

## Slide 4: From Nobel Prize to Extreme Light a technological Breakthrough enables ELI
Gérard Mourou and Donna Strickland won the 2018 Nobel Prize for Physics for proposing “Chirped Pulse Amplification” for high-power, ultrafast, extremely intense lasers.
Mourou proposed ELI in 2004, and from 2007-2010 initial research including 15 institutions and € 7.9M from the Seventh Framework Programme.
Optical Parametric Chirped Pulse Amplification (OPCPA)
Chirped Pulse Amplification (CPA)
AIR
VACUUM
D. Strickland and G. Mourou, Compression of amplified chirped optical pulses, Optics Communications. Volume 56, Issue 3, 1 1985

## Slide 5
TNSA mechanism
Typical Laser Intensity (1018-1020 W/cm2)
Accelerated Relativistic Electrons (multi MeV) traverse the thin target (0.1÷100 mm).
H-ultrathin rear-side layer is ionized by the electron beam and protons are generated.
Fast electron cloud builds up a quasi-electrostatic field exceeding ~10 TV/m accelerating protons in the forward direction to 10s-MeV energies.
TNSA features
Protons/ions are accelerated along the target normal
Ions with the highest charge-to-mass ratio (protons) dominate the acceleration, gaining the most energy (electric field screening effect)
Exponential ion energy distribution (large energy spread)
Target Normal Sheath Acceleration (TNSA)
a robust and experimentally well-established mechanism
Clark, PRL (2000); Maksimchuk, PRL (2000) Snavely, PRL (2000)

## Slide 6
Short duration @ source: bursts with duration ~ ps (acceleration time ~ laser pulse width)
Highly laminar source: eN < 0.1 p mm.mrad (virtual point source: ~ µm << real source)
Broad spectrum: continuum up to cutoff energy (lower divergence for higher energies)
High intensity pulse
F. Nurnberg et al, RSI, 80, 033301 (2019)
Ion Beam Properties
TNSA regime

## Slide 7
Laser-driven ion acceleration mechanisms
laser intensity vs. target density
Courtesy of S.S. Bulanov

## Slide 8
Borghesi, NIMA (2014)
Ion Acceleration experimental scaling
beyond the 100 MeV energy record?
Zeil, NJP (2010)
Higginson, Nat. Comm. (2018)
E  IL1/2

## Slide 9
Target Engineering (TNSA)
enhanced beam properties
Margarone et al, PRL109 (2012) 234801
Margarone et al, PRAB 18 (2015) 071304
Giuffrida et al, PRAB 20 (2017) 081301
Nano- and micro-structures for enhanced TNSA
PIC simulations
experimental spectra
proton cutoff energy
proton flux
beam homogeneity

## Slide 10
H-ribbon
L3-HAPLS
0.3J @3.3 Hz
ELISE II @ ELI
Target Engineering (HB-RPA)
enhanced beam properties
Cryogenic solid-H for enhanced Hole-Boring Radiation-Pressure-Acceleration
Chagovets et al, Appl. Sci. 2021, 11(4), 1680
repetition rate
energy bandwidth
PIC simulations
experimental spectra
H+
Margarone et al, PRL 2021 (submitted)
VULCAN-PW
400J/1ps

## Slide 11
Dosimetry & Sample Irradiation
Selection, Transport
& Diagnostics
Acceleration, Collimation
& Diagnostics
Ion Accelerator
ELIMED
ELIMAIA user beamline
D. Margarone et al., “ELIMAIA: A Laser-Driven Ion Accelerator for Multidisciplinary Applications”, Quantum Beam Science 2 (2018) 8
G.A.P. Cirrone et al., “ELIMED-ELIMAIA: The First Open User Irradiation Beamline for Laser-Plasma-Accelerated Ion Beams”, Frontiers in Physics 8 (2020) 564907
F. Schillaci et al., “The ELIMAIA Laser-Plasma Ion Accelerator: Technology Commissioning and Perspectives”, submitted to QuBS, Laser-Driven Irradiation Facility special issue
Lorenzo.Giuffrida@eli-beams.eu
ELI Multidisciplinary Applications of laser-Ion Acceleration

## Slide 12
ELIMAIA: Setup overview
In-air laser diagnostic station
(BDS) – on-shot & full-power
Laser Alignment and Plasma diagnostic stations
Ion and gamma diagnostic stations
Interaction chamber
Ion beam transport
Ion Dosimetry and sample irradiation
Lorenzo.Giuffrida@eli-beams.eu

## Slide 13
Ion diagnostics
TOF signal
TP raw data
Protons
Ions
Online data analysis (1-10 Hz)
raw
processed
g-Calorimeter
g-Scintillator detector
X/g-ray diagnostics
Plasma imaging/
spectroscopy
On-shot laser diagnostics
ELIMAIA : Online laser/plasma/ion diagnostics

## Slide 14
ELIMAIA Laser-Plasma Accelerators:
Reproducibility and stability shot-to-shot
Fluctuations | Single shot series | 0.5 Hz Rep. rate
Laser energy | 0.3% | 0.2%
Laser intensity @FWHM | 0.8% | 2.7%
Tbrems | 4.94 % | 4.6%
Photon flux | 1% | 1%
Laser intensity >> 3e21 W/cm2
Reduced fluctuations shot-to-shots

## Slide 15
ELIMAIA Laser-Plasma Accelerators:
Some Performances
Optimization phase
We tested with three laser contrast levels and defocusing:
different materials;
different thicknesses;
Main information
Max cut-off energy >> 30 MeV;
Proton fluxes @ 3 MeV >>1e11 protons;

## Slide 16
Proton imprint on RCF layers
ELIMAIA results looks above the scaling law for TNSA mechanism
ELIMAIA Laser-Plasma Accelerators:
ELIMAIA vs Literature results
42 MeV proton energy
M. Zimmer et al., Physical Review E, 2021

## Slide 17
ELIMED section: Setup overview
Date:
Page:
17
11.07.2024
ELIMED Station | Design parameters @ user sample
Proton energy | 5-60 MeV (angular spread and PMQ limited)
Ions/shot | 1∙108-1∙1010/sr
Bunch duration | ~10 ns
Ion beam aperture | ~ 1 deg (FWHM)
Ion beam spot size | 0.1-10mm (FWHM)
Repetition rate | Static setup allows for CW beams. Up to 1Hz in active energy modulation mode
Interaction Chamber
Collection System
Energy Selection System
Transport and Focusing System
Dosimetry and Irradiation System
Collection System:
5 PMQs, 36mm magnetic bore, 100 T/m gradient with 2% uniformity
Energy Selection system:
4 electro-dipoles, 55mm bore, 0.06 – 1.226 T with 0.5% uniformity, linear resolution with slit aperture size, active energy modulation possible
Dosimetry and Irradiation System:
SEM for beam current monitor, Multi-gap chamber for relative-online dosimetry, FC for absolute dosimetry, automated sample irradiation system

## Slide 18
18
Angular divergence = 5° (FWHM)
Transmission efficiency ~12% (9,2e7 H+/bunch)
Beam transport: TNSA-like protons simulation

## Slide 19
19
ELIMED section: experimental results 1
RCF stack@40 mm
25 MeV protons
100 shots with central energy of 20 MeV selected with about 30% of resolution [14-25MeV]
Angular divergence = 5° (FWHM)
Transmission efficiency ~12% (9,2e7 H+/bunch)

## Slide 20
Beams appears after adjustment with steerers and dipole4
Extraction point with MCP beam viewer
First beam extracted
First beam focused
Beam focused and MCP optimized to avoid saturation before delivering it to the in-air station for irradiation of samples
ELIMED section: experimental results 2

## Slide 21
First radiobiological experiment
First ever successful radiobiological experiment at ELI Beamlines with laser accelerated protons
Flagship experiment FLAIM (Flash and ultrahigh dose-rate radiobiology with Laser Accelerated Ions for Medical research) within the IMPULSE project
0.43 Gy, 30 min
1.48 Gy, 30 min
1.1 Gy, 30 min
Non-irradiated sample
new possibilities for radiobiological research at ELI Beamlines
1.1 Gy,
24 h
  Cell culture – normal skin fibroblasts AG01522
  Biological assay for DNA damage
    DSB 53BP1 foci

## Slide 22
Date:
Page:
22
11.07.2024
Scientific & Societal Impacts
ELIMAIA laser-plasma accelerator:
Advanced laser-driven ion mechanisms;
Laser-driven nuclear reactions for tertiary particle generation;
Ion stopping power with tunable ion source;
Machine learning studies.
~46MeV
~32MeV
~1deg div.
~42MeV
Courtesy of S. Kar (QUB, UK)
Proton beam from “coil target” (collimation and post-acceleration)
Courtesy of F. Consoli (ENEA, IT)
Alpha-particles source triggered by laser-driven pB nuclear fusion reaction
Neutrons from Pitcher-catcher
Laser-driven neutron research

## Slide 23
Date:
Page:
23
11.07.2024
Scientific & Societal Impacts
Multidisciplinary user applications using ELIMED:
Radiobiology, cancer treatment (hadrontherapy & BNCT), medical imaging
Radiation chemistry with protons & neutrons (pulsed radiolysis of water, management of nuclear waste)
Space radiation (electronics, radiobiology in space)
Material analysis for cultural heritage (PIXE, XRF, DPAA)
Non-destructive inspection of massive objects with proton & neutron radiography
ultrahigh dose rate and FLASH conditions in single shot or rep. rate

## Slide 24
L. Giuffrida, B. Rus, D. Margarone, P. Blaha, T. Chagovets, M. Cuhra, J. Cupal, F. Grepl, M. Greplova Zakova, N. Gamaniuova, A. Hadjikyriacou, V. Istokskaia, J. A. Jarboe, V. Kantarelou, L. Koubikova, T. Levato, D. Peceli, J. Psikal, F. Schillaci, S. Stancek, P. Szotkowski, M. Tosca, M. Tryus, A. Velyhan.
G.A.P. Cirrone, G. Petringa, R. Catalano, A. Pappalardo.
M. Borghesi, S. Kar, K. Prise, G. Schettino, P. Chaudhary, A. McCay

## Slide 25
Thank you for your attention!
Email: Lorenzo.Giuffrida@eli-beams.eu