## Slide 1: EuPRAXIA@SPARC_LAB FELs
Michele Opromolla (INFN-LNF)
on behalf of the EuPRAXIA@SPARC_LAB WA6 collabotion team
L.Giannessi, F.Nguyen, A.Petralia, V.Petrillo, L.Sabbatini, A.Selce, A.Vannozzi, F.Villa,
C.Boffo, I.Balossino, M.Del Franco, M.Galletti, A.Giribono, A.Ghigo, A.Iovine, N.Mirian, C.Vaccarezza
Fundamental research and applications with the EuPRAXIA facility at LNF
December 4th 2024

## Slide 2: EuPRAXIA@SPARC_LAB Machine layout
2
  Soft-X ray SASE FEL – water window, optimized for 4 nm
  Driven by X--band LINAC + PWFA stage
Modulator
Dispersive
section
Seed
Radiators
  VUV seeded HGHG FEL (50-180 nm)
AQUA
ARIA
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 3: Outline
AQUA
Undulator magnetic design
FEL tuning range
Expected radiation performances
Foreseen photon Diagnostics and Beamline
ARIA
Undulator line
FEL tuning range and properties
Expected radiation performances
Foreseen photon Beamline
Summary
3
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 4: AQUA

## Slide 5: AQUA undulator
Apple-X undulator:
increased PM field through “geometry”,
selectable polarization
Superconducting undulator
collaboration agreement with FNAL for
NbTi planar prototype
Target wavelength 3-4 nm @ 1 GeV: relatively short period required (12-20 mm)
Total available length ∼ 25-30 m, depending on linac spreader system, matching section, beam diagnostics and main beam dump.
Total undulator magnetic length: 20 m, 10 modules
Period length: 18 mm sufficient tuning range at fixed energy reach carbon /nitrogen K-edge
Polarization : variable fits with the requests from the scientific case
Type: Apple-X substantially higher field extended tuning range Kmax independent of polarization  fully symmetric
Experience from the SABINA Undulator @LNF (KYMA)
5
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 6: Apple-X undulator modeling and design
Interplay among aperture, magnetic strength, wavelength tunability and inner diameter constrained by wakefield effects on FEL performance
Pipe ext. diam. (mm) | 5.6
Pipe inner diam. (mm) | 5.0
Wedge cut (mm) | 2.8
φ aperture (mm) | 6.0
Bmax (T) in LP | 0.935
Kmax in LP | 1.572
Krms (max=aw in CP) | 1.111
max 𝜆0 (nm) @ 1 GeV | 5.25
Remanent field Br = 1.35 T
Undulator period λu = 18 mm
Material NdFeB
4 blocks / period
# of periods (eff.) N = 110
Lund= 1990.4 mm (10 modules)
Modeling parameters
6
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 7: Electron beam parameter acceptance analysis
Required e-beam properties from a modified Ming-Xie model analysing the FEL performance vs. the e-beam emittance and energy spread.
This analysis assumes:
a Gaussian beam (in current, energy, energy spread, transverse momenta and spatial distributions)
duration 5 fs, peak current 1.5 kA, average beta functions βx= βy =10 m, emittances εx= εy
The undulator is engineered to amplify radiation at 4 nm from a suitable beam.
The most efficient FEL operation in both linear and circular polarization can be achieved for:
Transverse slice emittances mm mrad
Relative slice energy spread
7
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 8: FEL tuning range – linear polarization
Analysis with a modified Ming-Xie model, assuming the reference e-beam:
Tunability both in beam energy gmec2
and in undulator gap gu
Limited lever arm in lin. Pol because of the lower gain:
shorter lres  lower K values  lower Ng/pulse, longer gain length and saturation length
By increasing beam energy (other parameters constant)  chance to make 4nm with performance similar to longer wavelengths
Energy (GeV)
Energy (GeV)
Energy (GeV)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Nphot/pulse
(x1010)
Pulse energy (μJ)
extended range
Sat Length (m) (magnetic)
8
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 9: FEL tuning range – circular polarization
Thanks to its symmetry, the Apple-X undulator provides the same Krms in both linear and circular polarizations
Sat Length (m) (magnetic)
Wider undulator gap tunability in Circular Polarization
“water window” wavelengths probed with higher Ng yield
By increasing beam energy (other parameters constant)
 saturation length below 20 m, most of the available spectrum; chance to reach for 3nm
Energy (GeV)
Energy (GeV)
Energy (GeV)
Wavelength (nm)
Wavelength (nm)
Wavelength (nm)
Nphot/pulse
(x1010)
Pulse energy (μJ)
extended range
9
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 10: Expected electron beam and AQUA FEL performances
Desired/foreseen average e-beam parameters from PWFA
Parameter | Unit | Range | Simulated
Energy | GeV | 1-1.2 | 1
Charge | pC | 25-50 | 25
Rms Bunch length | µm | 2-4 | 2
Peak current | kA | 1.5-3 | 1.5
Slice emitX,Y | mm mrad | 0.6-0.8 | 0.7
Slice rel. energy spread | ‰ | 0.2-0.3 | 0.3
AQUA FEL theoretical performances
Spectrum @25 m
Bandwidth
evolution
Power @25 m
10
Energy growth
(CP)
On average, photon briliiance of about
-

## Slide 11: AQUA FEL performances
<Energy> (µJ) | λ (nm) | <BW> (%) | <Photon number> | <Size> (µm) | <Div.> (µrad) | (m) | <> (fs)
17 | 4 | 0.3 | 3.4 | 90 | 100 | 22 | 15
<Energy> (µJ) | λ (nm) | <BW> (%) | <Photon number> | <Size> (µm) | <Div.> (µrad) |  | 
17 | 4 | 0.3 |  | 90 | 100 | 22 | 15
FEL performance in CP: ideal case of the Tested beam with Gaussian current profile
Expected FEL performance and stability from start2end EuPRAXIA@SPARC_LAB beams
FEL radiation @und. exit | Unit | Range error%
Wavelength λ | nm | 4 2%
Energy at 25 m | µJ | 5-20 50%
FWHM Pulse length | fs | 10 15%
Photon number |  | 2-4 45%
Bandwidth | % | 0.2-0.4
FEL radiation @und. exit | Unit | 
Wavelength λ | nm | 
Energy at 25 m | µJ | 
FWHM Pulse length | fs | 
Photon number |  | 
Bandwidth | % | 0.2-0.4
Sources of FEL
radiation instabilities
FEL single-spike regime  intensity fluctuations
E-beam energy jitter  resonant wavelength jitter
>80% successful (>Ng /pulse)
shots are expected
11
Average pulse properties
at the undulator exit
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 12: FEL Beamline
AQUA beamline
10m
20m
30m
12m
GDM
Mirror
Apertures
Spectrometer
Solid attenuators/filters
Polarization/time measure area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
Valves
Screens
Laser hutch
BPM
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
12
Courtesy of F. Villa

## Slide 13: FEL Photon diagnostics
Gas Intensity Monitors and BPMs
Ionization streaking
Transient reflectivity
Wavefront sensors
Grating spectrometer
Bladed BPM
YAG screen
Coherence measurements (transverse and longitudinal)
Longitudinal measurements
Single-shot diagnostics
Multi-shot diagnostics
Intercepting diagnostics
Courtesy of F. Villa

## Slide 14: FEL optics and transport
Filters (solids and gas attenuators)
Bendable mirror in K-B configuration
for tunable final focus
Split and delay systems (10s ps or 100s fs range)
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
14
Courtesy of F. Villa

## Slide 15: Preliminary estimations on losses
System | Transmission | #
Mirror chamber | 0.80 (0.85) | 1
BDA | 0.99 | 2
BPM | 0.98 | 2
Spectrometer | 0.75 (0.80) | 1
Monochromator | 0.08 to 0.02 | 1
Intensity monitor | 0.99 | 2
Time measurement | 0.99 | 1
Split & delay | 0.41 (0.52) | 1
attenuators | 1 to 0 | 3
YAG screens | 1 or 0 | 13
K-B focusing | 0.64 (0.72) | 1
 | Linear Pol. | Circular Pol.
Central wavelength range | 4.0 nm, 310eV | 4.0 nm
Spectral bandwidth (rms, % to central wavelength) | 0.088% | 0.117%
Beam length (rms) | 3.50 fs | 3.76 fs
Beam transverse size (rms) | 133 um | 132 um
Beam divergence (half angle) | 0.023 mrad | 0.022 mrad
Photons per pulse | 2.33*10^11 | 2.77*10^11
Polarization (direction) | H | C
Repetition rate | 100 Hz | 100 Hz
without monochromator and S&D: 34% (with R=85% mirrors: 44%)
with Split & Delay: 14% (23%)
with monochr. 1-g: 2.6% (3.3%) x
with monochr. 2-g: 0.8% (1.0%) x
with monochr.
2-g + S&D
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
15
Courtesy of F. Villa
AQUA FEL parameters
Total transmission
: 0.32% (0.52%) x
Notes: Qui sono riportati I dati per AQUA: parametri al FEL, elementi presenti sulla linea con stima della loro trasmissione e trasmissione totale per diverse configurazioni:
-base (senza monocromatore e split&delay)
-con solo lo split&delay nei ps
-con monocromatore (usando un solo reticolo per impulse che diventano di circa 0.5 ps al bersaglio o con due reticoli per ricompensare la dispersion). 𝜹𝝀/𝚫𝝀 indica quanta parte della banda viene fatta passare rispetto al totale (es: se voglio una risoluzione da 0.05% ho una trasmissione ridotta di un fattore 0.05/0.117-0.088 =approx ½)
-con monocromatore compensato e split&delay (il caso con più perdite)
Per ARIA I dati sono ancora in elaborazione, ci aspettiamo perdite uguali o leggermente migliori sulla polarizzazione S e più alte sulla P (da un conto preliminare la riflettività a 2° di grazing sull’oro (Au) per 150 nm è 0.95s/0.80p e a 50nm è 0.94s/0.85p mentre per la grafite (C ) i dati vanno dai 0.96s/0.62p dei 150 nm ai 0.96s/0.92p dei 50 nm). Gli specchi vengono fatti a bande affinacate, con diversi materiali come coating per sfruttarli in range di lunghezze d’onda diverse (es l’oro funziona meglio per fotoni molli, il carbonio per quelli più duri) cambiando la posizione degli specchi.

## Slide 16: AQUA Beamline Scientific Case
16
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
Courtesy of F. Stellato

## Slide 17: ARIA

## Slide 18: Baseline layout
Different and complementary to long-e bunch, low current and short seed (FERMI style)
M. Opromolla et al., FEL2022 TUP75 Proceedings
Target Eupraxia e-beam
E= 1-1.2 GeV
= 0.7-1.8 kA
= 2-34 µm rms
ε= 0.7 mm mrad
= 0.05%
LINAC+PWA
LINAC
18
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 19: Radiator Undulators
Main features:
variable gap, variable phase for adjustable polarization (six motors)
𝛌u = 55.2 mm, Np=42, Lu=2.4 m
working gap: 10 ÷ 32 mm
Similar to FERMI FEL-1 radiators built by KYMA in 2009-2010
Main Physical Specifications:
Phase error sF < 5 º rms
Trajectory offset error < 20 mm rms
Trajectory tilt error < 25 mrad rms
Peak-to-peak field error DB/B < 0.5% rms
Integrated Quadrupole (N/S) < 100 G
Integrated Sextupole (N/S) < 100 G/cm
19
Apple-II undulator, FERMI-style:
linear/circular polarization
Apple-X undulator, AQUA-style:
selectable polarization, optimal control
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 20: FEL tuning range
FEL:
Max harmonic = 10
Undulator K-range from FERMI FEL-1: Kmax = 3.4 (CR), 4.35 (LV), 5.45 (LH)
Electron beam parameters:
Energy 1.0 -> 0.7 GeV
Energy spread 200 keV @ 0.8 kA -> 400 keV@1.5 kA
Duration: > 100 fs (long bunch mode, 200 pC)
    -> 8 fs (short bunch mode, 30 pC)
Emittance 2 mm mrad in long bunch mode 0.8 mm mrad in short bunch mode
Beta function 10 m
Seed laser:
minimum seed energy of 20 uJ
average seed spot size of 0.5 mm^2
independent on the wavelength
seed duration 400 fs (long seed)
-> 200 fs (short seed), possibly
no frequency chirp –spectral width close to FTL
20
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 21: ARIA with short bunch & high current from LINAC+PWA
Lower harmonics (≤ 5) saturate after two or three radiators only.
Radiation can be extracted beforehand, using the last radiator for multi-pulse/2-color generation
Seed: 460nm, 170 fs FWHM
21
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 22: ARIA with long bunch & low current from LINAC
Intensity and spectrum stable.
Ultra-narrow bandwidth pulses are produced with longer electron bunches
 high intensity allows monochromator for spectrum enhancement
Seed: 460nm, 170 fs FWHM
22
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 23: ARIA short summary
ARIA operates in High Gain Harmonic Generation and may cover the VUV spectral range down to 50 nm with an undulator similar to the one of FERMI FEL-1. Contrary to FERMI it uses a seed longer than the electron bunch and uses the electron bunch shaping and control capabilities of Eupraxia@SPARC_LAB for controlling the light pulse properties.
A commercial laser based on an Optical Parametric Amplifier should have the correct pulse energy and features to seed ARIA.
Radiation properties at saturation
Short beam (a) and Long beam (b) case
23
It fills a niche in the world FELs scenario:
No other seeded FEL facility covers the full range 50-180 nm, except for the DALIAN light source
Superposition with HHG sources, but without limitations on polarization, photon energy tuning & intensity
Synchronization with HHG sources or external lasers for multicolor pump-probe operation.

## Slide 24: FEL Beamline
AQUA beamline
10m
20m
30m
12m
ARIA beamline
GDM
Mirror
Apertures
Spectrometer
Solid attenuators/filters
Polarization/time measure area
Monochromator area
Split & delay line area
Gas absorber
K-B mirrors
Exp. Chamber area
Valves
Screens
Laser hutch
BPM
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
24
Courtesy of F. Villa

## Slide 25: ARIA Beamline Scientific Case
25
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 26: Conclusions
The AQUA undulator line is optimized for 4nm-5.7nm → extended spectral range by tuning beam energy.
Ideal reference electron beam values as well as start-to-end beams from the EuPRAXIA@SPARC_LAB accelerator were used to perform 3D time dependent FEL simulations:
O(10) fs-long, O(10) µJ pulses with O(1011) Ng/pulse at 4nm were obtained
The FEL radiation stability has been discussed, shorter l with higher Ebeam or improved e-beam quality
Studies of new electron beam working points as well as stabilization methods are in progress
The ARIA FEL line is under study: this line will extend to VUV the spectral range covered by EuPRAXIA@SPARC_LAB
Feasibility and expected performance of such flexible and cost-effective VUV user facility delivering
15-100 fs-long FEL pulses close to Fourier transform limit are investigated
Selectable polarization VUV light allows to explore chirality and dichroism in biotic media
More detailed studies of photon diagnostics and experimental beamlines are in progress
26
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024

## Slide 27: EuPRAXIA_PP Survey
https://surveys.infn.it/index.php/718177
27
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
Courtesy of E. Principi

## Slide 28: Thank you for the attention!

## Slide 29: Supplementary slides

## Slide 30: AQUA
  Magnetic design & tuning range -> vacuum chamber geometry
  Longitudinal and transverse wake-fields
  Analysis of SABINA Undulator and first lessons for the AQUA undulator
  Magnetic: field quality, field integrals, trajectory and FEL amplification
  Mechanical: stability and reproducibility tests

## Slide 31: FODO analysis for both polarizations vs. Ebeam
Solving for the quad strengths at each beam energy
Quad (~ 10 cm magn. length) integral field gradients are such to sustain even higher beam energies 
Possible to reach for 3nm with the same undulator and quadrupole devices, if Ebeam 1.2 GeV
Courtesy of F. Nguyen

## Slide 32: Tuning range: choice of the undulator period
FEL performance analyzed with Xie’s scaling formulae accounting for 60% filling factor
From the K vs. gap formulae of a planar PMU with remanent Br = 1.2T, min. magnetic gap=6mm, beam stay clear=5mm:
18mm implies tuning range, plus saturation length contingency if operating at 4nm wavelength;
16mm improves the saturation length limit, but almost no tuning range
From the K vs. gap formulae of a planar NbTi SCU with beam stay clear=5mm:
2) 16mm improves the saturation length limit, and tuning range is granted as well
Courtesy of L. Giannessi
Courtesy of F. Nguyen

## Slide 33: Undulator specs
23

## Slide 34: Transverse resistive wall wakefields
Transverse RW wakefields induced inside the cylindrical Cu vacuum chamber of radius a=2… 3 mm affect the electron bunch orbit along the undulator line, depending on the initial transverse offset at entrance.
Analytical treatment based on K. Bane & G. Stupakov formulae and the relationship between transverse and longitudinal RW impedances are used to estimate the kick angle kT parameter
Preliminary conclusions
Short bunch: Max kick: 2×10-5 mrad/m but outside the current peak
Long bunch: same order of magnitude, but superimposed to the current profile
Courtesy of F. Nguyen

## Slide 35: Trajectory, matching
Quadrupole offset errors up to qx,y 0 μm do not hamper FEL lasing.
Quadrupole offset errors up to qx,y = 400 μm lead to an off-axis beam wander which can be pre-corrected with a corrector magnet (less than 10 mT if 3.6 cm-long), to ensure FEL amplification.
(Ideal correction is when correctors are embedded into the quadrupole, share same iron)
Examples of FODO matching

## Slide 36: Summary of Apple-X undulator tolerance studies
The physical parameters and specification of the AQUA undulator system are established, most of the sensitivity studies have been carried out.
Mechanical stability tests of the SABINA APPLE-X modules were performed.
The constructive design of the components requires engineering development and design support from industry.
Future studies will include tolerance of undulator&bpm misalignments, specs of phase shifters.
RW wakefields
Transverse alignments
Magnetic field errors
Longitudinal RW wakefields do not hamper the FEL lasing
transverse offset
-> 60 nrad kick
Rms field errors of few mT
1st (2nd) field error integrals
Symmetric (x=y) | off-axis injection
Offset | 
Tilt | 
Symmetric (x=y) | off-axis injection
Offset | 
Tilt | 

## Slide 37: SABINA

## Slide 38: Lessons learned from the SABINA Undulator
Mechanical stability and reproducibility
In collaboraton with the Holographyc Interferometry & Fibre Optic Sensors (HIFOS) Laboratory at ENEA (ref. M. Caponero) we measured the deformations of the undulator guilders
Magnetic error analysis
Indication on the undulator feasibility comparing the SABINA undulator and the ideal RADIA model to reconstruct magnetic dipolar errors along the undulator

## Slide 39
Courtesy of I. Balossino, A. Selce, A. Polimadei, A. Vannozzi, M. Del Franco, L. Sabbatini, M. Caponero
CAD model by KYMA
deformations in μm
Sensors
1
2
3
A diffraction grating is produced by modifying the refraction index of the core of a fiber (FBG Sensors).
Rough approximation: the refractive index has a sinusoidal modulation along the axis of the fibre.
The sensor length is 10 mm, temperature and strain sensing at the level 0.1K - 1/106 relative elongation sensitivity
Undulator Mechanical tests on the SABINA undulator
FBG measurements

## Slide 40: Brief summary of FBG strain measurements
Temperature dependence:
max deformation of 0.12 nm over 2.7 °C/15 hours
Mechanical
by moving the four arrays all together from the minimum gap to the maximum gap, and in small steps from minimum gap to 50 mm of gap opening
by shifting the phase at different undulator gaps. In Fig. (right) the effect of a phase shift with the undulator tuned at minimum gap is shown

## Slide 41: FBG strain measurement conclusions
The wavelength shifts are perfectly reproducible. No hysteresis or values not correlated to a gap macroscopic movement were observed, except for the temperature dependence
The largest observed wavelength shift is ∼0.2 nm for the gap sensors and a factor 2-5 lower for the strain sensor devices
Gap sensors, the reference length is the plates separation. The plate sepatation cannot be measured an is virtually zero. In order to estimate an upper limit, we may consider that over an hypothetical 1 mm gap, the variation would be ∽ 150 nm. This has a negligible effect on the undulator field
Strain sensors, the reference length is the sensor length: the local deformation is ∽300 nm/cm.
These deformation values are compatible or lower than those calculated by finite elements methods and confirm the reliability of the undulator mechanical structure
A finite element model of the long AQUA undulator module should provide a suitable estimate of the expected structure deformation under the effect of magnetic forces

## Slide 42: Undulator Mechanical tests on the SABINA undulator
Undulator tested for:
Temperature dependence over a rance of 3 °C
Magnetic forces: gap – phase variations opening
Sensors were used in two different ways:
as strain measurement, by gluing the fiber fully adhered to the surface of the magnet holder-plates;
as gap measurement devices, by placing the sensors between adjacent plates.
Distribution of sensors
FBG measurements

## Slide 43: EuPRAXIA@SPARC_LAB electron beam and AQUA FEL performances
Last start2end electron beam working point with jitters FEL simulation of a single shot
Witness @undulator | Average | Std. Dev.
Energy (GeV) | 1 | 0.0107
Charge (pC) | 29.8 | 0.2
Peak current (kA) | 2.5 | 
Proj. emitX (mm mrad) | 0.69 | 0.02
Proj. emitY (mm mrad) | 0.67 | 0.02
Proj. dE/E (%) | 0.44 | 0.015
Energy (µJ) | λ (nm) | BW (%) | Photon number | Size (µm) | Div. (µrad) | Lsat (m) | Lrad (fs) FWHM
13.54 | 4.004 | 0.3 | 2.7 | 170 | 27 | 23 | 15
Energy (µJ) | λ (nm) | BW (%) | Photon number | Size (µm) | Div. (µrad) | Lsat (m) | Lrad (fs) FWHM
13.54 | 4.004 | 0.3 |  | 170 | 27 | 23 | 15

## Slide 44: AQUA FEL performances: preliminary results from FEL statistics
FEL simulation statistics from the last simulated start2end e-beam working point, with jitters included
 | Unit | Average | Error | Relative error
Wavelength λ | nm | 4.0037 | 0.084 | 0.02
Energy at 25 m | µJ | 10.54 | 5.2 | 0.49
Photon number |  | 2.092 | 1.01 | 0.48
 | Unit | Average | Error | Relative error
Wavelength λ | nm | 4.0037 | 0.084 | 0.02
Energy at 25 m | µJ | 10.54 | 5.2 | 0.49
Photon number |  | 2.092 | 1.01 | 0.48
85/101 shots withphoton number per pulse
E-beam energy jitter  Radiation wavelength jitter
The FEL wavelength jitter reduces to 0.05 nm if only the photon pulses with > photons are considered.
Work in progress ...

## Slide 45: ARIA
Undulators, seed and tuning range

## Slide 46: ARIA performances analysis
A = Long pulse mode
B = Short pulse mode
e-beam | 
Energy | 0.7 -> 1 GeV
Peak current (A - B) | 500 – 1500 A
E-bunch charge (A - B) | 200 - 30 pC
Emittances (A - B) | 0.8 mm - mrad
Energy spread (A - B) | 1.5 – 3.5 (x10-4)
Energy (GeV)
Wavelength (nm)
P. Energy (𝜇J)
Energy (GeV)
Wavelength (nm)
P. Energy (𝜇J)
Long pulse mode
Energy (GeV)
Wavelength (nm)
P. Energy (𝜇J)
Energy (GeV)
Wavelength (nm)
P. Energy (𝜇J)
Short pulse mode
Based on Xie model

## Slide 47: Pulse duration
Pulse duration limit due
to gain bandwidth (fs)
Wavelength (nm)
Beam Energy (GeV)
e-bunch duration 15 fs – circular polarization – Aria beam parameters
Estimated as the FT Limit of the bandwidth calculated with the Xie scaling relations

## Slide 48: Pulse duration
Pulse duration limit due
to gain bandwidth (fs)
Wavelength (nm)
Beam Energy (GeV)
e-bunch duration 8 fs – circular polarization – Aria beam parameters
Estimated as the FT Limit of the bandwidth calculated with the Xie scaling relations

## Slide 49: Special modes of operation
The flexibility of this source can be used in a number of ways
Short & high current e-bunch, long seed.
Pulse duration limited by e-bunch duration & large gain bandwidth
(Flexible: can produce multiple phase-locked pulses)
e-beam
Seed
Multiple
FEL
pulses
Multiple pulses on a chirped seed: amplification of separated colors. Different colors can be further separated by amplification of different harmonics in the modulator (see ref. 3)
e-beam
Seed
Multicolor
FEL
pulses
Seed +
Double e-bunch
Chirped Seed +
Double e-bunch
Radiator tuned at
different harmonics
Some already explored !!
V. Petrillo, et al., Phys. Rev. Lett. 111, 114802 (2013) <- SPARC experiment in 2012
Ferrari, E., et al. Widely tunable two-colour seeded free-electron laser source for resonant-pump resonant-probe magnetic scattering. Nat Commun. 7, 10343 (2016).
Radiator

## Slide 50: ARIA FEL performances

## Slide 51: Long-bunch long-seed mode Linear Polarization
Beam energy (GeV)
FEL Wavelength (nm)
Pulse energy (μJ)
Pol. LH
h=2
h=3
h=4
h=5
A: Seed range 320-400 nm
High energy range 100-50 nm – higher power
Minimum gap/max K
h=6
h=7
Beam energy (GeV)
FEL Wavelength (nm)
Pulse energy (μJ)
Pol. LH
h=4
h=5
h=6
B: Seed range 600-800 nm
Continuous tuning in the range 60-180 nm
h=7
h=8
An OPA such as the TOPAS can seed the ARIA FEL line covering the spectral range 200-50 nm with a single OPA process 2HG (B). Improved performances below 100 nm can be achieved with the 4th HG process (A)
Courtesy of L. Giannessi

## Slide 52: EuPRAXIA@SPARC_LAB FELs in the international panorama
FEL facility | Wavelength (nm) | Energy (µJ) | Photon # () | Length (fs) | Rep rate (Hz)
AQUA | 4-10 | 10-20 | 1-5 | 10-20 | 100-400
FERMI | 4-100 | 10-500 | 1-50 | 50-100 | 50
FLASH | 4–60 | 10–500 | 1-100 | 10-200 | 
LCLS | 0.12-4.5 | 10-3000 | 1-1000 | 1-100 | 100-
SACLA | 0.6-4.5 | 10-20 | 1-2 | 10-50 | 60
Swiss-FEL | 0.7-7 | 10-100 | 1-10 | 1-100 | 100
PAL XFEL | 0.6-6.5 | 10-1000 | 1-1000 | 10-50 | 60
FEL facility | Wavelength (nm) | Energy (µJ) |  | Length (fs) | Rep rate (Hz)
AQUA | 4-10 | 10-20 | 1-5 | 10-20 | 100-400
FERMI | 4-100 | 10-500 | 1-50 | 50-100 | 50
FLASH | 4–60 | 10–500 | 1-100 | 10-200 | 
LCLS | 0.12-4.5 | 10-3000 | 1-1000 | 1-100 | 
SACLA | 0.6-4.5 | 10-20 | 1-2 | 10-50 | 60
Swiss-FEL | 0.7-7 | 10-100 | 1-10 | 1-100 | 100
PAL XFEL | 0.6-6.5 | 10-1000 | 1-1000 | 10-50 | 60
ARIA | 50-180 | 1-500 | 100 | 1-200 | 100-400
FERMI | 20-100 | 10-500 | 1-10 | 50-100 | 50
FLASH | 4-60 | 10-500 | 1-10 | 10-200 | 
Swiss-FEL | 30-100 | 10-200 | 0.5-5 | 1-100 | 100
DCLS | 50-150 | 50-500 | 5-50 | 100 | 50
ARIA | 50-180 | 1-500 | 100 | 1-200 | 100-400
FERMI | 20-100 | 10-500 | 1-10 | 50-100 | 50
FLASH | 4-60 | 10-500 | 1-10 | 10-200 | 
Swiss-FEL | 30-100 | 10-200 | 0.5-5 | 1-100 | 100
DCLS | 50-150 | 50-500 | 5-50 | 100 | 50

## Slide 53: Summary of experimental techniques and samples
M. Opromolla - Fundamental research and applications with the EuPRAXIA facility at LNF, Frascati 12/04/2024
Courtesy of F. Stellato