## Slide 1: ECAL and Magnet operation at Fermilab: acceptance criteria, testing and installation
C. Montanari
FNAL – INFN Pavia
DUNE-Italy Meeting – October 28, 2024

## Slide 2: Generalities
  Equipment being brought at Fermilab for installation and operation has to fulfill a set of minimal requirements related to safety.
  Specific requirements, as well as design, assembly and testing protocols, are detailed in several chapters of Fermilab Environment, Safety and Health Manual (FESHM - https://eshq.fnal.gov/manuals/feshm/). FESHM is a DOE approved document.
  Design requirements are based on the relevant ASME codes, although, in some cases, additional restrictions apply, due to specific environmental conditions.
  Equipment has to be provided with appropriate documentation to allow Fermilab review panels to verify conformity to safety requirements.
  Operational Readiness Reviews are processes that include review of documentation, testing of subcomponents and walkthroughs of installations, that have to take place before “Clearance” for operation can be granted.
  Written Work Plans, detailing installation or testing procedures, are routinely used to identify hazards and appropriate mitigation procedures.
  SAND-US group is formed to assist SAND Consortium in assembling, testing and operating the DUNE-SAND detector at Fermilab.

## Slide 3: Electrical Engineering Requirements (T. Shaw & L. Bagby)
  With the move of the detector to the Fermilab site, all power distribution must be retrofitted to follow North American standards - the National Electrical Code (NEC), or NFPA 70E. In addition, Fermilab provides several chapters in the Fermilab Environment, Safety and Health Manual (FESHM) which are relevant.
  All commercial powered equipment should pass a US nationally recognized testing laboratory (NRTL) and be installed and used in accordance with the listing. International code equivalencies or codes with reduced inspection requirements are listed in the technical appendix of FESHM 9110: Electrical Utilization Equipment Safety. For all unlisted or non-NRTL electrical equipment, FESHM 9111: Approval of Unlisted Electrical Equipment provides the steps required for the evaluation and approval by the Electrical Authority Having Jurisdiction (AHJ).
  Custom electronics will be reviewed according to the FESHM 9000 Electrical Safety chapters, Fermilab’s Electrical Design Standards for Electronics in Experimental Apparatus, and Fermilab’s Electrical Safety ORC Review Guidelines. Custom electronics are defined as any powered equipment which is not commercially available and includes all printed circuit boards, chassis which contain a collection of commercial/custom electronics with internal wiring completed by the user, any commercial equipment with a modification and any equipment which does not have a NRTL seal. Where an NRTL approved version of an item of equipment does not exist the procedure set out in FESHM 9111 shall be applied.
  For each electrical system (or subsystem), a documentation set should be produced which contains the required list of documents that will demonstrate that the equipment has been designed and assembled respecting safety principles and that it can be installed, commissioned, operated and then dismantled safely.

## Slide 4: Documentation required for electrical equipment (T. Shaw & L. Bagby)
Objective of analysis and scope of equipment to be analyzed.
References to design codes or standards that are utilized in the analysis.
Personnel and qualifications carrying out the analysis.
A system (or subsystem) level block diagram showing the entire planned installation, including both commercial and custom components. This must include any wire/cable connections with detailed information on wire/cable sizes (AWG or mm2), lengths and connectors. This is especially vital for all power paths.
Analysis showing all system level power paths provide appropriately sized fuses, wire/cable and connectors.
Complete schematics of any custom printed circuit boards with layout files and a detailed analysis of any power paths or power planes used. Use of fuses must be documented. If fuses are not used, a note on why they are not required must be provided.
Identification of any high voltage paths. (Hazardous Electrical Energy levels which will require additional documentation are identified in FESHM 9100 section 6.1).
Adherence to electric and mechanical tolerances on all connections.
Information on all commercial equipment, including NRTL or equivalent rating.
These documents shall cover the operational lifetime of the concerned equipment or detector. The versioning of these documents should be maintained and controlled on EDMS. The documentation provided must contain sufficient detail so that results are reproducible and peer-reviewable

## Slide 5: Reference Documents: Electricals
Document ID Number/URL | Document Title
https://esh-docdb.fnal.gov/cgi-bin/sso/ShowDocument?docid=7141 | FESHM 1071: Codes & Standards
https://esh-docdb.fnal.gov/cgi-bin/sso/ShowDocument?docid=3253 | FESHM 2110: Ensuring Equivalent Safety Performance when Using International Codes and Standards
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=375 | FESHM 9100: Fermilab Electrical Safety Program (Work Smarts Standard)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=521 | FESHM 9110: Electrical Utilization Equipment Safety (Work Smart Standard)
https://esh-docdb.fnal.gov/cgi-bin/sso/ShowDocument?docid=7567 | FESHM 9111: APPROVAL OF UNLISTED ELECTRICAL 6 EQUIPMENT
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=376 | FESHM 9120: AC Electrical Power Distribution Safety (Work Smarts Standard)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=377 | FESHM 9130: Management and Use of Cable Tray Systems (Work Smarts Standard)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=541 | FESHM 9140: Protection Against Exposed Electrical Bus (Work Smart Standard)

## Slide 6: Reference Documents: Electricals (cont.)
Document ID Number/URL | Document Title
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=378 | FESHM 9150: High Voltage Coaxial Connectors
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=379 | FESHM 9160: Low Voltage, High Current Power Distribution Systems (Work Smarts Standard)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=522 | FESHM 9170: Uninterruptible Alternating Current Power Back-Up Systems
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=380 | FESHM 9180: Hazard Mitigation for Electrical Workers (Work Smart Standard)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=2815 | FESHM 9190: Grounding Requirements for Electrical Distribution and Utilization Equipment
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=3311 | FESHM 2005: Operational Readiness Clearance
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=393 | FESHM 2110: Fermilab Energy Control Program (Lockout/Tagout)
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=2781 | Electrical Design Standards for Electronics in Experimental Apparatus
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=3270 | Electrical Safety ORC Review Guidelines
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=3270 | Fire/Life Safety ORC Review Guidelines for Experimental Installations
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=3270 | Operational Readiness Clearance (ORC) Guidelines
http://directorate-docdb.fnal.gov/cgi-bin/RetrieveFile?docid=34 | Fermilab Engineering Manual

## Slide 7: Mechanical and Cryogenics Engineering Requirements (M.J. Kim)
  For any system and component received at Fermilab and its leased spaces (at its remote sites) to be qualified for operations, a set of proper documentation proving the compliance with the applicable codes and standards shall be provided. To understand the requirements and types of documents necessary for each system or component to prove conformity, various chapters of Fermilab Environment, Safety and Health Manual (FESHM) must be reviewed and adequately followed at best effort. FESHM 1071 describes all applicable codes and standards for mechanical, cryogenics, electrical, fire protection, and pressure systems, required when designing, fabricating, testing, and operating a new one, evaluating the features and processes, and the assembly of the facility.
Document ID Number/URL | Document Title
https://esh-docdb.fnal.gov/cgi-bin/sso/ShowDocument?docid=7141 | FESHM 1071: Codes & Standards
https://esh-docdb.fnal.gov/cgi-bin/sso/ShowDocument?docid=3253 | FESHM 2110: Ensuring Equivalent Safety Performance when Using International Codes and Standards
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=456 | FESHM 5031: Pressure Vessels
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=362 | FESHM 5031.1: Piping Systems
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=366 | FESHM 5031.5: Low Pressure Vessels and Fluid Containment
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=528 | FESHM 5032: Cryogenic System Review
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=367 | FESHM 5032.1: Cryogenic Dewar Installation and Operation Rules
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=371 | FESHM 5033: Vacuum Vessel Safety
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=4112 | FESHM 5100: Structural Safety

## Slide 8: Reference Documents: Mechanics and Cryogenics
Document ID Number/URL | Document Title
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=356 | FESHM 10100: Overhead Cranes and Hoists
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=357 | FESHM 10110: Below-the-Hook Lifting Devices
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=358 | FESHM 10120: Powered Industrial Trucks
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=360 | FESHM 10130: Slings and Rigging Hardware
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=5540 | FESHM 10200: Lift Plans
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=6970 | FESHM 10210: Equipment Transport
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=3311 | FESHM 2005: Operational Readiness Clearance
http://esh-docdb.fnal.gov/cgi-bin/ShowDocument?docid=525 | FESHM 2060: Work Planning and Hazard Analysis

## Slide 9: Pressure vessels and piping
  Current EU directive: 2014/68/UE PED mandatory in Italy from February 15, 2016.
  Previous EU directive: 97/23/CE mandatory in Italy from February 25, 2000.
  Applies to equipment operating at relative pressure > 0.5 bar (design pressure).
  A DOE variance recognizes the substantial equivalence between the European Pressure Equipment Directive and the American ASME codes for the same equipment and allows use of EU certified equipment. This variance can only be applied to in kind contributions to DUNE.
  The variance applies to some of SAND’s components: GRAIN cryogenic system, tracker gas system, magnet external helium system and, in general, to all newly build components involving pressurized gases.
  The variance does not apply to KLOE’s magnet as it was built prior to the first EU Directive.
  Fermilab has a general need to accept “legacy/existing/reused/relocated” pressure equipment, which needs to be transferred to Fermilab from collaborating institutions and operated at Fermilab site. Such legacy/existing/reused/relocated equipment could be originally designed and constructed per ASME or International codes listed in 10CFR851 and its recent Variance, or, in infrequent occasions, it could lack any established code pedigree. Specifically, there is a need to evaluate the cryogenic pressure components of the KLOE superconducting magnet, which include small helium vessel located inside the magnet's turret and cryogenic piping, for which no code pedigree could be established.

## Slide 10: Fermilab Approval Process for KLOE Magnet
  Fermilab realizes that there is a difference between the set of rules applied for the newly constructed pressure equipment versus the set of the general post-construction rules applied for legacy/existing/reused/relocated pressure equipment, e.g. KLOE Helium System slated for transfer from INFN to Fermilab. The ASME/API procedures governing Fitness for Service (FFS) described in API-579 provide a methodology for the evaluation of pressure safety for existing post-constructed equipment.
To remediate this situation, Fermilab started on two initiatives:
    Development of a new Fermilab ESH Manual chapter 5036, which would describe application of FFS to the legacy/existing/reused/relocated pressure equipment at Fermilab, including equipment without any established code pedigree, e.g. KLOE.
    Working with an outside consultant, Mr. George Antaki, who is internationally recognized for his expertise in ASME/API FFS methodology, to evaluate safety of KLOE pressure equipment, including: assessment of risks and consequences of failures; assessment of inspections and tests; application of FFS methodology for interpretation of records,, inspections, tests, etc.; proposing replacements, repairs, enhancements needed to mitigate identified risks.
  As of Oct 2024, Mr. Antaki submitted a 48,000 USD proposal in three phases.

## Slide 11: Fitness For Service Proposed Process
Phase 1: Pedigree Assessment
    Determine the pedigree of the existing helium vessel and piping of the INFN KLOE magnet, compared to the construction rules of ASME VIII and ASME B31.3, which covers the following construction areas for the pressure boundary:
      Materials
      Code design
      Fabrication
      Examination
      Testing
    Fermilab and Mr. Antaki will have to work with INFN to review all available information for KLOE pressure equipment.
Phase 2: Compliance Actions
    If Phase 1 identifies shortcomings in the construction records of the pressure boundary of the existing helium vessel and piping of the INFN KLOE magnet, actions will be proposed to achieve an equivalent level of safety as the ASME Codes.

## Slide 12: Fitness For Service Proposed Process (cont.)
Phase 3: Fitness-for-Service
    Guidance will be developed to achieve fitness-for-service (i.e., continued safe and reliable operation) of the pressure boundary of the helium vessel and piping of the INFN KLOE magnet, in the form of:
      Proposed periodic inspections and tests.
      Fitness-for-service acceptance criteria of the results of the inspections and tests.
      Options for repairs or alterations if necessary.
A contract is being prepared, covering the first two phases with deliverables, in the form of documents, for each phase. Fermilab engineering is involved in the development and approval of the various steps, in particular the conclusions of Phase 2.
Testing of the magnet in Frascati and its replica at Fermilab will be fundamental milestones in the process.

## Slide 13: Milestones (in reverse order)
Magnet + ECAL + YOKE + internal support structure assembly in the cavern complete and ready to move in the alcove:
  March 2029
Start installation in the cavern:
  October 2028
Magnet delivered at Fermilab:
  March 2027
ECAL delivered at Fermilab:
  June 2027
Magnet tested in Frascati:
  July 2026
ECAL refurbished and tested in Frascati:
  November 2026

## Slide 14: Proposed timeline for SAND – construction and delivery (I)

## Slide 15: Proposed timeline for SAND – construction and delivery(II)

## Slide 16: Proposed timeline for SAND – construction and delivery (III)

## Slide 17: Proposed timeline for SAND – Installation (I)
ND Hall available for installation

## Slide 18: Proposed timeline for SAND – Installation (II)

## Slide 19: Proposed timeline for SAND – Installation (III)
SAND Positioned and ready for internal elements installation

## Slide 20: Proposed timeline for SAND – Installation (IV)

## Slide 21: Proposed timeline for SAND – Installation (V)
Beam checkout