## Slide 1: July 23-24 2024 NET@INFN CNAF (TIER1) Bilateral workshop Serbian Tier1-CNAF S.Zani (in behalf of the entire Network Department of INFN CNAF)

## Slide 2: New Datacenter state of art
INFN
CINECA
B5
C2
ECMWF
B5 Building OK
New Datacenter at Technopole
2,4km walking distance
7 km far fiber path
CURRENT
DATACENTER
(Viale Berti Pichat)
NEW DATACENTER
(Via Stalingrado)

## Slide 3: Physical connectivity of the building
ECMWF
INFN
CINECA
Fiber access from Via Ferrarese
Differentiated optical fiber accesses are foreseen for network operators from the two sides of the Technopole Area (Via Stalingrado e Via Ferrarese)
At the time of this presentation more than 140 single mode fibers have been installed by Lepida e TIM entering form via Ferrarese.
K2
Fibers in the other way (From Via Stalingrado) will be installed as far as the underground big anti flooding water expansion pool will be finished
Fiber access from Via Stalingrado
(To be done)
Anti flooding
pool
WORK IN PROGRESS
Technopole AREA

## Slide 4: Areas of the new Datacenter
High Density
And
Expansion
AREA
INFN DC
Building
B5
CINECA DC
Building
C2
FARMING
TAPE
LIBRARY
NETWORK
LOW Density Computing
AREA
High Density
Expansion
AREA
NOC
SOC
MEETING
ROOM
LEONARDO
“Temperate” water (36°C inlet) for DLC and cold water for Air Cooling
Up to 80kw/Rack
Cold water (26°C inlet) only for Air cooling (Cold isle) system (Up to 16 kW/Rack)
CNAF-Leonardo
Direct cabling connection <100m
100m
30m
FARMING / STORAGE
Resources
Dragon Fly
IB
CORE-1
A7812
OPN/ONE
Skyway
Skyway
LEONARDO
IB
IB
IB
IB
IB
16x100Gb Ethernet
CORE-2
A-7812
FARMING / STORAGE
Resources

## Slide 5
INFN CNAF TIER1 (Current architecture at CNAF in Viale Berti Pichat)
Nexus 9516
Nexus 9516
LHC OPN/ONE
VPC Link
General IP
100Gb/s
100Gb/s
4x10Gb/s
Disk servers (GPFS)
All disk servers directly conneted to COREs 2x 100Gb/s (NO OVERSUBSCRIPTION)
TOR
TOR
TOR
Farming Resources
Simple L2 LAG
All resources are connected to both Core Switches
TOR switches shoud handle VLAN (802.1Q) – Routing done on COREs (Simple configuration on TOR) permits to use switches produced by different vendors (Cisco, Juniper, Huawey, Lenovo, DELL, Extreme Networks, Super Micro).
2 Core Switch Routers
152 x 100 Gbps
288 x 10/25 Gbps
120 Switches (mainly TOR)
Circa 5500 x 1 Gbps
Circa 400 x 10Gbps
. . . . . . . . . . . . .
Cisco 95K
Cisco 95K
VPC (Virtual Port Channel)
CINECA
Hosted Resources
NE 10032
TR
TR
DCI
400 Gb su
1,2 Tb/s
Main data flows: Disk Server (GPFS) WNs
More than 600 Gbps sustained.
4x10Gb/s

## Slide 6: Network@TP
CNAF
Berti-Pichat
EPIC
Leonardo
LHC OPN/ONE
Transponder
Transponder
General IP
1,6 Tbps
1,2Tbps
IB/ETH GW
IB/ETH GW
TOR
TOR
6
General IP
SW/Router
SSNN
FARMING
STORAGE
NG FW
PHASE 1 numbers
10x 100GE WAN Ports
12x 100GE DCI – CNAF
120 100GE Ports (Storage)
60 100GE Ports (Farming)
16x100 GE Leonardo
2x100 Gbps
LHCONE
2x100 Gbps
CLOUD@CNAF
9,6 (4,8 net) Tbps
T1-CORE1
ARISTA
7812-R3
T1-CORE2
ARISTA
7812-R3
TOR
TOR
Disk Server
Disk Server
Disk Server
Disk Server
6 Tbps
Vxlan switching e routing wire speed
690 Tbps di throughput (Up to more than 800 x 400Gb ports)
4x100 Gbps
LHCOPN
Up to 16x100G
DCI

## Slide 7: Datacenter Extension Between Current CNAF site and New Technopole site
DCI
1,2Tbps
(3,2Tbps)
Available
INFN DC
(Old site)
2x100G (General IP)
10x100G Ethernet(DCI)
CISCO
Nexus 9516
CISCO
Nexus 9516
C-9500
C-9500
ARISTA
7812
ARISTA
7812
A-7280
A-7280
2x100G (General IP)
10x100G Ethernet(DCI)
INFN DC
(TECHNOPOLE)
vPC
Stackwise
Virtual
Collapsed
IP FABRIC
MUX A
MUX B
MUX A
MUX B
G30-1
G30-2
G30-1
G30-2
Transponders
Transponders
7km

## Slide 8: Tape Area Network Extension
New IBM TS4500
18 Tape Drive
IBM TS1170
FC Switch
FC Switch
FC Switch
SAN 64B-6
FC Switch
SAN 64B-6
TSM – HSM
7 Servers
(old)
IBM TS4500
19 Tape Drive
IBM TS1160
2 Dedicated Dark Fibers (7 km)
Transceiver FC SFP+
FC 32 Gb LWL on SM Fiber (10Km)
Brocade
INFN DC
(TECHNOPOLE)
INFN DC
(Via Berti Pichat
Old site)
Tape data transfer will be done on this extension
Dedicated Dark Fibers are in place
LW 10Km FC Transceivers acquired and installed on Berti Pichat FC Switches
New IBM TS4500 Tape Library and new FC Switches
1st IBM lib to be relocated at TP
The data migration will continue through the remote SAN, until the Oracle lib will be emptied
TSM – HSM
7 Servers
(new)
Oracle SL8500
- 20 Tape Drive
- 42 PB to be migrated
- To be dismissed

## Slide 9: DC Transfer phases
INFN
Nexus 9516
Nexus 9516
Nexus 7018
TIER1
Berti Pichat
LHC OPN/ONE
100Gb/s
100Gb/s
CINECA
TOR
TOR
TOR
TOR
CORE
CORE
TR
TR
DCI 1,2Tb/s
800Gb/1Tb (T1-T1 + T1-WAN)
2x100G (General IP)
LHC OPN/ONE
Nx100Gb/s
Nx100Gb/s
TOR
TOR
TOR
TOR
CORE /
SPINE
CORE /
SPINE
IB/ETH GW
IB/ETH GW
8x100 Gb/s
8x100Gb/s
Leonardo
DCI Between the two Datacenters
Data copy and devices transfer
Swap of the Wide Area Network Routing as far as hardware resources have been moved to the new Datacenter
Decommissioning of the old datacenter
B5
C2

## Slide 10: Conceptual CORE network Configuration
CORE-1
A7812
CORE-2
A-7812
SW/Router-1
SW/Router-2
L2 LACP
Port Channel
General IP
WAN
Underlay: IS-IS
Overlay: VLXLAN BGP EVPN
ESI
FARMING or STORAGE
Resources
OPN/ONE
DC
CORE-1
DC
CORE-2
Router-1
Router-2
ESI
SPINE
SPINE
DC
CORE-3
DC
CORE-4
FARMING or STORAGE
Resources
OTHER
Resources
Possible Scale UP
Evolution
General IP
WAN
OPN/ONE
Collapsed
IP Fabric

## Slide 11: Cabling
The Cabling system is concentrated from every row in the Network Room (Close to center of the building)
LC-LC MM (OM5) 1-100Gb Ethernet
LC-LC SM->1-400Gb Longer distance and 400G-FR4 Ethernet
MPO-12 MM (OM5) 40G-SR4, 100G-SR4, 400G-SR4.2 Ethernet
MPO-12 SM 400G Ethernet (400G-DR4)
RJ45 1-10Gbps

## Slide 12: Network Area
Cabling system from Network Area to every row in place
2x Modular Core Switch/Router (ARISTA 7812) –TIER1 Scientific DC
2x ”Switch/Router” (ARISTA 7280) – General Internet Access
15x Management Switch
2 Racks for GARR POP
NETWORK ROOM
ONE OF THEN TWO
CORE AND ROUTER RACKS
ARISTA 7812
ARISTA 7280

## Slide 13: LHCOPN
Optical
Private
Network
INFN CNAF
Italian TIER1
The LHCOPN is the private IP network that connects the Tier0 and the Tier1 sites of the LCG.
The LHCOPN consists of any T0-T1 or T1-T1 link which is dedicated to the transport of WLCG traffic and whose utilization is restricted to the Tier0 and the Tier1s.
ONLY IPs of WLCG Resouces have to be announced on this network
https://twiki.cern.ch/twiki/bin/view/LHCOPN/WebHome

## Slide 14: LHCONE
https://twiki.cern.ch/twiki/bin/view/LHCONE/WebHome
LHCONE is an L3VPN service to connect T2s to T2s and T1s to T2s
More than 140 Sites connected to this network
As for LHCOPN ONLY IPs of WLCG Resouces have to be announced on this network
Open
Network
Environment

## Slide 15: LHCONE MAP
INFN CNAF
TIER1

## Slide 16: CERN – CNAF DCI
As presented last year we have a pilot link based on multidomain Spectrum sharing Connection.
We activated a 4x100Gbps used as LHCOPN link for INFN-T1
Add/Drop
GEANT Open Line System
ROADM
8x AMP
Milan PoP
Geneva CERN DC
Add/Drop
GARR Open Line System
ROADM
3x AMP
Bologna CNAF DC
TRX
TRX
Nx100 G
or
Nx400 G
Nx100 G
or
Nx400 G
16
1.6 Tbps

## Slide 17: CERN-CNAF DCI (Pre production) Primary and backup path CERN-CNAF
Nexus 9516
Nexus 9516
0
CERN Router1
CERN Router2
2 Transponders
Infinera G30@CNAF
CNAF
CERN
1000 km
2 Transponders
Infinera G30@CERN
Spectrum Sharing (1,6Tbps over 400Ghz)
L3 Overlay
LHC-ONE
LHC-OPN (Backup)
4x100G
4x100G
LHC-OPN traffic on DCI Link 4x100 Gbps
Router GARR
Router GEANT
PRIMARY PATH (as-path: 2038-513)
BACKUP (as-path 2038-137-20965-513
SCS
2x100G
2x100G

## Slide 18: That’s it

## Slide 19: Backup Slides

## Slide 20: CERN-CNAF DCI
Courtesy GARR
RTT
15 ms
RTT
9.5 ms

## Slide 21: Low density Area
150 racks in place
Under Floor Cooling System operational
First 5 CPU Racks transferred in the new data center In low density area In production
First 64 PB of new storage resources are installed in the new data hall  configuration in progress
First Computing and storage resources

## Slide 22: High Density and expansion area
Network Cabling racks are in place
The High density farming area can host 3 rows of 16 Racks full of DLC systems (Up to 80 kw/Rack) or very dense air cooled systems (Up to 30kw/Rack)
An Expansion area of about 800 sqm is available for future use
FREE EXPANSION AREA

## Slide 23: Data Challege 2024 (Using DCI link)
On 400Gbps CNAF-CERN DCI Reached 220 Gbps (5 minute average)
On LHCONE (T1-T2 + T1-T1 per FZK e IN2P3) Reached 145 Gbps
Quite good rates reached (>200Gbps) and network don’t represent a limit for the data movement (Never saturated)

## Slide 24: Telemetry (On transponders)
Data observed via Telemetry on transponder devices (peaks close to 300Gbps)
285 Gbps
Telemetry gives us instant data (not average) and it is better to observe peaks.

## Slide 25: Fiber CUT on DCI (22/3/2024 – 27/3/2024)
OPN CERN – CNAF DCI
OPN-ONE CERN – CNAF (backup)
CUT 22/3/2024
During “CUT time” traffic
Flowed on LHC-ONE “Routed” Path

## Slide 26: CERN-CNAF DCI (Next steps)
DCI on spectrum sharing is ready for production
Pilot activities will continue
400Gbps and multiple 400Gbps Ethernet connections
Extension of the pilot to the new datacenter @Tecnopolo
Try to find a second optical path for redundancy
Improve automation on optical network programmability
Acknowledgments:
GARR Optical : Colantonio, Vuagnin
GARR Packet : Inzerilli, Marletta, Valiante
GARR DC & DevOps : Cesaroni, Chiarelli, Marzulli
CNAF Team: Zani, De Girolamo
CERN Team: Martelli
GEANT Team: SCS Team, Roberts
GARR Management/Amm/CTS

## Slide 27: Connection to Leonardo
General IP
WAN
IB
CORE-1
A7812
A-7812
L2 LACP
Port Channel
ESI
FARMING or STORAGE
Resources
OPN/ONE
Syway 1
Syway 2
LEONARDO
IB
IB
IB
IB
Dragon Fly
IB
16x100Gb Ethernet