## Slide 1: DAQ for HPGe array
A. Goasduff N. Toniolo

## Slide 2: Hardware
CAEN DIGITIZER V1:
  VME boards
  Single ended input channels (8/16 channels)
  250 MS/s
  Firmware: Trapezoidal filter (DPP-PHA)
  Conversion Differential to Single-Ended
CAEN CONET2 Bridge:
  A3818 PCIe board with 2/4 input link. Each link can manage up to 8 boards
  Maximum length 50m
DAQ Servers
  Available SuperMicro (AGATA/GALILEO) and HP server (physics b-DS) compatible with the A3818 PCIe board

## Slide 3: XDAQ system
Distributed DAQ system
  Used for CMS@CERN
  Dedicated application for PISOLO, EXOTIC, GALILEO, PRISMA, Ancillary AGATA developed in C/C++
  Digitizer CAEN already supported (version 1 and 2, DPP-PHA/DPP-PSD)
  Modular run control
    Developed in Python2.7 and ported to Python3.9
    Dedicated interfaces towards psi style e-log, grafana, epics interface, … all
    Both CLI and GUI based on Web Interface (ugly but functional)

## Slide 4: XDAQ Architecture
Software platform developed at CERN and design specifically for the development of distributed DAQ
Standard DAQ framework for CMS experiment
XDAQ provides:
  Platform independent services
  Peer-to-peer communication between DAQ blocks
  SOAP messaging for configuration/control/monitoring
Main Features:
  Device access
  Configuration, control and monitoring
  Maintainability and portability
  Scalability
Long standing experience at LNL:
  GASP spectrometer
  PRISMA/PISOLO,EXOTIC spectrometers
  GALILEO spectrometer
  AGATA ancillaries
  NEEDLE @ HIL
Readout Unit
CAEN A3818
Data Filtering
Event Builder
TCP receiver
CAEN V1725

## Slide 5: User supplied actors
Skeleton of data treatment actor in C/C++
For PANDORA:
  Low level data reduction:
    Energy selection?
    External conditions?
  Improved timing performances

## Slide 6: Monitoring and MetaDAta generation

## Slide 7: Data quality monitoring
Typical spectra written on disk:
  Quick and easy visualisation
  Possibility to reset the spectra using the run control
Monitoring of the ancillary data quality at different level of the DAQ:
  Data filtering
  Event builder

## Slide 8: Test bench
2 Cryo-pulse 5
1 NIM crate for the detector HV (CAEN N1471H) and pre-amplifier power supply
1 4U VME crate for the digitizer V1725
Supermicro server (DAQ + control HV)

## Slide 9: DAQ Test Detection setup
2 HPGe CANBERA Cryo-Pulse 5
  Bias: -5kV, Imon < 1 nA
  Resolution 2.3 keV FWHM @ 1.4 MeV (6 kHz rate, shaping 6 µs, baseline)

## Slide 10: Online reconstruction of coincidences
The XDAQ event builder reconstruct the events based on the time stamp information

## Slide 11: Offline timing performed at the LF
256 samples of the input signal are reprocessed at the LF:
  moving average
  Differentiation and integration
  CFD

## Slide 12: Effect on the time resolution
Gated on the 60Co coincidence:
  Online resolution: 128 ns
  Offline resolution: 15 ns
Improvement by a factor 8
Cost: Size of the single event: 36 B  548 B
In the present configuration it is not feasible for PANDORA (391 MB/s vs 60 MB/s)

## Slide 13: Simulated Acquisition cycle using dual timers
Logical signal from the tape:
- 0 moving
- 1 stopped
RESET THE TS OF THE DIGITIZER
Logical signal from the beam:
- 0 beam-off
- 1 beam-on

## Slide 14: Effect of the tape signal on the data
1
2
3
4
5
6
7
8
9
10
11

## Slide 15: Effect of the beam signal

## Slide 16: Conclusion
Detectors have been upgraded and tested with rate up to 100 kHz
Limitation on the detection efficiency due to the pile up rejection algorithm
DAQ system is ready to be installed at LNS
  Experience in remote gestion (NEEDLE@HIL, Warsaw)