## Slide 1
Fast accelerating approaches for Deep Learning in quantitative imaging
Mattia Ricchi, Fabrizio Alfonsi, Camilla Marella, Marco Barbieri, Alessandra Retico, Leonardo Brizi, Alessandro Gabrielli, Claudia Testa
National Institute of Nuclear Physics (INFN), Division of Bologna, Italy
Department of Computer Sciences, University of Pisa, Italy
Department of Physics and Astronomy, University of Bologna, Italy

## Slide 2
Magnetic Resonance Fingerprinting (MRF)
Magnetic Resonance Fingerprinting (MRF) is a fast quantitative MRI method that permits the simultaneous non-invasive quantification of multiple important properties of a material or tissue [Ma, D., Gulani, V., Seiberlich, N. et al. Magnetic resonance fingerprinting. Nature (2013)].
The MRF maps are quantitative: the value of the pixels is the real value of T1 and T2 of the tissues expressed in ms
Neural Network map reconstruction
Barbieri, Marco et al. A deep learning approach for magnetic resonance fingerprinting: Scaling capabilities and good training practices investigated by simulations. (2021).
T1
T2
Why accelerating the NN training?
MRF sequence is not standardised, several factors may influence the results:
Research centre / hospital
Scanner: vendor, magnetic field strength
Sequence and its parameters
Parameters to be retrieved
Every time the sequence is changed, the network must be trained again
Notes: Medicina personalizzata

## Slide 3
Magnetic Resonance Fingerprinting (MRF)
Magnetic Resonance Fingerprinting (MRF) is a fast quantitative MRI method that permits the simultaneous non-invasive quantification of multiple important properties of a material or tissue [Ma, D., Gulani, V., Seiberlich, N. et al. Magnetic resonance fingerprinting. Nature (2013)].
The MRF maps are quantitative: the value of the pixels is the real value of T1 and T2 of the tissues expressed in ms
Neural Network map reconstruction
Barbieri, Marco et al. A deep learning approach for magnetic resonance fingerprinting: Scaling capabilities and good training practices investigated by simulations. (2021).
T1
T2
Why accelerating the NN training?
MRF sequence is not standardised, several factors may influence the results:
Research centre / hospital
Scanner: vendor, magnetic field strength
Sequence and its parameters
Parameters to be retrieved
Every time the sequence is changed, the network must be trained again
Notes: Medicina personalizzata

## Slide 4
Magnetic Resonance Fingerprinting (MRF)
Magnetic Resonance Fingerprinting (MRF) is a fast quantitative MRI method that permits the simultaneous non-invasive quantification of multiple important properties of a material or tissue [Ma, D., Gulani, V., Seiberlich, N. et al. Magnetic resonance fingerprinting. Nature (2013)].
The MRF maps are quantitative: the value of the pixels is the real value of T1 and T2 of the tissues expressed in ms
Neural Network map reconstruction
Barbieri, Marco et al. A deep learning approach for magnetic resonance fingerprinting: Scaling capabilities and good training practices investigated by simulations. (2021).
T1
T2
Why accelerating the NN training?
MRF sequence is not standardised, several factors may influence the results:
Research centre / hospital
Scanner: vendor, magnetic field strength
Sequence and its parameters
Parameters to be retrieved
Every time the sequence is changed, the network must be trained again
Notes: Medicina personalizzata

## Slide 5
Field Programmable Gate Array (FPGA)
Configurable integrated circuit that can be repeatedly programmed after manufacturing.
Consist of configurable logic blocks, programmable interconnects, and flexible I/O, allowing for custom hardware solutions.
Key Advantages:
Parallel Processing: FPGAs can handle multiple operations simultaneously, ideal for high-performance computing and real-time processing.
Low and Fixed Latency: Direct hardware implementation reduces delay compared to software running on a CPU or GPU.
Custom Logic: Designers can implement specific algorithms directly in hardware, allowing for optimized performance.

## Slide 6
Neural Networks on FPGA
While GPUs have traditionally powered neural networks, FPGAs are gaining traction for their customizable hardware, better parallel processing, low and fixed latency and lower power consumption making then suitable for real time applications.

## Slide 7
Neural Networks on FPGA

## Slide 8
Neural Networks on FPGA
While GPUs have traditionally powered neural networks, FPGAs are gaining traction for their customizable hardware, better parallel processing, low and fixed latency and lower power consumption making then suitable for real time applications.
All of these works are just about inference on FPGA.
What about training?

## Slide 9
Why training a Neural Network on FPGA?
Performance and speed
Efficient parallel processing & custom architecture optimization
Energy efficiency
Lower power consumption compared to CPU and GPU
Flexibility
Reconfigurability for different neural network architectures and algorithms
Latency
Lower and fixed latency due to parallel processing and closer memory access
High throughput
The parallel processing capabilities of FPGAs can handle high data throughput
These characteristics make FPGAs particularly well-suited for real time applications of Neural Networks that require extensive and repeated training, also with very large datasets.

## Slide 10
Our project workflow
Simulation
Neural Network Training
HARDWARE – FPGA
Neural Network Training
MR Sequence
AI Prediction:
T1 and T2
AI Prediction:
T1 and T2
Comparison
SOFTWARE

## Slide 11
Neural Network Quantization Aware Training
Reduce network dimensions to meet available FPGA resources
Perform Quantization Aware Training so that the network operates with integers only
Dense
T1
Real and Imaginary parts of signal
T2
256
128
64
32
Dense
Dense
Dense
Dense
16
The quantized model uses lower precision without affecting the neural network performance.

## Slide 12
Neural Network Quantization Aware Training
Reduce network dimensions to meet available FPGA resources
Perform Quantization Aware Training so that the network operates with integers only
Dense
T1
Real and Imaginary parts of signal
T2
256
128
64
32
Dense
Dense
Dense
Dense
16
The quantized model uses lower precision without affecting the neural network performance.

## Slide 13
Neural Network Quantization Aware Training
Reduce network dimensions to meet available FPGA resources
Perform Quantization Aware Training so that the network operates with integers only
Dense
T1
Real and Imaginary parts of signal
T2
256
128
64
32
Dense
Dense
Dense
Dense
16
The quantized model uses lower precision without affecting the neural network performance.

## Slide 14
Neural Network VHDL implementation
Low-level approach, writing every firmware component in VHDL
Node working principle
Implemented in VHDL the function
that represents the behaviour of a single node.
Backpropagation process
Implemented in VHDL the following formulae for backpropagation
These two blocks will cover all the NN operations by serial iterations. The whole NN operations cannot be implemented in FPGA concurrently because of resource limitation.
Notes: To separate the firmware in different clock domains to allow the firmware compiler to place the components more freely

## Slide 15
Accelerator FPGA based card: Alveo U250 (1.7M LUTs, 3.4M Flip-Flops, 12k DSPs, 2.6k BRAMs)
Resources used
Percentage of the available resources that are used, including the internal memory.
Based on synthesis results, clock frequency of 200 MHz is feasible, but aiming at 250 MHz.
Node resources
Backpropagation resources
Backpropagation synthesis
Node synthesis
FPGA Neural Network synthesis and resource estimation
LUTs | 8%
FFs | 4%
DSPs | 40%

## Slide 16
Accelerator FPGA based card: Alveo U250 (1.7M LUTs, 3.4M Flip-Flops, 12k DSPs, 2.6k BRAMs)
Resources used
Percentage of the available resources that are used, including the internal memory.
Based on synthesis results, clock frequency of 200 MHz is feasible, but aiming at 250 MHz.
Node resources
Backpropagation resources
Backpropagation synthesis
Node synthesis
FPGA Neural Network synthesis and resource estimation
LUTs | 8%
FFs | 4%
DSPs | 40%

## Slide 17
FPGA preliminary simulation
Node simulation
Python run
16 nodes implemented both in python and on the FPGA.
Same input and weights were given to the nodes in python and on the FPGA.
Exactly the same results were obtained.
Mathematical syntax has been correctly implemented on the FPGA

## Slide 18
Time estimates
200 MHz targeted clock frequency, feasible based on synthesis results
The network is trained with 250 Millions simulated data:
250M forward passes, each pass taking 56 clock cycles
16 nodes
16 nodes …
250M backpropagations, each pass taking 104 clock cycles
32-16 backprop 32-16 backprop
…
Total latency
1 clock cycle
1 clock cycle

## Slide 19
Time estimates
200 MHz targeted clock frequency, feasible based on synthesis results
The network is trained with 250 Millions simulated data:
250M forward passes, each pass taking 56 clock cycles
16 nodes
16 nodes …
250M backpropagations, each pass taking 104 clock cycles
32-16 backprop 32-16 backprop
…
Total latency
1 clock cycle
1 clock cycle

## Slide 20
Time estimates
200 MHz targeted clock frequency, feasible based on synthesis results
The network is trained with 250 Millions simulated data:
250M forward passes, each pass taking 56 clock cycles
16 nodes
16 nodes …
250M backpropagations, each pass taking 104 clock cycles
32-16 backprop 32-16 backprop
…
Total latency
Total training time on CPU hours
Total training time on FPGA minutes
1 clock cycle
1 clock cycle

## Slide 21
Conclusions and future work
MRF is an important and powerful technique that provides quantitative brain maps with a single acquisition
Helps to move in the direction of personalized healthcare
Neural Networks are crucial in the reconstruction of MRF quantitative maps
Once the neural network is trained it is accurate and fast, but its training is really demanding
We are developing a hardware accelerated neural network able to reconstruct MRF quantitative maps
With a clock frequency of 250 MHz, we are expecting to be able to train the network in less than 3 minutes
Implement optimizing algorithms for
Pipelines for additions and multiplications
Clock domain management
Optimizers for backpropagation
This approach has the potential to enable real-time brain map reconstruction
Scanners with integrated NN hardware accelerator for map reconstruction
Analysis on mobile devices

## Slide 22
Mattia Ricchi
National Institute of Nuclear Physics (INFN), Division of Bologna, Italy
Department of Computer Sciences, University of Pisa, Italy
Department of Physics and Astronomy, University of Bologna, Italy
mattia.ricchi@phd.unipi.it
Thank you for your attention