## Slide 1: Benchmarking Headtail with e-cloud observations with LHC 25ns beam
H. Bartosik, W. Höfle, G. Iadarola, Y. Papaphilippou, G. Rumolo

## Slide 2: Outline
Part I
  Observations with 25ns beams in LHC and estimation of δmax in the LHC arcs
  Reproducing machine observations with HEADTAIL simulations
Part II
  Dependence on distribution of electron cloud
  Dependence of instability onset on build-up parameters
Part III
  Comparison of simulations with beam observations with large chromaticity

## Slide 3: Scrubbing history of the LHC arcs
G. Iadarola and G. Rumolo (Chamonix 2012)
24 bunches
Up to 288 bunches
Injected (with Q’>15)
δmax≈2.1
26/08: 48 bunches with Q’≈2

## Slide 4: Observations with 25ns beam in the LHC
June 29th: 24 bunches: strong emittance growth, but no instability
August 26th: 48 bunches on beam 2 with 1e11p/b and standard chromaticity (Q’x≈Q’y≈2)
Injection with transverse damper  dumped after ~1000 turns (beam excursion)
Injection without transverse damper  dumped after ~500 turns (fast beam loss)
Further MDs in October: up to 288 bunches injected
high chromaticity (Q’x≈Q’y≈15) needed for stabilizing the beam
Clear signature of electron cloud effects: pressure rise, heat load, emittance growth along the bunch train, losses …
Suitable to benchmark simulation
codes
~ 150 turns
Losses vs. time

## Slide 5: Post mortem of the 2 beam dumps on August 26th
 explains why 24 bunches could be injected and stored …
notable oscillations only
for last bunches …
up to ±5mm
~ bunch 25 is the first unstable
mainly coupled bunch oscillations
single + coupled bunch oscillations
without transverse damper
with transverse damper
The ~last 73 turns before the beam dump are stored in the post mortem …

## Slide 6: Simulation procedure
Single passage of 48 bunches
Equal bunch intensities (1.0e11p/b)
Transverse emittance of εx=εy=3.5μm
Electrons move in dipole field
Beam screen approximated as ellipse
PyECLOUD
Headtail
Headtail
HEADTAIL
e- distribution from PyECLOUD
e-cloud reset after bunch passage
Electrons move in dipole field
Each bunch simulated individually
Simulation of 500 turns
48x
1x
Headtail simulation 1
Headtail simulation 1
48x
e- distribution at bunch entrance
bunch 48

## Slide 7: Simulation results – onset of instability
No instability in horizontal plane (e-cloud distributed in dipoles only)
   Consistent with coupled bunch motion observed in LHC
Onset of vertical instability at bunch 26 with
  δmax=2.1 (as determined from heat load data), R0=0.7
  20000 primary electrons with a uniform spatial distribution
  LHC beam and machine parameters (1e11p/b, εx=εy=3.5μm, Q’=2, …)
Losses are taken into account (collimators placed at 5.7σ, as in the real machine)

## Slide 8: Simulation results – all 48 bunches
Rise time of vertical instability on the order of few tens of turns
Maximal oscillation amplitude of about 1mm
  Up to 5mm observed in LHC with dampers on
  Up to 2mm observed in LHC without dampers
Coherent oscillations until emittance growth and significant losses stabilize the beam

## Slide 9: Outline
Part I
  Observations with 25ns beams in LHC and estimation of δmax in the LHC arcs
  Reproducing machine observations with HEADTAIL simulations
Part II
  Dependence on distribution of electron cloud
  Dependence of instability onset on build-up parameters
Part III
  Comparison of simulations with beam observations with large chromaticity

## Slide 10: Dependence on “stripes”
… it’s mainly the central electron density that determines the instability threshold
99% of beam

## Slide 11: Dependence on number of primary electrons
Onset of instability can be inferred approximately from the central electron density
Instability threshold in LHC at injection energy is around ρc≈1e12e-/m3
  Consistent with simulations assuming uniform electron cloud
Onset of the instability depends on the number of primary electrons
  Unlike the estimation of δmax from the heat load data where the saturation level counts

## Slide 12: Dependence on distribution of seed electrons
  s
Uniform distribution of primary electrons
Gaussian distribution + 10% uniform background
 Similar instability onset but very different central density in the saturated part of the train

## Slide 13: Scanning build-up parameters
Scanning δmax and number of primary electrons
Combinations where instability onset is between bunch 23-27 considered compatible
Investigated range of number of primary electrons/bunch corresponds to ~10-200nT
 More seed electrons needed for uniform distribution due to smaller central density

## Slide 14: Outline
Part I
  Observations with 25ns beams in LHC and estimation of δmax in the LHC arcs
  Reproducing machine observations with HEADTAIL simulations
Part II
  Dependence on distribution of electron cloud
  Dependence of instability onset on build-up parameters
Part III
  Comparison of simulations with beam observations with large chromaticity

## Slide 15: Large chromaticity – beam observations …
Further MDs for scrubbing the LHC with large chromaticity
  Q’x≈Q’y≈15 needed in addition to transverse feedback for stabilizing the beam
  Injection of up to 288 bunches, but with (fast) emittance blow-up and slow losses
Norm. Vertical emittance [mm mrad] – Beam2 14/10/2011
Reminder: estimated here δmax≈1.8

## Slide 16: Large chromaticity – simulation …
δmax=2.1 with 32000 primary e-/bunch (uniform) - Q’x≈Q’y≈15
δmax=2.0 with 19200 primary e-/bunch (Gaussian + 10% uniform) - Q’x≈Q’y≈15

## Slide 17: Summary and conclusions
Onset of vertical single bunch e--cloud instability can be reproduced in good agreement
  using δmax estimated from heat load data analysis
  combining PyECLOUD for build-up and HEADTAIL for beam dynamics simulations
  Simulations show fast emittance growth and strong losses, similar to observations in LHC
Instability onset depends strongly on central electron density seen by the bunch
  Central density before saturation depends strongly on the distribution of primary electrons
  Uncertainty on pressure and initial distribution of primary electrons plays important role for the onset of instability but is of minor concern for the analysis of heat load data
Large chromaticity helps stabilizing the beam but still emittance blow-up and losses
  Observed both in simulations and in the LHC
Could be interesting to include the effect of the damper in the single bunch simulation
Coupling between bunches should also be taken into account
  Self consistent model of electron cloud effects for studying horizontal coupled bunch instability
   Combine HEADTAIL with PyECLOUD …

## Slide 18
Thank you for your attention!

## Slide 19: Backup slides – horizontal cuts

## Slide 20: Backup slides – stripes only