## Slide 1: Full simulation study of a hadronic calorimeter for a future muon collider
110o Congresso Nazionale SIF
Bologna, September 9-13, 2024
Lisa Generoso
University and INFN Bari
On behalf of the IMCC Collaboration

## Slide 2
Why a multi-tev muon collider ?
Point-like particle
Clean collisions
Full CoM energy available for hard collisions
(as in e+e- colliders)
5 years of operation
Ideal probe for Higgs physics
m 200me
negligible loss of the beam energy due to bremstrahlung
 High energy frontier
(as in hadron colliders)
Proton collider of a much higher CoM energy
Vector Boson Fusion
 Higgs Factory
 |  | #Higgs
3 TeV | 1 ab-1 | 5 x 105
10 TeV | 10 ab-1 | 1 x 107
 |  | #Higgs
3 TeV | 1 ab-1 | 5 x 105
10 TeV | 10 ab-1 | 1 x 107
Improve the precision of Higgs couplings to the per-mille level
Measure Higgs self-coupling constant
Observe trilinear and quartic coupling
https://arxiv.org/abs/2303.08533
https://arxiv.org/abs/2303.08533

## Slide 3
muon collider CHALLENGE
UNSTABLE NATURE OF MUONS

Beam Induced Background (BIB)
DETECTOR :
Radiation hard technology
Good time resolution
z
y
x
ᵠ
DESIGN FOR A
3 TeV MUON COLLIDER DETECTOR
Tracking system
Calorimeter system
  PbF2 ECAL (CRILIN): new proposal from LNF-PD INFN
  MPGD HCAL: new proposal and protptype developement from INFN Bari
3.6 T magnet yoke + muon system
Muon decay products + interaction with the detector material (mostly photons and neutrons)
Asynchronous arrival time
https://arxiv.org/abs/2303.08533
MDI : shielding tungsten nozzles

## Slide 4
WHY AN MPGD-based HCAL?
Resistive Micro Pattern Gaseous Detectors
Satisfy all the previous requirements ✔️
+
High rate-capability O(MHz/cm2)
Cost-effective for large-area instrumentation
MPGD-based HCAL
60-layer SAMPLING CALORIMETER
Layer thickness: 2.65 cm - cell: 1 cm2
HCAL requirements:
Radiation hard to withstand ~10-5 GRad/year
Time resolution of O(ns)
Energy resolution 60% /√E
Fine granularity (1 – 3 cm2)
Longitudinal segmentation
GEOMETRY OF THE CALORIMETER SYSTEM IMPLEMENTED IN THE FULL DETECTOR SIMULATION SOFTWARE (iLCSoft)
HCAL LAYER COMPOSITION:
Iron (absorber) 20 mm
Argon (active material) 3 mm
Copper (RO electronics) 0.1 mm
PCB (RO electronics) 0.7 mm
Air (environment) 2.7 mm
CRILIN ECAL
5-layer SEMI-HOMOGENEOUS CALORIMETER of PbF2
Layer thickness: 4 cm - depth: 0.9 λI

## Slide 5
1000 events generated with Whizard at 3 TeV
On average :
  ~50 particles in each di-jet event
  ~10 hadrons per jet
STUDY OF  H 
DI-jets event analysis
mean energy : ~9 GeV for (~80% of the hadrons)
  ~15 GeV for p, n, ,
~95% of particles below 20 GeV
Most of the particles produced at the interaction point convert their energy into hadronization processes
 high particle multiplicity / low particle energy
Detector characterization with monochromatic guns with energy in the observed range 1.5-100 GeV
#PARTICLES PER EVENT
#HADRONS PER EVENT

## Slide 6
Calorimeter showers
Simulation of monochromatic guns performed through the DD4HEP package
Particles release energy deposits (HITS) in the calorimeter volume
noES Sample
MIP-like behaviour in ECAL
Shower starts in HCAL
Shower profile in HCAL
CLUSTER FORMATION
Pandora PFA
A cone-based forward projective clustering algorithm
grouping ECAL and HCAL hits into clusters
ENERGY RECONSTRUCTION OF CLUSTERS
ECAL HITS  ANALOG READOUT: EECAL
HCAL HITS  DIGITAL READOUT: EHCAL
Eraw = EECAL + EHCAL
EH Sample
ECAL absorber ~ 1𝛌I
Shower starts in ECAL
ECAL+HCAL

## Slide 7
DIGITAL READOUT
Cluster ENERGY - HCAL
HCAL energy: increasing function of the total number of HCAL hits associated with the cluster
EHCAL =(NTOT)
At high EMC, more shower particles might impinge on the same cell
Larger energy deposit in the cell, but one single hit is counted
 Saturation of energy resolution at high energies
LOW ENERGY
HIGH ENERGY
IMPROVEMENT
3 LEVEL DIGiTIZATION
SEMI-DIGITAL READOUT
Set 3 energy thresholds: T1 - T2 - T3
Count separately HCAL hits within the different energy ranges (, , )
HIGH ENERGY
Event digitization and reconstruction with Marlin through the DDMarlinPandora package
The cluster energy is a weighted sum
EHCAL =
with , and depending on NTOT
To assess the best combination of T1 - T2 - T3 : threshold scan based on the energy distributions of hits at different EMC of the incoming
 Energy resolution as final the figure of merit :
0.2 – 4 – 12 keV

## Slide 8
Digital vs SEMI-DIGITAL READoUT (RO)
HCAL ENERGY RESOLUTION
Reconstruction of the noES samples with Digital RO (DRO) and Semi-Digital RO (SDRO) Thr: 0.2-4-12 keV
Linear calibration of the energy spectra of clusters, accounting for energy underestimation due to invisible energy
Gaussian fit of the calibrated energy distributions
Extract the mean Eclu and the sigma
 resolution points /Eclu
Fit function
Comparable performances below 6 GeV
DRO: Saturation at high energies of the fit function with an evident increase in the experimental points
Better performances of the SDRO :
  /Eclu =

## Slide 9
CRILIN ECAL + MPGD HCAL (SDRO)
ENERGY RESOLUTION of the full calorimetric system
guns with EMC of 1.5-100 GeV noES + EH sample
Ad hoc calibration of the energy spectra accounting for different responses of ECAL and HCAL
Average resolution from the fit:
      /Eclu =
With respect to the intrinsic HCAL resolution :
The constant term C slightly decreases  better reconstruction at high energies
The stochastic term S increases  fluctuations due to analog read out of the ECAL

## Slide 10
BIB IN HCAL
BIB containment within the first 20 layers of HCAL
Probability of a cell to be fired in the first layer :
BIB : ~ 1 x 10-5
5 GeV : ~ 0.2 x 10-5
20 GeV : ~ 0.8 x 10-5
      potential problems for low energy pion reconstruction
ARRIVAL TIME
1500 events of BIB generated at the Muon Collider in 1 BX : 
Arrival time distribution is uniform in the range 7-20 ns, while signal peaks at 6 ns
   Cut at t > 10 ns ~50% BIB rejection

## Slide 11
CLUSTER ENERGY RECONSTRUCTION with bib
Reconstruction of the w/wo BIB noES samples with SDRO Thr: 0.2-4-12 keV
Compatible in resolution with BIB overlaid
However, the parameter S, accounting for uncertainties, remains below 60%
 Satisfied the energy resolution requirements for an imaging HCAL in a multi-TeV Muon Collider
BIB IMPACT ON ENERGY RESOLUTION
 | Signal | Signal+BIB
S [%] | 43.78 9.75 | 44.40 12.66
C [%] | 12.61 1.73 | 14.89 2.15
 | Signal | Signal+BIB
S [%] |  | 
C [%] |  | 

## Slide 12
Characterization and optimization of the innovative MPGD-based HCAL for the Muon Collider in a full simulation of the detector environment
CLUSTER RECONSTRUCTION
Implementation of SDRO with the optimal threshold choice:
0.2-4-12 keV
HCAL intrinsic energy resolution :
/Eclu = 45.27%/ 12.35%
Significant improvement wrt DRO
Stochastic term below 60%, as required for imaging HCALs at Muon Colliders
In the innermost layers of HCAL, occupancy of the BIB hits comparable to that of the Signal
However, the energy resolution is negligibly affected by the BIB overlay
 further improvement is expected for a cut on BIB hits
at arrival times > 10 ns provided the necessary electronics
FUTURE STEPS
Optimize Particle Flow event reconstruction to analyze energy of jets
CONCLUSIONS

## Slide 13
FOR THE ATTENTION
THANK YOU

## Slide 14
BACKUP SLIDES

## Slide 15
Pandora Particle Flow Algorithm
Clustering
ECAL+HCAL
Cluster = ECAL hits + HCAL hits
Cone-based forward projective clustering algorithm from the innermost to the outermost layer
Efficiency tested with 1 per event  expected 1 cluster per event
Detector efficiency = (nr. events with 1 cluster) / (sample size )
Low energies EMC  big fraction of zero-cluster events due to impossibility of finding and merging neighboring hits
  low multiplicity of produced and reconstructed hits
For EMC > 9 GeV, saturation at ~95%
BUT many MULTIPLE CLUSTERS  Discard all the multiple-cluster events and perform the cluster energy analysis with SINGLE CLUSTER events
Data

## Slide 16
Pandora Particle Flow Algorithm
Clustering
Algorithm Efficiency tested with 1 per event  expected 1 cluster per event
Algorithm Effective efficiency is given by (nr. single-cluster events) / (sample size )
  At low energies EMC  dominates the fraction of zero-cluster events
  For EMC > 9 GeV, increasing number of MULTIPLE CLUSTERS
Algorithm logic:
designed to rather separate true clusters than merge energy
deposits from multiple particles into a single cluster
multiple clusters result from unmerged groups of hits, each
carrying a fraction of the true cluster energy
Discard all the multiple cluster events, and associate single clusters within a ΔR < 0.2 from the MC

## Slide 17
THRESHOLD CHOICE
SEMIDIGITAL READOUT
ENERGY DISTRIBUTIONS OF SIMHITS NORMALIZED BY THE NUMBER OF ENTRIES
The choice of T2 and T3 should be based on the ESimHit values at which the difference between the curves is more evident :
From 0 to ~2.5 keV the curves are almost indistinguishable
After 2.5 keV, the tails tend to increase with EMC  the probability of having larger energy deposits for high EMC is higher
For ESimHit 10 keV, the curves feature significant fluctuations (especially at low EMC)  the number of entries above a high threshold decreases significantly

## Slide 18
SEMIDIGITAL RO - THRESHOLD CHOICE
HCAL ENERGY RESOLUTION
Energy resolution as the figure of merit to assess the best threshold combination
A too-small T3 (~3 keV) makes the resolution above 48 GeV worse
Comparable results obtained for fixed T3 = 12 keV and varying T2
 The best combination is the one providing the minimum C parameter: 0.2-4-12 keV

## Slide 19
SEMI-DIGITAL READOUT
Cluster ENERGY - HCAL
ENERGY THRESHOLDS
T1 = 0.2 keV : set by the sensitivity [10 fC] of the readout electronics
T2 - T3 : threshold scan based on the energy distributions of hits at different EMC
 Energy resolution as the figure of merit to assess the best combination :
0.2-4-12 keV
At each energy point EMC, , and are obtained by a minimization
The dependence of , and on on NTOT is obtained by a 2nd order polynomial fit

## Slide 20
LINEAR CALIBRATION – noES selection
Cluster ENERGY
HCAL  invisible energy  energy underestimation
CALIBRATION
Gaussian fit of the cluster energy distributions
Represent Eclu mean = as a function of EMC
Linear fit  apply the corrective parameters : Ecalib = (Eclu-b)/a
BEFORE CALIBRATION
AFTER CALIBRATION

## Slide 21
CALIBRATION – noES + EH sample
Cluster ENERGY
ECAL and HCAL have different responses
Double peaks in monochromatic guns
 separate calibrations
  EH : Ecalib = a ErawECAL + b
  noES: Ecalib = c ErawHCAL
a, b and c are obtained by minimizations
AFTER CALIBRATION

## Slide 22
10 GeV
Charged vs Neutral hadrons
Similar cluster energy reconstructed for and K0 at corresponding energy points
50 GeV

## Slide 23
HCAL HITS
BIB CHARACTERIZATION
Uniform longitudinal distribution without prominent differences from the pion guns
   No possible cut on the z
SimHit average energies of ~ 4 keV  twice the value of the signal hits
   No possible cut changing the RO energy thresholds
Arrival time distribution is uniform in the range 7-20 ns, while signal peaks at 6 ns
   Possible cut at t > 10 ns
Z-axis
HIT ENERGY
ARRIVAL TIME

## Slide 24
CLUSTER RECONSTRUCTion with bib
BIB-only clusters have average energies of ~ 0.75 GeV
small high-energy tail partially overlapping with cluster energies of 5 GeV pions
well distinguishable from cluster energies of 20 GeV pions
SIGNAL and BIB separately
Almost negligible decrease in energy :
Due to BIB ONLY CLUSTERS produced by low-energy particles
 Overall BIB does not affect Custer energy reconstruction at EMC > 5 GeV
BIB OVERLAY ON SIGNAL

## Slide 25: CLUSTER MULTIPLICITY
Comparison AT 20 GeV
SIGNAL
SIGnal+BIB
BIB-only
BIB-only: Low clustering efficiency: ~70% of 0-cluster events
SIGNAL vs SIGNAL+BIB:
Increase of multicluster events: on average from 1.61 (SIGNAL-only) to 3.09 (SIG+BIB) clusters per event
Decrease in clustering efficiency: from ~50% (SIGNAL-only) to ~35% (SIG+BIB) 1-cluster events

## Slide 26: CLUSTER-Pion ΔR
Selection on single-cluster events (fewer entries in SIGNAL+BIB)
The SIGNAL+BIB has SIGNAL clusters, BIB clusters, or MIXED clusters (RecHits from the pion or the BIB)
Hits from the BIB are uniformly distributed in space and arbitrarily far from the pion path
 BIB and MIXED clusters result in having larger ΔR wrt the MC pion
 Distribution means : 66% increase at 5 GeV - 87% increase at 20 GeV
Comparison : SIGNAL - Signal+BIB

## Slide 27: CLUSTER SIZE
Comparison: SIGNAL - Sig+BIB
Overlaying BIB on the signal  slight decrease in clustering efficiency and cluster size
BIB and MIXED clusters have on average a larger ΔR < 0.2 not passing the matching selection criterion
BIB-only clusters have a small number of hits  decrease the mean of the distributions
SIGNAL and BIB separately
SIGNAL AND BIB merged