## Slide 1: An Update on the FOOT Experiment Programma anni futuri Richieste 2025 Sblocchi SJ
M. Villa (INFN Bologna)
05 September 2024

## Slide 2: The FOOT Collaboration (2025)
93+6 Authors, 33+2 Institutions
Italy, France, Germany, Japan, Cuba, +India
3 Continents (Europe, Asia, America)
INFN:
12 units (Ba, Bo, LNF, LNGS, Mi, Na, Pg, Pi, Rm1, Rm2, TIFPA, To)
66 researchers & 13 technologists
28.9 FTE (25.5 researchers, 3.4 technologists)
2025:
LNGS : Preparation/development of nuclear emulsions
Calicut University (Kerala, India): participation to the analysis (MAECI - mobility of researchers)

## Slide 3: Data taking campaigns already performed
Beam | Target | Energy MeV/u | Statistics (millions, electronic set-up only) | Integral Differential elemental | Integral Differential isotopic | direct | Inverse | Emul-sions | Campaign
O | C C2H4 | 200 400 | 0.06 | angle | NO | YES | NO | Yes Yes | GSI 2019 GSI 2020
O | C C2H4 C C2H4 | 200 200 400 400 | 14.2 12.2 5.5 6.5 | angle | NO | YES | NO | Yes | GSI 2021
He | C | 100 140 200 220 | 18.5 19.6 13.5 14.4 | angle | NO | YES | NO | No | HEID 2022
C | C | 200 | 4.1 | angle | NO | YES | NO |  | CNAO 2022
C | C C2H4 | 200 200 | 3.2 2.0 | Angle Energy | YES | YES | YES | Yes | CNAO 2023
Analysis status
published
In the pub phase
Only detector calib
Det calib.
Started

## Slide 4: Vertex & Inner tracker – CNAO 2023
Vertex spatial resolutions

## Slide 5: Magnet and Intermediate Tracker!
BTF test
CNAO set-up

## Slide 6: LNF measurements. 3D mechanical and magnetic model
Needed several iteration to get the real «as built»
Several tests for different «real positions» of M1 & M2
Permanent magnets BH curves from producer.
Chart: M2
Chart: M1
Max 2% disagreement.
<0.5% at B max

## Slide 7: MSD status
A lot of effort to understand well the detector. W.r.t. the starting condition:
Changes in firmware to reduce induced noise in the strips
Optimized tracking of the pedestals (that might vary in a run)
Updated definition of hit clusters with two thresholds (Seed, signal)
Optimized spatial reconstruction, taking into account the eta-dependence
Energy deposition calibrated w.r.t. the eta-dependence
Checked all the samples from GSI 2021 to CNAO 2023

## Slide 8: η correction: application to the energy release
Apply η-correction → Sensor response correctly flattened!!
16O
16O
He
C
16O @ 400 MeV/u
5mm C target
16O
N
C
B
Be
Li
He
In-flight interations can be well identified if they happens after MSD
Median on a track

## Slide 11: TOF Wall – Energy calibration – CNAO 2023
Routine calibration at each data taking: check of timings and energy deposits

## Slide 12: Calorimeter calibration
Set-up almost completed
Module holding mechanics to be substituted
HIT2022: few modules calibrated with p, He, C, O
CNAO2023: all modules calibrated with p & C

## Slide 13: Charge dependence of the parametrization
HIT 2022
CNAO 2023

## Slide 14: GSI 2021 analysis – electronic set-up – 16O+C, 400 MeV/n
Few detector elements: SC, BM, TW (no VTX, ITR, MSD, CALO)
  «high» background from in-flight interactions
Full analysis chain; MC closure test OK;
Efficiencies validated for each detector
H
He Li Be B C N
1 2 3 4 5 θ [°]
He

## Slide 15
GSI 2021 analysis –
electronic set-up –
16O+C2H4, 400 MeV/n
Ongoing analysis of C2H4
Preliminary results
1 2 3 4 5 θ [°]
H
He Li Be B C N
He

## Slide 16
Analysis of 16O @ 200 MeV/n on C and C2H4 targets almost completed:
  Improvements in data-driven effects added on Monte Carlo reconstruction (background, misalignments, local distortion due to chemical development…)
  Evaluation of total and reaction cross sections
  Evaluation of systematics effects by data-driven methods
Emulsions: data analysis and cross section measurement
ECC
SC
BM
BEAM →
Paper on cross section measurements with16O at 200 MeV/n on C, C2H4 and H in preparation
S1: Vertexing
S2: Charge identification
S3: Momentum
C (C2H4) layer
Emulsion film
Lexan
Tungsten
Tungsten
Lead
Beam
One beam energy, but
interactions at several energies…

## Slide 17: Integrated cross section H
Total reaction cross section
Total production cross section
PRELIMINARY
# of vertices
# of fragments
PRELIMINARY

## Slide 18
Paper published on Charge identification of fragments produced in 16O at 200 MeV/n and 400 MeV/n on C and C2H4 targets
Publications and papers in preparation (emulsions)
Paper on cross section measurements with16O at 200 MeV/n on C, C2H4 and H in preparation
doi.org/10.3389/fphy.2023.1327202

## Slide 19
Access to the direct kinematics of p+C fragmentation cross sections
All the emulsions from the Pilot test have been scanned with the fast optical microscope
Developed a strategy to identify target fragmentation events: more than 1500 events reconstructed so far
3D displays of reconstructed events
Proton
Proton
NIT emulsions first results
Developments/problems:
Improved optics for the scanning microscopes
Tracks and interactions are clearly seen
Vertices can be easily reconstructed
Impinging proton track is weak
Emulsion preparation and development to be studied carefully

## Slide 20
Nuclear cluster structures can be probed by studying preferential dissociation channels (such as )
clustering has not been thoroughly explored in the energy regime accessed by FOOT
Analysis on-going with 2019 FOOT emulsion DATA ( on carbon and polyethylene targets)
The detection of correlated pairs (relative angle ) is used to measure the production of in the fragmentation of the oxygen nucleus
clustering physics with nuclear emulsions
Observed Production of in DATA

## Slide 21: Future: 2025-2027
- At the moment there is no portable competing experiment with FOOT  no external improvements on cross section measurements.
- We are still working towards differential cross sections for hadrontherapy
- C+C, C+C2H4, O+C, O+C2H4 in different conditions at Ekin < 400 MeV/n
A lot of interest also for higher energies for radioprotection (O+C, O+C2H4 at > 500 MeV/n)
At CNAO there is a broad interest on 4He: both for therapy and for diagnostics
Far Future (>2027)
- O-O cross section (for space radioprotection) and Ca+C cross sections (for hadrontherapy) are also very interesting in their fields

## Slide 22: Foreseen data taking campaigns
Beam | Target | Energy MeV/u | Integral Differential elemental | Integral Differential isotopic | Direct | inverse | Emul-sions | Campaign
C | C C2H4 | 100-200 | Angle Energy | YES | YES | YES | YES (NIT?) | CNAO 2025
O | C | 500-700 (?) | Angle Energy | YES | YES | YES | YES | GSI 2026
C | C C2H4 | 200-300 | Angle Energy | YES | YES | YES | - | CNAO 2026
P | C | 100-220 | Angle Energy | YES | YES | - | NIT | CNAO 2026
C | C C2H4 PMMA | 320-400 | Angle Energy | YES | YES | YES | YES | CNAO 2027
He | C C2H4 PMMA | 200-400(?) | Angle Energy | YES | YES | YES | YES | CNAO 2027

## Slide 23
Capitolo | Richieste (k€) | Voci principali
Inventariabile | 0 | Finanziati su PRIN/MAECI o altro
Consumo | 47 | NA: chim x emulsioni, LNF: mecc+schede,
Apparati | 0 | Finanziati su PRIN/MAECI o altro
Trasporti | 5 | BO, LNGS, MI, PI
Missioni | 144 | Tutti: prese dati a CNAO, meeting di collaborazione, tests, calibrazioni. NO GSI
Pubblicazioni | 0 | Finanziati su MAECI, principalmente
Totale | 195 | per una spesa pro capite di 6.7 k€/FTE
Richieste finanziarie 2025
Storico richieste: 2017: 274 k€, 2018: 815k€, 2019: 868 k€, 2020: 545 k€, 2021: 389 k€
2022: 434 k€, 2023: 317 k€, 2024: 286 k€

## Slide 24
Algoritmo missioni
Viaggio ITA (AR): 220€, viaggio EU (AR): 440€
Giorno ITA, giorno EU: 180€
2 Meeting di collaborazione ITA (per molti)
Presa dati 1-4 persone per sede
Trasporti per BO, LNF, MI, PI, TO (>1 m3, >200 kg, sicurezza)

## Slide 25
Sede | Richieste (k€) | Voci principali
BO, LNF, MI, PI, RM1, RM2, TIPFA, TO | 17 | Metabolismi laboratorio (2 k€/sede in media)
LNGS | 5 | Prodotti chimici per emulsioni / smaltimento
BO, LNF | 8 | Schede elettroniche (DAQ, Nuovo VTX)
LNF | 5 | Sensori MIMOSA di riserva
NA | 11,5 | Emulsioni e reagenti chimici
Totale | 46,5 | 
Richieste consumo 2025

## Slide 26
Richieste di sblocco | Richieste (k€) | Sezione/voci principali
SJ missioni x CNAO | 23.0 | Varie sedi coinvolte (non tutte)
SJ Bonus dottorandi | 24.5 | BO (da usare per il CNAO)
Richieste addizionali & sblocchi
Nessuna richiesta addizionale!  In caso di necessità ci aiuteremo tra le sezioni
SJ totali: 70 k€ - Richieste sblocco 48 k€, restituzione di 22 k€
Prossime prese dati: CNAO – Novembre 2024 – (+BTF prenotata per fine novembre)

## Slide 27: Milestones
Milestone | Data | 
Proceeding/articolo con risultati preliminari campagna 2023 set-up elettronico | 31-dic-2025 | 
Proceeding/articolo con risultati preliminari emulsioni 2023 | 31-dic-2025 | 
Test su fascio del nuovo rivelatore di vertice | 31-dic-2025 | 
Test su fascio di un prototipo di nuovo TofWall | 31-dic-2025 | 
Sottomissione lavoro strumentale FOOT | 31-dic-2025 | 
Proceeding/articolo R&D su emulsioni NIT per FOOT | 31-dic-2025 | 

## Slide 28
Grazie per l’attenzione!