## Slide 2: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Features of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 3: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Features of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 4: At the end of Eithies LEP-II was the King
Linacs and synchrotrons were used to inject in the 28 km synchrotron where both electron and positrons were accelerated up to 100 GeV to collide with a centre of mass energy of 200 GeV
LHC was designed, prototyped, and ready to make use of the LEP 27 km tunnel and of most of its injection accelerator complex
Aerial view of the CERN site with an indication of the circular LEP tunnel

## Slide 5: A Great success for LEP-II
96 GeV:
Mean Nb/Cu
6.1 MV/m
100 GeV: 3500MV
Mean Nb/Cu
6.9 MV/m
104 GeV: 3666MV
Mean Nb/Cu
7.5 MV/m
design
Accelerating Field Evolution with time
Final energy reach limited by
allowable cryogenic power
from G. Geschonke’s Poster for the ITRP visit to DESY

## Slide 6: LEP-II success pushed for the LHC

## Slide 7: But Leptons needed to complement LHC
Leptons (e-, e+, m-, m+) are Fermions, i.e. matter constituents
e+
e-
Ereact. = Ec.m. = 2 Ebeam
Ereact. cannot be controlled and it is unknown
u
u
d
u
u
d
Gluon-Gluon Collision
Ereact. << 2 Ebeam
p
p
Hadrons (p, , ions) are complex composite particles
Fighting for Luminosity

## Slide 8: Livingston chart for Colliders
K. Yokoya, 2014
CEPC
CEPC-hh

## Slide 9: No Circular e+e- Collider after LEP !
Synchrotron Radiation
From an electron in a magnetic field:
Energy loss must be replaced by RF system
$  Ecm2
Electron Gun
Deliver stable beam current
Damping Ring
Reduce transverse phase space (emittance) so smaller transverse IP size achievable
Bunch Compressor
Reduce σz to eliminate hourglass effect at IP
Positron Target
Use electrons to pair-produce positrons
Main Linac
Accelerate beam to IP energy without spoiling DR emittance
Final Focus
Demagnify and collide beams

## Slide 10: All competitors were Normal Conducting
30 GHz
NC Traveling wave
vph ≈ c and vg < c Nornal Conducting
11.4 GHz

## Slide 11: SRF in 1990, when TESLA was born
“Livingston Plot” from H. Padamsee
All SRF cavities operated in CW
CW = Continuous Wave

## Slide 12: But… all Linear Colliders must be pulsed
All the LCs must be pulsed machines to improve efficiency. As a result:
duty factors are small
pulse peak powers can be very large
RF Pulse
Bunch Train
Beam Loading
<10-200 ms
<1 µs-1ms
1-300 nsec
100 m - 300 km
…………………....
……
gradient
with further input
without input
filling
loading
accelerating field pulse:
C. Pagani - ISLC08 - Lecture 1
Oak Brook, October 20, 2008

## Slide 13: The Origin of TESLA (The SRF Linear Collider)

## Slide 14: Ws Summary by Hasan Padamsee

## Slide 15: From the H. Padamsee’ Summary - 1

## Slide 16: From the H. Padamsee’ Summary - 2

## Slide 17: From the H. Padamsee’ Summary - 3

## Slide 18: What we need to use SRF
The power is deposited at the operating temperature of few K
We need to guarantee and preserve the 2 K environment
Cavity is sensitive to pressure variations; only viable environment is sub-atmospheric vapor saturated He II bath
We need a thermal “machine” that performs work at room temperature to extract the heat deposited at cold
The Thermal machine efficiency is just a fraction of the Carnot efficiency
Less favorable Geometrical Factor G

## Slide 19: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Feature of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 20: Cryomodule & Cavity Concept from Cornell
9-cell, 3 GHz
Support Posts, Gas Return Pipe, 2 Shields
2 Phase line, RF power via Coaxial cables

## Slide 21: Memories from the Cornell Workshop

## Slide 22: 1992: DESY hosts the TESLA Collaboration
Develop SRF for a TeV Linear Collider
  Increase gradient by a factor of 5 (Physical limit for Nb at ~ 50 MV/m)
  Reduce cost per MV by a factor 20 (New cryomodule concept and Industrialization)
  Make possible pulsed operation (Combine SRF and mechanical engineering)
Major advantages vs NC Technology
  Higher conversion efficiency: more beam power for less plug power consumption
  Lower RF frequency: relaxed tolerances and smaller emittance dilution
as in 1992
Björn Wiik

## Slide 23: The TESLA SRF Cavity, 1.3 GHz, 9-cell

## Slide 24: TESLA Cryomodule Design Rationales
High Performance Cryomodule was central for the TESLA Mission
More then one order of magnitude was to be gained in term of capital and operational cost
High filling factor: to maximize real estate gradient
Long sub-units with many cavities (and quad): cryomodules
Sub-units connected in longer strings
Cooling and return pipes integrated into the main cryomodule
Low cost per meter: to be compatible with a long TeV Collider
Cryomodule used also for feeding and return pipes
Minimize the number of cold to warm connections for static losses
Minimize the use of special components and materials
Modular design using the simplest possible solution
Easy to be alligned and stable: strict beam requirements: +/- 0.3 mm (rms)

## Slide 25: Cryomodule Evolution at Fermilab

## Slide 26: Schematic Longitudinal Layout

## Slide 27: The Fermilab Support Post

## Slide 28: Design Review by DESY (and INFN)

## Slide 29: CRY 1 – Some new Hints from Fermilab

## Slide 30: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Features of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 31: CFY-1: the FNAL-DASY-INFN Compromize

## Slide 32: Support Posts (FNAL Design) - 1
Support Posts are the mechanical cryogenic connections of the HeGRP (He Gas Return Pipe) that supports all the active elements. FNAL Design
The insulating element is a fiberglass pipe dimensioned in order to keep the eigenfrequencies high
Stainless Steel and aluminum flanges are shrink-fitted for mechanical connection to GRP, thermal shields and room temperature support
Each support post has been tested by compression-tension cycles to verify the stiffness of the interference junction
A break test shown that the post break point is about 100 kN

## Slide 33: Support Posts (FNAL Design) - 2

## Slide 34: CRY 2 , new shields and fabrication strategy

## Slide 35: CRY 3, the reference for most projects

## Slide 36: Cryomodule & Assembly as Crucial as Cavity
Required plug power for static losses < 5 kW / (12 m module)
Reliable Alignment Strategy
Sliding Fixtures @ 2 K
“Finger Welded” Shields
Three cryomodule generations to:
improve simplicity and performances
ensure precise alignment
minimize the cost

## Slide 37: From Cry 1 Prototype to Cry 3
Extensive FEA modeling (ANSYS™) of the entire cryomodule
  Transient thermal analysis during cooldown/warmup cycles,
  Coupled structural/thermal simulations
  Full nonlinear material properties
Detailed sub-modeling of new components and Laboratory tests
  Finger-welding tests at ZANON
  Cryogenic tests of the sliding supports at INFN-LASA

## Slide 38: The Three Generations in TTF
Cry 1
Cry 2
Cry 3
1st Module in TTF I
Module 1 & 2 in TTF I Module 1, 2 & 3 in TTF II
Module 4 & 5 in TTF II
RF gun
400 MeV
120 MeV
800 MeV
ACC 1
ACC 2
ACC 3
ACC 4
ACC 5
4 MeV

## Slide 39: Cryoodules installed in TTF II
ACC 4 & ACC 5
ACC 2 & ACC 3
RF gun
400 MeV
120 MeV
800 MeV
ACC 1
ACC 2
ACC 3
ACC 4
ACC 5
4 MeV

## Slide 40: 2nd Generation TESLA Cryomodule
New strategy for tolerances and allignment

## Slide 41: New Shield Connection by “Finger Welding”

## Slide 42: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Features of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 43: 3rd Generation TESLA Cryomodule
Reduce the Cross Section and use a standard “pipeline” tube
  Redistribute the internal components
  Reduce the distances to the minimum
Improve the connection of the active elements to the HeGRP
  Sliding fixtures to allow “Semi Rigid Coupler” and Superstructures
Reduce alignment sensitivity to the forces on the HeGRP edges
  Move the external posts closer to the edges
  Include the 300 mm bellow in the in the backbone referencing
Further simplify the assembling procedure
  Simplify coupler cones and braids
  Reduce by a factor two the shield components
System thought for mass production cost cutting
  Tolerances reduced to the strictly required ones
  Simpler components and standard tubes wherever possible

## Slide 44: Cry2 & Cry3: Cross Sections
1 m
0

## Slide 45: Cry3 Cross Section
Helium tank
Coupler port
Thermal shields
Sliding support
HeGRP & System backbone
Support Post
Two phase line
Pressurized He feeding
Shield cooling return pipes
WPM
Shield cooling pipes

## Slide 46: Cry2 to Cry3: Diameter Comparison

## Slide 47: Helium GRP, Posts & Invar Rod
C1
C2
C3
C4
C5
C6
C7
C8
magnet
Fixpoint Invar rod

## Slide 48: C-Shaped Fixtures and Rolling Needles
Four C-Shaped stainless steel fixtures are used to define the position of each one of the thirteen active elements:
8 cavities and 1 quadrupole package. Each active element has four titanium pads welded to the helium tank
Each active element is independently referred to the module axis through screws and “belleville” pushers on both x and y directions of each of the four pads
Rolling needles reduce drastically the longitudinal friction
The longitudinal position of each active element is defined through a fixture to the reference Invar Rod. This makes its position independent from the elongation and contraction of the supporting HeGRP

## Slide 49
Runner
Pad
Rolling needles
Spring Washers
C-shaped support

## Slide 50: Finger-Welded Shield Behavior
Cooldown simulation of the 4.2 K and 70 K aluminum thermal shields.
We used a simultaneous 12 hour linear cooldown.
The maximal thermal gradient on the shields (upper left graph) is below 60 K, a safe value.
The temperature fields show that the gradient is concentrated in the welding region, where the fingers unload the structure
Maximum shield temperature
Maximum temperature gradient
Temperature during cooldown

## Slide 51: Thermo-mechanical analysis of Shields
Applying the computed temperature field, deformations and stress distribution can be easily computed.
Maximum stresses are within acceptable limits
Maximum deformations due to asymmetric cooling are below 10 mm.
Maximum shield displacement
Maximum stresses during cool-down

## Slide 52: From Prototype to Cry 3
Extensive FEA modeling (ANSYS™) of the entire cryomodule
  Transient thermal analysis during cooldown/warmup cycles,
  Coupled structural/thermal simulations
  Full nonlinear material properties
Detailed sub-modeling of new components and Laboratory tests
  Finger-welding tests at ZANON
  Cryogenic tests of the sliding supports at INFN-LASA

## Slide 53: Contents
Introduction
To the TESLA Cryomodule Design Concept
From Cry 1, the Prototype, to Cry 3
Main Features of the Cry 3 Reference Design
WPMs, Experience & Picture Gallery

## Slide 54: WPMs to qualify alignment strategy WPM = Wire Position Monitor
Cry 2
Cry 3
Module 1 & 2 in TTF I Module 1, 2 & 3 in TTF II
Module 4 & 5 in TTF II
On line monitoring of cold mass movements during cool-down, warm-up and operation
Cry 1
1st Module in TTF I
2 WPM lines with 2 x 18 sensors 4 sensors per active element
8 mm bore radius
1 WPM lines
1 sensors per active element 25 mm bore radius
1 WPM line
7 sensors/module 25 mm bore radius

## Slide 55: Large ammount of thermal sensors

## Slide 56: Large Bending in First Cooldown (CRY 1)
The Big Banana
New Cooldown procedure thanks to the WPM’s measurements during the first “fast” cooldown

## Slide 57: Safe Cooldown of ACC4 and ACC5

## Slide 58: ACC4 & ACC5 Met Specs
Still some work at the module interconnection Cavity axis to be properly defined

## Slide 59: WPM as Vibration Sensors
A WPM is a sort of microstrip four channel directional coupler. A 140 MHz RF signal is applied on a stretched wire placed in the center of the monitor bore.
A Wire Position Monitor (WPM) system has been developed for on-line monitoring of the cold mass during cooldown and operation.
The low frequency vibrations of the cold mass, amplitude modulate the RF signals picked up by the microstrips.
The microphonics (and the sub-microphonics) can be recovered de-modulating the microstrip RF signal.
A C
A C
y
B D
B D
x
01 y 03 y 21 x y
10 x 30 x 12 x y
y = a D + a D3 + a D2D
x = a D + a D3 + a D D2
V +V
V −V
D =
V +V
V −V
D =
TTF2-ACC4
TTF2-ACC5
WPM1
WPM4
WPM7
WPM8
WPM11
WPM14
Post
Post

## Slide 60: TESLA Cryomodule Concept Peculiarities
Positive
  Very low static losses
  Very good filling factor: Best real estate gradient
  Low cost per meter in term both of fabrication and assembly
Project Dependent
  Long cavity strings, few warm to cold transitions Large gas return pipe inside the cryomodule
  Cavities and Quads position settable at ± 300 µm (r m s) Reliability and redundancy for long MTTR (Mean Time To Repair)
  Lateral access and cold window natural for the coupler
Constraints
  Long MTTR in case of non scheduled repair
  Moderate (± 1 mm) coupler flexibility required
ILC Acc. Workshop
Beijing, 16 August 2005

## Slide 61: Module assembly picture gallery - 1

## Slide 62: Module assembly picture gallery - 2

## Slide 63: Module assembly picture gallery - 3

## Slide 64: Module assembly picture gallery - 4

## Slide 65: Module assembly picture gallery - 5

## Slide 66: Module assembly picture gallery - 6

## Slide 67: Module assembly picture gallery - 7

## Slide 68: Module assembly picture gallery - 8

## Slide 69: Module assembly picture gallery - 9

## Slide 70: Module assembly picture gallery - 10

## Slide 71: Design changes important for ILC
Move quadrupole to the center
Quad/BPM Fiducialization
High pressure rinsing and clean room assembly issues
Movers for beam based alignment? Why not if really beneficial
Short cavity design
Cutoff tubes length by e.m. not ancillaries (coaxial tuner)
Cavity inter-connection: Flanges and bellows (coating?)
Fast locking system for space and reliability (CARE activity)
Bellow waves according to demonstrated tolerances
Coaxial Tuner with integrated piezo-actuators
Parametric “Blade Tuner” or equivalent for real estate gradient
Integration of fast tuner (piezo actuated) underway
Longer module design: 10-12 cavities
ILC Acc. Workshop
Beijing, 16 August 2005

## Slide 72: The INFN Cryomodule for XFEL & ILC