## Slide 1: Strip FE Chip Readout
F.Giorgi – SVT strip chip meeting

## Slide 2: Simulation schematic blocks
MC generator
Reduced and rivisited version of the one used for pixels
128 Strip channels
FE logic
Readout
(4x256x1 equivalent pixels)
Pisa FE logic
Trigger buffers, TS tag/request handling ecc.
Trigger handling
Hit encoding
Hit de-queue

## Slide 3: Monte Carlo Generator features
Parameters (typical)
  Channels (128)
  Cluster size [static] (for now: 1)
  ToT bits (4)
  ToT resolution [time corr. to 1 ToT step] (?)
  Rate trimmer
Uniform extractor IEEE.math_real.uniform()
  period ~ 2.3 * 1018
  Uniform spatial distribution
  Exponential ∆t distribution
  Uniform ToT distribution
2 counters for effi. estimation
  Generated hit counter
  Generated on busy channel counter
Emulated comparator output pulses (CMP)
  ToT value extraction (1 to 2(ToTbits)-1)
  CMP pulse length = ToT extracted * ToT resolution
Chart: 
∆t Exp distribution
ns
counts

## Slide 4: Monte Carlo Generator features
Parameters (typical)
  Channels (128)
  Cluster size [static] (for now: 1)
  ToT bits (4)
  ToT resolution [time corr. to 1 ToT step] (?)
  Rate trimmer
Uniform extractor IEEE.math_real.uniform()
  period ~ 2.3 * 1018
  Uniform spatial distribution
  Exponential ∆t distribution
  Uniform ToT distribution
2 counters for effi. estimation
  Generated hit counter
  Generated on busy channel counter
Emulated comparator output pulses (CMP)
  ToT value extraction (1 to 2(ToTbits)-1)
  CMP pulse length = ToT extracted * ToT resolution
4-bit value
counts
Chart: 
 | 1987 | 1979 | 1920 | 1974 | 1857 | 1977 | 2029 | 1942 | 2045 | 2028 | 2019 | 1992 | 1955 | 2025 | 2046
4-bit ToT unif. distribution

## Slide 5: Monte Carlo Generator interface
Input
  Test_clk (1 ns) / resets / enables
  “Busy” (128 lines)
Output
  Hit (single pulse for each extraction)
  New hit ( Hit AND busy )
  ToT (strip array (128) of ToT bits (4) )
  CMP emulated output
  Hit counter
  Hit on busy counter

## Slide 6: Stand-alone preliminary test
MCgen
CMP
Busy
loopback
hit generated with a ToT = 14
another hit generated @ 19775 ns
CMP not re-triggered(?)  total CMP length is 140 ns = prev. ToT (14) *10 ns ToT resolution
busy_hit_count incremented by 1
rough inefficiency estimate due to occupancy by busy_hit_count/hit_count.

## Slide 7: Stand-alone preliminary test
Rate (MHz) | ToT res. (ns) | Min (ns) | Max (ns) | Effi
30 | 10 | 10 | 150 | 98.3%
20 | 10 | 10 | 150 | 98.9%
10 | 10 | 10 | 150 | 99.3%
30 | 5 | 5 | 75 | 99.1%
20 | 5 | 5 | 75 | 99.5%
10 | 5 | 5 | 75 | 99.8%
Pulse range
~10k hit statistics
128 channels
busy_hit_count
hit_count
1 -

## Slide 8: StripMCgenerator entity