## Slide 1: Superconductivity
Alessio Rettaroli Alessandro D’Elia
Corso Nazionale di Criogenia e Vuoto
5-8 Novembre 2024

## Slide 2
What is superconductivity
It is a state of matter in which electrons behave differently with respect to normal conductors.
Superconductors have peculiar electrical and magnetic properties
Discovered by Heike K. Onnes in 1911 in its cryogenic laboratory

## Slide 3
Introduction
1908: Liquefied Helium for the first time (4.2 K)
1911: discovered that at 4.2 K the Mercury showed zero resistance
1900
2000
1950
1957
1911
1933-35
1962

## Slide 4
Introduction
1900
2000
1950
1957
1911
1933-35
1962
1933: Meissner and Ochsenfeld discovered the so-called Meissner effect: expulsion of magnetic field from superconductors
1935: The Meissner effect was explained by Fritz and Heinz London with the London equations

## Slide 5
Introduction
1900
2000
1950
1957
1911
1933-35
1962
1950: Ginzburg-Landau theory, a phenomenological explanation of superconductivity
1957: BCS theory (after Bardeen, Cooper, Schrieffer), a microscopic explanation of SC

## Slide 6
1900
2000
1950
1957
1911
1933-35
1962
Introduction
1962: B. D. Josephson predicted the Josephson effect: a tunneling process at the base of electronic devices mainly used in research

## Slide 7
Lev Davidovich Landau (1962)
For pioneering theories on condensed matter, especially liquid helium
Kamerling Onnes (1913)
For his research on the properties of matter at low temperatures which also led to the production of liquid helium
J. Bardeen, L.N. Cooper, J.R. Schrieffer (1972)
For their jointly developed theory of Superconductivity, known as BCS theory
I. Giavier, B.D. Josephson (1973)
For the experimental discovery regarding the tunneling phenomenon in superconductors and the theoretical prediction of the properties of a supercurrent through a tunnel barrier (Josephson effect)
J. G. Bednorz, K.A. Muller (1987)
For their important success in the discovery of superconductivity in ceramic materials
A. A. Abrikosov, K.L. Ginzburg, A.J. Leggett (2003)
For pioneering contributions to the theory of superconductivity and superfluidity
Nobel prizes for superconductivity

## Slide 8
Macroscopic properties
1) Superconductivity is a phenomenon happening at low temperatures
Certain materials become superconductors below their critical temperature Tc.
Tc is usually very small.

## Slide 9
Temperature: how low?
By PJRay - CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=46193149
Typical materials are:
Ceramic materials
Iron based
Metallic alloys
Elements
100 K dark side of the moon
40 K Pluto surface
4 K Mercury, the first discovered

## Slide 10
Macroscopic properties
Onnes observed an abrupt decrease in electrical resistivity of Mercury
Electrical current can endlessly flow in a superconducting circuit (called supercurrent), until a critical current Ic.
2) Zero electrical resistivity
Normal conductors: residual resistivity

## Slide 11
Macroscopic properties
3) Magnetic field is expelled
(Meissner effect - 1933)
Di Piotr Jaworski, PioM EN DE PL; POLAND/Poznań - Inspiration: Image:EXPULSION.png, Public domain, https://commons.wikimedia.org/w/index.php?curid=325237
Magnetic field is expelled until a critical fiel Bc is reached, above which the SC is back to normal conductor
Notes: Spiegato poi nel 1935 da equazioni di London

## Slide 12
Macroscopic properties
4) It is exclusively a Quantum Effect
Superconductivity cannot be explained by classical physics
Notes: Spiegato poi nel 1935 da equazioni di London

## Slide 13
Summarizing
3) Magnetic field is expelled
2) Zero electrical resistivity
1) Low temperatures
Critical temperature Tc
Critical current Ic
Critical field Bc
T(K)
R(W)

## Slide 14
Some theory: BCS

## Slide 15
Atoms
Electrons move around the atomic nucleus on discrete orbits (like the planets in the solar system)

## Slide 16
Atoms
Each «orbit» has different dimension, shape and energy. In quantum mechanics they are called orbitals.

## Slide 17
From atoms to solids
Atoms closely packed form a crystalline lattice. The orbitals of the different atoms mix, forming electronic bands of allowed energy where the electrons can exist.

## Slide 18
From atoms to solids
The crystalline lattice vibrates creating collective wave-like motion
The frequency and amplitude of these vibrations, depend on multiple frequencies, most importantly the temperature

## Slide 19
Cooper pairs formation
At low temperature the lattice vibrations become negligible. The negative charge of an electron generates a deformation of the lattice creating a cloud of positive charge that will attract a second electron. These couple of electrons are called Cooper pairs, and are the main charge carriers in a superconductor.

## Slide 20
Electrons vs Cooper pairs
Electrons moving in a lattice scatter with the atomic nuclei. This reducs their mobility and is the first source of electrical resistance in a metal
Electrons must be in separate states because of Pauli exclusion principle. Cooper pairs are Bosons that condensate in the lowest energy level.
Cooper pairs, travel to the lattice without scattering => no electrical resistance
Normal metal
Superconductor

## Slide 21
Classification by critical temperature
Historically, 30 K is considered as the threshold between:
Low temperature SC
Tc < 30 K
High temperature SC
Tc > 30 K
Room temp. 300 K
Absolute zero 0 K -273.15 °C
30 K
Liquid N2 77 K

## Slide 22
Classification by critical temperature
Low
High

## Slide 23
Low temperature superconductors
Usually metals or simple alloys
«Conventional» conduction mechanism
Not very high Hc2 (with some exceptions)
Al Tc=1.2 K

## Slide 24
YBa2Cu3O7 Tc=92.6 K
YBCO
High temperature superconductors
High temperature superconductors are complex oxides. In contrast to most of the low Tc superconductors, at room temperature they show a ceramic (insulating) behaviour.
In these materials the cooper pairs conduction happens in the CuO2 planes (usually insulating at room temperature)
In addition to having a high Tc, these class of materials also exhibits extremely high Hc2 and critical current, making them extremely appealing for multiple allications (e.g. super high intensity magnets).

## Slide 25
The most used liqud gases are the Liquid Nitrogen (cheapest) and the Liquid Helium (coldest)
Cryogenic techniques
Dilution refrigerators use the thermodynamic properties of a mixture of liquid He3 and He4
Liq. Nitrogen (N2) 77 K
Liq. Helium (He4) 4.2 K
Dilution refrigerator
10 mK

## Slide 26
Classification by magnetic properties
Superconductor
Meissner state
Is
For T < Tc
and B < Bc
Magnetic field B
Type I superconductors
By Frederic Bouquet (user:Fbouquet),Julien Bobroff (user:Jubobroff) LPS, Orsay, France, CC BY-SA 3.0
Perfect diamagnetism (Meissner effect)
The magnetic field is completely expelled, because the SC creates an equal and opposite field inside
normal
SC

## Slide 27
Classification by magnetic properties
Type II superconductors
SC
Mixed SC
normal
For T < Tc
and Bc1 < B < Bc2
For magnetic fields Bc1 < B < Bc2 there is an intermediate state (Mixed state) in which part of the magnetic flux lines can penetrate.
Small paramagnetic behaviour

## Slide 28
Classification by magnetic properties
Type II superconductors
These regions are cylindrical, and made out of a normal core. The cylinders contain the magnetic flux lines.
Picture of the Abrikosov lattice, with increasing B field.

## Slide 29
Classification by magnetic properties
Type II superconductors
On the border a supercurrent flows like in a vortex.
These cores are called fluxons, or magnetic vortices.
The amount of magnetic field entering these cores is quantized. Only integer multiples of the flux quantum enter the superconductor

## Slide 30
Type II superconductors – energy dissipation
Fluxons are like ’’charges’’ in the superconductor, so they are subject to a Lorentz force due to the external magnetic field
B
A Lorentz force implies a movement: fluxons move inside the SC (flux flow)

## Slide 31
Type II superconductors – energy dissipation
B
Fluxons have a normal core, meaning that they contain electrons
Electrons moving in a material dissipate energy = the material have a resistivity.
Type II SC have a small resistivity
Notes: Esistono comunque modi per limitare la dissipazione

## Slide 32
Applications in research
Josephson junctions
Based on Quantum tunneling
Macroscopic effect of a quantum phenomenon
A supercurrent can flow without applied voltage, by the effect of Cooper pairs tunneling through the insulator

## Slide 33
Applications in research
SQUID: Superconducting QUantum Interference Device
Two Josephson junctions in loop. The concatenated magnetic flux is quantized the current is proportional to the flux quanta
SQUIDs are powerful magnetometers:
Half flux quantum detectable:
Minimum magnetic field detected:
(The Earth magnetic field is )

## Slide 34
Quantum technologies

## Slide 35
Qubit
By Abhishek Dubey
Qubits exploits the states superposition to increase calculation power
A two level quantum system is required
JJ provide a solid state system that mimics the features of an artificial atom with discrete energy levels

## Slide 36
Transmon
The transmon is the most simple qubit
It is composed by a Josephson junction shunted by two capacitors
Superconductive circuits are the most promising candidates for large scale scalability!

## Slide 37
Transmon
A resonant cavity is necessary to read the qubit in a non-destructive way
In quantum emchanics, the measurements of a quantum states, makes the wave function collapse destruction of the states superposition

## Slide 38
Applications in everyday life
Superconducting wires are used to build powerful SC magnets, because SC wires do not have resistance --> no heating due to Joule effect
Medical use. MRI, 0.2 – 7 T
Powerful magnets
Accelerators. LHC has 8.3 T magnets
Nuclear fusion. ITER tokamak has11.8 T

## Slide 39
Applications in everyday life
SC Maglev
Central Japan Railway Company
Niobium-Titanium SC magnets are also used to develop frictionless Maglev trains
Levitation
Guidance
Propulsion

## Slide 40
Applications in everyday life
Magnetoencephalography (MEG)
Array of SQUIDs as magnetometers used in neuroscience to detect the small magnetic fields of the brain activity
The brain cortex can be seen, because the skull is magnetically transparent
Magnetic field of human brain:

## Slide 41
Applications in COLD lab
CryOgenic Laboratory for Detectors
Resonant cavities coated with superconductors
Parametric amplifiers
Superconducting magnet (9 T)
Josepshon junctions and SQUIDs as single-photon detectors
Qubits as single-photon detectors

## Slide 42
Thank you for your attention