## Slide 1
DCH FEE
TDR contents discussion

## Slide 2: Outline
Design goals
Requirements
  Specification for charge measurement based DAQ
    dE/dx & time measurements : resolution, dynamic range and linearity
  Cluster Counting option
    dE/dx measurements : resolution, dynamic range and linearity
DCH front-end system: block diagram
ON DETECTOR electronics
    Preamplifiers
    dE/dX based on charge measurements
    dE/dX based on Cluster Counting
Cabling
HV Distribution
    dE/dX based on charge measurements
    dE/dX based on Cluster Counting
OFF DETECTOR electronics
  Triggered Data Path
    Digitizing Modules
        dE/dX based on charge measurements
        dE/dX based on Cluster Counting
OFF DETECTOR electronics
  Triggered Data Path
      Concentrators Modules
    UnTriggered Data Path
      Option #1 - Concentrators Modules
      Option #2 – See Trigger Section
Radiation Environment Policy
Grounding and shielding ….
Conclusion
Questionnaire

## Slide 3
Design goals

## Slide 4: Design goals
SuperB Drift Chamber (DCH) front-end electronics is designed to extract and process the 8056 (to be finalized) sense wire signals to:
measure the electron drift times to the sense wires for tracking purpose (momentum of charged particles)
Measure the energy loss of particles per unit length, dE/dx (particle identification)
provide hits information to the trigger system (trigger primitives)
Measurement of the energy loss of particles per unit length, dE/dx (particle identification) can be implemented by
Measuring the charge collected on the sense wire (discarding high values to remove Landau fluctuations)
Counting the number of cluster generated by the particle crossing the cell
Decision : within the first half of 2012

## Slide 5
Requirements

## Slide 6: Specifications for charge measurements
Overall expected single cell σE ≈ 30 % (dominated by chamber contribution)
  Electronic contribution must be enough low to make it negligible. E.g.: σEL= 15% of σE (4.5%)  sqrt(σE2 + σEL2 ) ≈ σE
Assuming ≈ 50 fC the charge released from a mip (gas gain=105) , σEL = 5%  single channel ENC ≈ 50 fC * 0.05 ≈ 2.5 fC
σE dominated by gas amplification effects:
  Lower range: σEL (2.5 fC ) (could be 3σEL)
  Higher range: ≈ 500 fC (BaBar experience)
Dynamic range
dE/dx Goal: measure particle energy loss with precision of the order of 7.5% (BABAR) despite large fluctuations involved in single measurement (“truncated mean” method)
Resolution
Linearity of the order of 2% matches system requirements
Linearity

## Slide 7: Specifications for time measurements
Overall expected σS ≈ 130μm  dominated by chamber contribution
  σS limits: statistics of primary ionization, electrons diffusion, electronic
  Chamber contribution (σSC ) raw estimation ≈ 440/sqrt(NP) ≈ 110 μm for a 90/10 He/Iso gas mixture
  σEL ≈ sqrt(σS2 - σSC2 ) ≈ 70 μm  σS ≤ 1.5 ns ( 3 * 16 μm/ns drift velocity)
    Main error sources are jitter (time walk + noise) and TDC (digitizing noise)
    Jitter
    Noise: Δt = σN/ (dV/dt) ≈ σN* τ/Vmax (τ = peaking time)
      Assuming σN = 4 mV rms, Vmax = 30 mV, τ = 4 ns  σEL ≈ 0.5 ns
    Time walk contribution: assuming τ = 4 ns a time walk of the order of 1.5 ns with 20 dB input signal dynamic is obtained  quite high  possible (partial) compensation using FADC sampled values
      Digitizing noise ≈ Δ/sqrt(12) with Δ ≈ 1 ns  ≈ 0.3 ns
 Time resolution is dominated by signal time walk
TDC range depends on gas mixture drift velocity and cell size  SuperB DCH max drift time ≈ 600 ns  TDC range ≈ 1us
Dynamic range
Particle tracks reconstruction based on (ionized) electrons drift time toward the sense wire
Resolution
A linearity of ≈ 1% fulfill measurement requirements
Linearity

## Slide 8: Cluster Counting option
Pros
  Particle identification improvement
  Dedicated time measurement not required
  Possible improvement in spatial resolution
Cons
  High sampling frequency digitizers
  Fast processing
  Wide bandwidth and high power requirement front-end (environment noise sensitivity increase)
  Good cables for on-detector  off-detector connection required (bigger size)
  Termination resistor required (system noise baseline) with dedicated PCB
FADC resolution is a function of the lowest sampled signal and system noise
  6 fC wire signal (gas gain 3x105), 10 mV/fC shaper-amplifier, safety factor = 2  30 mV signal
  If we consider only the contribution of termination resistor (bottom limit – peaking time = 3 ns – gain = 10 mV/fC ) we get about 2 mV rms
Resolution
Pros & Cons
Total ionization in 1.2 cm high cell (average) ≈ 30e (90/10 – He/Iso)
Each electron correspond to a different level in output voltage  3 bits/electron  8 bits FADC
Linearity ≈ 2%
Dynamic range and linearity

## Slide 9
DCH front-end system: block diagram

## Slide 10: DCH Front-End system: Block diagram
< 5 m
cables
#173 (48 chs)
#1152 (8 chs)1
121
DAQ
173 OL
16 (12 cores) OL
#16
DAQ
16 OL @ 2Gbits/sec
ECS
16 OL @ 2Gbits/sec
DIOM
Pre-HV boards
121
TRIGGER
TIOM
64 OL @ 1.2Gbits/sec
or Copper Links
#16
ON-DETECTOR ELECTRONICS
DCH BACKWARD END-PLATE
8056 chs
121
ECS
12 cores Fiber Optical Cable patch-panel
16 (12 cores) OL
or Copper Links
OFF-DETECTOR ELECTRONICS
Data Conversion
Trigger Primitive Generation
Boards
173 OL
1 = Cluster Counting option
Trigger option 1: Data Conversion generates trigger primitives
Trigger option 2: Data Conversion board host a Trigger Mezzanine board for partial superlayer tracks reconstruction

## Slide 11: DCH Front-End system: Block diagram
ON DETECTOR electronics

## Slide 12: ON DETECTOR electronics - #1
Front End Boards contain HV blocking capacitors, protection networks, preamplifiers and (eventually0 shapers.
Boards are located on the backward end-plate to maximize S/N ratio and are connected to the Data Conversion boards (located on external crates) through coaxial or twisted pairs cables (Cluster Counting = coaxial)
The end-plate will be divided in (sub)sectors  more cells will be grouped in a single multi-channel preamplifier-shaper board
Preamplifier
Wire signal is used both for charge and time measurement  preamplifier should not worsening too much signal time information (rise time).
Because gas mixture slow drift velocity and moderate detector parasitic capacitance a 80/100 MHz bandwidth transimpedance preamplifier match system requirements
Channel density is not so high and circuit design not so complex  approach based on SMT technology possible  profiting of high bandwidth, low noise SiGe devices developed for mobile-phone applications
dE/dx based on charge measurement
Preamplifier output must reflect as much as possible the wire current input signal, then current amplifier based on fast circuit topologies with low sensitivity to detector capacitance must be used (for example circuits based on current conveyor topology)
dE/dx based on Cluster Counting

## Slide 13: ON DETECTOR electronics - Preamplifier for charge measurements
CDET = 0 pF
CDET = 24 pF
0 mV
100 mV
200 mV
300 mV
400 mV
0 mV
100 mV
200 mV
300 mV
400 mV
8 ns
10 ns
12 ns
14 ns
16 ns
18 ns
20 ns
22 ns
24 ns
PD < 30 mW @ 4V
10 fC
50 fC
10 fC
50 fC

## Slide 14: ON DETECTOR electronics - #2

## Slide 15
Cabling

## Slide 16: Cabling - Signal #1
ON DETECTOR electronics will provide good amplification, but signal levels are still quite low.
Micro-coaxial cables or shielded twisted cables must be used to minimize noise environmental pickup
  Problem can arise due to the cable jacket. Many halogen free cable are quite rigid (large bending radius)
Braid shield twisted pairs offer a good compromise between cost, noise environmental shielding and bandwidth. Nevertheless shielded connectors could be a problem in the ON DETECTOR side
Both micro-coaxial and braid shielded twisted pairs are available in round and flat assembling. Flat assembling is (generally) better for ON DETECTOR front end boards connection, while round cables are better for routing and Digitizing Boards connections.
  Decision will follow the technique adopted for dE/dx measurement
dE/dx based on charge measurement
Micro-coax: 50 Ω / 0.83 – 1.3 mm diameter

## Slide 17: Cabling – Signal #2
Besides considerations for dE/dx based on charge measurements cables for Cluster Counting must features high bandwidth, low losses and controlled impedance (Shielded Controlled Impedance)
There are several assemblies available. Cost is a function of modularity, type of connector and type of cable, but is generally higher than solution for charge measurement because the BW requirement.
  Again, decision on type of cable will follow the technique adopted for dE/dx measurement
dE/dx based on Cluster Counting
Our Price: $1.83
Vol. Pricing: Quantity:25+50+100+Price:$1.67$1.52$1.38
Stock: 65
Mated height: 1.4 mm (55.12 mil)
Cable diameter: 0.7 mm (27.6 mil)
Length: 5.9" (150 mm)
Connectors: Super micro plug
Frequency: DC-7GHz
VSWR: 1.4:1 max
Standard lead time: 4 weeks ARO
1.88 mm diameter

## Slide 18
HV Distribution

## Slide 19: HV distribution
Enough modularity to avoid too many dead channels in case of single chamber channel problem
Modularity is function of the distance from inner layer (example: 2 boards in inner layer – 5 boards in outer layer)
Good feedback of the current dragged by the inner layers (≈ 1 nA) and by the outer layers (≈ 10 nA)
General considerations
1MΩ
2.2 nF
1MΩ
500 pF
10MΩ
10MΩ
Ch 1
Ch 8
Filter Box
[Outside Detector]
Distribution Board
[number of boards is a function of chamber layer]
CH1
Main
Power Supply
BOARD #1
BOARD #N
1MΩ
500 pF
10MΩ
10MΩ
Ch 1
Ch 8
HV Distribution – dE/dx by means of charge measurement

## Slide 20: HV distribution
1MΩ
2.2 nF
Filter Box
[Outside Detector]
Distribution Board
[number of boards is a function of chamber layer]
CH1
Main
Power Supply
BOARD #1
BOARD #N
HV Distribution – dE/dx by means of Cluster Counting
1MΩ
500 pF
10MΩ
Ch 1
RT
10MΩ
Ch 8
RT
1MΩ
500 pF
10MΩ
Ch 1
RT
10MΩ
Ch 8
RT
500 pF
500 pF
500 pF
500 pF

## Slide 21
Triggered Data Path
Digitizing Modules

## Slide 22: Triggered Data Path : Digitizing Modules - Latency (pre-FEX) buffers
First electron(s) cluster arrival time
dE/dx by means of wire signal charge measurement or Cluster Counting
Feature Extraction ON BOARD
Data continuously digitized and readout ONLY if L0 Trigger is delivered
DISCR
< 1 μs
FADC
LPF
TDC
< 1 μs
FADC
Buffer
dE/dE by means of charge measurement – Latency buffers (pre-FEX)
dE/dE by means of Cluster Counting – Latency buffers (pre-FEX)
32 samples (8 bits) @ 28 MHz ≈ 35.7 ns sampling period
≈ 1ns time resolution over-threshold TDC values
Single event buffer size : 32 x 8 bits
32 x 8 x 6 ≈ 6.8 μs latency time
  Separated FADC and TDC buffers
1000 samples (8 bits) @ 1 GHz
Single event buffer size = 1000 x 8 bits
1000 x 6 = 6 μs latency time
6 events buffer looks enough for trigger decision processing

## Slide 23: Triggered Data Path : Digitizing Modules - Event Buffers
COUNTER (0 – n)
L1 FIFO
Sampled data
DATA RO SM
(FEX)
Pushing mode
ADDR
Ev7
Ev6
Ev5
Event RO buffer
(Derandomizer)
Concentrator board
Trigger Latency Time + n samples (Dual-port memory)
2
1
0
n
Sampling clock
ADDR
L1 (synchronized by sampling clock)
Read ADDR
FiFO Empty
FiFO Read
Data (counter value @ L1)
(counter value @ L1) - Latency
32 word (16 bits) block data readout
Over-Threshold data (from comparator)
2
1
0
n
Ev4
Ev3
Ev2
Ev1
Ev0
≈ 72 ns (Dead Time)
56 MHz x 4 clk
16 bits bus
≈ 50 ns (Dead Time)
56 MHz x 6 clk
16 bits bus
NB: Higher transfer rates are possible but as Digitizer Modules SHOULD use Rad Tol components. Then we can not use high performances SRAM based FPGAs.
Es : ACTEL ProAsic max internal frequency ≈ 350 MHz
16/32 data path
Digitizer Module Address (2 Bytes)
Flag (1 Byte)
Trigger Tag (1 Byte) – 5 bits in BaBar
Counter (1 Byte)
Charge (2 Bytes)
Time (2 Bytes)
ADC sample @ Time
Data Stream Example (10 bytes)
BW requirements = 8056 (N. channels) x 10% (occupancy) x 20 (bytes) x 8 (bits) x 150 kHz ≈ 19 Gbits/sec (foreseen: 16 fibers @ 2 Gbits/sec = 32 Gbits/sec)
NB: we have used 20 bytes in calculation instead of 10 (safety factor)
Ev3
Ev2
Ev1
Ev0
Data RO Buffer

## Slide 24: Triggered Data Path : Digitizing Modules – Event Readout
SAMPLING CLK
L1
SAMPLED DATA
READOUT CLK
READOUT ADC DATA

## Slide 25: Triggered Data Path: TDC Implementation
Simulations show it is possible to implement a 4xOversampling – 1ns time resolution TDC in a ACTEL ProAsic3 device
Caveat
  No radiation mitigation technique can be applied to PLLs and (probably) to the high frequency section of 4xOversampling TDC
  FPGA internal resources could be not enough to manage data conversion & feature extraction for an acceptable number of channels.
  At the moment no Ser-Des are available

## Slide 26: Triggered Data Path : Digitizer Modules – CC
After FEature Extraction (primary cluster detection): 30 words (16 bits) containing time arrival information (worst case)
Assuming FEX implemented on Digitizing Board
BW requirements = 8056 (N. channels) x 10% (occupancy) x 32 (words) x 16 (bits) x 150 kHz ≈ 62 Gbits/sec
(foreseen: 16 fibers @ 2 Gbits/sec = 32 Gbits/sec)

## Slide 27: Triggered Data Path : Concentrators
Data
12 chs connector
DAQ section
Data Conversion boards
@ 48 CHS
OL @ 2Gbits/sec
DAQ
ECS
DAQ section
ECS section
DATA CONVERSION CONCENTRATORS/OL
Data Conversion OL (576 channels): 48 (chs) x 12 (Data Conversion) x 0.10 (occupancy) x 20 (bytes) x 8 (bits) x 150 kHz ≈ 1.4Gbits/sec
Total amount of DATA CONCENTRATORS OL : 14 (foreseen 16)
Total amount of ECS CONCENTRATORS OL : 14 (foreseen 16)
12 cores Fiber Optical Cable Splitter
ECS
12 chs connector
ECS section
CONCENTRATORS
DATA
CONVERSION
BOARD 12

## Slide 28: UnTriggered Data Path – Option #1
OL @ 1.2Gbits/sec
OL @ 1.2Gbits/sec
OL @ 1.2Gbits/sec
OL @ 1.2Gbits/sec
TRIGGER
12 cores Fiber Optical Cable Splitter
Data Conversion Boards
@ 48 CHS
12 (number of boards) x 48 (number of chs per board) x 7 MHz (Channel sampling frequency) ≈ 4 Gbits/sec
Trigger Concentrators : 14 – Trigger OL : 56 (foreseen 64)
TRIGGER CONCENTRATOR
Trigger Concentrators
Data Conversion
Board #3
≈ 1 Gbits/sec
Data Conversion
Board #3
Data Conversion
Board #3
Data Conversion
Board #3
≈ 1 Gbits/sec
Data Conversion
Board #3
Data Conversion
Board #3
Data Conversion
Board #3
≈ 1 Gbits/sec
Data Conversion
Board #3
Data Conversion
Board #3
Data Conversion
Board #3
≈ 1 Gbits/sec
Data Conversion
Board #3
Data Conversion
Board #3
TRIGGER

## Slide 29: Radiation Environment Policy
Only qualified components will be used. Anyway SiGe HBT transistors technology is inherently radiation hard
ON DETECTOR electronics
OFF DETECTOR electronics - NO CC
Only Rad Tol components will be used in Data Conversion and Concentrators Boards
  We have already shown it is possible to implement a ≈ 1 ns resolution TDC and FADC readout by means of (lash-ROM based) Rad Tol FPGA (Actel ProAsic)
OFF DETECTOR electronics - CC
Cluster Counting requires lots high performances FPGA  NO Rad Tol
  People think to to use neutron shielding (pure polyethylene ..)

## Slide 30: SuperB Integration Questionnaire - #1
Author: G.Felici, G. Finocchiaro, M. Roney - 31-10-2011 - v1.0
Number of channels
8056 (to be finalized according to minimum allowed inner DCH radius)
ON DETECTOR - Power dissipation per channel - Preamplifier Boards
Standard dE/dx by means of charge measurement: 30 mW/ch - BW ≈ 80/100 MHz
Cluster Counting: 100 mW/ch - BW ≈ 250MHz
OFF DETECTOR - Power dissipation per channel - Data Conversion Boards (contribution to Feature Extraction to be checked)
Standard dE/dx: 0.9 W/ch (48 chs/board – 43W/board) ≈ 7.3kW total could be 0.7 W/ch (64 chs/board - 45 W/board) due to improvement in component power requirements ≈ 5.7 kW total
Cluster Counting: 5 W/ch (8 chs boards – 40W/board) ≈ 41kW could be 2.5W/ch (16 chs/board – 40W/board) due to improvement in component power requirements ≈ 20kW total
OFF DETECTOR - Power dissipation per channel - Concentrators
Assuming the same number of concentrators for both options (Feature Extraction on Data Conversion boards): 70 mW/ch (Concentrators boards must be located in non hostile environment): 650W

## Slide 31: SuperB Integration Questionnaire - #2
OFF DETECTOR - Trigger - Primitives Generation
Option1: Off-Detector electronics generates only primitives à power requirement already considered in Data Conversion board
Option2: Off-Detector electronics includes electronics for partial super-layer track reconstruction  Off-Detector power and housing requirement would (slightly) change. The option is under study.
ON DETECTOR - Volume occupied by the electronics (drawings of electronic modules – non available yet)
HV distribution boards on forward endplate - Preamplifier boards on backward endplate. Position (both boards): 2-3 cm from endplate. Height (board + support) 8-10 cm  Nitrogen gas enclosure volumes are being determined ????
OFF DETECTOR - Volume occupied by the electronics (drawings of electronic modules – non available yet)
HV: 2 Crates 19"- wide, 8U-high Euro-mechanics rack (Ref: CAEN SY1527LC)
Standard dE/dx - 48 chs/board - 16 boards/crate: 173 boards (according to superlayer geometry) à 11 VME crates 19" x 8U (6+2) enclosure (Ref : CAEN VME8100 ) 64 chs/board - 16/boards/crate - 132 boards  could be 9 VME crates 19" x 8U (6+2) enclosure (Ref : CAEN VME8100)
Cluster Counting - 8 chs/board - 16 board/crate: 63 VME crates 19" x 8U (6+2) enclosure (Ref : CAEN VME8100 ) 16 chs/board - 16 bards/crate  could be 32 crates VME crates 19" x 8U (6+2) enclosure (Ref : CAEN VME8100)

## Slide 32: SuperB Integration Questionnaire - #4
OFF DETECTOR - Number and size of Read-out cables or fibers
Data Conversion à Trigger (option 1): 64 fibers (150 kHz trigger rate - 10% occupancy - 20% safety - 1.2 Gbits/s link) Data Conversion à Trigger (option 2): partial super-layer track reconstruction in Data Conversion Board : 48 chs/board  173 links - 64 chs/board  132 links
Number and size of slow control cables
16 fibers
Minimum bending radius
Fibers: depends on assembly. Single fiber: 2 in; bundle: 15 times external bundle diameter. Waiting for ETD decision
ON-DETECTOR LVPS cables: depends on the assembling. Assuming a round shielded (aluminum foil) bundle of 12 cables à 12 x cable diameter (12 conductors – 1.5 mm^2 size à outer diameter ≈ .520 in ≈ 13.2 mm
ON-DETECTOR HV cables: depends on the assembling. Assuming a shielded (aluminum foil) bundle of 12 cables à 12 x cable diameter (12 conductors overall cable diameter ≈ 9 mm)
ON-DETECTOR Signal cables [Very Preliminary] Standard dE/dx: assuming a flat assembly of 12 cables à 24 x cable diameter (micro-coax cable diameter ≈ 0.5 mm - aluminum foil shielding)
ON-DETECTOR Signal cables [Very Preliminary] Cluster counting: assuming a flat assembly of 12 cables à 12 x cable diameter (RG178 cable diameter ≈ 1.8 mm)

## Slide 33: SuperB Integration Questionnaire - #3
Max tolerable distances between the detectors to the electronic modules:
ON-DETECTOR – OFF-DETECTOR ≈ 5 m
Access frequency on the external electronic per year
12 access/year (after debug)
Frequency access on the detector per year
1-2 access/year (after debug) (including HV)
Modularity of the electronic unit (housing racks)
200 cm (45 rack units)
ON DETECTOR - Number and size of power cable
Preamp LV power cables: 12 chs/board modularity  768 cables – 1.5 mm^2 size
HV cables: less than 100
OFF DETECTOR - Number and size of Read-out cables or fibers
Data Conversion à Concentrators: 168 fibers
Concentrators à DAQ: 16 fibers

## Slide 34: SuperB Integration Questionnaire - #5
Shielding requirements (thermal and electrical)
Thermal: NO Electromagnetic: if cluster counting will be implemented some shielding could be useful. For standard approach (dE/dx by means of charge measurement) the magnetic field return iron should be enough May be SVT shielding required ??
Information drawings on the cable distribution on the detector geometry: non available yet
Only preamplifiers should be installed on backward-end plate. Connection to off-detector electronics will be implemented by coax cables (Cluster Counting) or coax/twisted cables (standard dE/dx). Cables should leave the detector along the outer diameter
Requirement of cooling system - Backward Endplate - flow, temperature and type of fluid
Standard dE/dx: 300W  air flow cooling should be enough to provide good air exchange ≈ 1000 m^3/h - coarse calculation: (3.16 x Watt) /(Dt*0.589) à Dt = 4 (!), degrees, PD = 300W  500 m^3/h) Cluster counting: 1 kW  liquid cooling required
Requirement of cooling system - Allowed detector temperature variations: backward end-plate
4 degrees (????)
Size of the chiller
ON DETECTOR + OFF DETECTOR electronics ??

## Slide 35: SuperB Integration Questionnaire - #6
Cooling pipes distribution at sub detector ends (drawings)
Not available yet
Describe other requirements that have an impact of the space available like auxiliary equipment, minimum space for accessibility, etc
1.5 mt in front of racks 0.5/1 mt behind racks Full access to end-plates (backward and forward) during detector access OPTIONAL : electronics for local debug (table, PC etc.)
Describe other requirements that have an impact of the space available like space for the commissioning operations and assembly
Full access to end-plates (backward and forward) during detector access

## Slide 36: Conclusions
Design goals have been defined
Two different implementation of dE/dx measurements have been evaluated and will be reported in TDR. Measurements on Cluster Counting are going on and final decision about the technique that will be used to measure dE/dx will be taken within the first half of 2012
The technique used for dE/dx measurement has a NOT minor impact on number of boards, power requirement, interconnections cables, HV distribution boards and grounding (shielding).
HV distribution modularity will follow the chamber layer (less cells for the internal layers, more cells for the external ones)
Only Rad Tol components will be used in front-end boards (NO CC). If selected components has no qualification they will be qualified.
Grounding/shielding policy has not been defined yet
Probable (!!!) number of (optical) links : 16 for DATA, 16 for ECS and 64 (173) for TRIGGER
    Board design will start after the decision on dE/dx technique to be used