## Slide 1: Deep Underground Neutrino Experiment
Francesco Di Capua
Gr1-NA meeting
03/10/2024

## Slide 2
Long-baseline Neutrino Oscillation: what we know
The 3 know flavor states e, , are linear combination of 3 mass eigenstates 1, 2, 3 through the Pontecorvo-Maki-Nakagawa-Sakata (PMNS) unitary matrix UPMNS
Previous oscillation experiments determined the two mass-squared differences and the three mixing angles

## Slide 3: The era of precision for neutrino physics
Remarkable progresses in last 20 years in determining neutrino properties

## Slide 4
Long-baseline Neutrino Oscillation: what is still missing?
Goal for next generation experiments:
Measure CP and determine if CP is violated
Determine the neutrino mass ordering (sign of 231)
Determine the octant of
Understand if the three-flavor picture of the oscillation is complete
Finally the absolute neutrino mass or if neutrino is its own anti-particle are still unknown (not accessible with osc. exp.)

## Slide 5: Neutrino Oscillation in the 3-flavor model
Measure neutrino and antineutrino oscillation as a function of L/E
Very long baseline large matter effect
CPV and mass ordering are totally non-degenerate
Broadband neutrino energy high statistics over full oscillation period. Spectral information resolves degeneracies between , and CP

## Slide 6: The Deep Underground Neutrino Experiment (DUNE)
The most powerful neutrino beam in the world (1.2 MW upgradable to 2.4 MW) will be sent from Fermilab (Chicago) to SURF (South Dakota) along 1300 km distance to be detected by four liquid argon far detector modules (70 kton LAr) at 1.6 km deep underground and a near detector complex at 560 m from the neutrino source
  Wide-band neutrino energy spectrum enables detailed fitting of the oscillation parameters
  Long-baseline allows to unambiguous measurement of the neutrino mass ordering
  LAr TPC technology allows for precise reconstruction of the neutrino interactions
  Near Detector complex allows for a careful control of systematics
  Underground location of the Far Detector modules enables a wide astroparticle measurement program

## Slide 7: DUNE: a broader physics program
Long-baseline wide-band neutrino beam
  Measurement of CP violation phase and determination of neutrino mass ordering in a single experiment with spectral information
Underground location (1600 m) Access to astrophysical neutrinos
  Supernova neutrino burst detection sensitive to e component
  Atmospheric neutrino capability of identification
  Solar neutrinos potential detection of hep flux
Massive detector with excellent tracking and calorimetric information
  Search for nucleon decay like the baryon number violating channel p k+
Intense beam and capable Near Detector Complex
  Precise neutrino physics
  BSM search

## Slide 8: The Long Baseline Neutrino Facility
High intensity primary proton beam (60-120 GeV) on a graphite target (1.1-1.9)x1021 pot/yr
Neutrino beamline at a slope of 5.8°
Expected neutrino fluxes
Forward Horn Current (FHC) neutrino-enhanced
Reverse Horn Current (RHC) antineutrino-enhanced
Wide band beam
8

## Slide 9: The Long Baseline Neutrino Facility
DUNE neutrino beam is far higher intensity than present-day experiments
Very high flux covering the full neutrino oscillation curve between the oscillation minimum (1.27 GeV) and the oscillation maximum (2.54 GeV) with coverage of second maximum (0.8 GeV)
Recent development: Beam upgrade (ACE-MIRT) could increase beam intensity > 2 MW by decreasing the time between spills from 1.2 s to 0.6 s, can be achieved before DUNE operations begin
9

## Slide 10: A lot of neutrinos interactions
disappearence:
appearance: octant of , CP , mass ordering
In the first year DUNE will collect 150 oscillated events (assuming a beam rump up to 1.2 MW, 2 Far Detectors, Normal Order and CP =0)
10

## Slide 11: LAr TPC: working principle
Detection principle first conceived by C. Rubbia (1977)
Charged particle from neutrino interaction in LAr produces free ionization electrons and scintillation light (128 nm)
Light is quickly detected by photon detection system
Electrons slowly drift to anode instrumented with readout wires/strip
Each wire/strip plane provide a 2D (s, t) view of the ionization event. Multiple 2D views results in a 3D image of the event
11

## Slide 12: LAr TPC: particle imaging at kTon scale, flavor identification & energy reconstruction
Good capability of pion reconstruction (in final state for 60% of DUNE interactions)
Excellent electron/muon separation
ProtoDUNE data
Simulated neutrino events
3 GeV interaction
2.5 GeV interaction
12

## Slide 13: Far detector: two different readout technologies
FD1 module will use Horizontal Drift technology: four 3.5 m drift regions (3.5 m x 12 m x 58 m), charge readout with 348,000 wires in 150 Anode Planes Assembly (APA). Similar to ICARUS, MicrobooNE, SBND. Photon detection: X-Arapuca module (SiPM based light trap), about 300,000 SiPM
FD2 module will use Vertical Drift technology (two volumes 13.5 m x 6.5 m drift x 60 m), charge readout with strips (perforated PCB). Photon detection on the field cage walls and on the cathode @300 kV; decoupling from HV achieved with optical fibers for power and signal transmission. Larger active volume, cheaper than FD1 and similar performances
Charge Readout Planes (CRP)
FD1
APA
FD2
13

## Slide 14: Near Detector Complex
Main purpose
  measure the rate and spectrum of v’s before oscillations
  constraint systematic uncertainties (flux, cross-sections, detector response) for oscillation measurement
ND is a (movable) LArTPC (ND-LAr) + muon spectrometer (TMS) and a fixed magnetized tracker+calorimeter (SAND)
Off-axis data constrains energy dependence of neutrino cross sections
Same target and same technology to predict reconstructed Ev in Far Detector
On-axis magnetized detector (SAND) for beam monitoring and neutrino energy measurement: repurposes solenoid magnet and ECAL from KLOE,
SAND allows fine-grained, particle-by-particle reconstruction with very low rescattering, excellent for highly exclusive neutrino-nucleus measurements
14

## Slide 15: DUNE Construction: Phase I
Detector installation starting in 2026
Full near + far site facility and infrastructure
Two 17 kt LArTPC modules
1.2 MW upgradeable neutrino beamline
Movable LArTPC ND+muon spectrometer, SAND
On-axis near detector
15

## Slide 16: Building DUNE: construction schedule
Far site excavation is complete
Next: Building and Site infrastructure work until mid-2025
Cryostat warm structure has been shipped from CERN to US, to be installed in 2025-26
Detector installation in 2026-27
Purge and fill with liquid argon in 2028
Physics in early 2029
Beam physics with Near Detector 2031
16

## Slide 17: DUNE Construction: Phase II
Two additional Far Detector modules (on overall fiducial 40 kt)
Beamline upgrade to >2 MW (ACE-MIRT)
More capable Near Detector (ND-GAr)
Vertical Drift module is the baseline design for Phase II FD modules
Several proposal to improve light collection (FD3): Aluminum Profiles with Embedded S-Arapuca (APEX) and PoWER (POlymer Wavelenght shifter ed Enhanched Reflection)
The phased construction program allows the development of the technology to expand the DUNE physics scope (, dark matter…)
FD4 is the «Module of Opportunity», more ambitious design are being considered, including pixel readout, integrated charge-light readout, low-background modules and non-LAr technologies
17

## Slide 18: ProtoDUNEs at CERN
First Phase of ProtoDUNEs
  Construction and operation of ProtoDUNEs at CERN (2018-2020)
  Succesfull demonstration of the DUNE LArTPC
  Several ongoing analysis (hadron-Ar cross section)
Second Phase of ProtoDUNEs (2020-2023 construction + operations 2024-2025)
  ProtoDUNE Horizontal Drift
  Final technical solution for all FD-HD subdetectors
  Detector filled and currently taking data with charged-particle beams and cosmic muons
  ProtoDUNE-Vertical Drift
  Realization of a Module-0 detector in 2022-2023
  LAr will be transferred to ProtoDUNE-VD in October with operations starting in early 2025
18

## Slide 19: Neutrino energy spectra at Far Detector
Sensitivity to
  If is DUNE will measure an enhancement in electron neutrino appearance, and a reduction in electron antineutrino appearance
Sensitivity to mass ordering (MO)
  If MO is normal, DUNE will measure a much larger enhancement in electron neutrino appearance, and a reduction in electron antineutrino appearance, with respect to inverted order
MO, and all affect spectra with different shape, additional handle on resolving degeneracies
19

## Slide 20: Mass order and CPV DUNE Sensitivity
For best-case oscillation scenario DUNE will reach
  >5Mass Ordering sensitivity in 1 year
  >3 CPV sensitivity in 3.5 years
For worst-case oscillation scenario
  >5 Mass Ordering sensitivity in 3 year (no matter the value of or any other parameter)
In long term DUNE can establish CP violation at > 3 for 75% possible values of
20

## Slide 21: Astrophysical neutrinos in DUNE
Neutrinos from atmospheric, solar and core collapse supernovae
  Argon target gives unique sensitivity to MeV-scale electron neutrinos
    Charged Current (CC) interaction on Ar
      >1.5 MeV)
      >7.5 MeV)
    ES on electrons
    Neutral Current (NC) interaction on Ar
21

## Slide 22: Supernova burst neutrinos
DUNE will observe thousand of neutrino interactions from a galactic supernova burst
Time and energy spectra are sensitive to core collapse mechanism and stellar evolution
  Neutronization through electron capture (depending from oscillation and MO)
  Matter falling into core during accretion
  Emission cools as neutrinos diffuse
Pointing capabilities: ES channel, about 5° resolution
22

## Slide 23: DUNE activities in Naples
Main involvment in the Photon Detection System
Characterization of the PDS module (Megacell)
European site for vaporation of the wavelength shifter
Active participation to ProtoDUNE (analysis and simulation)
Proposal for a new design for Far Detector 3
  Simulation and perfomance study
  In situ R&D small prototypes
PDE of SiPMs at cryogenic temperatures

## Slide 24: Photon Detection System (FD)
VUV scintillation light produced in LAr
PTP shifter deposited on the dichroic external side converts VUV light to a wavelenght < dichroic cutoff (light transmitted)
The internal WLS bar converts the primary shifted photons to a wavelenght > dichroic cutoff (light is trapped)
After reflections the photons can be detected by SiPM positioned laterally with respect to the WLS plane

## Slide 25: Photon Detection System in VD detector
PD modules mounted on the cathode (at 300 kV) and on the cryostat walls (membrane) behind the transparent (70%) field cage
Square geometry: dimension 65 cm x 65 cm
A single large WLS light guide plane
160 lateral SiPMs
SiPMs mounted on flexible strips
320 double side (cathode) + 352 single sided (membrane)
12

## Slide 26: PDS-VD module tested in Naples
241Am source (250 Bq)
A PDS module of the DUNE Far Detector 2 with SiPM readout assembled in Napoli and performances in LAr first time tested in the Collaboration

## Slide 27: Electronics
Cold amplifier
Warm second stage amplifier
Signal processing and analysis

## Slide 28: DUNE WLS Evaporation Site in Naples
Evaporation of the cathod (320 double sided) and membrane (320+32 single sided) XA-VD modules
Evaporator design inherited from the Campinas evaporation chamber with
Relevant improvements:
  larger chamber with 120 cm diameter providing +100% evaporation throughput wrt Campinas evaporator
  multiple crucibles to assure more uniformity in the coatings and speed up the process
Pumping system sized to ensure 2 full coating processes/day

## Slide 29: Chamber Design and Production
Chamber already designed and now in production phase
Several accommodations at the bottom base for crucibles (optimization of the position will be done in commissioning phase)
Pumping port 250 mm diameter (DN 250 ISO-F)
Several lateral and top ISO-K 100 flanges
Pumping station with a 40 m3/h and 2300 l/s turbopump Several lateral and top ISO-K 100 flanges
Motorized system on the top of dome with motion feedthrough to rotate a support structure disk to hold the filters

## Slide 30: Chamber Design and Production
Chamber already designed and now in production phase
Several accommodations at the bottom base for crucibles (optimization of the position will be done in commissioning phase)
Pumping port 250 mm diameter (DN 250 ISO-F)
Several lateral and top ISO-K 100 flanges
Pumping station with a 40 m3/h and 2300 l/s turbopump Several lateral and top ISO-K 100 flanges
Motorized system on the top of dome with motion feedthrough to rotate a support structure disk to hold the filters

## Slide 31: Crucibles
water cooling system
pneumatic opening
Crucibles produced and tested in vacuum
PID controlled temperature, with a very good set point stability
Crucible directly mounted in flange DN 100 ISO-K
Electro-pneumatic opening and cooling system
Maximum operating temperature 500°C, working temperature at 250-300°C
250°C

## Slide 32: FD2 evaporation site: programming of the operations
Substrate dimension of 14,4×14,4 cm2
Disk holder for filters with 112 cm diameter
Up to 24 filters for evaporation process can be accommodated
Evaporator lab will be completed by Q4 2024
Commissioning of the system and ready to start by Q1 2025
About 17000 substrates to be coated
2 shift for day: 8-10 hours
48 filters/day
Required 346 days (about 70 weeks)
2 years of operation involving INFN technicians

## Slide 33: DUNE WLS evaporation operations
The evaporator will be housed in an ISO-6 clean room within a new cryogenic infrastructure under construction at the Department of Physics in Naples, funded by the PNRR (IRIS Project)
33

## Slide 34: Absolute PDE measurement
Absolute measurement of the photodetection efficiency (PDE) of different SiPMs
In different conditions (warm/cold)
For different wavelengths down to VUV region

## Slide 35: The setup

## Slide 36: Summary
DUNE is a next generation long-baseline oscillation experiments and astrophysics neutrino observatory
Very reach program in the next decade (about 20 years lifetime)
  Neutrino and anti-neutrino Oscillations with CPV investigation
  Studies of MeV-scale neutrinos
  BSM searches
LNBF and DUNE making rapid progress on facility construction, with excavation complete and components under construction
DUNE Naples group very active in this process
DUNE science begins in this decade

## Slide 37: Backup slides

## Slide 38
FD2 evaporation site: programming of the operations
 | Number of modules | Number of filters per module | Total number of filters
Membrane modules | 352 | 16 | 5632
Cathode modules (double side) | 320 | 32 | 10240
Spares | ?? | ?? 10% ?? | 750
Total |  |  | 16622
Duration of whole evaporation process estimated at approximately 4-5 hours
Main steps of the process:
Measure of mass for each 2 or 3 filters before and after the evaporation
Filters positioning on the holder disk
Preparation of the control samples
Insertion in the chamber
Vacuum phase
Evaporation with PTP
Opening of the chamber and removal of the disk
Removal the filter and place them in the proper boxes
Check of the control samples
2 shift for day: 8-10 hours
48 filters/day
Required 346 days (about 70 weeks)
2 years of operation involving INFN technicians.

## Slide 39: DUNE precision measurements
Ultimate precision 6°-16° in
World-leading precision (for long baseline experiments) in
39

## Slide 40: DUNE sensitivity to solar neutrinos
Neutrinos from the Sun
  DUNE has excellent sensitivity to 8B solar neutrinos above ~10 MeV, and discovery sensitivity to the hep solar flux
  DUNE can improve upon existing solar oscillation measurement via day-night asimmetry induced by matter effect (bottom plot shows hypothetical DUNE result at old best fit point)
40

## Slide 41: Beyond three-flavor Oscillation

## Slide 42: BSM searches with the Far detector
DUNE due to large mass and long exposure time is sensitive to rare processes (proton decay, n-nbar oscillation) and new physics of cosmogenic origin
Boosted Dark Matter produce low energy soft e/p and spatially proximate e+e- pair