## Slide 1: High Performance Computing - HPC
Daniele Cesini – INFN-CNAF
Enrico Mazzoni – INFN-Pisa

## Slide 2: Glossary: GFLOPS and TDP
GFLOPS: Billions of Floating Point Operations per second
  Max GFLOPS of a system can be calculated using:
TDP: Thermal Design Power is the maximum amount of heat generated by the CPU that the cooling system in a computer is required to dissipate in typical operation (*)
(*) From wikipedia
FROM ARK.INTEL
(Clock in GHz)
G

## Slide 3: Once upon a time....
Serial number 001 Cray-1™
  Los Alamos National Laboratory in 1976
  $8.8 million
  80 MFLOPS scalar, 160/250 MFLOPS vector
  1 Mword (64 bit) main memory
  8 vector registers
    64 elements 64bit each
  Freon refrigerated
  5.5 tons including the Freon refrigeration
  115 kW of power
    330 kW with refrigeration
Serial number 003 was installed at the National Center for Atmospheric Research (NCAR) in 1977 and decommissioned in 1989
(*) Source: Wikipedia
The vector machines

## Slide 4: Wireless technology inside

## Slide 5: CRAY-XMP...Vector MultiProcessor
1982 CRAY-XMP 2 processors
  9.5 ns clock cycle (105 MHz)
  2x200MFLOPS
  2Mwords (64 bit) = 16MB
1984 CRAY-XMP four processors
  800 MFLOPS
  8Mwords
    64 MB main memory
  about US$15 million
    plus the cost of disks!!!
CRAY-XMP48 @ CERN in 1984
(*) source: http://cerncourier.com/cws/article/cern/29150

## Slide 6: The Cray-2
The Cray-2 released in 1985
  4 processors
  250MHz (4.1 ns)
  256 Mword (64bit) Main Memory
    2 GByte
  1.9 GFLOPS
  150 - 200 kW
  Fluorinet cooling
  16 sq ft floor space
  5500 pounds
  About $17 million
(*) http://archive.computerhistory.org/resources/text/Cray/Cray.Cray2.1985.102646185.pdf

## Slide 7: Microprocessors
The Intel 4004
1971
The Intel 8080
1974
The Intel 8086
1978
The Intel 80286
1982
The Intel 80486
1989
In the 80s started the replacement of vector supercomputers with Massively Parallel Processors (MPP) and Clusters assembled from a larger number of lower performing microprocessors

## Slide 8: The attack of the Killer Micros
Caltech Cosmic Cube
  By Charles Seitz and Geoffrey Fox in1981
  64 Intel 8086/8087 processors
  128 kB per processor
  6 dimensions hypercube
Taken from the title of Eugene Brooks' talk "Attack of the Killer Micros"
at Supercomputing 1990
(*)http://calteches.library.caltech.edu/3419/1/Cubism.pdf

## Slide 9: Massively Parallel Processor (MPP)
A single computer with many networked processors
  Specialized interconnect networks
  Low latency interconnection
Up to thousands of processors
Some examples
  Connection Machines (CM-1/2/200/5)
  Intel Paragon
  ASCI series
  IBM SP
  IBM BlueGene

## Slide 10: Thinking Machines
1985: Thinking Machines introduces the connection Machine CM-1
Connection Machine CM-200
  maximum configuration of 65536 1-bit CPUs(!)
  floating-point unit for every 32 1-bit CPUs
  A cube composed of 8 cubes
    each cube contains up to 8096 processors
  (The curved structure is a Data Vault - a disk array)
  40 GFLOPS peak
1991: CM-5
  Featured in “Jurassic Park”
(*) Sources:
http://www.corestore.org/cm200.htm
http://www.new-npac.org/projects/cdroms/cewes-1999-06-vol1/nhse/hpccsurvey/orgs/tmc/tmc.html
http://en.wikipedia.org/wiki/Thinking_Machines_Corporation

## Slide 11: Intel Paragon MPP
Launched in 1993
Up to 2048 (later 4000) Intel i860 RISC microprocessors
  Connected in a 2D grid
  Processors @ 50 MHz
World most powerful supercomputer in 1994
  Paragon XP/S140
  3680 processors
  184 GFLOPS peak
(*) Source: Wikipedia

## Slide 12: ASCI Red MPP
  1996 At Sandia Laboratories
  Based on the Paragon architecture
  Fastest supercomputer from 1997 to 2000
    1.4 TFLOPS (peak) in 1997
      9152 cores
    3,2 TFLOPS (peak ) in 1999
      9632 cores
  1st supercomputer above
1 TFLOPS
(*) Source: Wikipedia
TERA SCALE

## Slide 13: IBM BlueGene/Q MPP
  Trading the speed of processors for lower power consumption
  System-on-a-chip design. All node components were embedded on one chip
  A large number of nodes
  5D xTorus interconnect
  Compute chip is an 18 core chip
    The 64-bit PowerPC A2
    4-way simultaneously multithreaded per core
    1.6 GHz
    a 17th core for operating system functions
    chip manufactured on IBM's copper SOI process at 45 nm.
    204.8 GFLOPS and 55 watts per processor
  Up to 20 PFLOPS (peak)
    16384 cores
(*) Source: Wikipedia
PETA SCALE

## Slide 14: Clusters
[a cluster is a] parallel computer system comprising an integrated collection of independent nodes, each of which is a system in its own right, capable of independent operation and derived from products developed and marketed for other stand-alone purposes
Dongarra et al. : “High-performance computing: clusters, constellations, MPPs, and future directions”, Computing in Science & Engineering (Volume:7 , Issue: 2 )
(*) Picture from: http://en.wikipedia.org/wiki/Computer_cluster

## Slide 15: Top500.org
Nov 2022 List

## Slide 16: Frontier
Frontier, or OLCF-5, is the world's first and fastest exascale supercomputer, hosted at the Oak Ridge Leadership Computing Facility (OLCF) in Tennessee, United States
It is based on the Cray EX and is the successor to Summit (OLCF-4).
As of March 2023, Frontier is the world's fastest supercomputer.
Frontier achieved an Rmax of 1.102 exaFLOPS
Frontier uses 9,472 AMD Epyc 7453s "Trento" 64 core 2 GHz CPUs (606,208 cores) and 37,888 Radeon Instinct MI250X GPUs (8,335,360 cores).
© Wikipedia

## Slide 17
Summit OLCF-4 supercomputer
United States Department of Energy awarded a $325 million contract in November, 2014 to IBM, Nvidia and Mellanox for the construction of Summit and Sierra
Summit is tasked with civilian scientific research and is located at the Oak Ridge National Laboratory in Tennessee.
Sierra is designed for nuclear weapons simulations and is located at the Lawrence Livermore National Laboratory in California.
Summit is estimated to cover the space of two basketball courts and require 136 miles of cabling
600 GB of coherent memory addressable by all CPUs and GPUs
800 GB of non-volatile RAM that can be used as a burst buffer or as extended memory.
Non-blocking fat-tree topology using a dual-rail Mellanox EDR InfiniBand interconnect for both storage and inter-process communications traffic
© Wikipedia

## Slide 18: Fugaku Supercomputer
The supercomputer is built with the Fujitsu A64FX microprocessor.
  Based on the ARM version 8.2A processor architecture
  Fugaku was aimed to be about 100 times more powerful than the K computer
    i.e. a performance target of 1 exaFLOPS
The initial (June 2020) configuration of Fugaku used 158,976 A64FX CPUs joined together using Fujitsu's proprietary torus fusion interconnect.
An upgrade in November 2020 increased the number of processors
  To reach 442 petaFLOPS
1 Billion $ total cost

## Slide 19
Sunway TaihuLight

## Slide 20: Sunway TaihuLight
Architecture
The Sunway TaihuLight uses a total of 40,960 Chinese-designed SW26010 manycore 64-bit RISC processors based on the Sunway architecture.
Each processor chip contains 256 processing cores, and an additional four auxiliary cores for system management (also RISC cores, just more fully featured) for a total of 10,649,600 CPU cores across the entire system.
The processing cores feature 64 KB of scratchpad memory for data (and 16 KB for instructions) and communicate via a network on a chip, instead of having a traditional cache hierarchy.
http://www.netlib.org/utk/people/JackDongarra/PAPERS/sunway-report-2016.pdf

## Slide 21: Applications

## Slide 22: HPC - Applications
Molecular Dynamics
NAMD, Quantum Espresso, Gromacs, Gaussian, etc..

## Slide 23
Earth simulation
WRF, MM5, GLOBO, NEMO, etc..
HPC - Applications

## Slide 24: HPC- Applications

## Slide 25: HPC - Applications
Fluid Dynamics

## Slide 26: HPC - Applications
Brain Simulation

## Slide 27
General relativity
The scientific case: high resolution simulation of inspiral and merger phase of binary neutron stars system
  one of source of the gravitational waves that are the observational target of the LIGO/VIRGO experiment
Computation performed using The Einstein ToolKit
Result obtained on Galileo at CINECA
© Roberto De Pietri , Roberto Alfieri - INFN Parma and Parma University, 2012
HPC - Applications

## Slide 28: HPC – key components

## Slide 29: Componenti chiave
Interconnessione dei nodi
Condivisione dei dati
Gestione dei job e contesa delle risorse

## Slide 30: Interconnessione dei nodi
In tutti i campi di applicazione dell’HPC il calcolo in un punto del dominio dipende dai risultati nei punti prossimi vicini
Questo comporta la necessità di scambio continuo di dati fra i nodi coinvolti nel calcolo
Quindi la rete deve garantire grande banda passante e bassa latenza, oggi giorno si hanno due possibilità InfiniBand o OmniPath

## Slide 31: InfiniBand
(*) Source: FS
Nasce nel 1999 dalla fusione di due progetti Future I/O e NextGeneration I/O
Nello stesso anno nasce Mellanox
Oggi arriviamo fino a 800Gb/s (XDR)
La vera forza è l’offload: RDMA, GPUDirect RDMA, SHARP

## Slide 32: InfiniBand: topologie
Fat-Tree: connessione gerarchica multilivello, salendo dalle radici (nodi) al tronco si aumenta il numero di link
Dragonfly: i nodi sono raggruppati in sottogruppi di piccole dimensioni completamente connessi, i sottogruppi sono collegati fra di loro
Hypercube
Torus
Mesh
| Topology | Scalability | Latency | Bandwidth | Fault Tolerance | Complexity |
|--------------|-------------|-----------|-----------|-----------------|------------|
| Fat-Tree | High | Moderate | High | High | High |
| Dragonfly | Very High | Low | Very High | Moderate | High |
| Hypercube | Moderate | Low | Moderate | High | Moderate |
| Torus | High | Low | High | Moderate | High |
| Mesh | Moderate | Moderate | Moderate | Low | Low |

## Slide 33: OmniPath?
Fratello economico di InfiniBand
Prestazioni simili, latenza leggermente più alta
Scalabilità (n. di nodi) simile
Manca la parte di off-load

## Slide 34: Condivisione dei dati
Un filesystem che sia accessibile da tutti i nodi del cluster, ma:
Sia in grado di reggere all’accesso parallelo delle applicazioni, magari molti processi che accedo a pochi file
Evitare il lock a file, necessario lock a blocchi
Esere in grado di scalare le prestazioni
File System Parallelo

## Slide 35: Parallel File Systems
Dati distribuiti fra più server conenssi in rete
I/O coordinato fra nodi client e server in modo da ottimizzare le prestazioni
Stripe a livello di file, i singoli blocchi sono scritti su diversi storage gestiti da diversi server
Non è necessario sapere dove si trovano i file, name space globale
Avere la possibilità di separare metadati e dati
Si aumentano le prestazioni aggiungendo sistemi di storage e/o server spesso in modo trasparente all’utenza
Due possibilità
  IBM SpectrumScale (GPFS)
  Lustre

## Slide 36: Gestione dei job
Tipicamente si hanno molti utenti che condividono la risorsa HPC, quindi:
  Necessario ottimizzare l’accesso per non sprecare tempo CPU e potenza elettrica
  Utenti diversi possono avere diritti diversi sul tempo macchina
  Utenti diversi possono avere priorità di accesso diverse
  Il sistema di batch permette una regolazione da “gentiluomini” di queste varie esigenze
  Ma deve sapere che è un cluster HPC

## Slide 37: Batch System per HPC
Deve “concepire” il fatto che un job giri su più nodi
Quindi saper tener traccia dei nodi assegnati ad un job
Fornire all’utente le informazioni relative ai nodi assegnati al job
Possibilmente: meccanismi furbi di gestione delle risorse come reservation e backfill

## Slide 38: Reservation / Backfill
© IBM LSF https://www.ibm.com/support/knowledgecenter/en/SSETD4_9.1.3/lsf_admin/backfill.html

## Slide 39: Batch System per HPC
Esistono vari Batch System, quelli che vanno per la maggiore nel settore HPC sono
LSF, di IBM a pagamento
SLURM, progetto opensource nato dalla collaborazione fra varie entità, nasce esplicitamente per il supporto HPC molti dei più grandi presenti nella Top500 lo usano