## Slide 1
SHADOW4: Advanced Ray-Tracing for the Design and Simulation of X-Ray Optical Systems
Manuel Sánchez del Río
srio@esrf.eu
1Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
(Thanks to Juan Reyes-Herrera, Xianbo Shi and Luca Rebuffi)
Contents
Ray tracing
SHADOW history
OASYS ecosystem
Shadow4
  API
  Components (examples)
Doc/education

## Slide 2: Ray Tracing and Geometrical Optics
Ray tracing in X-ray optics is a simulation method used to model how X-rays propagate and interact with optical components, like mirrors, lenses, and monochromators.
It relies on approximate solutions to Maxwell's equations that are valid as long as the light waves propagate through and around objects whose dimensions are much greater than the light's wavelength.
It's essential for designing and optimizing beamlines at synchrotrons as well as any X-ray optical system.
p
x
y
z
z
x
Energy, Intensity
y
z
x
q

## Slide 3: Ray Tracing and Geometrical Optics
Applications:
Determine beam characteristics: shape, size, divergence, and focal spot.
Determine spectral resolution.
Optimize optical alignment and component positioning.
Diagnose aberrations or misalignments.
DLSR: CohFract=100%
EBS-ESRF: coherence fraction at 10-100 keV: 1-10%
Software (synchrotron world):
SHADOW: https://github.com/oasys-kit/shadow4
XRT: https://github.com/kklmn/xrt
McXtrace: https://www.mcxtrace.org
RAY and RAY-UI Franz Schaefers et al. https://www.helmholtz-berlin.de/forschung/oe/np/optik-strahlrohre/arbeitsgebiete/ray_en.html
Limitations:
Pure ray tracing doesn’t account for coherence, diffraction, or interference

## Slide 4: 40 YEARS OF Shadow
Franco Cerrina (♰2010)
SHADOW
M. Sanchez del Rio, et al.J. Synchr. Rad.18, (2011) http://dx.doi.org/10.1107/S0909049511026306
Python API
XOP/ShadowVUI
Kernel (Fortran9x)
Generic ray tracing package for optics
Specialized in SR (storage ring sources, grazing optics, crystals…)
Helped to most 2-4th generations of SR facilities
Used/cited in a huge number of papers
SHADOW 1 & 2
SHADOW3
SHADOW1 1984-1990 VAX-VMS mainframes
SHADOW2 1990-2010 Unix workstations+Windows
Teaching about the birth of synchrotron light:
the role of Frascati and a missed opportunity
G. Margaritondo
https://doi.org/10.1107/S160057752400300X

## Slide 5: OASYS – ShadowOui (2014)
ShadowOUI = Shadow3 in OASYS
Luca Rebuffi
Manuel Sanchez Del Rio
SRW
XOPPY
Orange
https://orangedatamining.com/
SYNED
Utilities
WOFRY
ShadowOUI

## Slide 6: 2014: ShadowOUI1= SHADOW3 + ORANGE2
SIZE RESOLUTION FLUX
0.6 eV
---> Integrated Flux : 1.25321e+13 ph/s
[1] L Rebuffi and M Sanchez del Rio J Synchr. Rad. 23 1357-1367 (2016) https://doi.org/10.1107/S1600577516013837
[2] https://orangedatamining.com/

## Slide 7: ShadowOUI: not only SHADOW3
Corrections for coherent optics (HYBRID1)
Surface error databases DABAM2, DABAM2D
Preprocessors (surfaces, reflectivity, VLS, diaboloids3)
Elements: CRL, TF, Benders, etc.
Loops & Heat load loops4
New crystal structures (high d-spacing5)
[1] Shi et al. 2014 https://doi.org/10.1107/S160057751400650X
[2] Sanchez del Rio et al. 2016 https://doi.org/10.1107/S1600577516005014
[3] Sanchez del Rio et al. 2021 https://doi.org/10.1107/S160057752100401X
[4] Rebuffi et al. 2020 https://doi.org/10.1107/S160057752000778X
[5] Yu et al. 2022 https://doi.org/10.1107/S160057752200707X

## Slide 8: OASYS add-ons
SRW
XOPPY
SYNED
Facility Add-Ons, e.g. ESRF
WOFRY
SHADOWOUI
WISER
OASYS Main
SHADOW4
XRayServer, …
Tools
Ray tracing
Wave optics
1.3
INTEROPERABILITY
https://oasys-kit.github.io
Extensions
Notes: Before starting, I would like to do the following statement, all calculations presented here were performed using OASYS tools

## Slide 9: SHADOW4
SHADOW4 is a new Kernel, and a new interface, for new generations of sources
Fully developed in Python
OO programming
OASYS experience and ad-hoc developments
Fast enough
Preparing 5th generation
SHADOW is an interactive tool adapted for common laptops
Just called SHADOW4
Simplified interface (less widgets, generic mirrors, crystals, etc.)
Optimized (better communication)
Automatic scripting
Facilitate interoperability with other tools (e.g. for partial coherence)
Adapted for AI integration and Digital Twins
Easy transition from laptop prototyping to High-Performance Computing (HPC) and Cloud Computing
Open Source and Collaborative Development
Educational material for interactive learning
Fortran: compilation: obsolete technology, poorly structured code
Python API maintenance and extension
Python packaging (wheels)
Sustainability
SHADOW3 problems:

## Slide 10: Shadow4 Kernel: Application User Interface
S4Beam: traditional beam data (nrays, 18)
Automated scripts with OASYS
Documentation: https://shadow4.readthedocs.io
API
S4Beamline
S4LightSource
S4BeamlineElement
S4ElectronBeam
S4MagneticStructure
S4OpticalElement
ElementCoordinates
…

## Slide 11: Shadow4: Geometrical Sources
In cartesian coordinates
In polar coordinates
Sources/Magnetic structures
  SourceGeometrical, SourceGridCartesian, SourceGridPolar)
Source: Real space Source Divergence
Focus with an ellipsoidal mirror
Real space Divergence

## Slide 12: Shadow4: Synchrotron Sources
1) https://doi.org/10.48550/arXiv.2406.16446
2) https://doi.org/10.1107/S1600577525000190
Fake Geometrical Source
(Gaussian spatial + Gaussian divergency + e- energy spread)
789.938eV
806.060eV
814.121eV
Sources/Magnetic structures
  S4BendingMagnet (upgraded methods1)
  S4Wiggler (included short IDs)
  S4GaussianUndulator, S4Undulator (upgraded methods2)

## Slide 13: Shadow4: Optical Elements
Optical elements
  S4Screen (screens, slits, stops, absorbers)
  S4IdealLens, S4Empty,… (ideal elements)
  S4PlaneMirror, S4SphereMirror, S4EllipsoidalMirror, …, S4AdditionalNumericalMeshMirror
  S4PlaneGrating, … (including VLS)
  S4PlaneCrystal, … (undistorted perfect crystals in reflection)
  S4PlaneMultilayer, … (also graded, in depth or laterally)
  S4Interface, S4Lens, S4CRL, S4Transfocator (refractors)

## Slide 14: Shadow4 Kernel: models and algorithms
  S4OpticalSurface (S4Conic1, S4Toroid, S4Mesh)
  Include methods for reflection, refraction, scattering (gratings, crystals)
[1] https://arxiv.org/abs/2406.04079
[2] http://dx.doi.org/10.1107/S160057752400924X
[3] https://github.com/tschoonj/xraylib
[4] https://github.com/oasys-kit/dabax
Optical constants (scattering factors, refraction indices, crystal structures)
  preprocesor data file
  direct link
    xraylib3
    DABAX4
  PreRefl: Absorption/refraction for attenuators, mirrors, lenses
  crystalpy2: library for Crystals
  MLayer
Physical model (reflectivities)
preprocessors
code
Geometrical model

## Slide 15: Mirror Optics
Aberrations/beam wavefront distortion:
Surface shape: looking for optimized shape (e.g. diaboloid)
Surface error:
  methods (geometrical, hybrid) and databases (DABAX)
  thermal load (optics evaluation, avoid and correction)
Misalignement tools / Tolerances
H
V
Optimized toroid: p:q = 2:1
Diaboloid: 4th degree surface
Parabolic (meridional) section
Elliptical (sagittal) approx. section
Point-to-point focusing (stigmatic):
Ellipsoid (exact)
Toroid (approx.)
Toroid Diaboloid
ALS
ALS-U
Zero emittance
Sanchez del Rio et al. 2021 https://doi.org/10.1107/S160057752100401X

## Slide 16: Grating Optics (in reflection)
Resolution:
Schemes (SX700, DRAGON, PGM, SGM, VLS, etc.)
Surface error: shape, thermal, slope errors
Aberration reduction (e.g. Czerny-Turner RAMAN spectrometer)
70 μm (FWHM) source (double monoch.)
Point source (double monoch.)
70 μm (FWHM) source (single monoch.)
Point source (single monoch.)
Sanchez del Rio et al (2006) http://doi.org/10.1088/0031-8949/73/5/014
θ = 5◦ for all M
θ = 3.7◦ for M2 and M5
λ = 514.5 nm (green)
M5
M4
M5
M4

## Slide 17: Lens Optics
Individual trace of each surface:
Effects of lens distance and depth (adiabatic focusing)
Misalignement tools / Tolerances
Surface error:
  Wave/hybrid methods and databases (DABAX2D https://github.com/oasys-esrf-kit/dabam2d )

## Slide 18: Crystal Optics
Mosaic
Perfect
Dynamical theory for undistorted crystals (crystalpy)
Bragg:
  Flat symmetric (most Double Crystal Monochropmators)
  Asymmetric
    beam expansion (real or divergence)
    high resolution
    backscattering (rainbow)
  Distorted/bent crystal diffraction profile via external reflectivity (TO DO)
  Geometric effect of bending (Johann, Rowland, etc.)
  Johansson (TO DO)
  Types
    Si, Ge, C*
    High d-spacing: Quartz, sapphire, ADP, YB66
    (any structure)
Laue (TO DO) (Thin undeformed crystals in shadow3)
(TO DO) (symmetric Bragg in shadow3)

## Slide 19: Complementary with other OASYS methods
Analytical model (by hand)
Ray tracing (Shadow4)
Hybrid model (Shadow4)
Wave optics & partial coherence 1D (WOFRY)
2D partial coherence:
Monte Carlo (multi e-) (SRW)
Coherent Mode Decomposition (COMSYL)
[1] M. Sanchez del Rio et al. 2019 https://doi.org/10.1107/S160057751901213X
COMPLEXITY

## Slide 20: User Support / Teaching / OASYS schools
I Grenoble (ESRF) 2019
II Lemont IL (ANL) 2019
III Berkeley (LBNL) 2023 https://github.com/oasys-kit/bloms2023
IV Hamburg (DESY) 2025 https://github.com/oasys-kit/oasys_school_desy
…

## Slide 21: Summary / Conclusions
SHADOW version 4 is a python-based new version, completely rebuilt, of the traditional ray tracing code by Franco Cerrina
It is fully integrated in the OASYS ecosystem
Sustainable software (maintainable, reusable, open source, documented, with tests, funding support, reproducible, adaptable)
We encourage users and developers to try it, use it, and play with it. We are open for collaborations and further developments

## Slide 22: Extra Slides

## Slide 23: Shadow4: advanced tools – Hybrid1 method
Corrects ray tracing considering scattering and diffraction when the beam has a high coherence
Includes scattering by o.e.’s boundaries (slits, mirrors, gratings, lenses)
Manages the surface error (delegated from o.e.)
Fully rewritten code2
Scriptable
[1] Shi et al. 2014 https://doi.org/10.1107/S160057751400650X
[2] https://github.com/oasys-kit/shadow4-advanced

## Slide 24: Shadow4: beta testers are welcomed!
Send issues in https://github.com/oasys-kit/shadow4/issues
Shadow3
Shadow4
beam converter
matching results