## Slide 1: Francesco Stellato University of Rome Tor Vergata & INFN on behalf of the WA8 collaboration team & (in particular/in addition) Emiliano De Santis, Tomas André, Richard Bean, Massimo Ferrario, Augusto Marcelli, Velia Minicozzi, Emiliano Principi, Nicusor Tımneanu, Carl Caleman
Photon Science at EuPRAXIA@SPARC_LAB:
Free Electron Laser Biological Applications
@
Frascati - June 16th, 2025

## Slide 2
The EuPRAXIA project
The EuPRAXIA@SPARC_LAB Free-Electron Laser beamline(s)
Biological applications:
  Coherent Diffraction Imaging
  Coulomb Explosion Imaging
  X-ray Spectroscopy
Outlook
Outline

## Slide 3
EuPRAXIA: first European project to develop a particle accelerator research infrastructure based on plasma acceleration concepts driven by laser and linac technologies.
EuPRAXIA is one of the projects on the European Strategy Forum on Research Infrastructures (ESFRI) Roadmap of 2021.
The accelerated beam will drive a Free Electron Laser (FEL) source
The EuPRAXIA project
Assman et al. Eur. Phys. J. (2020)
https://www.eupraxia-pp.org/

## Slide 4
Two sites: one TBD
One: here! Frascati National Laboratory (INFN, Italy).
  EuPRAXIA@SPARC_LAB
The EuPRAXIA project
Ferrario et al. Nucl. Instr. Met. (2018)

## Slide 5
Electron beam-driven FEL
EuPRAXIA@SPARC_LAB
https://sparclab.lnf.infn.it/sparc_lab-home/eupraxiasparc_lab/
1 GeV X-band RF linac and an upgraded FLAME laser up to the 0.5 PW range
Compact FEL source, equipped with a user beamline and an experimental endstation at 4-10 nm wavelength, driven by a high gradient plasma accelerator
(+ a VUV beamline @ 50-180 nm)

## Slide 6
Beamline 1 AQUA
Beamline 2 ARIA
EuPRAXIA@SPARC_LAB - FEL Beamlines
Endstation

## Slide 7
AQUA
Self Amplified Spontaneous Emission (SASE) FEL
lasing in the soft X-rays
@ 4-10 nm
(covering the water-window)
+
ARIA
seeded FEL lasing in the VUV
@ 50-180 nm
EuPRAXIA@SPARC_LAB - FEL Beamlines

## Slide 8
AQUA ARIA
EuPRAXIA@SPARC_LAB - Beamlines
WA 8 – Users
Parameter | Value
Wavelength | 4-10 nm
Photons/pulse on sample* | 10 10 - 10 11
Pulse duration | < 10 fs
Repetition rate** | 100 Hz
Parameter | Value
Wavelength | 50-180 nm
Photons/pulse | 10 13 - 10 14
Pulse duration | 20/200 fs
Repetition rate** | 100 Hz
* An order of magnitude range is given, since final numbers will depend on the beamline optics
** Options to run @ 400 Hz are being explored

## Slide 9
Coherent imaging
X-ray absorption
Raman
spectroscopies
Photoemission
Ions
Coulomb Explosion
Proteins
Viruses
Bacteria
Cells
Metals
Semiconductors
Superconductors
Magnetic materials
Organic molecules
Science @ AQUA

## Slide 10
Science @ AQUA
Technique | Samples
Coherent imaging | Cells, organelles, nanomaterials Water window for high-contrast hydrated samples
Photon scattering | Molecules, nanoparticles Structural and dynamical characterization
X-ray Spectroscopy | Warm-dense matter, organo-metallic compounds, magnetic materials K, L and M edges falling in the FEL energy range
Photoelectron Spectroscopy | Carbon-based materials, batteries, biomolecules Chemical dynamics
Ion Spectroscopy | Astrochemistry, biomolecules Radiation-matter interaction dynamics
This is a general overview and, besides coherent imaging, these techniques are possible both at the baseline AQUA beamline and at the “beyond-the-baseline” ARIA
Pump-probe experiments to perform time-resolved measurements

## Slide 11
Biological applications @ AQUA

## Slide 12
When the photons hit the sample, a diffraction pattern is originated
The diffraction pattern is the |FT| of the sample electron density
|FT|-1
Diffraction pattern
k - space
Sample image (electron density)
real space
Coherent Diffraction Imaging (CDI)

## Slide 13
Diffraction pattern
Particle injection
One pulse,
one measure
A detectable signal must be recorded before the sample is destroyed
FEL pulses are so bright and short that the signal is damage free
> 106 patterns needed
Experimentally & computationally challenging…
R. Neutze et al, Nature 406 (2000)
Courtesy of SLAC
Diffract-and-destroy @ FELs

## Slide 14
3D images can be obtained merging info from several shots
Since the sample is destroyed by the FEL photons,
many identical samples are needed
Ekeberg et al. PRL (2015)
Bio-samples Coherent Imaging

## Slide 15
Why AQUA? The «water-window»

## Slide 16
The expected resolution is tens of nanometers
However, only room-temperature measurements of fully hydrated samples allow aquiring 2D images of living cells and of organelles in their native state
CDI in the «water-window»
4 nm
2 nm
Water window: energy region between
Oxygen and Carbon K-edge
2.34 nm – 4.4 nm (530 eV -280 eV)
«Sweet spot» for imaging of biological samples in their native environment: water is transparent, the samples are not!

## Slide 17
CDI @ LCLS
A yeast nucleus diffraction pattern exhibiting clearly visible speckles
Atomic Molecular and Optical science beamline CAMP Chamber
pnCCD
520 eV (2.4 nm) photons 3x2 μm2 focus - 2 μJ
pnCCD
pnCCD
FEL beam
Water jet
LCLS experiments
(still) unpublished data

## Slide 18
A gas-dynamic virtual nozzle (GVDN)
will inject micron-sized liquid
columns in the FEL beam
CDI @ AQUA – Sample Delivery
Liquid line
Gas line
Liquid jet
Gas line
Gas bottle
Sample reservoir

## Slide 19
Enables 2D/3D imaging of hydrated biological samples
Acheivable resolution ≈20 nm
'Diffraction-before-destruction' mode
CDI @ AQUA – Simulated experiments
Reconstructed electron density
Simulated diffraction pattern of an icosahedral 500 nm virus hit by an AQUA pulse:
1011 photons @ 4.3 nm, 5 µm diameter beam
2D CCD detector
@ 15 cm camera-length
with 1024x1024 75 µm pixels

## Slide 20
Schematization of a 500 nm diameter virus injected in a 1 μm thick water jet.
500 nm C40H60O20N1010
500 nm H2O
CDI @ AQUA – Simulated experiments
Wavelength | Relative Absorption (Virus vs. Water)
4.3 nm (just above C K-edge) | 3.3X more absorption by virus
4.4 nm (just below C K-edge) | 0.85X absorption (virus < water)
Within the water window, the signal-to-background ratio improves nearly 4X, enabling enhanced contrast for imaging carbon-rich structures like viruses.

## Slide 21
FEL pulses ionize molecules. The ionized atoms repel each other and “explode” due to Coulomb forces.
In pump-probe, time-resolved experiments: ultrafast structural changes at femtosecond resolution.
André, T., Dawod, I., Cardoch, S., De Santis, E., Tîmneanu, N., & Caleman, C. (2025). Protein Structure Classification Based on X-Ray-Laser-Induced Coulomb Explosion. Physical Review Letters, 134(12), 128403
Coulomb Explosion Imaging (CEI)

## Slide 22
Tracking ion trajectories allows distinguishing among macromolecules in different conformational states.
André, T., Dawod, I., Cardoch, S., De Santis, E., Tîmneanu, N., & Caleman, C. (2025) Physical Review Letters, 134(12), 128403
Coulomb Explosion Imaging (CEI)

## Slide 23
CEI @ AQUA – Sample Delivery
A liquid jet is sprayed into a system of aerodynamic lenses, producing small droplets with a thin solvent layer surrounding the sample.
The droplets quickly dry, and the samples are surrounded by no or very few solvent molecules.

## Slide 24
CEI @ AQUA – Experimental Scheme
Sample Delivery
Molecules (e.g., proteins) are injected as isolated particles via aerosol jets.
Ionization and Explosion
The FEL pulse causes multi-ionization.
A Coulomb explosion occurs, ejecting ions radially.
Detection
Ion positions are recorded by position-sensitive detectors.
The spatial pattern reflects the original molecular geometry.
Analysis
Simulations and clustering help reconstruct and classify 3D shapes.

## Slide 25
100 MD independent simulations per protein FEL Explosion simulation using the MC/MD code MOLDSTRUCT.
  FEL Gaussian pulse: 12 fs (EuPRAXIA@SPARC LAB)
  Simulation time: 300 fs
  Ion trajectories projected onto a virtual 4π spherical detector
Pattern Classification
  Dimensionality reduction
  Each explosion = a point in 2D space
CEI @ AQUA – Experiment Simulation

## Slide 26
CEI @ AQUA
2 proteins have been simulated
Nucleoporin
(pdb ID:4mhc)
PAN Avian Influenza Virus protein
(pdb ID: 4e5e)
Distinct patterns between different proteins → effective classification

## Slide 27
Soft X-ray Spectroscopy @ AQUA
Absorpion Spectroscopy
No monochromator @ day-one
SASE w/o monochromator (👻ghost-spectroscopy) scheme
Emission Spectroscopy
Downstream spectrometer (dispersive crystal + photon detector) for X-ray emission measurements
Klein, Y., Tripathi, A. K., Strizhevsky, E., Capotondi, F., De Angelis, D., Giannessi, L., ... & Shwartz, S. (2023). High-spectral-resolution absorption measurements with free-electron lasers using ghost spectroscopy. Physical Review A, 107(5), 053503.

## Slide 28
The AQUA energy spectrum allows scanning:
K-edge: Carbon
Hydrocarbons, aminoacids
L-edges: Sulphur, phosphorus, chlorine
Aminoacids,
M-edges: transition metal, lanthanides
Porphyrins, metalloproteins, imaging contrast agents, anti-cancer drugs
Experimental Techniques
X-ray spectroscopy: absorption (and emission)

## Slide 29
AQUA will enable biological imaging experiments at nanometric resolution.
Molecular Dynamics simulations support the effectiveness of CDI and CEI on hydrated biosamples with the AQUA parameters.
X-ray spectroscopy  atomic resolution structures around selected elements
Conclusions & Outlook
🔬 Imaging of organelles and whole living cells
🦠 even in the presence or absence of pathogens (e.g., viruses)