## Slide 1: AI Tools for Plasma Diagnostics by X-ray Imaging and Spectroscopy in the PANDORA Project Frame
High Precision X-ray Measurements 2025
Jun 16 – 20, 2025
Laboratori Nazionali di Frascati INFN
Bianca Peri on behalf of the PANDORA Collaboration

## Slide 2: Outline
Introduction: CCD X-rays Imaging
First steps: Imaging & Clustering Tools
Neural Networks
Conclusions & Perspectives
2

## Slide 3: Introduction: CCD X-rays Imaging

## Slide 4
Motivations and Physical Background
Plasma is excited by Electron-Cyctron-Resonance by microwaves and confined by magnetic fields
A multidiagnostic system surrounding the plasma chamber was developed to measure plasma parameters
Goal: investigate beta decay in stellar like Electron-Cyclotron-Resonance plasma in compact trap, for fundamental studies in Nuclear Astrophysics and its application.
THE PANDORA PROJECT

## Slide 5
Motivations and Physical Background
Plasma is excited by Electron-Cyctron-Resonance by microwaves and confined by magnetic fields
A multidiagnostic system surrounding the plasma chamber was developed to measure plasma parameters
Method: ECR plasmas emit radiation from microwave to hard X-rays and this radiation can be used to investigate plasma parameters in different regimes
THE PANDORA PROJECT
Goal: investigate beta decay in stellar like Electron-Cyclotron-Resonance plasma in compact trap, for fundamental studies in Nuclear Astrophysics and its application.

## Slide 6
Sensitivity range ~0,5 ÷ 30 keV (>95% QE within the range)
Sensor Size: 2,76 cm x 2,76 cm(2048x2048 Pixels)
Pixel size: 13.5 µm x 13.5 µm
Lead Pin-hole (diameters 400 μm)
Lead multi-disks collimator system to reduce the scattering noise, increasing resoltution and signal-to-noise ratio
‘‘Live’’ plasma structure and
X-ray emission investigations
Experimental Set-up
Space resolution: 500mm
Energy resolution: 236 eV @ 8 keV
CCD Camera & Pin-hole System

## Slide 7
State of the Art Single Photon Counting Algorithm
High Precision X-ray Measurement 2025 - Introduction
5
Ar filterd
Ta filterd
Ti filterd
 Decoupling of photon number versus energy
very short exposure-time (@ 50-500ms)
thousands of SPhC frames
Minimize the pile-up probability
Cluster Size Filtering:
Large size (> 5 pixels): multi-photons
Small size (≤ 5 pixels): single-photon
Each pixel becomes an indipendent spectrally-sensitive detector:
SPATIALLY-RESOLVED SPECTROSCOPY pixel-by-pixel

## Slide 8
State of the Art Single Photon Counting Algorithm
High Precision X-ray Measurement 2025 - Introduction
5
Ar filterd
Ta filterd
Ti filterd
Each pixel becomes an indipendent spectrally-sensitive detector:
SPATIALLY-RESOLVED SPECTROSCOPY pixel-by-pixel
Check on Giorgio Finocchiaro’s Talk: Space and time-resolved X-ray spectroscopy technique by CCD pinhole camera
 Decoupling of photon number versus energy
very short exposure-time (@ 50-500ms)
thousands of SPhC frames
Minimize the pile-up probability
Cluster Size Filtering:
Large size (> 5 pixels): multi-photons
Small size (≤ 5 pixels): single-photon

## Slide 9
Employing a Machine Learning Algorithm allows to:
Improve the energy resolution
Improve the signal to noise ratio
Minimize the spurious effect contribution
Purposes and Goals
High Precision X-ray Measurement 2025 - Introduction
6
We decided to use an Hybrid Approach
Un-supervised Model
Supervised Model
Bwconncomp:
State of the art tool for image analysis
Clustering Algorithms:
AI tool for clustering used for pattern recognition, and labelling
Neural Net:
Supervised model that works with labelled data to learn identify and classify events
Previous Algorithm
Furthermore, it will push towards different goals, such as:
Identification of specific patterns
Online Analysis Options

## Slide 10: First steps: Imaging & Clustering Tools

## Slide 11
Events | Area | N Local Max | Eccentricity | ….
1 | 20 | 1 | 0.3 | ----
2 | 4 | 3 | 1 | ----
----- | ---- | ---- | ---- | ----
1° step
MATLAB
Connettivity based tool for imaging recognition.
Bwconncomp
High Precision X-ray Measurement 2025 -First steps: Imaging & Clustering Tools
7

## Slide 12
Prior Definition of Cluster Number
Strong Dependence on Initialization Conditions
Excellent time efficiency and scalability
Spheroidal clusters
Distance between objects and centroids
Feature 2
Feature 1
K-means is used to group features based on similarities.
Euristic method for the evaluation of the cluster number in our dataset, based on the mean Silhouette Score.
High Precision X-ray Measurement 2025 -First steps: Imaging & Clustering Tools
8
Clustering Algorithm: K-means
2° step

## Slide 13
Prior Definition of Cluster Number
Strong Dependence on Initialization Conditions
Excellent time efficiency and scalability
Spheroidal clusters
Distance between objects and centroids
Feature 2
Feature 1
K-means is used to group features based on similarities.
Euristic method for the evaluation of the cluster number in our dataset, based on the mean Silhouette Score.
High Precision X-ray Measurement 2025 -First steps: Imaging & Clustering Tools
8
Clustering Algorithm: K-means
2° step
Feature 1
Feature 2

## Slide 14: Neural Network

## Slide 15
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 16
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 17
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
Events | Area | N Local Max | ….
1 | 20 | 1 | ----
2 | 4 | 3 | ----
----- | ---- | ---- | ----
K-means
1°step: bwconncomp
2°step: K-means
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 18
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
Dataset
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
Events | Area | N Local Max | ….
1 | 20 | 1 | ----
2 | 4 | 3 | ----
----- | ---- | ---- | ----
K-means
1°step: bwconncomp
2°step: K-means
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 19
Dataset
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
Label
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
Events | Area | N Local Max | ….
1 | 20 | 1 | ----
2 | 4 | 3 | ----
----- | ---- | ---- | ----
K-means
1°step: bwconncomp
2°step: K-means
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 20
Dataset
Are specific algortihm, such as the neural networks, both linear and convolutional, that has to be train to work as classifier with the help of a Labeled dataset.
Supervised Algorithm
Label
They learn how to make the wanted classification based on the dataset using the label as feedback for the training.
Neural Network
3° step
Events | Area | N Local Max | ….
1 | 20 | 1 | ----
2 | 4 | 3 | ----
----- | ---- | ---- | ----
K-means
1°step: bwconncomp
2°step: K-means
Classification
High Precision X-ray Measurement 2025 - Neural Network
9

## Slide 21: Data Preparation and Labelling
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
K-means IDX
…
…
N Events
Dataset
Labels
Gas mixing configuration: only Kr
CCD_plasma_13_11_24
Atomki Lab- Debrecen Hungary
The most important parameter for the label determination
Main k-means parameter for events discrimination
Binary distinction preliminarly
High Precision X-ray Measurement 2025 - Neural Network
10

## Slide 22: Data Preparation and Labelling
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
K-means IDX
…
…
N Events
Dataset
Labels
We made it into a binary values
Ranging from 0 to 1
Normalized between 0 and 1
Normalization function optimized for the neural network called mapminmax.
Normalization needed
Careful evaluation of the distribution
High Precision X-ray Measurement 2025 - Neural Network
11

## Slide 23: Data Preparation and Labelling
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
K-means IDX
…
…
N Events
Dataset
Labels
We made it into a binary values
Ranging from 0 to 1
Normalized between 0 and 1
Normalization function optimized for the neural network called mapminmax.
Normalization needed
A binary variable was created, employing the results coming from the k-means output, i.e. the cluster index
Balanced Dataset
High Precision X-ray Measurement 2025 - Neural Network
11

## Slide 24: Data Organization
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
K-means IDX
…
…
…
…
…
…
…
…
…
…
N Events
Dataset1
Labels1
TRAINING
70%
Used to train the net, updating the weight between the layers based on these data
VALIDATION
15%
TEST
15%
Used during training to monitor and track the net performances: overfitting, learning
Used after training to evaluate the net performances: on new data.
High Precision X-ray Measurement 2025 - Neural Network
12

## Slide 25: Data Organization
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
… | … | …
K-means IDX
…
…
…
…
…
…
…
…
…
…
N Events
Dataset1
Labels1
TRAINING
70%
VALIDATION
15%
TEST
15%
Randomization Needed
Allows for a more efficient training.
It’s a particularly usefull procedure to obtain a rappresentative dataset division.
High Precision X-ray Measurement 2025 - Neural Network
12

## Slide 26: Net Development
Feed-Forward Net [PATTERNET], which is the simplest neural net, easy to built and to train with specific charcateristic:
It flows in one single direction, without any cycle or feedback connection
Neuron Layers Connected via algorithm-evaluated weights
TYPICAL STRUCTURE
Input Layer
Hidden Layers
Output Layer
High Precision X-ray Measurement 2025 - Neural Network
13

## Slide 27: Net Development
Feed-Forward Net [PATTERNET], which is the simplest neural net, easy to built and to train with specific charcateristic:
It flows in one single direction, without any cycle or feedback connection
Neuron Layers Connected via algorithm-evaluated weights
TYPICAL STRUCTURE
Input Layer
Hidden Layers
Output Layer
High Precision X-ray Measurement 2025 - Neural Network
Input data, organized and classified in train, validation and test, labeled.
In our case we will have 3 neurons as we employed 3 features
13

## Slide 28: Net Development
Feed-Forward Net [PATTERNET], which is the simplest neural net, easy to built and to train with specific charcateristic:
It flows in one single direction, without any cycle or feedback connection
Neuron Layers Connected via algorithm-evaluated weights
TYPICAL STRUCTURE
Input Layer
Hidden Layers
Output Layer
High Precision X-ray Measurement 2025 - Neural Network
The hidden neurons layers act on the data weighting them based on specific activation function depending upon the training algorithm, modulating non linear relationship between data
The non-linearity of the model is introduced by two parameter the weight W and the bias b.
Where λ is the adaptive step, and p the conjugate direction
13

## Slide 29: Net Development
Feed-Forward Net [PATTERNET], which is the simplest neural net, easy to built and to train with specific charcateristic:
It flows in one single direction, without any cycle or feedback connection
Neuron Layers Connected via algorithm-evaluated weights
TYPICAL STRUCTURE
Input Layer
Hidden Layers
Output Layer
High Precision X-ray Measurement 2025 - Neural Network
Once in the 1-neuron Output Layer, the information have to be processed by the default sigmoid function into a interpretable results, such as the probability of belonging to a specific class (mainly used for binary classification)
13

## Slide 30
Net Training
Parameters | Value
Neurons in the Hidden Layer | 10
Training Algorithm | SCG
Number of Epoch | 300
Number of Events | 7767611
Activation Function | Tansig
Activation Function Output | Logsig
Minimum Gradient | 1 e-6
Maximum Fails | 10
Loss Function | Cross Entropy
High Precision X-ray Measurement 2025 - Neural Network
14

## Slide 31
Net Training
High Precision X-ray Measurement 2025 - Neural Network
15
FP
TN
TP
FN

## Slide 32
Net Training
High Precision X-ray Measurement 2025 - Neural Network
15

## Slide 33
First Results
High Precision X-ray Measurement 2025 - Neural Network
Channels
Channels
Ag
Kr
Al
16
2% FWHM @ Kr peak

## Slide 34: Conclusions & Perspectives

## Slide 35
Conclusions & Perspectives
High Precision X-ray Measurement 2025 - Conclusions & Perspectives
Test of the Methods performances on a new dataset
Further training of the Net on different dataset
Test of the Net Performance on simulated data
TO DO LIST
Validation of the AI based unsupervised Algorithm K-means
First Results on the data coming from the last experimental Campaign
Development and Training of a Feed-Forward Neural Network
ACHIEVEMENTS
17
MC Simulations

## Slide 36: Thanks for the Attention
High Precision X-ray Measurements 2025
Jun 16 – 20, 2025
Laboratori Nazionali di Frascati INFN

## Slide 37: Back-up Slides

## Slide 38
Thermodynamic Parameters & Emissivity models
Soft X-ray spectrum can be converted into X-ray emissivity density J(hν) by calculating the emissivity volume VP and geometrical efficiency Ωg
Emissivity Model
Thermodynamic Parameters
Total energy emitted per unit time, volume and energy, through photons of energy hν
The plasma X-ray spectrum can be decomposed into continuous bremsstrahlung and discrete line emission, so de emissivity density: Jtheo(hν) = Jtheo,brem(hν) +Jtheo,line(hν)
Warm Electron population (0.5-30 keV)

## Slide 39
Full-field Energy Spectrum: Gas Mixing
Al
Xe
Fe
Fluorescence peaks and Bremsstrahlung Continuum for Gas Mixing Measurement in the last experimental campaing at ATOMKI Lab

## Slide 40
Validation of the Method
Ta Lα
Ag
Ar
Ti Kα,Kβ
Multiple Features Spectrum:
AI Algorithm
Cluster Size
Number of Local Max =1
Eccentricity
FWHM Ta (keV) | Intensity Ti (Counts) | IMP/IDP Ti | IMP/EP Ta | Counts
0,2535 | 17377326 | 10,78818 | 3,309524 | 3,1 x10^7
0,2531 | 15518357 | 12,05066 | 3,42512 | 2,7 x10^7
High Precision X-ray Measurement 2025 -First steps: Imaging & Clustering Tools
7

## Slide 41
Results of K-means on New Data Set
Gas mixing measures, Krypton Plasma. Esperimental Campain November 2024- Debrecen, Hungary
Multielemental Analysis. FPT 2024- INFN-LNS Catania, Italy
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 42: Net Development
Among the Feed-Forward Nets in MATLAB we choose the already optimized net for structured data in classification problems: PATTERNET
Parameters Definition
Neurons in the hidden layer: we need to esperimentally determine the number trying 5, 10(default), 15 and 20
Loss Function used: it measures the distance between the net prediction and the reality. We want to minimizing it. The CrossEntropy Function is the optimized one for binary classification so evaluated:
Number of Epochs: it represents the number of time the data are read by the net, also to be test esperimentally (200-500)
Minimum Gradient: to measure the gradient and if no usefull adjustment were made it kills the train (no time waste) 1 e-6
Maximum Failure: maximum number of iteration without change generally 6-10 (avoid overfitting)
Training Algorithm: Scale Conjugated Gradient (SCG) is optimized for fast convergence, empolying an adattive step learning rate.
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 43
1st Attempt to Train
Real Class
Predicted Class
TP
FP
FN
TN
Let’s explore the confusion Matrix:
We have the Predicted Class in rows, and the Real Class in the coloumns. So we can easily highlight the
True Positive(True predicted Correclty),
False Positive(True predicted Wrong),
True Negative(False predicted Correctly) and
False Negative(False predicted Wrong) class.
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 44: Data Check
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
Dataset1
In this case we’re working with a binary feature (box plot not so informative): as we can see there’s a significant imbalance. If the neural net has an hard time recognizing the zero pattern, the dataset can be balanced by different techniques:
Oversampling, simply repeating the events multiple time to match the order of magnitude of the 1 class
Class Weighting, setting different weights on the two classes, without modifing the dataset
A combination of the two techniques
Of course we need to compare the performance of the neural net with and without the balancing processes.
Strong correlation with the output!
X^2 98 e p
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 45: Data Check
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
Dataset1
This feature is indeed better distributed, in fact it shows a wide box, with the median closer to the higher value, meaning more than half of the data is distributed on higher value.
More over it’s not necessary to balance it, and it also show a smaller correlation to the output in respect to the other two features, as expected.
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 46: Data Check
Number Of Local Max | Clustersize | Eccentricity
… | … | …
… | … | …
Dataset1
The box is really narrow and it’s easy to tell that the distribution is peaked on small value. It shows a great number of higher value outliers. This means that the distribution is not balanced at all, but its correlation to the output is significant, we do have to modify it:
Cut off the outliers brutally and make a new normalization
Make a log-transform in order to make the model more sensible in the lower part of the distribution
Make it into a categorical feature with a new binning
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 47
Validation Check 1: Number of Local Max
As expected the Confusion Matrix shows that we have a 100% accuracy, so all the prediction were correct, furthermore the Loss Function was minimize sharply, with a strong coherence in behaviour between train, validation and test. Lastly the training stopped due to the gradient stop condition.
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 48
Validation Check 2: Eccentricity
The Confusion Matrix shows that we have a 100% accuracy, so all the prediction were correct, furthermore the Loss Function was minimize, with a strong coherence in behaviour between train, validation and test. Lastly the training stopped due to the gradient stop condition.
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 49
Validation Check 2.1: Cluster Size
Normalized dataset
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 50
Validation Check 2.2 : Cluster Size
Non-normalized dataset
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 51
Validation Check 2.3.1 : Cluster Size
Normalized Cut dataset (@50)
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 52
Validation Check 2.3.2 : Cluster Size
Normalized Cut dataset (@30)
High Precision X-ray Measurement 2025 - Back-up Slides

## Slide 53
Validation Check 2.3 : Cluster Size
Let’s compare different BoxPlot graph, obtained with the whole dataset, the cutted one at 50 and at 30.
Whole Dataset
Cut at 50 Dataset
Cut at 30 Dataset
High Precision X-ray Measurement 2025 - Back-up Slides