## Slide 1: Betatron X-ray Radiation in the EuPRAXIA Advanced Photon Source Project
Federica Stocchi
University of Rome Tor Vergata & INFN-LNF
On behalf of SPARC_LAB & EuAPS collaborations

## Slide 2
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 3
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 4
Laser WakeField Acceleration
A plasma-based accelerator is a compact X-rays source
How is the betatron radiation produced in the laser-driven configuration?
Laser pulse as driver
Pulse duration
Gas jet
Laser WakeField-based accelerators can produce accelerating gradients up to GV/m
Accelerator size: mm-cm

## Slide 5
Laser WakeField Acceleration
Courtesy J. Vieira, R. Fonseca/GoLP/IST Lisbon
An accelerating electric field is achieved from charge separation:
The laser beam (the driver) is focused on a gas jet, creating a plasma channel
It pushes the plasma electrons away from the positive ions, creating a positive region with a bubble-like structure
Plasma wave
An electric field is established inside the bubble
Plasma channel of 3 mm from LWFA

## Slide 6
Plasma electrons from back of the bubble can be self-injected (strong and non-linear regime) into this region
Longitudinal electric field acceleration along the laser propagation axis
Radial electric field oscillations in the plasma channel around the reference trajectory
Emission of synchrotron-like radiation: Betatron radiation
Laser WakeField Acceleration

## Slide 7
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 8
X-ray Betatron Radiation
Betatron radiation vs Synchrotrons and FELs
X-ray betatron radiation
Broad energy spectrum from soft to hard X-rays
Critical energy of some keV :
High peak brilliance
photons/pulse with betatron strength parameter
fs bunch length
Micron source size
Spatially coherent
Synchrotrons
FELs
Monochromatic radiation
fs bunch length
Spatially coherent
High peak brilliance
Broad energy spectrum
Tens of hundreds of microns source size
10s of ps bunch length
High peak brilliance

## Slide 9
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 10
EuPRAXIA Advanced Photon Source
EuAPS: EuPRAXIA Advanced Photon Sources project
Supported by PNRR fundings
Collaboration among INFN, CNR, University of Tor Vergata
Milestone of the EuPRAXIA project
  Laser-driven X-ray betatron radiation source @INFN-LNF
  High repetition rate laser @CNR-INO Pisa
  High power laser @INFN-LNS
Milano
Pisa
Frascati/Roma Tor Vergata
Potenza
Catania
Where | Target
INFN-LNF | Plasma Source
INFN-LNF | Synchronization
INFN-Mi | Simulation & Data Analysis
CNR-Potenza | Photon Diagnostics
Tor Vergata | End User Station
CNR-Montelibretti | Photon Time Diagnostics
EuAPS@LNF

## Slide 11
EuPRAXIA Advanced Photon Source
M. Ferrario, et al. NIM B 309 (2013), 183-188
SPARC_LAB facility
SPARC bunker
FLAME laser

## Slide 12
EuPRAXIA Advanced Photon Source
M. Ferrario, et al. NIM B 309 (2013), 183-188
SPARC_LAB facility
SPARC bunker
FLAME laser
M. Galletti, F. Stocchi, et al. Appl.Sci (2024), 14, 8619
Parameter | Value | Unit
Laser power | 200 | TW
Laser energy | 6 | J
Wavelength | 800 | nm
Pulse duration | 30 | fs
Focal spot (FWHM ) | 18 | 
Parameter | Value | Unit
Laser power | 200 | TW
Laser energy | 6 | J
Wavelength | 800 | nm
Pulse duration | 30 | fs
Focal spot (FWHM ) | 18 | 
Ti:Sa FLAME laser system
Probe pulse with some mJ of energy and 40 fs temporal length

## Slide 13
EuPRAXIA Advanced Photon Source
M. Ferrario, et al. NIM B 309 (2013), 183-188
SPARC_LAB facility
SPARC bunker
EuAPS beamline

## Slide 14
EuPRAXIA Advanced Photon Source
Main laser beam
Probe laser beam
Top view
Parabolic mirror chamber:
Laser focusing
Interaction chamber:
Laser interaction with the gas (He, , Ar)
X-ray betatron radiation generation
LWFA diagnostics
User chamber
Photon science experiments
Courtesy of S. Lauciani
3 m

## Slide 15
EuPRAXIA Advanced Photon Source
Parameter | Value | Unit
Photon Critical Energy | 1 -10 | keV
Pulse duration | 10-50 | fs
Number of Photons/pulse | 107-109 | 
Repetition rate | 1 | Hz
Beam divergence | 3-20 | mrad
Electron Beam Energy | 100-500 | MeV
Plasma Density | 1018-1019 | cm-3
Expected parameters
Simulation of radiation spot
by A. Frazzitta
M. Galletti, et al. Appl.Sci 14, (2024), 8619
A. Curcio, et al. Nucl. Instr. Meth. Phys. Res. B , 42 (2017)
A. Curcio, et al. Phys. Rev. Accel. Beams, 20, (2017)
8

## Slide 16
EuPRAXIA Advanced Photon Source
User experimental chamber
Structure with 3 units of 1m length
Vacuum level down to mbar
Each unit has different flanges for coupling with an external laser pulse and for the installation of other diagnostics
X-ray CCD Camera (1): imaging array 2048 x 2048, 15 x 15 µm2 pixel size, it’s placed on a linear stage (2)
Sample holder: a hexapod (3) for a sample placement precision around ±0.05 µm and ±20 mdeg, Z and XY linear stages (4,5)
5
F. Galdenzi, et al. Condens. Matter 9, 30, (2024)

## Slide 17
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 18
Applications
Possible applications (in ascending order of complexity):
Static imaging
Static X-ray absorption spectroscopy
Static X-ray emission spectroscopy
Time-resolved pump-probe X-ray absorption spectroscopy
Time-resolved pump-probe X-ray emission spectroscopy
Time-resolved imaging
1 shot
13 shots
Contrast 68%
S. Fourmaux, et al. "Single shot phase contrast imaging using laser-produced Betatron x-ray beams," Opt. Lett. 36, 2426-2428 (2011)
Phase Contrast Imaging
Stellato, F., et al. “Plasma-Generated X-ray Pulses: Betatron Radiation Opportunities at EuPRAXIA@SPARC_LAB”.
Condens. Matter (2022), 7, 23.

## Slide 19
Applications
Reale et al. - MIDIX Soft X-rays microradiography
EuAPS Pilot Experiment: Green Science
X-ray imaging of leaves (and wood) aiming at the (tens of) microns resolution
Experiments performed with the broad radiation spectrum filtered by different materials to obtain difference maps emphasizing the presence of heavy metal contaminants  pollution control
Broad energy spectrum → X-ray spectroscopy
Spatial coherence → X-ray phase contrast imaging
Pulse duration tens of fs → Time-resolved experiments
High brightness → High photon flux and small source size → Fast processes
Courtesy F. Stellato

## Slide 20
Applications
System magnification: 2.7
Maximum resolution: 19
Contrast 55%

## Slide 21
Outline
Laser WakeField Acceleration
X-ray Betatron Radiation
EuPRAXIA Advanced Photon Source project @LNF
Applications
Outlook

## Slide 22
Timelines
OPERATION
OPPORTUNITY FOR USERS!
Courtesy A. Falone
THANK YOU FOR YOUR ATTENTION!