## Slide 1: Stilbene detectors: characterization, n+12C preliminary results and future developments
Musumarra, M.G. Pellegriti, D. Papanikolaou,
C. Massimi, R. Mucciola, R. Sahoo and N. Patronis
for the n_TOF collaboration
Meeting Nazionale n_TOF, Bologna 21/11/2024

## Slide 2: OUTLOOK
Papanikolaou Dimitrios/Pellegriti M. G.
1. Development motivations: (n,γ), (n,n) and (n,n’) reactions
2. LoI’s for PSTIL in-beam characterization @ n_TOF
3. PSTIL Structure and specs
4. Detector Characterization
5. Pulse Shape Discrimination (PSD)
6. Principal Component Analysis (PCA)
7. Preliminary results on 12C(n,n)12C measurement at EAR1
8. Summary of the activities in 2024
9. Status of the PSTIL set-up and Future developments
(2)

## Slide 3
Papanikolaou Dimitrios/Pellegriti M. G.
“Big” C6D6 Liquid scintillators
Large & segmented C6D6
Solid organic scintillators
Read-outs/Power supplies
Solid
Higher density
No Chemical hazard
n/γ discrimination
Compact array of small C6D6
Motivation for developing the prototype: (n,γ) measurements
(3)

## Slide 4
Papanikolaou Dimitrios/Pellegriti M. G.
12C(n,n)12C and 12C(n,n’)12C* benchmark
G.M. Hale, Nuclear Data Sheets 118 (2014) 165
AZURE (R-matrix) calculations
12C(n,n)12C
Motivation for developing the prototype: (n,n) and (n,n’)measurements
(4)

## Slide 5
INTC
PSTIL 2024
EAR 1
Papanikolaou Dimitrios/Pellegriti M. G.
INTC
PSTIL 2023
EAR 2
LoI’s for PSTIL in-beam characterization @ n_TOF
(5)

## Slide 6
PSTIL structure and specs (Stilbene-cylinder 1’’x1’’ )
50 μm Al window
Carbon Fibre housing
Development started on 2022
8 modules available 4 INRAD + 4 PROTEUS
(6)

## Slide 7
Contents
Detector Characterization (radioactive sources)
Pulse Shape Discrimination (PSD)
Principal Component Analysis (PCA)
Preliminary results on 12C(n,n)12C measurement at EAR1
Future Analysis
(7)

## Slide 8
Detector Characterization
Papanikolaou Dimitrios/Pellegriti M. G.
(8)
Detector Characterization

## Slide 9
Experimental set-up used for characterization
Papanikolaou Dimitrios/Pellegriti M. G.
(9)
Multi-Detector Array
Regular Tetrahydron base
Lightweight 3D-printed PLA holders
Thin hollow Al rods
Power Supply
Voltage Distributor (4 Channels)
Multi-Detector Array
**Developed at INFN-CT, Sezione di Catania**
source position
137Cs, 60Co or AmBe
pStil0 (PROTEUS)
pStil1-2-3 (INRAD)

## Slide 10
Detector Characterization: 137Cs and 60Co source
Papanikolaou Dimitrios/Pellegriti M. G.
(10)
Rise/Fall time
 | Rise Time (ns) | Fall Time (ns)
INRAD | 3.966 ± 0.003 | 14.13 ± 0.06
PROTEUS | 4.051 ± 0.002 | 14.43 ± 0.05
**Averaged for ~40000 events**
Savitzky-Golay Filtering
Implementation of a signal smoothing process
10% - 90%

## Slide 11
Detector Characterization
Papanikolaou Dimitrios/Pellegriti M. G.
(11)
γ-γ Time Coincidence with 60Co source
Time Pick-Off
Crossover Timing
Constant Fraction Discriminator (CFD) method
Derivative method

## Slide 12
Detector Characterization
Papanikolaou Dimitrios/Pellegriti M. G.
(12)
γ-γ Time Coincidence
Time Resolution
Time Resolution (ns) |  | 
 | INRAD - PROTEUS | INRAD - INRAD
Derivative | 0.74 ± 0.03 | 1.08 ± 0.02
Leading Edge | 0.78 ± 0.03 | 1.12 ± 0.02
CFD | 0.73 ± 0.03 | 1.13 ± 0.03
PROTEUS - INRAD
INRAD - INRAD

## Slide 13
Pulse Shape Discrimination (PSD)
Papanikolaou Dimitrios/Pellegriti M. G.
(13)
Pulse Shape Discrimination (PSD)

## Slide 14
Pulse Shape Discrimination (PSD)
Papanikolaou Dimitrios/Pellegriti M. G.
(14)
Methodology - Parameters
“Discrimination
Ratios”
Charge Integration
Method

## Slide 15
Pulse Shape Discrimination (PSD) - AmBe source
Papanikolaou Dimitrios/Pellegriti M. G.
(15)
PSD Distributions
INRAD
INRAD
INRAD
PROTEUS
Using an 241Am-Be source
**Provided by INFN-LNS**
-300 pC threshold to account for pile-up

## Slide 16
Pulse Shape Discrimination (PSD)
Papanikolaou Dimitrios/Pellegriti M. G.
(16)
PSD FOM
Slicing the PSD Distributions
(60-360) keVee
(800-1100) keVee
PSD FOM |  | 
 | 60-360 keVee | 800-1100 keVee
pStil0 - PROTEUS | 1.22 ± 0.01 | 1.64 ± 0.08
pStil1 - INRAD | 1.29 ± 0.01 | 1.69 ± 0.03
pStil2 - INRAD | 1.22 ± 0.01 | 1.86 ± 0.06
pStil3 - INRAD | 1.22 ± 0.01 | 1.60 ± 0.04

## Slide 17
Pulse Shape Discrimination (PSD)
Papanikolaou Dimitrios/Pellegriti M. G.
(17)
PSD FOM as a function of energy
Slicing the PSD Distributions
Difficult to comparatively assess the results!
Type of scintillator
QE of the PMT
Energy of the incident particles
Performance of electronics
**
Just accounting for the QE of a PMT, differences in FOM up to 30% can be introduced
**

## Slide 18
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(18)
Principal Component Analysis (PCA)

## Slide 19
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(19)
So why PCA ?
5 Initial Parameters! ...
Pulse-height
Charge (short, long, tail)
Pulse-width
...
Pulse-width
**
A lot of missed opportunity
**

## Slide 20
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(20)
PCA – Scree Plots
% Variance |  |  |  | 
 | pStil0 | pStil1 | pStil2 | pStil3
PC1 | 87.0 | 85.7 | 85.0 | 85.3
PC2 | 10.0 | 11.0 | 11.5 | 11.3
SUM | 97.0 | 96.7 | 96.5 | 96.6
Overall, more than 96% of the variation is preserved in the first two PCs
Lower the dimensionality from
5D to 2D !

## Slide 21
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(21)
PCA – Biplots
A biplot is another enhanced graphical representation used in PCA that displays both the PC scores of the observations and the loadings of the variables on the same plot
Scores represent the transformed coordinates of the observations in the new PC space
The position of each point indicates its projection of the original data point onto the PCs

## Slide 22
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(22)
PCA – Physical Interpretation
Principal Component 1
PC1
Pulse-width
Negative loading on PC1.
Inversely correlated with the other variables on this component.
ToT → proportional to energy loss.
Pulse-height, Charge (short), Charge (long)
High positive loadings on PC1.
It suggests that PC1 represents the overall signal strength or energy deposited by the particle, as these parameters are directly related to the signal amplitude and integrated charge

## Slide 23
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(23)
PCA – Physical Interpretation
Principal Component 2
PC2
Charge (tail)
High positive loading on PC2.
Reflects PSD contribution of slower signal components, confirming the basis of PSD by charge integration
Pulse-height and Charge (long)
Relatively small loadings on PC2, Suggesting they are equivalent for the purpose of discrimination, as expected

## Slide 24
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti M. G.
(24)
PCA – Physical Interpretation
Verifying the validity of an unsupervised technique for discrimination

## Slide 25
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(25)
Preliminary results on 12C(n,n)12C measurement at EAR1

## Slide 26
New equalization/distribution box
PSTIL set-up in EAR1 - October 2024
Det # | θlab
1 and 8 | 100°±6°
2 and 7 | 120°±6°
3 and 6 | 140°±6°
4 and 5 | 160°±6°
d=12cm, ΔΩ=0.04sr
INRAD
PROTEUS
1
2
3
4
5
6
7
8
Papanikolaou Dimitrios/Pellegriti M. G.
EAR1 – 12C Measurements
Experimental Set-Up
(26)

## Slide 27
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(27)
88Y Stability Check
1st run
2nd run
3rd run
Stabilized Electronics – 3 runs
160o
160o
120o
100o
140o
100o
120o
140o

## Slide 28
EAR1 – 12C Measurements /AmBe source
Papanikolaou Dimitrios/Pellegriti M. G.
(28)
Filtering
Amp/Area filtering
amp/area: 0.074 threshold to select neutrons
+ pile-up rejection
Preliminary PSA is used
160o
160o
120o
100o
140o
100o
120o
140o

## Slide 29
EAR1 – 12C Measurements /AmBe source
Papanikolaou Dimitrios/Pellegriti M. G.
(29)
Filtering
Amp/Area filtering
amp/area: 0.074 threshold to select neutrons
+ pile-up rejection

## Slide 30
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(30)
Spectra
Normalized 12C spectra
0.074 amp/area threshold
5keV Binning
No pile-up
tflash range
Preliminary PSA is used
160o
160o
120o
100o
140o
100o
120o
140o

## Slide 31
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(31)
Spectra
Normalized Empty Spectra
0.074 amp/area threshold
5keV Binning
No pile-up
tflash range
Preliminary PSA is used
160o
160o
120o
100o
140o
100o
120o
140o

## Slide 32
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(32)
Spectra
Clean Spectra
0.074 amp/area threshold
5keV Binning
No pile-up
tflash range
Preliminary PSA is used
160o
160o
120o
100o
140o
100o
120o
140o

## Slide 33
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(33)
Spectra
Clean Spectra
0.074 amp/area threshold
5keV Binning
No pile-up
tflash range

## Slide 34
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(34)
Spectra
Clean Spectra
0.074 amp/area threshold
5keV Binning
No pile-up
tflash range
R = (1.28 ± 0.04) %
preliminary estimation

## Slide 35
Future Analysis
Papanikolaou Dimitrios/Pellegriti M. G.
(35)
Future Analysis

## Slide 36
Papanikolaou Dimitrios/Pellegriti M. G.
Future Analysis
(36)
Fine tune the PSA. Find the best input parameters for discrimination.
Retrieve the flux of EAR1 and correct the normalized spectra.
Correct for areal density and neutron efficiency.
Compare with R-Matrix calculations.

## Slide 37
Papanikolaou Dimitrios/Pellegriti M. G.
(37)

## Slide 38
Status of the PSTIL set-up and future developments
ITEM | n. | PROVIDER | STATUS
1’’x1’’ crystal | 10 | PROTEUS | Expected to arrive at INFN-CT this week
PMT | 10 | Hamamatsu | Sub judice 2025
Power base | 10 | Sens-Tech | Sub judice 2025
Mechanical arrangement for 18 modules and new target holder in carbon fiber (coll. Trieste)
Ancillary detectors for (n,cp): small-volume, low-power.
One PSTIL module power: 5Vx50mA suitable for in-vacuum applications
Ancillary detectors for (n,n’) measurements: coupling with LaBr3
8 Modules ready and tested
Papanikolaou Dimitrios/Pellegriti M. G.
(38)

## Slide 39
THANKS!

## Slide 40
BACK-UP SLIDES

## Slide 41
Experimental set-up
Papanikolaou Dimitrios/Pellegriti Maria G.
(41)
Stilbene Detector Modules
(pStil)
Solid-State Organic Scintillators
(x3) 1”x 1” cylindrical INRAD trans-stilbene detector
(x1) 1”x 1” cylindrical PROTEUS trans-stilbene detector
Carbon fiber housing
Aluminium cover in the front window
Al window
Stilbene
Crystal
(C14H12)
PMT
**Developed at INFN-CT, Sezione di Catania**
High counting rate with no HV needed
pStil Modules
**Currently used & tested at nTOF/CERN**

## Slide 42
99.2% enrichment
New targets: 13C and 12C target
12C for target preparation test @ CERN
75 micron
Papanikolaou Dimitrios/Pellegriti Maria G.
(42)

## Slide 43
New Targets: 10B and 11B target
Antonio Massara and Martina Ursino
Papanikolaou Dimitrios/Pellegriti Maria G.
(43)

## Slide 44
EAR1 Flux
Papanikolaou Dimitrios/Pellegriti Maria G.
(44)
Flux Distributions (in eV)

## Slide 45
Beam interception function
Papanikolaou Dimitrios/Pellegriti Maria G.
(45)
Beam size vs neutron energy

## Slide 46
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti M. G.
(46)
Filtering
tflash filtering
tflash: ± FWHM x-values range for each detector

## Slide 47
EAR1 – 12C Measurements
Papanikolaou Dimitrios/Pellegriti Maria G.
(47)
Filtering
tflash filtering
tflash: ± FWHM x-values range for each detector
 | FWHM (ns) | σ (ns)
pStil1 - INRAD | 26.57 ± 0.02 | 11.28 ± 0.01
pStil2 - INRAD | 25.42 ± 0.02 | 10.79 ± 0.01
pStil3 - INRAD | 25.32 ± 0.02 | 10.75 ± 0.01
pStil4 - INRAD | 19.16 ± 0.02 | 8.14 ± 0.01
pStil5 - PROTEUS | 16.22 ± 0.02 | 6.89 ± 0.01
pStil6 - PROTEUS | 19.97 ± 0.02 | 8.48 ± 0.01
pStil7 - PROTEUS | 23.00 ± 0.02 | 9.77 ± 0.01
pStil8 - PROTEUS | 24.45 ± 0.02 | 10.38 ± 0.01

## Slide 48
Detector Characterization
Papanikolaou Dimitrios/Pellegriti Maria G.
(48)
Simulated Detection Efficiency using GEANT4 simulation toolkit
Isotropic
Point Source
** Preliminary**
Simulated Detection Efficiency

## Slide 49
Pulse Shape Discrimination (PSD)
Papanikolaou Dimitrios/Pellegriti Maria G.
(49)
Methodology – Pile-Up Regection
Higher counting rates can cause overlap between pulses
Peak Pile-Up
For a time window of 320ns and a rate of 1kHz
For ~106 events we expect
~300-400 pile-up events
~95 pulses
*G. F. Knoll, Radiation Detection And Measurement, John Wiley and Sons, 2000

## Slide 50
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(50)
So why PCA ?
5 Initial Parameters! ...
Pulse-height
Charge (short, long, tail)
Pulse-width
...
Pulse-width
**
A lot of missed opportunity
**

## Slide 51
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(51)
PCA Concept
Data Standardization
**
PCA is affected by the scales of the variables.
Normalizing the data to have a mean of 0 and a variance of 1
**
Computing the Covariance Matrix
** Captures the correlations between pairs of variables **
Computing the Eigenvalues and Eigenvectors
**
The eigenvectors (PCs) determine the directions of the new feature space, and the eigenvalues determine their magnitude (variance) along these new axes
**
Sorting the Eigenvalues and Eigenvectors
**
Sorted in descending order.
The top k-eigenvalues and their eigenvectors are selected to form the PCs
**
Transforming the data
**
The original data is projected onto the new PC axes
**

## Slide 52
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(52)
PCA – Scree Plots
“Elbow” Method
Kaiser-Guttman criterion
The value of k, defining an ‘elbow’ or ‘knee’ or ‘point of inflexion’ in the graph, is then taken to be the number of PCs to be retained
Considering eigenvalues. According to this rule, only the PCs with eigenvalues greater than 1 should be retained
Subjective methods

## Slide 53
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(53)
PCA – Scree Plots
% Variance |  |  |  | 
 | pStil0 | pStil1 | pStil2 | pStil3
PC1 | 87.0 | 85.7 | 85.0 | 85.3
PC2 | 10.0 | 11.0 | 11.5 | 11.3
SUM | 97.0 | 96.7 | 96.5 | 96.6
Overall, more than 96% of the variation is preserved in the first two PCs
Lower the dimensionality from
5D to 2D !

## Slide 54
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(54)
PCA – Loadings Plots
Graphical representation used in PCA to visualize the relationships between the original variables and the PCs
Mathematically speaking, loadings are the coefficients of the original variables in the linear combinations that define the PCs
For a given PC zk, the loadings are given by the eigenvectors vk is the eigenvector (loading) corresponding to the k-th PC

## Slide 55
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(55)
PCA – Biplots – Target Groups
Custom class for the selection of indices, from the PSD distributions, corresponding to gamma-rays and neutrons
Flexible selection using the left mouse button
PSD + PCA

## Slide 56
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(56)
PCA – Physical Implication
Energy Deposition
High positive loadings of pulse-height and charge parameters on PC1 indicate that this component captures the energy deposition characteristics of the particles
Signal Shape and Duration
Negative correlation of pulse-width with PC1 and its small positive loading on PC2 suggests that the pulse width is related to the pulse amplitude.
Anti-correlation could be associated to the fact that the pulse width is calculated at 50% of the signal (more investigation on that).
Tail Charge
Strong positive loading of charge (tail) on PC2 highlights the importance of the signal's tail in identifying slower processes or particles with extended interaction times

## Slide 57
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(57)
PCA – Scree Plots
4 Detectors

## Slide 58
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(58)
PCA – Loadings Plots
4 Detectors

## Slide 59
Principal Component Analysis (PCA)
Papanikolaou Dimitrios/Pellegriti Maria G.
(59)
PCA – Biplots
4 Detectors