## Slide 1
Adaptive Optics: large deformable mirrors
TECH-FPA PhD Retreat 2025 - LNGS
Roberto Biasi

## Slide 2: Outline
Very brief company introduction
Some AO concept
Large, contactless adaptive mirror technology
  Motivation for large adaptive mirrors
  Technology description and performances
Main deployed und ongoing projects
Other applications besides ground-based astronomy
High-density technology
Conclusions

## Slide 3: Four Main Business Unit

## Slide 4: Where we are, what we do
New premises located in the industrial area of Bolzano-south, South Tyrol
  11.000 m2
  Electronics labs
  Mechanical workshop
  Thermal and EMC tests
  Optical test areas
  Large clean integration room: 400m2, 20t overhead crane, large climatic test pit
The internal capabilities cover the entire process of electronic systems design and manufacturing
  Hardware design (digital, analog)
  Firmware (FPGA, microcontrollers)
  Software
  Control system design and multiphysics simulation
  Prototyping
  Integration of complex mechatronics systems
  Testing
  Production

## Slide 5: Microgate Engineering
The Engineering division operates mainly in the field of astronomy:
  Adaptive optics systems for large telescopes
  High performance real-time computers
  Motion control systems
  Metrology
  Optical communication

## Slide 6: Micro Photon Devices
Micro Photon Devices is a spin-off company of Microgate and Politecnico di Milano established in 2004
Development and production of single-photon counting modules based on Single-Photon Avalanche Photodiodes (SPADs)
Main customers include NASA, QTI, MIT, University of Vienna, Facebook, IIT, Harvard, Stanford, Oxford, Heriot-Watt University
In-house capabilities cover the entire process, from design to production and testing
Single pixels and arrays
Politecnico
di Milano

## Slide 7: Adaptive optics: what is it?
Adaptive optics is a technology that allows correcting the image blurring typically caused by the atmospheric turbulence. Even if the concept was introduced in 1953 (H.W. Babcock), the first adaptive optics systems for ground-based astronomic telescopes were introduced in the 90’s
Other applications: optical communication, space debris control, medical imaging, high resolution printing systems, military equipment
The adaptive mirror is deformed in real-time, so to compensate the waveform aberrations; a control loop tries to minimize the residual aberration measured by a wavefront sensor.

## Slide 8: Science and technology motivations
Telescope size 2x every 40 years
Why building larger telescopes?
  Larger light collection surface: look at fainter objects
  Improved angular resolution
E-ELT
GMT
TMT
But… this only yields for a perfectly corrected telescope… in reality we are limited by:
static and slow aberrations of the telescope
atmospheric turbulence, telescope vibrations
→ active optics
→ adaptive optics

## Slide 9: Atmospheric parameters
Atmospheric seeing (FWHM of the PSF) Excellent seeing at primary astronomy sites is rarely below 0.5”
8-m telescope diffraction limit in K: 0.07”
40-m class ELT: 0.014”
Large telescopes need adaptive optics to exploit their large size!
Fried Parameter r0 (atmospheric coherence length)
Actuator spacing (on entrance pupil) ~ 15cm
Greenwood time constant τ0
Mirror bandwidth ~ 5ms

## Slide 10: Image improvement through AO
LBT AO – A.Riccardi, 2010
With AO
Theoretical best PSF

## Slide 11: Large, contactless adaptive mirror technology: how it started
The voice-coil based, contactless adaptive mirror has been conceived by Piero Salinari (Osservatorio Astrofisico di Arcetri) in 1993
P.Salinari, C. Del Vecchio and V.Biliotti, A study of an adaptive secondary mirror,” in Proc. ESO Conference, ICO-16 Satellite Conference, Active and Adaptive Optics, August 1993

## Slide 12: Italian industry and research team
Integrated mechanical design
Mechanical manufacturing
Opto-mechanical integration
Original concept
Scientific advisor
Optical testing
Control system design
Simulation
Electronic design (HW, SW)
Electronics manufacturing
Control design and dynamic
simulation
Integration and test
Department of Aerospace Science and Technology

## Slide 13: Motivation for a large adaptive mirror
Astronomy-related
Adaptive correction on the telescope optical mainstream (typically M2)
  All instruments can take advantage of the AO correction
  M2 well conjugated with the ground layer, containing most of the turbulence power density
  Improved throughput and reduced background/IR emissivity, no added surfaces
  Increase of the observation efficiency
  Minimize non common path aberrations
General
Reduced power density for high power applications (momentum transfer, industrial lasers)

## Slide 14: The large, contactless adaptive mirror concept
The thin (<2mm) mirror levitates and is actively and massively controlled by a large number of electromagnetic actuators
The actuators are contactless, only magnetic forces are transferred to the mirror
The distance feedback is provided by co-located capacitive sensors measuring the distance between thin mirror and reference surface
Reference body
Cold plate
F
Capacitive sensor armatures
Magnets
Control electronics

## Slide 15: Technology pros and cons
Pros
Technology compatible with fabrication of large DMs, in particular M2:
  transmission efficiency
  background / IR emissivity
  reduced non common path aberration
  well conjugated to ground layer
Large stroke
  AO + field stabilization + chopping on a single unit
Hysteresis- and friction-free
Very accurate non-AO operation
  position feedback to a reference surface
Fail-safe against actuators faults
Cons
Operation requires a complex closed loop
Thin shell
  Long and expensive fabrication process
  Might require specific handling tools
Not suitable for small, high-density DMs
Power dissipation, also in static conditions

## Slide 16: Control concept
Input (typical 500-2000 Hz): deformable mirror shape commands.
Feedback (~80 kHz sampling): control the gap between the mirror and the reference body at each actuation point. Controller with a proportional, integral and pure electronic damping term.
Feedforward (same sampling as input): sum of the static necessary to set the command and a dynamic contribution to compensate in open loop the system dynamics.
+ -
PI Controller
Voice Coil Motors
Capacitive sensors
WFS loop frequency (up to 3kHz)
co-located loop frequency (~ 80kHz)
DeformableMirror
Feedforward
+
+
Electronic Damping
-
RTC
DM Cmds
WFS measurement
Control Forces
Mirror deformation

## Slide 17: Dynamic simulation
Time domain
We have developed and continuously improved a comprehensive set of numerical tools capable to analyze the system in all the relevant domains:
Frequency domain → Analysis of frequency responses
Time domain → Simulation of time histories
Laplace domain → Root locus analysis
The simulators are developed in house using different languages/environments and exploiting different hardware architectures:
Matlab, Python, C, C++
CPUs (with multi-thread option), GPUs.
Frequency domain
FEM
ELT-M4 Unit
Laplace domain

## Slide 18: Dynamic simulation
The system modeling is intrinsically multiphysics, covering:
Structural dynamics (usually starting from FEMs)
Fluid dynamics (custom reduced set of Navier-Stokes equations or more simplified models)
Servo controls (inner mirror control loops, telescope optical loop)
Different levels of system modeling, HiFi vs LoFi descriptions: depending on the needs, balance between the analysis accuracy and the computational time and resources
The reliability of all the simulators has been cross-checked through the correlation with experimental results.
Other design aspects (others than dynamic) covered by simulation:
Electromagnetic simulation, e.g. for the VCM design and optimization
System power consumption analysis

## Slide 19: Typical performances
Optical and static
    Mirror flatness ~20nm rms WF (typically limited by measurement setup) – adaptive mirror flattened ‘closing a static loop’ with an interferometer – similar performance demonstrated also by segmented systems
    Actuators print through in the order of 1 nm rms
    ‘Blind’ (open AO loop) stability enabled the internal metrology, in the order of 1.5 nm/°C → allows co-phasing of multiple segments
    Accurate absolute calibration of the internal metrology, ~ 20 nm ptv over > 100µm stroke, allowing ‘open loop’ correction of quasi-static aberrations
Co-phasing of ESO ELT M4 demonstration prototype segments

## Slide 20: Typical performances
Dynamic and stroke
    Settling time < 0.75ms for all corrected modes
    Maximum overshoot within 10% of command
    Typical wavefront residual error after correction < 40nm rms (median atmospheric seeing, 0.9” @ λ=0.5µm, 20 cm actuators spacing on M1)
    Very large stroke, > 100 µm → tip-tilt correction, low order aberrations, chopping …

## Slide 21: Typical performances
Reliability
    Fail safe operation guarantees system operability also in case of actuators failure
        No mechanical link/constraint between actuator and mirror
        Failure modes allowing minimal impact on operation, e.g. position sensor failure
    Specific autonomous systems implemented to assure the safety of the thin shell in case of earthquake or strong wind
    Some cooling system failures occurred mainly due to bad operation at telescope level, none being catastrophic. Direct expansion gas cooling implemented in the most recent systems to avoid system damage in case of leakage

## Slide 22: Large, contactless DMs history: the first steps…
1997 - Early prototypes
1999 - MMT ASM prototype
2002 - MMT 336
First adaptive secondary
@ SPIE International Symposium on Astronomical Telescopes and Instrumentation - KONA 1998
R.Biasi, D.Gallieni MMT adaptive secondary prototype development
G.Brusa, A.Riccardi et al Adaptive secondary P30 prototype: laboratory results
R.Biasi, L.Fini, P.Mantegazza et al Control Electronics for an Adaptive Secondary Mirror

## Slide 23: Serving the largest observatories
MMT 336 Multiple Mirror Telescope
University of Arizona
2008
Large Binocular Telescope
LBT Corporation
2010
Magellan Baade Telescope
University of Arizona
2002
2016
Very Large Telescope
ESO
2030?
Giant Magellan Telescope
GMT
ESO –ELT M4 + MORFEO
2028
2027
Subaru
Observatory of Japan
Major delivered projects
Major ongoing projects (in construction)
Continuous technology improvement (4th generation):
Dynamic and static performances
Reliability
Power dissipation
Follow technological trends (long-term maintainability)

## Slide 24: VLT DSM
Very Large Telescope (ESO, Paranal, Chile) UT4
the largest Adaptive Mirror ever built: 1.12 m diameter, 1170 actuators, 29mm spacing
Customer: European Southern Observatory (ESO)
Reliably working on the telescope since early 2016

## Slide 25: European Extremely Large Telescope M4
Cerro Armazones (Chile)
Primary mirror: 39m
MAIT Kick-off: 2015
First light: 2028
Customer: European Southern Observatory (ESO)
Adaptive M4
  2.54m diameter
  Segmented thin mirror
  Monolithic SiC structural reference body
  5352 actuators, 30mm spacing
  180 FPGA-based control bricks
  On-board computational power: ~1 TMAC/s
https://elt.eso.org/mirror/M4/
https://elt.eso.org/telescope/adaptiveoptics/

## Slide 26: ESO ELT final integration and testing

## Slide 27: ELT MORFEO Multiconjugate adaptive Optics Relay For ELT Observations
Serving the first-generation instruments of the ESO-ELT:
  MICADO (Multi-AO Imaging Camera for Deep Observations)
  HARMONY (High Angular Resolution Monolithic Optical and Near-infrared Integral field spectrograph)
M9 – DM1: 0.88m, convex, 928 actuators, 26mm spacing
M10 – DM2: 1.22m, concave, 1225 actuators, 31mm spacing
Very tight ‘blind’ stability requirements, ±25nm in 10 hours
https://elt.eso.org/instrument/MORFEO/

## Slide 28: Giant Magellan Telescope (GMT)
Cerro Las Campanas (Chile)
Primary mirror: 7 x 8.4 m (equivalent to 24.5 m)
Final design Kick-off: 2015
First segment MAIT Kick-off: 2021
First light: 2030?
Customer: GMT Organization (USA/AUS/ROK/BRA/CHIL/ISRL)
Adaptive Secondary Mirror
  7 independent segments
  1.05 m diameter each
  7x675 = 4725 actuators, 36mm spacing
  Very tight ‘blind’ segments co-phasing requirement, ~60 nm over 120s (interferometric metrology between segments’ RBs)

## Slide 29: Subaru ASM
Mauna Kea (Hawaii)
Primary mirror: 8.2 m dia
Adaptive secondary: 984 actuators, 1.23 m dia, 35mm spacing
Final design completed early 2022
MAIT Kick-off: March 2022
Delivery in 2026, on-sky 2027
Customer: National Astronomical Observatory of Japan

## Slide 30: Other applications: space active optics
LATT (Large Aperture Telescope Technology)
VCM contactless technology adapted to active optics application for space
ESA contract (led by OHB-CGS)
φ 0.4 m, 19 actuator prototype
1.3 mm stroke
Tested thermally and in vacuum
Reached TRL 5
Ongoing activity at INAF-Osservatorio Astrofisico di Arcetri: SPLATT, Segments and Pyramids for Large Aperture space Telescope Technology
R.Briguglio, SPIE2022+ICSO2022 https://sites.google.com/inaf.it/splatt

## Slide 31: Other applications: space debris laser ranging and optical communication
ASI – SDLR
Space Debris Laser Ranging Station
Space Debris Laser Ranging Station, with Laser Guide Star assisted adaptive optics
Italian Space Agency - Matera Space Center Giuseppe Colombo
1m telescope, 0.31m adaptive secondary mirror, 84 actuators, 28mm spacing
Laser Guide Star (589nm)
Uplink correction of the ranging laser
Compatible with momentum transfer
Delivery of the full station: June 2026

## Slide 32: High Density technology development
The current technology has a ‘physical’ actuators’ spacing limitation @ ~ 23-25mm
Higher density is demanded by several applications, including:
  Astronomy, aiming to wide-field correction in the visible
  Solar astronomy, optical communication, laser ranging → strong daytime turbulence, low r0
  High power laser applications → reduce power density by correcting on a large pupil, but not too large…
Development ongoing at Microgate and ADS International (AdOptica), aiming to reach 15mm spacing, while keeping the intrinsic key-advantages of the contactless technology
Additional goal: improve actuators efficiency and optimize electronics architecture to reduce on-board power consumption

## Slide 33: EST preliminary design
Canary Islands, a first-class site for astronomical observations.
Primary mirror: 4.2 m dia
Adaptive secondary: approx. 2000 actuators, 0.8 m dia
New concept of actuators, higher concentration of actuators on the surface
Preliminary Design ongoing, completed early 2025, including a 169 actuators prototype
Customer: Instituto de Astrofísica de Canarias

## Slide 34: Conclusions
The large, contactless adaptive mirror technology has continuously evolved in the past 30 years
Efficiently and reliably operating on the largest astronomic observatories
Units in construction for the next-generation ELTs
Other applications besides astronomy (space, space debris, optical communication, high power lasers)
Higher density technology development in advanced progress

## Slide 35
Wenn eine Idee nicht zuerst absurd erscheint, taugt sie nichts.
A.Einstein
Thank you for your attention!