## Slide 1: Future Perspectives on Gaseous Detectors and the DRD1 R&D Program
TECH-FPA PhD Retreat February 17-21, 2025
Piet Verwilligen INFN Bari

## Slide 2: Future Perspectives on Gaseous Detectors and DRD1 R&D Program
Introduction
Operating principles
A historical Introduction
High-Luminosity LHC Upgrades
R&D on Gaseous Detectors
DRD1 Collaboration
OUTLINE

## Slide 3: Future Perspectives on Gaseous Detectors 1. Introduction – On Tools and Instrumentation
“New directions in Science are launched by new tools much more often than by new concepts”
The effect of a concept-driven revolution is to explain old things in new ways”
The effect of a tool-driven revolution is to discover new things that have to be explained”
Freeman Dyson (Imagined Worlds)
Freeman Dyson 1923 - 2020
Idea & Slide © Werner Riegler
Nobel Prizes in Physics (statistics @ 2008 by W.Riegler)
31 for Theory
56 for Experiments & Instrumentation

## Slide 4: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles
Plot © Rob Veenhof

## Slide 5: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Choice of Gas (mixture)
Slide © Rob Veenhof

## Slide 6: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Primary Ionization
Remember, if energy of * is high enough to ionize on the L-shell we have a jump in
Non-gaussian tails
Structures in the cluster size
mpv
dE/dx (restr)
dE/dx (unrestr)

## Slide 7: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Transport
Drift velocity of electrons in pure Argon is slow – why?
Electron – Atom cross-sections for Ar
Add a quencher gas: e.g. CO2
Electron – Atom cross-sections for CO2
0.0% CO2
0.1% CO2
0.5% CO2
1.0% CO2
5.0% CO2
10% CO2
50% CO2
100% CO2

## Slide 8: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Transport
Drift velocity of electrons in pure Argon is slow – why?
Add a quencher gas: e.g. CO2
Microscopic Simulation of an electron in Ar:CO2 @ 1kV/cm
Plots © Rob Veenhof

## Slide 9: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Transport
Slides © Rob Veenhof

## Slide 10: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Transport
Plot © H Schindler
CH4

## Slide 11: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Amplification
Slides © Rob Veenhof

## Slide 12: Future Perspectives on Gaseous Detectors 2. Gaseous Detectors Operating Principles: Charge Amplification

## Slide 13: Gaseous Detectors – a very brief history 3. A historical Introduction
CSC Cathode Strip Chamber
DT Drift Tube
DC Drift Chamber
HL-LHC Upgrade ATLAS
LEP – Aleph, Delphi LHC - Alice
LHC - TOTEM
HL-LHC - CMS
LHC – ATLAS & CMS
LHC – ATLAS & CMS
LHC & HL-LHC ATLAS & CMS
SppS: UA1,UA2 LEP – OPAL
Tevatron - CDF Dafne - KLOE
Slide © Maxim Titov

## Slide 14
1st electronic particle Detector: SWPC (1908)
Single Wire Proportional Counter (SWPC)
Slide © Fabio Sauli

## Slide 15: The Revolution of 1968: MWPC
Electronic particle track detection is now standard in all particle detectors
The progress in experimental particle physics is driven by the advances and breakthrough in instrumentation, leading to the development of new, cutting-edge technologies:
1968: George Charpak developed the Multi-Wire Proportional Chamber, which revolutionized particle detection and HEP - which passed from the manual
to the electronic era.
1992:
Slide © Maxim Titov

## Slide 16: Multi-Wire Proportional Chamber (MWPC)
Simple idea to multiply SWPC cell  First electronic device allowing high statistics experiments !!
s ~ 2 mm
Slide © Maxim Titov
Near wire: radial field (AMP) Far away: linear field (DRIFT)
High-rate MWPC with digital readout: Spatial resolution limited by wire spacing: = 0.5 mm
Charge readout from segmented cathode: Spatial resolution determined by Signal/Noise (S/N) Typical (i.e. very good): S=20k, N=1k electrons: S/N=20, = 0.1 mm
Spatial resolution limited by wire-spacing. Better resolution requires more wires closer together, which leads to instabilities.
Segmented Cathode Readout => Cathode Strip Chambers (CSC)

## Slide 17: Drift Chamber (DC) & Drift Tube (DT)
FIELD
ANODE
FIRST DRIFT CHAMBER OPERATION (H. WALENTA ~ 1971);
HIGH ACCURACY DRIFT CHAMBERS (Charpak-Breskin-Sauli ~ 1973-75)
Choose drift gases with little dependence vD(E)→ linear space - time relation r(t)
The spatial resolution is not
Typical single point resolutions of drift chambers: 50 to 150 µm
primary ionization statistics: how many ion pairs, ionization fluctuations dominates close to the wire
diffusion of electrons in gas: dominates for large drift length
electronics: noise, shaping characteristics constant contribution (drift length independent)
Slide © Maxim Titov
Addition of Field-shaping wire to avoid low field region

## Slide 18: Drift Chamber: Discovery of W & Z bosons
UA1 used the largest wire / drift chamber of its
day (5.8 m long, 2.3 m in diameter)
Z  ee (white tracks) at UA1/CERN
Discovery of W and Z bosons
C. Rubbia & S. Van der Meer,
1984:
Slide © Maxim Titov

## Slide 19: Birth of the Time Projection Chamber (TPC)
Slide © Rob Veenhof

## Slide 20: Birth of the Time Projection Chamber (TPC)
ALEPH (CERN)
PEP4 (SLAC)
STAR (LBL)
Invented by David Nygren
(Berkeley) in 1974
Proposed as a central tracking device for the PEP-4 detector @ SLAC in 1976
An ultimate drift chamber design is TPC concept - 3D precision tracking with low material budget & PID through differential energy loss dE/dx measurement and/or cluster counting dNcl /dx tech.
More (and even larger) TPCs were built, based on MWPC readout, a powerful tool for:
  Lepton Colliders (LEP, Higgs Factories)
  Modern heavy ion collisions
  Liquid and high pressure TPCs for
neutrino and dark matter searches
New generation of TPCs use MPGD-based
readout: e.g. ALICE Upgrade, T2K, ILC, CepC
ALICE TPC (CERN)
2021: Replace MWPC-readout
with 4-GEM staggered holes
Slide © Maxim Titov

## Slide 21: MWPC as UV-Photon detector in RICH
Ring Imaging Cherenkov (RICH) detectors
  Idea: identify a charged particle (measure velocity) by measuring the opening angle of the (UV) Cherenkov radiation generated by the particle in a Cherenkov radiator
  Only few UV photons detected, need good spatial resolution to reconstruct the ring => Gaseous detectors with good position resolution, e.g. MWPC
  2 Approaches: photo-sensitive gases: TMAE, TEA OR solid-state -convertor (CsI)
Slide © E. Nappi
ALICE & COMPASS RICH:
Readout pads covered with CsI
Cherenkov- generated in C6F14 (liquid radiator), passes through UV-transparent window (quartz)
interacts in reflective photo-cathode (CsI)
Ejected electron ionizes the gas and is detected by the MWPC
NEW Slide

## Slide 22: Gaseous Detectors with Parallel Plates Resistive Plate Chambers (RPCs) & Multi-gap RPCs (MRPC)
Parallel Plate chamber (PPCs) consist of thin (few mm) gas gap operated in an intense electric field, with excellent time resolutions (down to 50ps)
PPCs improved by introduction of Resistive plates to quench the discharge (protect electronics) and keep rest of the detector active
 | RPC | MRPC
# gaps | 1-2 | 10-20
Detect Size | 2m2 | 0.1m2
System Size | 5000-7500 m2 | 200m2
Rate Cap | 10 kHz/cm2 | 500 Hz/cm2
Time Res LHC | 1-2ns | 50-75ps
Time Res Prot | 500 ps | 15-20 ps
 | RPC | MRPC
# gaps | 1-2 | 10-20
Detect Size | 2m2 | 0.1m2
System Size | 5000-7500 m2 | 200m2
Rate Cap |  | 
Time Res LHC | 1-2ns | 50-75ps
Time Res Prot | 500 ps | 15-20 ps
MRPC
ALICE: 200m2 TOF @ 50ps
RPC

## Slide 23: Micro-Pattern Gaseous Detectors: Bridging gap between Wire Chambers and Silicon detectors
Pixel System:
a ~ 100 µm
a < 10 µm
Advantages of gas detectors:
low radiation length
large areas at low price
flexible geometry
spatial, energy resolution …
Problem:
rate capability limited by space charge defined by the time of evacuation of positive ions
Solution:
reduction of the size of the detecting cell (limitation of the length of the ion path) using chemical etching and photo-lithographique techniques developed for microelectronics and keeping at same time similar field shape.
Slide © Maxim Titov

## Slide 24: Micro-Strip Gas Chamber (MSGC) An Early MPGD
Typical distance between wires limited to ~1 mm due to mechanical and electrostatic forces
Typical distance between
electrodes ~100 µm
Multi-Wire Proportional Chamber (MWPC)
Micro-Strip Gas Chamber (MSGC)
MSGC significantly improves rate capability
due to fast removal of positive ions
Excellent spatial resolution
A. Oed, NIMA263 (1988) 351
Slide © Maxim Titov

## Slide 25
 | Vertex | Inner Tracker | PID/ Photon Det. | EM CALO | HAD CALO | MUON Track | MUON Trigger
ATLAS | - | TRD (straws) | - | - | - | MDT, CSC | RPC, TGC
CMS | - | - | - | - | - | DT, CSC | DT, CSC, RPC
TOTEM | - | - | - |  | - | GEM | GEM
LHCb | - | Straws SciFi | - | - | - | MWPC | MWPC, GEM
ALICE | - | TPC (MWPC Upgrade to 4-GEM) | TOF(MRPC), PMD, HPMID (RICH-MWPC), TRD (MWPC) | - | - | MWPC | RPC
CMS DT + RPC
ALICE MRPC
ATLAS TGC
Proven robustness, stability ensure reliable operation for decades (including HL-LHC), supported by aging mitigation, advanced electronics, repair accessibility, and a sustainable approach (environmental-friendly)
ATLAS TRD -straw
Slide © Anna Colaleo & Maxim Titov
Gaseous Detectors in LHC Experiments
25

## Slide 26
Performance of LHC Wire-based Detectors Examples from the CMS Experiment: Drift Tubes & Cathode Strip Chambers
Segment | DT | CSC
# Chambers | 250 | 540
Efficiency | > 99% | > 99%
Spatial Res | 250 um | 50-150um
Timing Res | 2ns | 2ns
CSC System
DT System

## Slide 27
Higgs Candidates @ LHC Muon gaseous detectors:
(2 Z-Boson candidate events
decaying into 4 muons in CMS and ATLAS)
2013 Nobel Prize in Physics for Higgs Boson Discovery
Slide © Maxim Titov
Discovery of the Higgs Boson

## Slide 28
Micromegas
GEM
THGEM
Rate Capability: MWPC vs GEM:
Micromegas
Gas Electron Multiplier (GEM)
Thick-GEM (LEM), Hole-Type & RETGEM
MPDG with CMOS pixel ASICs (“GridPix”)
Micro-Pixel Chamber (µ-PIC)
µ-Resistive WELL (µ-RWELL)
Resistive-Plate WELL (RPWELL)
µPIC
µ-RWELL
InGrid
RPWELL
Micro-Pattern Gaseous Detectors - MPGD
Slide © Maxim Titov

## Slide 29
Thin metal-coated polymer foil chemically pierced by a high density of holes
Electrons are collected on patterned readout board.
A fast signal can be detected on the lower GEM electrode for triggering or energy discrimination.
All readout electrodes are at ground potential.
Positive ions partially collected on GEM electrodes
Induction gap
e-
S1 S2 S3 S4
e-
I+
A difference of potentials of ~ 500V is
applied between the two GEM electrodes.
 the primary electrons released by the ionizing particle, drift towards the holes where the high electric field triggers the electron multiplication process.
F. Sauli, NIMA386 (1997) 531
Gas Electron Multiplier - GEM
Slide © Maxim Titov

## Slide 30: Micro Mesh Gaseous Structure (MICROMEGAS)
Micromesh Gaseous Chamber:
micromesh supported
by 50-100 mm insulating pillars
Small gap: fast collection of ions
Y. Giomataris, NIMA376 (1996) 29
Slide © Maxim Titov
Micro-Mesh Gaseous Structure - MicroMegas

## Slide 31
Upgrade of the MWPC-based photon detector of COMPASS
Need to reach higher rates up to 100kHz/cm2
Need detector with short signal (avoid long ion drift)
Upgrade: 3-stage hybrid MPGD
Double Thick-GEM + Micromegas
Reflective CsI coating on top of THGEM1 layer
Slide © Silvia Dalla Torre
Photon Detection with Hybrid Thick-GEM+MM
NEW Slide

## Slide 32
https://ep-news.web.cern.ch/content/atlas-
new-small-wheel-upgrade-advances-0
https://ep-news.web.cern.ch/upgraded-alice-tpc
https://ep-news.web.cern.ch/content/demonstrating-
capabilities-new-gem
ATLAS NSW MicroMegas
ALICE GEM-TPC
CMS GEM muon endcaps
The successful implementation of MPGDs for relevant upgrades of CERN
experiments indicates the degree of maturity of given detector technologies for constructing large-size detectors, the level of dissemination within the HEP community and their reliability
Slide © Maxim Titov
Future Perspectives on Gaseous Detectors 4. High-Luminosity LHC Upgrades

## Slide 33
Gaseous Detector upgrade at the HL-LHC
Table © Maxim Titov

## Slide 34
Advancements in MPGDs:
Fuelling ATLAS, CMS, ALICE Upgrades in Run 3
  ATLAS New Small Wheel with Micromegas
  CMS GE1/1 with 3-GEM
  ALICE TPC with 4-GEM readout for TPC
Three ground-breaking LHC upgrades, incorporating MPGDs, embarked on their several year R&D journeys in close collaboration with RD51, leveraging dedicated facilities at the GDD-RD51 Laboratory.
Slide © Anna Colaleo
MPGD Upgrades LHC: first experience Run 3

## Slide 35
Peculiarities of ATLAS NSW Muon Upgrade's Resistive MM:
Screen-printed resistive strips capacitive-coupled to Cu strips.
Araldite passivation on edges for uniformity, less edge effects.
Thin metallic micro-mesh at ground potential.
"Floating" mesh integrated in drift panel
Operates at -60 V with 93/5/2% Ar/CO2/isobutane mixture.
1200m2 resistive MM: installation ended beginning of 2022
Read-out strip positions need < 30 μm accuracy. Chamber position within 80 μm accuracy. A granite table 8 um precision
Resistive Micromegas (MM) + small Thin Gap Chambers (sTGCs) for Trigger & Track Reco @ HL-LHC
Precision tracking (∼ 100 µm/plane, > 90% efficiency) for s(pt/pt) < 15% at muon pT​ ≈ 1 TeV/c
particle flux: up to 20 kHz/cm2 rejecting fake triggers.
Slide © Anna Colaleo
MPGD Upgrades LHC: first experience Run 3

## Slide 36
GEM+ Cathode Strip Chambers (CSC) allows for muon momentum measurement in a single station, which helps reduce considerably L1 trigger rate@ HL-LHC
GE1/1: 144 100 3-GEM (72 per endcap)1.55 < |η| < 2.18
High-rate O(kHz/cm2)
Efficiency > 98%
Space (time) resolution ≈ 300 μm (8 ns)
Gas mixt: Ar/CO2 70/30
(low GWP)
CMS triple-GEM detectors peculiarities:
3/1/2/1 mm gaps
Single-mask GEM technology
mechanical foil stretching technique
15-years-long R&D on design, components and materials (longevity, outgassing studies, etc.)
GEM GE1/1 chambers installed: Sept. 2020
Slide © Anna Colaleo
MPGD Upgrades LHC: first experience Run 3

## Slide 37
New readout chambers which enables continuous readout@50 kHz in Pb-Pb
 choice of 4-GEM
Total effective gain ~ 2000
Energy res. σ(E)E < 12%
Intrinsic ion-blocking capabilities (IB <1%)
Keep space-charge distortions at a tolerable level
Mixture Ne-CO2-N2 (90-10-5) (high ion mobility)
TPC reinstallation in the ALICE cavern (August 2020)
JINST 16 (2021) P03022
140𝜇𝑚 pitch
280 𝜇𝑚 pitch
280 𝜇𝑚 pitch
140𝜇𝑚 pitch
R&D synergies between the ILC TPC and the T2K-II ND TPC.
Slide © Anna Colaleo
MPGD Upgrades LHC: first experience Run 3

## Slide 38: Success Story: MPGD Technologies @ CERN
The integration of MPGDs in large experiments was not rapid, despite of the first large- scale application in COMPASS at SPS in the] 2000’s
Scaling up MPGD detectors, while preserving the typical properties of small prototypes, allowed their use in the LHC upgrades
 Many emerged from the R&D studies within the CERN-RD51 Collaboration
Slide © Maxim Titov

## Slide 39
2008:
2018:
Many of the MPGD Technologies were introduced before the RD51 was founded
With more techniques becoming available, new detection concepts were introduced and
the existing ones were substantially improved during the RD51 period (2008-2023)
Beyond 2023, RD51 served as a nuclei for the new DRD1 (“all gas detectors”) collaboration, anchored at CERN, as part of the ECFA Detector R&D Roadmap
RD51 Spokespersons:
L. Ropelewski (2008-2022)
M. Titov (2008-2015, 2023)
S. Dalla Torre (2016-2022)
E. Oliveri (2023)
arXiv:1806.09955
RD51 CERN-based “TECHNOLOGY - DRIVEN R&D COLLABORATION” was
established to advance MPGD concepts and associated electronics readout systems
RD51 community: ~ 90 institutes, 500 members
RD51 Collaboration Legacy 2008 - 2023
Slide © Maxim Titov

## Slide 40
MPGD Technology Development & Dissemination
R&D Tools, Facilities and Infrastructure
The success of the RD51 is related to the “RD51 model” inperforming R&D: combination of generic and focused R&D with bottom-up decision processes, full sharing of experience, “know-how”, and common infrastructure, which allows to build community with continuity and institutional memory and enhances the training of younger generation instrumentalists.
Community and Expertize (RD51 Scientific Network)
CERN Courier (5 pages) Volume, October 2015
https://rd51-public.web.cern.ch/
RD51 Collab legacy: “the RD51-Model”

## Slide 41
2023
ECFA DRD proposals
2020
ESPP update
HEP strategic projects
2019
Granada Symposium
WGs and Physics Briefing Book
2021
ECFA detector R&D roadmap
TF & community workshops
2025
DRD MoUs
collaborations active
2026-27
ESPP update
10 Global Recommendations
GR4: international coordination & organization of R&D activities
GR6: establish long term strategic funding program
Form international DRD collaborations
hosted at CERN (CERN/SPC/1190)
Conveners: Anna Colaleo (INFN-Bari), Leszek Ropelewski (CERN)
Experts: Klaus Dehmelt (SUNY), Barbara Liberti (INFN-Rome2), Maxim Titov (CEA Paris-Saclay), Joao Veloso (Univ. Aveiro)
Link to the coordination team : Silvia Dalla Torre (INFN-Trieste)
Slide © Anna Colaleo
Future Perspectives on Gaseous Detectors 5. R&D on Gaseous Detectors: towards a long-term detector R&D plan
41

## Slide 42
HL-LHC after LS4
Higgs Factories
Hadron physics
Muon Collider
Future hadron colliders (FCC-hh/eh colliders)
SuperKEKB, DUNE ND
PANDA
Cygnus
Darksphere
DM, solar axions, ββ0ν-decay, neutrino, nuclear, astroparicle
Rare event search, fixed target (LFV, Kaon physics)
EiC
MegII
HIKE
MU2E
DarkSide20 and ARGO
Slide © Anna Colaleo
Main Targets of Gaseous Detector R&D

## Slide 43
IDEA
3-6 Muon Stations
Space resolution, σx, of O(100)um
Efficiency ~ 98-99%
Time resolution: few ns: trigger/BX-id
Rate: few KHz/cm2 – MHz/cm2
Low GWP gas mixture
G.Bencivenni
New, innovative, possibly more cost-effective concept
Silicon vertex detector
Short-drift, ultra-light wire chamber
Dual-readout calorimeter
Thin and light solenoid coil inside calorimeter system
3 muon stations in the return yoke
Double resistive layer (DRL)
Double DLC layers connected through matrices of conductive vias to the readout electrodes
Silver Grid (SG)
Single DLC layer grounded by condutive strip lines realized on ttop of he DLC layer)
μRWell
RPC -30 × 30 mm2 cells @CLD/CEPC
MPGD/RPC@ Muon collider
μRWell 50x50 cm2 (tiles) also for pre-shower @FCC
@High Rate: Different Grounding schema for fast current evacuation at high rate
Rate > 10 MHz/cm2
Based on CLIC detector design; technology developments carried out for LCs
All silicon vertex detector and tracker
3D-imaging highly-granular calorimeter system
Coil outside calorimeter system
6-7 muon stations in the return yoke
MUCOL
Slide © Anna Colaleo
Muon Detector for FCC-ee / CEPC / MuColl

## Slide 44
<10kHz/cm2
R < 1m :
Rate>500 kHz/cm2
<0.5kHz/cm2
Current muon system gas detector technology will work for most of the FCC detector area
Forward region ( r < 1 m)  more R&D would be needed
Barrel Muon system (2 layers) : 2000 m2
Endcap Muon System (2 layers): 500 m2
Forward Muon System: (4 layers): 320 m2
Hardest challenge
pp collisions at 100 TeV (FCC-hh)
Pileup: 1000 events/bunch crossing  spatial resolution, timing
Muon barrel and endcap
Charged rates ~ 5x104 cm-2s-1
photon rates ~ 5x106-8 cm-2s-1
N fluence ~1014 cm-2  shielding can mitigate effect
Muon System, tracking and trigger capabilities with resolution of 50 um, σpT/pT≈5% at 10TeV
Muon Detector for FCC-hh
Slide © M.Aleksa & G.Aielli

## Slide 45
The IDEA drift chamber (DCH)
Approach at construction technique of high granularity and high transparency Drift Chambers
The dE/dx < 3% , momentum resolution: σ(pT)/pT ≈ 0.4% at 100 GeV/c with cluster counting, a desirable achievement :
Large number of channels,
gas gains ∼5×105
long drift times (slow drift velocity),
trigger rate (Z0-pole at FCC-ee) = 25kHz/cm²
on-line real time data reduction algorithms
new wire material studies
new wiring systems for high granularities/ new end-plates / new materials
  GAS: 90% He – 10% iC4H10
  Radius 0.35 – 2.00 m
  Total thickness: 1.6% of X0 at 90o
2m track, 100 samples σ(dE/dx) = 4.5%
εcount = 80%
Slide © Anna Colaleo
Drift Chambers for FCC-ee / CEPC

## Slide 46
Straw tube components (for PANDA-STT
Self-supporting straw tubes with thin anode wire and an aluminised Mylar cathode wall offers a combination of short drift time, low mass, and high spatial resolution tracking by using long (a few meters) and small diameter (< 1 cm) straws, arranged in planar layers.
NA62 Straw station
COSY-TOF Straw tracker
 | TOF-STT [5] (COSY) | PANDA STT/FT (FAIR) | NA62 [3] (CERN-SPS) | COMET [6] (J-PARC) | COMET+ | COMET+ | SHiP [7] (CERN-SPS) | 
Mylar wall | 32 µm* | 27 µm* | 36 µm | 20 µm | 12 µm | 12 µm | 36 µm | 
Winding | helical, 2 strips glued |  | longitudinal ultrasonic welding |  |  |  |  | 
Manufacturer | Commercial (LAMINA, UK) |  | JINR, Dubna |  |  |  |  | 
Tube diam. | 10.0 mm | 10.0 mm | 9.8 mm | 9.8 mm | 5.0 mm |  | 20 mm | 
Cathode | Al (30 nm) | Al (100 nm) | Cu/Au (50/20nm) | Al (70nm) | Al (70nm) |  | Cu/Au (50/20nm) | 
Tube length | 1050 mm | 1400 mm | 2100 mm | 600 -1100 mm |  |  | 5000 mm | 
Straw no. | 2704 | 4224 / 12224 | 7168 |  |  |  | 16000 | 
In vacuum | yes | no | yes | yes | yes |  | yes | 
Status | Exp. finished (2009-2013) | Prod. ongoing, exp. in 2025 | Experiment ongoing | Production completed | In develop- ment |  | Planned | 
Specific R&D | Vacuum tracker | Low X/X0 solenoid tracker | Vacuum tracker | Thinnest wall vacuum tracker |  |  | Long straws in vacuum | 
Innovative straw detectors are foreseen at both future storage rings and fixed target facilities.
NA62 is the state-of-the-art straw tracker
New ultrasonic welding technique to close the straw and to keep them straight and withstand the vacuum pressure without breaking
rates up to 40 kHz/cm (500 kHz/straw), ageing resistance up to ∼ 1 C/cm/wire
material budget of a straw module ∼ 0.7% X/X0
1.2% X/X0, spatial resolution∼150 µm
Slide © Anna Colaleo
Inner/Central Tracking with PID: Straw Tubes
Table © Peter Wintz

## Slide 47
M. Ruan
arXiv: 2003.01116
ILC-TPC: Target requirement: point resolution 100 um in transverse plane and dE/dx resolution < 5% reached with all technologies (GEM, MM and GridPix)
If dE/dx combined with ToF using SiECAL, P < 10GeV region for pion-K separation covered
Track Distortions in ILC TPC @ 250 GeV (L~1034 cm-2), 3.8 T
beam-beam effects are dominant: primary ion density 1-5 ions/cm3 track distortions < 5 µm
- Gas amplification 103 distortions of 60 µm  gating device is needed
10.1016/j.nuclphysbps.2015.09.174
Exploit ILC bunch structure as 1 ms long bunch trains will arrive every 200 ms
Gating GEM gate opens 50 us before the 1st bunch and closes 50 us after the last bunch:
  Measured electron transparency >80 % (as in simulations) for ∆V ~ 5V
Slide © Anna Colaleo
Inner/Central Tracking with PID: TPC + MPGD

## Slide 48
  Single ionisation electrons are detected with high efficiency
  dE/dx by cluster counting
  Measuring IBF for Gridpix is a priority, expected 𝒪(1‰)
50 cm track length with ~ 3000 hits
each is electron from the primary ionisation
for track reconstruction, in case of curved tracks
Micromegas + GEM studies for CEPC / FCC-ee to minimize ion backflow
9000 Z ➙ qq’ events + Bhabha background estimation needed
HZ/WW/tt running Pad readout (MM + GEM)
Z pole running(@1036): primary ion density 1000 ions/cm3
 tracks distortions O(mm)  Pixelated readout  GridPix
CEPC/FCC: No bunch structure  continuous beam (cfr. ALICE)
The maximum possible information from a track is acquired:
Slide © Anna Colaleo
Inner/Central Tracking with PID: TPC + MPGD

## Slide 49
Studies done within CALICE collaboration:
AHCAL Scint+SiPM 3 x 3 cm2 granularity
DHCAL glass RPC 1 x 1 cm2 granularity
SDHCAL RPC/MICROMEGAS/RPWELL
1 x 1 cm2 granularity
high granularity ( = 50um, = 5ns) at low cost
Low pad multiplicity
radiation hard detector
good energy resolution, bkg rejection:
SDHCAL with RPC
New handle: Fast- timing
    If pico-second-time and energy information at each point along the track
    ⇒ 5D imaging reconstruction
    better assignment of deposit to PV timing
    Better construction of the shower
F. Simon
The Particle-flow approach
   1x1 cm2 pad: energy resolution in SDHCAL same as AHCAL with software compensation
Facilities: (ILC/C3, FCC-ee, CEPC, Muon collider, Hadron Physics).
Slide © Anna Colaleo
Hadron Calorimetry: Steel abs + RPC/MPGD

## Slide 50
ALICE TOF detector (160m2) achieved time res. ~ 60 ps)
New studies with MRPC with 20 gas gaps using a low-resistivity 400 μm-thick glass  down to 20 ps time resolution
Gaseous Detectors: Micromegas with Timing (RD51 Picosec Collaboration)
σ ~ 25 ps timing resolution (per track)
Multi-Gap Resistive Plate Chambers (MRPC):
Z.Liu
Slide © Anna Colaleo
Large Area Fast Timing Detectors
Achievable by reducing gas gap thickness (~100 μm)
Increased number of gaps for large-area uniformity
Rate capability up to 100 kHz/cm²
   Thinner and lower resistivity plates
Focus on identifying cost-effective materials
Precise mechanical stability and uniformity (≈1-10 μm)
Robust radiation-hard photocathodes
Stable high-gain operation and IBF optimization

## Slide 51
TPCs are commonly used in rare event searches.
Lens-like Effect: Density-driven magnification/demagnification.
Different Readouts: Charge, negative-ion, dual-phase, optical.
Typically, MPGD are used for the TPC amplification stage.
WIMP, DM & Neutrino Experiments
Nuclear Recoil Discrimination:
  Large Tons @ high pressure : Noble liquid (Ar, Xe) + gas (MPGD) amplification and readout.
Light element as target: low energy threshold and low radioactive background
  Ar o Ne mixture 1-10 bar with stable gain and without energy degradation
Direction of WIMP Flux
3D Reconstruction: 20 mbar - 1 bar pressure for accurate 3D tracking.
  Various Readout Methods: Ionization electron, negative ions, electron ionization and optically based readouts at atmospheric pressure (Cygnus)
Particle Trackers for Neutrino Oscillation NDs
Pressurized Argon-based TPCs: E.g., Dune ND at 10 bar.
‘TPC == single reconstruction-tool’
TPCs for:
neutrino-interaction
active targets for nuclear reactions
TPCs as reaction/decay chambers

## Slide 52
Future Perspectives on Gaseous Detectors Some examples from the Migdal & Cygnus Experiments
Invesigate Migdal effect (for DM-searches)
Cygnus Experiment for Directional DM-search
Slide Materials © Davide Pinci

## Slide 53
Collaboration type: Community-driven with the R&D environment: common infrastructures (labs, workshops), common R&D tools (software and electronics ), cross-disciplinary exchange
Scientific organization in Working Groups: provides a platform for sharing knowledge, expertise, and efforts, by playing a crucial role in identifying, guiding, and supporting strategic detector R&D directions, facilitating the establishment of joint projects between institutes.
Work Packages (WP): long-term project addressing strategic R&D goals, outlined in the updated European Strategy for Particle Physics with dedicated funding lines.
Common Projects (CP): short-term blue-sky R&D or common tool development with limited time and resources, supported by the Collaboration Common funds.
R&D PROJECTS
R&D FRAMEWORK
Technology interests in DRD1
(based on initial Survey)
*
Slide © Anna Colaleo
Future Perspectives on Gaseous Detectors 6. Implementation of the Detector R&D (DRD1) collaboration

## Slide 54
  Group together institutes research interests around Applications with a focus on a specific task(s) devoted to a specific challenge (Detector R&D theme ), typically related to specific Detector Technologies and to the development of specific tool or infrastructure
WP1: trackers/hodoscopes
WP2: Drift Chambers
WP3: Straw Chambers
WP4: Tracking TPCs
WP5: Calorimetry
WP6: Photon detectors
WP7: Timing detectors
WP8: Reaction/Decay TPCs
Currently implemented WPs
Additional WP on beyond fundamental physics also considered
*
Slide © Anna Colaleo
Implementation of DRD1 Collaboration Strategic R&D => Work Packages

## Slide 55: DRD1 Work Package Example for Photon Detectors (WP6)
Challenges for the photon detectors
Preserving Photocathode Efficiency:
  Suppressing ion backflow
  Developing more robust photoconverters
Front-End Electronics (FEE):
  Development of very low noise FEE
  Large dynamic range FEE
Detector Performance Improvement:
  Enhanced spatial resolution
  Improved time resolution
  Fast charge collection for maximum rate capability
TRD System Enhancement:
  Better separation between transition radiation and ionization process in TRD systems
Area of application: nuclear physics, hadron physics, future ee, and eA machines. Timeline: >2030
WPs are currently in preparation: interested institutes are drafting confidential documents with detailed information about milestones, deliverables over the years and available/needed resources for the R&D program accomplishment.
Slide © Anna Colaleo
NEW Slide

## Slide 56
Implementation of DRD1 Collaboration Common Tools & Infrastructure => Working Groups
Slide © Beatrice Mandelli
e.g. Working Group 3 Gas & Material studies

## Slide 57
Implementation of DRD1 Collaboration Common Tools & Infrastructure => Working Groups
Slide © Piet Verwilligen
e.g. Working Group 4 Simulation, Modelling & SW

## Slide 58
Implementation of DRD1 Collaboration Common Tools & Infrastructure => Working Groups
Slide © Y.Tsipolitos & E.Oliveri
e.g. Working Group 7 Common Test Infrastructure
30m
30 m | 3-4 x year | GeV/c
107 particles/spill ~1 spill/minute |  | 
30 m | 3-4 x year | 
107 particles/spill ~1 spill/minute |  | 
12 m | 137 Cs | 14 TBq
662keV
12 m

## Slide 59
Large community of 161 institutes, 700 members, 33 countries based on previous RD51 collaboration
https://drd1.web.cern.ch
https://cds.cern.ch/record/2885937
DRD1 Collaboration in Action 2024 - …
First School for PhD Students
2023: 2 community meetings
2024: 3 collaboration meetings, Several WG meetings, WP meetings, CB meetings, …

## Slide 60
Physics discoveries are mostly Tool-Driven
Gaseous detectors are around for > 100 years
  They have undergone many improvements / revolutions
  Are relatively “easy” to build and to modify
  Simulation tools have been developed in the past
    Are freely available to you to play around with
    However are not complete and require you to develop further
    Remember: with Simulation you prove you understand your Results
Understanding State-of-the-Art detectors allows you to propose modifications to improve them further
The DRD1 collaboration groups GD experts worldwide
  To share new developments, to develop new tools, to test together
  To work together on the development of Detectors of the future
  To create a friendly atmosphere where one can learn and teach
  We are waiting for you to join and push the limits of instrumentation
Conclusions, final Thoughts, … and Questions

## Slide 61
“If I have seen further it is by standing on the shoulders of GIANTS” – Isaac Newton
  I have not seen further, but I still thank all GIANTS that have introduced me to the field and of who I have recycled slides, materials, ideas ….
Recommended REFERENCE books:
Recommended LECTURE series:
  Werner Riegler – Signals in Detectors - 2019 - https://indico.cern.ch/event/843083/
  Rob Veenhof – MPGDs - 2017 - https://indico.cern.ch/event/676702
Acknowledgements & References

## Slide 62
Interesting SEMINARS:
  CERN Detector Seminar series: https://indico.cern.ch/category/84/
A non-exhaustive selection:
  S.Levorato – Technical Challenges for the new T2K high-angle TPCs https://indico.cern.ch/event/1431318/
  M.Bianco – The GEM Detectors within the CMS Experiment https://indico.cern.ch/event/1175363/
  E. Oliveri – Charged particle timing in the sub-50ps regime with Micromegas https://indico.cern.ch/event/667607/
  F. Sauli – GEM Detectors 20 years of Development and Applications https://indico.cern.ch/event/574840/
  E. Nappi – Trends and Perspectives of RICH detectors in High Energy Physics https://indico.cern.ch/event/178123/
  C. Garabatos – The ALICE TPC Upgrade with GEMs https://indico.cern.ch/event/275624/
  C. Williams – ALICE Time of Flight Detectors https://indico.cern.ch/event/149006/
  S.Dalla Torre – Novel Photon Detectors based on Thick GEM technology for COMPASS https://indico.cern.ch/event/145264/
DRD1 Gaseous Detector School: https://indico.cern.ch/category/18473/
Acknowledgements & References

## Slide 63: Future Perspectives on Gaseous Detectors and DRD1 R&D Program
Back-up slides
Picture © Luigi Filici CCBY License

## Slide 64
Front view of the CMS detector barrel part
ex. TF1 Muon System
Performance targets and main drivers from facilities
Detector R&D Themes (DRDTs)
Needs/benefits for physics reach
Ex. Muon system
DRDT 1.1 - Improve time and spatial resolution for gaseous detectors with longterm stability
DRDT 1.2 - Achieve tracking in gaseous detectors with dE/dx and dN/dx capability in large volumes with very low material budget and different read-out schemes
DRDT 1.3 - Develop environmentally friendly gaseous detectors for very large areas with high-rate capability
DRTD 1.4 - Achieve high sensitivity in both low and high-pressure TPCs
ECFA Detector R&D Roadmap content Example for Task Force 1 (TF1) Gaseous Detectors
Slide © Anna Colaleo

## Slide 65: ECFA Detector R&D Roadmap Summary of R&D Challenges for different Applications
Slide © Anna Colaleo

## Slide 66: DRD1 Approval Process & Review
Scientific and Resource Reporting and Review by a Detector Research and Development Committee (DRDC)
Assisted by the ECFA Detector Panel (EDP): the scope, R&D goals, and milestones should be vetted against the vision encapsulated in the Roadmap
Funding Agency involvement via a dedicated Resources Review Board (~once every two years)
Yearly follow-up by DRDC report to SPC (CERN Scientific Policy Committee)  Council
As projects develop, some aspects should be expected to transition into approved experiment- specific R&D (outside the DRD programme)
In addition, as stated in the General recommendations (GSR7) funding possibilities for “Blue-sky” R&D should be foreseen
Slide © Anna Colaleo