## Slide 1: PIONEER: A next-generation rare pion decay experiment
David Hertzog / University of Washington
Some of us at a recent meeting in TRIUMF
Physics Goals
Experimental Concept and Innovative Solutions
Technical Progress and Status
FCCP 2025
Notes: Abstract: The fundamental principle of Flavor Universality is a centerpiece of the Standard Model of Particle Physics. PIONEER is a new experiment set to challenge this principle by studying the rarest decays of the charged pion. With this new apparatus, we aim to improve the rare pion decay measurements up to 15-fold over the current ones and probe the Standard Model at energy scales beyond the reach of colliders. Our experiment design benefits from past-generation experiments and employs emergent technologies in tracking and calorimetry. In this talk, I will discuss the physics case of the experiment, review its conceptual design and present the ongoing R&D effort toward building the detector for the first phase of the project. I will also describe the additional physics goals, which include exotic searches and, in a slightly reconfigured setup, a measurement of pion beta decay to determine Vud in a theoretically clean manner.

## Slide 2: Next Generation Muon (g-2) Goal dam ~ 140 ppb
David Hertzog, University of Washington
for the E989 Muon (g-2) Collaboration
FCCP2015 Flavor Changing and Conserving Processes
FCCP in 2015 !! It all turned out quite well

## Slide 3: Lepton Flavor Universality The weak interaction bare gauge couplings among leptons are the same e / m / t
The weak-interaction “strength” is associated with the Fermi Constant, GF
Muon decay provides the most precise measurement
  Technically it determines Gm, which is usually just called GF … because we believe in LFU
GF(MuLan) = 1.166 378 7(6) x 10-5 GeV-2 (0.5 ppm)
PRL 106, 041803 (2011)
Phys. Rev. D 87, 052003 (2013)
Questioning the validity of what others took to be true…

## Slide 4: Physics Case I: Precision Test of Lepton Flavor Universality
Gauge coupling the same for all flavors
  PIONEER will test this fundamental principle to 0.01%
(0.18%)
(0.01%)
PIENU at TRIUMF
Cirigliano & Rosell
Pion decay ratio
  provides unique opportunity
  The SM prediction is very precise!
    15x more so than experiment
    Strong helicity suppression
LFU
‘Helicity suppression’
term: ~2.3 x10-5
Phase space term: ~ 5.5
Fully computed at NLO
O(10-4) uncertainties at NNLO
Notes: Anderson and Neddermeyer, 1936, nearly 90 yrs

## Slide 5: The p  e n decay was first discovered in 1958, but these days, one can even make a rough measure as a “Student Exercise”
Univ. Heidelberg, Mainz, and ETH Zurich Practicum at PSI
September 2025

## Slide 6: In our case, we aim for 10-4 precision on this rare ~10-4 branch
  Most sensitive test of LFU
  Many BSM scenarios exist, SMEFT
    coupling, 4-fermion operators
  sensitive to very high mass scales
    also T and S currents

## Slide 7: Physics Case II: Testing CKM Unitarity
Cabibbo Anomaly: 2-3 discrepancy
  Vud and Unitarity,
  Vus measurements disagree
Tensions in the first row CKM unitarity test
(0.27%)
(0.27%)
0+→0+ (0.030%)
Neutron (0.050%)
Unitarity
1σ ellipse (PDG)
Cirigliano et al. PLB 838 (2023) 137748
A big improvement needed to be competitive
PiBeta doi.org/10.1103/PhysRevLett.93.181803
Pion beta decay
  provides theoretical cleanest determination of as dominant uncertainties from hadronic and nuclear structure
These are actually smaller

## Slide 8: PiBeta concept with PIONEER’s LYSO calorimeter option
PIONEER sensitivity projection
  3 and 6-fold improved measurement (Phase II,III)
  Simplest beta decay process in theoretical pristine system
  Competitive probe with completely different error budget
Method
  two back-to-back gammas
  high beam rate required: 107 @ 85 MeV/c
Phase III goal
PIONEER Phase II
PIONEER Phase III
PDG24

## Slide 9: Physics Case III: Search for Weakly Coupled Physics:
Goal of PIONEER
Increase reach of the global search program for feeble interactions (ie ALPs, heavy neutrinos, …) by an order of magnitude in the 10—100 MeV range
Physical Review D 97(7) 072012 (2018)
Physics Letters B 798 134980 (2019)​
Phys. Rev. D 102, 012001 (2020)​
Phys. Rev. D 101, 052014 (2020)​
Phys. Rev. D 103, 052006 (2021)​
Many signatures explored by TRIUMF PIENU
PIONEER will collect an unprecedented set of pion decays (surpassing existing sample by at least a factor 10)
Excellent opportunity to search for feeble interactions producing new particles in the pion decay
Will appear as a modification of the energy spectrum lineshape in the calorimeter spectra (bump or shape)
W. Altmannshofer, J. Dror, and S. Gori
Phys. Rev. Lett. 130, 241801
Recent development with Lepto-philic axion-like particles

## Slide 10
PSI Approved Proposal Jan. 2022
Has become a high-priority experiment at PSI
Since the proposal, we have been very actively designing and simulating the experiment
I will share some progress

## Slide 11: Pion decay (at rest) related to measuring
11
Reminders
tp+ = 26 ns 140 MeV
tm+ = 2197 ns, 106 MeV
53 MeV
70 MeV
99.99%
1.23e-4
p+ stop at t =0

## Slide 12: The ideal and realistic e+ energy spectrum:
Realistic e+ spectrum in the time window (5 – 35) ns after p stop
The tail: 0.5% systematic correction
Muon decays in flight can boost positrons to the high energy region: 0.1% correction
Some muon stops confused as pions: 0.1% - 0.2% correction
Pileup from old muons: must mitigate
Define and count events above and below threshold
Finite resolution and incomplete energy collection in the calorimeter result in a tail

## Slide 13: Why so challenging?
Identify the 1 in 104 p->e decays, with a misidentification factor below 1 part in 104
While the decay times and positron energies are different, the physics processes in the detectors are energy dependent
  scattering, annihilation, Bhabha probabilities
Need high statistics,
  Large and uniform acceptance
  High beam rate (pileup)
Strategy
  Innovative imaging target and high-resolution, fast calorimeter
  MC – data comparisons in great detail
Analyses are being developed in advance with highly realistic simulation framework
  Classic “Rule Based”
  Advanced Machine Learning techniques

## Slide 14
@TRIUMF
@PSI
0.8p
NaI(Tl)
19 X0
CsI
3p CsI
12 X0
Calorimeter depth too small to resolve tail
Uneven crystal performance
NaI: excellent resolution, but slow so rate limited
Shower leakage in single crystal depends on angle
Small overall acceptance
Two previous-generation Pion Decay Experiments: PIENU and PEN/PIBETA
Limitations and lessons learned to design “next-gen”

## Slide 15: In any analysis, one must determine from a Master Formula:
= Counts in the “high bin” … above ~56 MeV
= Counts in the “low bin” (Michel decays) … below ~56 MeV
= p+  e+ events that deposit less than 56 MeV in the Calo
= the acceptance ratio (vs q). Quite critical because the positron energies from p+  e+ and p+  m  e+ events differ significantly (especially at the low end)
All vs polar angle q

## Slide 16: PIONEER experimental strategy:
65 MeV/c DC positive pion beam @ 300 kHz
Stop in a segmented imaging target
Measure positron energies from p-> e and p->m->e with a high-resolution calorimeter
Record “region of interest” both before and after the stop
Generic diagram

## Slide 17: Approved to use the high-rate pion piE5 beam at PSI
piE5 @ PSI - World’s Brightest Stopped Pion Beam
  Now: Fundamental muon physics: MEG II, Mu3e
Our 2023 measurements of existing beam
  Rate: 300k π/s stopped in ATAR: ok at 65 MeV/c
  Momentum bite: ∆p/p <2%: marginal
  Spot size: <2 cm FWHM: not yet achieved
  µ,e less than 10% π: needs second focus extension
X
Y
A challenging work in progress to design these elements
Pions at 65 MeV/c have
  b = 0.42
  Decay length (cbgt) L = 3.6 m
m
p,m,e
p
e
0 1 2 3 4 5 m
18% left
Pion survival fraction from Separator to Target

## Slide 18: Key development for PIONEER: LGAD-based Active TARget
Highly segmented and instrumented.
48 planes of 20 mm x 200 m x 120 m strips
4800 channels
ATAR provides 5D track information
3D position (x,y,z).
Time: 100 ps single hit / few ns pulse pair resolution
Energy in each strip: MIPs to heavily ionizing pion and muon tracks distinguished
100 Strips
48 Layers

## Slide 19: (TI)* Low Gain Avalanche Diodes (LGAD)
*trench-isolated to avoids cross talk to neighboring strips
Silicon Diodes: p-n junction separated by an intrinsic layer (undoped)
LGADs: additional highly doped layer generates a very high electric field → avalanche effect
Signal amplification allows for thin sensors and very good timing resolution
Gain mechanism can saturate for large energy deposit and introduces an angle dependency. We are studying this carefully
ATAR Demonstrator: 16-planes to be tested in 2026 with TI-LGAD sensors from FBK, FAST3 amplifiers, and SAMPIC 6 GSPS digitizers

## Slide 20: The ATAR has a deep connection to Italy !
TI LGADs
FAST3 amplifier

## Slide 21: Pion processes in ATAR
Rπ (65 MeV/c) ~ 4 mm, (stops in center region)
Rμ (4.1 MeV) ~ 0.8 mm
6.6 mm
* Represents Bragg peak with large energy deposit
Example Event Display
Marker size ∝ Edep
X
y
z
z

## Slide 22: How these processes will appear in ATAR
Rπ (65 MeV/c) ~ 4 mm, (stops in center region)
Rμ (4.1 MeV) ~ 0.8 mm
“MIP”
dE/dx ~ 50 keV / 120 um-thick sensor
DTAR/Trig
e+ “MIP”
e+ “MIP”
Bragg peak
Bragg peak

## Slide 23: Minimizing the low-side tail is part of Calorimeter design
#X0, depth containment
RM: lateral containment
PIENU single large crystal
(their data & simulation)
2 RM
2 RM
12 X0 (like PEN)

## Slide 24: What calorimeter might work in [0 – 70] MeV range?
Common features
  High light yield (>30,000 g/MeV)
  “Fast” 40 ns decay time
  Both aim at resolution <2%
  Both aim at good timing
Significant differences (LYSO/LXe)
  Segmented  311 PMTs ~420 nm
  Single volume  1650 VUV sensors
  Density (see scaled pics)
  Data load (LXe >100 higher)
  LYSO is slightly radioactive
The original idea
(TRIUMF and Japan exploring)
Fid. Volume
Since then …
(SJTU, ETH Zurich, UW exploring)

## Slide 25: LYSO R&D very promising …
NaI(Tl)
LYSO
Lutetium–yttrium oxyorthosilicate (LYSO):
By weight: 73% Lutetium, 18% Oxygen, 6% Silicon, ~0% Cerium (dopant), 3% Yttrium
X0 = 1.14 cm , RM = 2.07 cm
Decay time = 40 ns
Light yield 30,000 γ/MeV
λpeak 420 nm -> conventional PMTs
Radioactive (< 1 MeV constant rumble)
Non hygroscopic, negligible temperature dependence, radiation hard
Tested 10-array
  Nucl.Instrum.Meth.A 1075 (2025), 170320
goal
achieved
1.52% @ 70 MeV
LYSO
Tested 6 full-sized, tapered crystals (August, 2025)
I am sharing work our group is helping to lead on LYSO but PIONEER has not finalic will share some progress we’ve made with LYSO here (but decision is not made!)

## Slide 26: Connection of Calo and ATAR hardware to main systematic: The Tail Correction
events with energy below occur ~ () of the time
events with energy below occur 99.9% of the time
Measure to 1%
Suppress by 107
Signal event:
Highly ionizing pion stop
MIP positron
Defined by pion lifetime alone
Background
Highly ionizing p and m stops
MIP positron
Defined by both muon and pion lifetimes
Timing and energy alone give 104 suppression

## Slide 27: Pivot to our developing analysis methods: 3 essential tasks

## Slide 28: Basic steps involve finding the tracklets
For most events, time separation is clear and events “behave”
p enters  t0
p  m at t1
m  e at t2
time
t0
t1
t2

## Slide 29: Including the more challenging ones for topological reasons or owing to important sub-dominant processes
t𝜋
t𝜇
te
Do these tracklets all belong to the same sequence?
What about those old muon decays?
In this approach, we look for
Time grouped hits
Patterns to match
Energy deposits vs expected
Final directional fits to establish q/f of positron
And do our best to fit and classify
In a classic “Rules-based approach”

## Slide 30: Advanced AI/ML techniques that adapt to the event topologies based on extensive training
Which particle(s) is responsible for this track?
Neural network without attention:
Here,
Fixed sets of questions about event
Likely gives same time & weight to each statement.
But is capable of picking up on details requiring understanding of many things at once
→
This approach struggles with subtle conclusions because of its inflexibility in asking questions and weighting the relevance of different testimonies
Omar Beesley (UW)
“Transformer” based network
Here:
Adapts questions based on the context of the witness (hits, etc) and what is learned from other hits, etc.
Weighs the relevance of information based on previous experiences
Picks up on subtle information requiring details from aspects of the event
Dynamic weighting: identifying Bragg peaks, grouping time-coincident hits, and leveraging 4D detector data to infer 5D trajectories. Unlike traditional models that rely on distribution moments and outliers, transformers explicitly learn relationships between hits

## Slide 31: An example of how a Rules based approach can differ from our AI/ML approach in the prediction of the Pion stop location in the ATAR for both Pienu and Michel events
Omar Beesley (UW)
The muon track is incorrectly appended to the pion track so the pion stop is wrong
The AI model, as figured out how not to make this error

## Slide 32: Status of PIONEER: A next-gen campaign
Fundamental R&D on LGADs and Calorimeters
2026 Test beam desires
  piE5 Phase Space
  16-Plan ATAR Demonstrator
  Large LXe prototype (if funding is realized)
Significant work ongoing on electronics, triggering, digitizers, & DAQ
PSI shuts down in 2027 and much of 2028.
We are seeking Euro collaborating groups to join this campaign and take leadership in any of these areas I’ve mentioned

## Slide 33: (some from the) PIONEER Collaboration
  A next generation rare pion decay experiment

## Slide 34: The types of events we will encounter … (I am making it look easy here; it’s not)
Signatures
  DAR decay at rest
  DIF decay in flight
5D tracker will provide
  (x,y,z,t,E)
We have launched a major effort to develop reconstruction programs to identify these channels
  “Conventional” track finding / pattern finding / track fitting
  Machine learning, where we help guide the programs through the different choices

## Slide 35: Rare Pion Decays: History
The branching ratio is so small that for a while the process was excluded
, meaning ~1 out of every 104 pions decay to an electron
Lokanathan and Steinberger (1955):
Range telescope at Columbia Nevis cyclotron: (90% CL)
Anderson and Lattes (1957):
Magnetic spectrometer at Chicago cyclotron: (90% CL)
 Causing a lot of confusion…

## Slide 36: Rare Pion Decays: History
Discovery… CERN in early years
CERN circa 1958
~ 40 events

## Slide 37: Processes that create the energy spectrum & ATAR identification capability
Rπ (65 MeV/c) ~ 4 mm,
Rμ (4.1 MeV) ~ 0.8 mm
Critical component, develop based on emergent 5D tracker technology (x, y, z, t, E)
  provide unprecedented topological info on pion decay vertex
  suppress by 6-orders of magnitude to measure tail
Specifications
  5-D tracking
    20x20x6 mm3
    x,y 200 μm, z 120 μm
    t ~ 200 ps, pulse pair 2 ns
PIONEER specific
  5000 channels
  dynamic range several 100
      MIPS 40 keV – μ (4000 keV)
  minimal cross talk
  minimal dead material
(Not yet adding in the effect from pileup from beam and old muons)

## Slide 38: Physics Case III: Search for Weakly Coupled Physics: Heavy Neutrinos, Dark Sector
  highly suppressed in SM
  but not for weakly coupled “massive” particle
2-body decays
  peak searches in
3-body decays: ,
X could be a scalar, axion like particle, vector, …
possible decay modes: , ,
PIENU also searched for
  , ,
  PIONEER: typical 10-fold improvement in 10-100 MeV range expected
Altmannshofer, Dror, Gori PRL 130, 241801 (2023)
Altmannshofer, Giffin, Gori, Jackson, Luong
In preparation
Preliminary

## Slide 39: Energy resolution with “bench” sources on single crystals
Na22
Co-60
Na-24*
  1.38, 2.76 MeV
*15 hr half life made by bombarding 18 MeV deuterons on Al button
(2g sum)
(2g sum)
(Resolution is sigma of a Gaussian)
(2g sum)
2g implies coincidences of lower energy lines
(this is why they are used in most PET scanners now)
511 keV
2.76 MeV
1.17 & 1.33 MeV
LYSO
NaI
PMT

## Slide 40: Energy and timing resolution of a 10-array
Crystal to crystal in beam, same event
LED flashes all crystals; DT between them
Timing
Energy
@CENPA, with improved PMT bases
goal
achieved
1.52% @ 70 MeV
Measurements of a LYSO crystal array from threshold to 100 MeV
Nucl.Instrum.Meth.A 1075 (2025), 170320

## Slide 41: Design of a Tapered Array for PIONEER
Characteristics of interest
311 19 X0 (217 mm) length crystals w/ 8 different shapes
Stainless mount + spacer
LYSO
PMTs + compression
Cyanoacrylate used to glue crystals to stainless

## Slide 42: Test beam 4 weeks ago…
LYSO
NaI(Tl)
1.97% energy resolution measured at 70 MeV
“Online” very preliminary results

## Slide 43: Then, a subset of events with NO p->m->e should reveal lineshape
2 RM
2 RM

## Slide 44: Pion Beta Decay … historical
Interestingly, in the same PRL issue as the Re/m measurement, the next article is:
(0.56%)
PiBeta doi.org/10.1103/PhysRevLett.93.181803
PiBeta Experiment at PSI
Two back-to-back photons Very low energy positron