## Slide 1
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
First characterization of the gas tracker of the new focal plane detector of the MAGNEX spectrometer for the NUMEN project
DeSyT2025 - Feb. 24-26, 2025
Antonino Pitronaci
February 24th - 26th, 2025
UniCT DFA ”E. Majorana” INFN - Laboratori Nazionali del Sud
Tutor: Chiar.mo Prof. F. Cappuzzello
Co-Tutors: Dr. M. Cavallaro
Dr. D. Carbone
DeSyT2025 - Feb. 24-26, 2025

## Slide 2: NUMEN: NUclear Matrix Elements for Neutrinoless double-beta decay
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Objectives: getting data-driven information on neutrinoless double-beta (0νββ) Nuclear Matrix Elements (NMEs);
Methods: measurements of Heavy-Ion induced Double Charge Exchange reaction cross-section;
Experimental setup @INFN-LNS:
  K800 Superconducting Cyclotron (CS);
  MAGNEX large acceptance magnetic spectrometer;
International Project Network:
NUMEN Collaboration: 34 International Research Institutes - 105 Researchers
DeSyT2025 - Feb. 24-26, 2025 1/15

## Slide 3: The key role of Heavy-Ion induced Double Charge Exchange reactions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Neutrinoless double-beta decay
Double Charge Exchange reaction
Common properties:
same mother/daughter nuclei;
short-range Fermi, Gamow-Teller and rank-2 tensor operators;
DCE-reactions advantages:
No Qvalue dependence;
higher yield due to the nuclear interaction;
Details on HI-DCE reactions: - F. Cappuzzello et al. PPNP 128 (2023), 103999
DeSyT2025 - Feb. 24-26, 2025 2/15

## Slide 4: MAGNEX: a large acceptance magnetic spectrometer
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Technological challenges
high tracking performances:
(FWHM)
(FWHM) (FWHM)
high identification power:
Bearing unprecedented high-intensity beams (1013 pps at the target);
Radiation hardness;
How to handle with aberrations?
Magnetic field mapping: MAGNEX peculiarity;
COSY infinity: algebraic methods-based software, allowing to solve the equation of the motion at high order to obtain the energy(ies) and angles at the target point
- D. Torresi et al. NIMA 989 (164918), 2021
Technological challenges: - F. Cappuzzello et al. IJMPA 36(2130018) 2021

## Slide 5: MAGNEX: a large acceptance magnetic spectrometer
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Technological challenges
high tracking performances:
(FWHM)
(FWHM) (FWHM)
high identification power:
Bearing unprecedented high-intensity beams (1013 pps at the target);
Radiation hardness;
How to handle with aberrations?
Magnetic field mapping: MAGNEX peculiarity;
COSY infinity: algebraic methods-based software, allowing to solve the equation of the motion at high order to obtain the energy(ies) and angles at the target point
- D. Torresi et al. NIMA 989 (164918), 2021
Technological challenges: - F. Cappuzzello et al. IJMPA 36(2130018) 2021

## Slide 6: The new focal Plane Detector
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Gas tracker:
  gas at low pressure: (10-30) mbar;
  based on M-THGEM;
  high tracking resolution & rate robustness;
PID-Wall (details: Dr. C. Lombardo talk)
  ∆E-stage: SiC detector;
  E-stage: CsI(Tl) scintillator;
  high radiation hardness to bear 1013ions/cm2
DeSyT2025 - Feb. 24-26, 2025 4//15
Track-reconstruction & PID
New FPD details: - F. Cappuzzello et al. IJMPA 36(2130018) 2021

## Slide 7: The gas tracker prototype
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
DeSyT2025 - Feb. 24-26, 2025 5/15
M-THGEM advantages:
High achievable gain, stability, robustness, ideal for heavy-ions detection;
M-THGEMs details: - I. Ciraldo et al. NIMA 1048 (167893), 2023
Vertical section of the tracker & electric field lines within a 3-THGEM obtained with COMSOL.

## Slide 8: The experimental setup and methods for the electric characterization
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental setup
Probe: α by 241Am radioactive α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Tool: pico® by INFN-Sez. Napoli
DeSyT2025 - feb. 24-25, 2025 8/13
Experimental methods
Measurements of currents:
      - Shutter closed: dark currents;
            - Shutter open: charge carriers;
DeSyT2025 - Feb. 24-26, 2025 6/15
track

## Slide 9: The experimental setup and methods for the electric characterization
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
DeSyT2025 - feb. 24-25, 2025 9/13
Anodic dark current(s)
electron current
DeSyT2025 - Feb. 24-26, 2025 7/15
Experimental setup
Probe: α by 241Am radioactive α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Tool: pico® by INFN-Sez. Napoli
Experimental methods
Measurements of currents:
      - Shutter closed: dark currents;
            - Shutter open: charge carriers;

## Slide 10: I-V characterizations
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental methods
DeSyT2025 - Feb. 24-26, 2025 8/15
  Measurements performed varying:
  - ;
  - ;
Observations:
- follows an exponential trend;
- saturation of up to 800 V;

## Slide 11: On the gas tracker properties: the Gain and the Ion Backflow
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Antonino Pitronaci
Gain: electron-amplification factor
IBF: fraction of the produced ions reaching the cathode
Consistent with NUMEN requirements!
DeSyT2025 - Feb. 24-26, 2025 9/15

## Slide 12: First coupling of the gas tracker prototype and a SiC-detector
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental setup
Probe: collimated α by 241Am α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Experimental methods
Antonino Pitronaci
DeSyT2025 - Feb. 24-26, 2025 10/15
Track measurements in correlation:
  distribution;
  distribution;
Track measurements in coincidence with SiC;
track

## Slide 13: First coupling of the gas tracker prototype and a SiC-detector
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental setup
Probe: collimated α by 241Am α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Experimental methods
Antonino Pitronaci
DeSyT2025 - Feb. 24-26, 2025 11/15
    Centre of gravity algorithm:
Track measurements in correlation:
  distribution;
  distribution;
Track measurements in coincidence with SiC;

## Slide 14: First coupling of the gas tracker prototype and a SiC-detector
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental setup
Probe: collimated α by 241Am α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Experimental methods
Antonino Pitronaci
DeSyT2025 - Feb. 24-26, 2025 12/15
Track measurements in correlation:
  distribution;
  distribution;
Track measurements in coincidence with SiC:
  Goals: measurements of ;

## Slide 15: First coupling of the gas tracker prototype and a SiC-detector
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Experimental setup
Probe: collimated α by 241Am α-source;
Working regime: i-C4H10 @ [10-30] mbar;
Experimental methods
Antonino Pitronaci
DeSyT2025 - Feb. 24-26, 2025 13/15
Track measurements in correlation:
  distribution;
  distribution;
Track measurements in coincidence with SiC:
  Goals: measurements of ;

## Slide 16: The experiment IRRAD4 @IFUSP – University of São Paulo (BR)
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
In-beam characterization of the tracker:
Position and angular resolutions;
Tracker performances as a function of the angle wrt incident ion beam;
Tracker response to the beam rate;
Experimental setup:
Pelletron beams:
  and ;
Safiira setup:
  Beam spot: 300 m;
  Angular divergency: 0.2° FWHM
Analysis ongoing!
Conclusions

## Slide 17: Conclusions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
I-V characterizations with particles:
  exponential trend of ;
  saturation of ;

## Slide 18: Conclusions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
I-V characterizations with particles:
  exponential trend of ;
  saturation of ;
  Gain and IBF;

## Slide 19: Conclusions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
I-V characterizations with particles:
  exponential trend of ;
  saturation of ;
  Gain and IBF;
Consistent with NUMEN requirements!

## Slide 20: Conclusions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
I-V characterizations with particles:
  exponential trend of ;
  saturation of ;
  Gain and IBF;
First coupling gas tracker prototype and SiC-detector:
  Tracking performances:
    Goals: measurements of ;
    Angles compatible with setup geometry;

## Slide 21: Conclusions
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
I-V characterizations with particles:
  exponential trend of
  saturation of ;
  Gain and IBF;
First coupling gas tracker prototype and SiC-detector:
  Tracking performances:
    Goals: measurements of ;
    Angles compatible with setup geometry;
First in-beam test: IRRAD4 @IFUSP:
  Position and angular resolutions;
  Tracker performances as a function of the angle wrt incident ion beam;
  Tracker response to the beam rate;
Analysis ongoing!

## Slide 22
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Thanks for your kind attention!

## Slide 23
The new FPD of MAGNEX: first results
Antonino Pitronaci
Preliminary concepts
The gas tracker prototype
Electric characterization
First coupling: gas tracker and SiC-detector
IRRAD4 @IFUSP
Conclusions
Backup slide: scheme of connesctions for the tracker and SiC coupling