## Slide 1
28 GHz ECRIS results and development at RIKEN
T. Nagatomo
on behalf of Ion Source Team, RIKEN Nishina Center

## Slide 2
RIBF
@ RIKEN Nishina Center
He, 18O, 48Ca, 70Zn, 78Kr, 124Xe, 238U
Typical beams
345 MeV/u 70Zn 820 pnA
345 MeV/u 238U 120 pnA
RIBF
Super Heavy Element Synthesis (SHE)
R28G-S
R28G-K
For RIBF

## Slide 3
345 MeV/u
238U86+ 120 pnA
on Target
CS1
CS2
CS1: U34+ → U64+ 20 %
CS2: U64+ → U86+ 25 %
Charge Stripping (CS)
3.2 keV/u
238U35+ ~ 3000 pnA
from ECRIS(~110 μA)
Current Performance of RIBF
+ Stable beam for ~1 month
As a routine supply
R28G-S

## Slide 4
Production of intense V ion beam for SHE (Z=119)
Beam intensity for Super Heavy Element Synthesis (SHE)
3.5 keV/u
51V13+ > 11,000 pnA
from ECRIS(~150 μA)
+ Stable beam for > 1 month
As a routine supply
R28G-K

## Slide 5
RIKEN 28-GHz ECRIS
18 GHz Klystron (1.5 kW)
or TWTA (0.7 kW)
Specsifications | Unit | R28G-S/K | SECRALII | VENUS | FECR
Frequency | GHz | 28 +18 | 28 | 28+18 | 45 + 28
RF power | kW | 10 | 10 | 10 | 20+10
Vext | kV | 22 | 25 | 25 (FRIB) | 50
Chamber ID | mm | Φ150 | Φ125 | Φ150 | >Φ140
Warmbore ID | mm | Φ172 | Φ142 |  | Φ165
Mirror fields | T | 3.8/2.3 | 3.7/2.2 | 4.0/3.0 | ≥6.4/3.2
Brad (@ r) | T, @ mm | 2 @ 75 | ∼2.0 @ 63 | 2 | 3.8 @ 75
Mirror length | mm | 525 | 420 | 500 | ∼500
Conductor material | - | NbTi | NbTi | NbTi | Nb3Sn
Cooling capacity | W @ 4.2 K | 8 | >5 | 4∼5 | >10.0
R28G-S:
RIKEN 28GHz SC ECRIS for RILAC II (RIBF)
R28G-K:
RIKEN 28GHz SC ECRIS for RILAC (SHE)
28 GHz Gyrotron ( > 8 kW @ DC break)
＋

## Slide 6
Microwave Injection and Metal Evaporation Oven
The end face (cross section) of the waveguide is the flange face of the plasma chamber.
→ No special modifications (e.g. horn shaped)
28 GHz
18 GHz

## Slide 7
Crucible (High Temperature Oven)
Vanadium powder
Ceramic crucible
(Y2O3)
W crucible
To avoid the chemical reaction between the crucible and vanadium, we used theY2O3 inner crucible.
Calculated (line) and Obtained temperature (triangles) of the oven using IR camera as a function of the heating power
J. Ohnishi et al, ECRIS2018
Temperature (℃)
2500
2000
1500
1000
500
0

## Slide 8
Consumption rate of V and Ti ( High temperature oven)
The consumption rate increases exponentially with increasing the oven power. The consumption rate of Ti is much higher than that for V. It is due to the difference in their vapor pressure.
Melting point of Ti: ~ 1941 K
Melting point of V : ~ 2183 K
J. Ohnishi et al, ECRIS2018, Catania, Italy, WEB4
8
6
4
2
0
Consumption Rate (mg/h)
dM (μg/cm2/h)

## Slide 9
To provide
more Intense Metal beam …

## Slide 10
Maximized Beam intensity of V13+ as a function of microwave power and neutral gas pressure
V13+
1.96kW
1.28kW
2.95kW
V13+
V. + N2

## Slide 11
Right figure shows the charge state distribution of multi-charged V ion at 3.5 kW. We observed that the beam intensity of V13+ was about 1 mA. It should be stressed that the beam intensity of multicharged N ions is remarkably lower than those of V ions compared to the charge state distributions at lower microwave power (1.25 kW, left figure), even the gas pressure at 3.5 kW was significantly higher than that for lower power.
RF power =1.25 kW, 9x10-5 Pa
with consumption rate of 3.6 mg/h
RF power =3.5 kW, 15x10-5 Pa
with consumption rate of 26 mg/h
Beam intensity of V13+ as a function of microwave power
Higurashi et al., ICIS2023

## Slide 12
V13+ ~100emA
V13+ ~900emA
Emittance Growth of V13+ as a function of Iext (Idrain)
Iext = 7.8 mA
Higurashi et al., ICIS2023

## Slide 13
Next Goal:
Intensity of 300 μA (“acceleratable”)
Good stability
U35+ beam

## Slide 14
(Absent a long-term stable supply)
250-μA U35+ with 10.5 mg/h.
Long period beam of 1 month was
U35+ (110μA) with 2.4mg/h
Current status of U35+ beam supply
High consumption causes unstable beam intensity.
Anti-deposition shield may be effective.
→ Morning session, tomorrow
To avoid the instability,

## Slide 15
(a)
(b)
(c)
Charge state distributions of highly charged U ions. Ion source was tuned to maximize the beam intensity of 33+(a), 42+(b), and 50+(c) at the microwave power of about 3000 W.

## Slide 16
?
Microwave power (W)
nrms - Beam Emittance
?
4000 W
Emittance Growth (Iext) in the U35+ case?

## Slide 17
Glynnis et al, ECRIS2024
=
=
We should pay attention to the εadd(Iext) < Acceptance.
Glynnis et al, ICIS2023

## Slide 18
Summary
・ Two RIKEN 28 GHz ECRIS are in operation;
from R28G-S, HCI beam to RIBF, and from R28G-K, to SHE experiments.
・R28G-S routinely supplies 110 µA U-beam, and R28G-K routinely supplies 150 µA V-beam.・
・To achieve higher intensity, V-ion beams of ~1 mA were successfully produced.
It is necessary to adjust the amount of neutral gas, especially the vanadium vapor, and the microwave power.
Emittance growth was measured as a function of Iext.
・Iext dependence of emittance for U beams up to 250 uA showed a relationship = .
Similar trends were observed for the Ar beam.
・ To achieve the target U beam supply of 300 uA, it is necessary to increase the microwave intensity to 4 kW as well as the U vapor volume by about five times the current level at most.
・ It is also necessary to suppress the beam intensity instability caused by the increase in vapor volume and emittance growth as a function of Iext.

## Slide 20
RIKEN 28-GHz ECRISs for RILAC II and RILAC
SC-ECRIS（RILAC）and LEBT
SC-ECRIS（RILAC II）and LEBT
RFQ
SC-ECRIS
Analyzing magnet
Faraday
cup
Paired Solenoid
Q magnet
Paired Solenoid
3 m

## Slide 21
(Absent a long-term stable supply)
250-μA U35+ with 10.5 mg/h.
Long period beam of 1 month was
U35+ (110μA) with 2.4mg/h
Current status of U35+ beam supply
High consumption causes unstable beam intensity.
Beam intensity of highly charged U ions

## Slide 22
After the beam extraction, the beam is focused using a solenoid coil before passing through the dipole analyzing magnet to select the ion charge state.
RMS Emittance and Focusing Solenoid Current
= + +
Beam Emittance of Uranium (U35+)
Focusing lens (Solenoid Coil)
In previous studies*, emittance size of the generated beam can be reduced by increasing the focusing solenoid current.
Y. Higurashi, et. al., 2016 Proc. of ECRIS2016 (Busan) MOBO04
This suggests minimal aberration for y-emittance and this can be used to deduce the εECRIS and εSpace-charge
Analyzing the beam emittances, it is important to distinguish the growth factors
In this case, beam aberration along the beamline can be the cause and
the x-emittance should be carefully considered.
ECRIS SMT 26 December 2024