## Slide 1: 28-45 GHz ECRIS results and development at IMP
Hongwei Zhao， Liangting Sun
On behalf of IMP ECRIS team
IMP
Institute of Modern Physics, CAS, 730000, Lanzhou, China
PIBHI25 April 7-9, 2025, INFN-LNS, Catania, Italy

## Slide 2
Outline
24-28 GHz SECRAL-I & SECRAL-II results and performance
45 GHz FECR results and performance
Discussion

## Slide 3
Who needs high frequency ECRIS? (RF ≥ 24 GHz)
Most of cyclotrons do not need HF ECRIS (Axial injection with inflector and space-charge). Only the cyclotrons need to raise beam energy through higher charge state and also need higher beam intensity.
IMP SFC, LBNL-88 cyclotron..
Heavy ion linacs ( with RFQ) do need higher intensity with high charge state
FRIB, HIAF-iLinac, SPIRAL2, RIKEN linac-injector, IMP linac-injector…

## Slide 4
HIRFL requests high intensity HCI with SECRAL I&II
CSRm
CSRe
SSC
SFC
Physics | Needed Ion Beam Energy (MeV/u)
Equation of state of nuclear matter at low temperature and high density Quarkonium symmetry energy | Xe: 105pps E = 400 - 600
 | C: 105pps E = 400 - 600
Baryon number fluctuations QCD critical point | 238U7x+: 104 pps E = 500－700
 | C: 105 pps E = 500
CEE
ECR (50~100 eμA U46+)SSC-LinacSSCStriperU74+CSRm≥500 MeV/u U74+
CSR External target Experiment
CEE
U46+
U74+
SECRAL-I: U46+
High Intensity
238U46+ beam
HIRFL
facility layout

## Slide 5
SHE Facility-CAFe 2 with SECRAL III
LEBT
RFQ
MEBT
SRF-Linac
SHANS-2
HEBT
LECR5
Layout of CAFE-2
Heavy ion Linac
Experimental Area
Ca13+ >40 eμA
by LECR5
Ca13+
~28 eμA
Parameters | Design | Unit
Particles | Ca～Zn | -
M/Q | ~1/3 | -
Energy | ~6 | MeV/u
Intensity | 3-5/10~20 | pμA
Operation Mode | CW | -
High Intensity SC HC HI linac for Medium Mass Metallic Ion Beams dedicated to SHE (119&120)
Upgraded the ADS SC proton linac
Demo-machine (A/Q=3)
New source: SECRAL-III, 28GHz
Notes: .

## Slide 6
LEAF facility with FECR (prototype for HIAF)
FECR
0.5 MeV/A
RFQ
FC5
Layout of LEAF Platform
FC1
LEAF: Low Energy high intensity highly-charged heavy ion Accelerator Facility
45GHz FECR

## Slide 7
HIAF facility with SECRAL IV and HFECR
T1
iLinac
SECR
HFRS
SRing
T2
T3
T4
T5
T6
BRing: Booster Ring
C: 569 m
Bρ: 34 Tm
SRing: Spectrometer ring
C: 278m
Bρ: 15Tm
iLinac: Superconducting linac
E: 17 MeV/u( 238U35+)
I : 1 emA
iLinac-2 (reserved)
E: 150 MeV/u U46+
CW: >10 pμA U46+
~50 pμA U35+/ 3-5 Hz@0.5~2 ms
High Intensity CW/Pulsed Ion Beams
High Intensity heavy-ion Accelerator Facility (HIAF)
28 GHz SECRAL- IV
45 GHz HFECR

## Slide 8
SECRAL-II, 24-28GHZ
Ion species | Charge state | SECRAL& SECRAL-II 24~28 +18 GHz 6-10 kW [eμA]
40Ar | 12+ | 1420
 | 16+ | 620
 | 18+ | 15
78Kr | 18+ | 1030
 | 28+ | 145
129Xe | 26+ | 1100
 | 30+ | 365
 | 42+ | 16
209Bi | 31+ | 680
 | 41+ | 100
238U | 34+ | 620
 | 35+ | 545
 | 46+ | 61
 | 55+ | 13
This maximum beam intensities can not be delivered to the accelerator due to stability
Typically, long-term operational beam intensity:
60-80% maximum intensities for gaseous ions
50-60% maximum intensities for metallic ions
Maximum beam intensities produced by SECRAL&SECRAL-II

## Slide 9
High Intensity Uranium Beam Production by 24-28 GHz ECRIS
14.5 + 10 GHz AECR-U
(oven + URe2 alloy)
28 GHz VENUS
(oven + URe2 alloy)
28 GHz VENUS
(HTO + UO2)
28 GHz SECRAL-II
(IHO + UO2)
18 GHz SuSI
(Sputtering)
24 GHz SECRAL
(Sputtering)
28 GHz SCECRIS/RIKEN
(Sputtering)
28 GHz SCECRIS/RIKEN
(HTO + UO2)
High Intensity U35+
High performance ECRIS
Reliable high-T oven >2000℃
HTO: High temperature resistor heating oven, IHO: Inductive heating oven
U35+ 545 eμA
24 GHz SECRAL-II
(IHO + UO2)
Notes: Solutions 4: High Intensity Uranium Beam production by high performance ECRIS with reliable high temperature oven around 2000 degree C.
This graph shows the U35+ beam intensity evolution in the past 20 years produced by different ECRISs.
Berkeley AECR-U and VENUS are pioneers for high intensity U beam production,
And then following by SuSi, SECRAL, RIKEN SCECRIS, SECRAL-II with sputtering, and High temperature resistor heating oven. It was last year SECRAL-II produced U35+ 545 euA with Inductive heating oven

## Slide 10
High Intensity Uranium Beams by SECRAL-II
Production of 545 eμA 238U35+ by SECRAL II
Material: UO2+O2,IHO
Frequency: 24+18 GHz
μW power: ~7.9 kW
Total drain: ~13.2 emA

## Slide 11
Record Intensities of Uranium Beams by SECRAL-II
18 GHz
24 GHz
Oven
Power Supply
Features:
High performance SECRAL-II ion source
High power: 7 kW@24 GHz + 2 kW@18 GHz
Reliable IHO oven: >2000℃
U Charge State | SECRAL-2023 (eμA) | Records as of 2022 (eμA) | Contributors as of 2022
33 | 640 | 450 | SECRAL-II/IMP1
34 | 620 | 400 | VENUS/LBNL2
35 | 545 | 310 | VENUS/LBNL，SECRAL-II/IMP
42 | 100 | 62.6 | SCECRIS/RIKEN3
46 | 61 | 36.2 | SCECRIS/RIKEN
50 | 38 | 20.1 | SCECRIS/RIKEN
54 | 19 | 10.4 | SCECRIS/RIKEN
56 | 9.5 | 0.9 | SECRAL-II/IMP
58 | 2.7 | 0.7 | SECRAL-II/IMP
W. Lu et al., Rev. Sci. Instrum. 90, 113318 (2019)
J. Benitez, et al., ECRIS2012, THXO02-talk
T. Nakagawa, Cyclotron’22, invited talk
SECRAL-II

## Slide 12
SECRAL-II routine operation for HIRFL in 2023
No. | Ion | Vextr(kV) | Date | Time (Hr) | 0FC1 (μA) | 1FC1/2 (μA) | E (Mev/u) | Accelerators and experimental setup
1 | 181Ta35+ | 13.00 | 12.26-1.31 | 863.5 | 50-80 | 1.0 | 1.52→16 | SECR+SFC+SSC→ TR5
2 | 54Fe17+ | 20.17/21.55 | 2.2-2.15 | 311 | 80-140 | 4.4 | 6.17→70 | SECR+SFC+SSC→ RIBLL1
3 | 36Ar12+ | 20.36 | 2.15-3.1 | 318 | 120 | 4 | 6.17→70 | SECR+SFC+SSC→ RIBLL1
4 | 86Kr17+ | 18.91 | 3.20-4.1 | 280.5 | 200 | 4.5 | 2.345→25 | SECR+SFC+SSC → TR6/TR5
5 | 56Fe15+ | 17.71 | 4.2-4.26 | 575 | 60 | 4 | 4.3→25/120 | SECR+SFC+CSRm → CSRe
6 | 94Zr19+ | 12.74 | 5.23-6.5 | 289 | 60 | 2.4 | 1.613→17 | SECR+SFC+SSC→ RIBLL1
7 | 129Xe27+ | 14.05 | 6.6-6.14 | 182 | 280 | 4.5 | 1.844/19.5 | SECR+SFC+SSC→ TR5
8 | 64Ni19+ | 19.89 | 7.29-8.3 | 122.5 | 40 | 2.5 | 5.361→19 | SECR+SFC+SSC→ RIBLL1
9 | 64Ni19+ | 20.89 | 9.13-9.28 | 346.5 | 40 | 2.2 | 5.361→19 | SECR+SFC+SSC→ RIBLL1
10 | 129Xe31+ | 18.39 | 9.29-10.6 | 161 | 110 | 2.0 | 4 | SECR+SFC → 128-T1
11 | 56Fe17+ | 22.86 | 10.21-11.8 | 430 | 30 | 1.3 | 6.3 | SECR+SFC → 128-T1
12 | 78Kr26+ | 19.85 | 11.17-12.31 | 1041 | 210 | 11 | 5.971 → 450 | SECR+SFC → CSRm
SECRAL-II total operation beam time in 2023: 4920 hours

## Slide 13
SECRAL-II routine operation for HIRFL in 2024
No. | Ion | Vextr(kV) | Date | Time (Hr) | 0FC1 (μA) | 1FC1/2 (μA) | E (Mev/u) | Accelerators and experimental setup
1 | 124Sn27+/30+ | 17.4/15.5 | 2.22-3.13 | 481.5 | 50/30 | 2.2 | 2.345→ 25 | SECR+SFC+SSC →RIBLL1
2 | 181Ta35+ | 13.00 | 3.15-4.10 | 634 | 40 | 0.8 | 1.52→16 | SECR+SFC+SSC →TR5
3 | 78Kr26+ | 19.85 | 5.25-6.14 | 480 | 130 | 4 | 5.971 → 350 | SECR+SFC+BLN+CSRm+CEE
4 | 78Kr19+ | 18.60 | 6.14-6.17 | 69.5 | 130 | 3 | 4 | SECR+SFC+BLN+CSRm
5 | 86Kr24+ | 15.82 | 6.17-6.23 | 136.5 | 120 | 3 | 4 | SECR+SFC+BLN+CSRm
6 | 36Ar15+ | 16.29 | 6.23-7.3 | 242 | 150 | 3 | 6.17 | SECR+SFC→ 128#-T1
7 | 36Ar12+ | 20.84 | 7.3-7.21 | 423 | 200 | 4.5 | 6.17 → 70 | SSECR+SFC+SSC+RIBLL1
8 | 86Kr27+ | 21.03 | 7.26-7.31 | 110 | 50 | 4 | 6 | SECR+SFC→ TL2
9 | 56Fe17+ | 22.86 | 9.14-11.3 | 1193 | 45 | 2 | 6.3 | SECR+SFC→ TL2
SECRAL-II total operation beam time in 2024: 3769.5 hours

## Slide 14
Uranium Beam Production 238U46+ by SECRAL-I
SECRAL-I
SECRAL-I: 28 GHz ECR ion source
Upgraded from 24 GHz SECRAL
Ø 120 mm ID plasma chamber
10 kW max. μW power
Micro-channel cooling Al plasma chamber

## Slide 15
Uranium Beam Operation 238U46+ for SSC-Linac by SECRAL-I
Lower emittance for higher charge state
SECRAL-I delivered 238U46+ beam to SSC-Linac for 568.5 hours with intensity
25-30 eμA from 17/11/2023 to 03/01/2024.

## Slide 16
HIRFL Uranium Beam Operation with SECRAL-I
238U46+—1.48MeV/u
238U46+—15.53MeV/u
238U74+—500MeV/u
CEE
AMS
Stripper： 46+ 74+
25~30 eμA 238U46+
500MeV/u 238U74+ @1×108 ppp
Notes: 25-30 euA U46+ from SECRAL-I was accelerated by the SSC-linac upto 1.48 MeV/A, and then re-accelerated by this big SSC cyclotron upto 15.53 MeV/A, and we got 8.7 euA U46+ beam extracted from the SSC cyclotron. After stripping to U74+ which was injected into the synchrotron CSRm, and accelerated upto 500 MeV/A, we had 10E8 ppp in the ring for physics experiments.

## Slide 17
Long-term stability of high-intensity highly-charged heavy ion beams delivered by SECRAL II
High-intensity highly charged heavy ion beams produced by SECRAL II at 6-7 kW /24-28 GHz RF power were delivered to existing accelerator facility HIRFL-SFC cyclotron.
250 eμA of 78Kr26+ , 27 days continuously, 200 eμA of 129Xe32+ 10 days continuously
Demonstrating good long-term stability
27 days beam operation continuously for HIRFL
10 days beam operation continuously for HIRFL
24 GHz + 18 GHz
28 GHz + 18 GHz
±7.6%

## Slide 18
Long-term stability of high-intensity highly-charged heavy ion beams delivered by SECRAL II
2021---28+18 GHz-Ar15+

## Slide 19
Long-term operation at high-intensities of highly-charged beams
SECRAL-II
Time (hours)
±9.0%

## Slide 20
Current 1.6×109ppp
SECRAL-II: ~350 eμA （~4 times historical operation current）
  High current：SFC--8.5 AMeV/15 eμA
  CSRm Beam Current Increase by a factor of 5
36Ar15+
SECRAL-II: ~280 eμA (not available before)
  High current：SFC--6 AMeV/12 eμA
  CSRm Beam Current Increase by a factor of 10
78Kr26+
Current 1.2×109ppp
SECRAL-II: ~200 eμA (not available before)
  High current ：SFC—3.9 AMeV/8 eμA
  CSRm Beam Current Increase by a factor of 5
129Xe32+
Current 6.3×108ppp
CSRm performance enhancement together with other technical improvements
SECRAL-II operation improved performance of HIRFL-CSRm

## Slide 21
Outline
24-28 GHz SECRAL-I & SECRAL-II Results and Performance
45 GHz FECR Results and Performance
Discussion

## Slide 22
Specs. | Unit | Value
Frequency | GHz | 45
RF Power | kW | 20
Chamber ID | mm | ≥Ø140
Mirror Fields | T | ≥6.4/3.2
Brad | T | ≥3.2
Mirror Length | mm | ~500
Bmax in conductor | T | ~11.8
Magnet coils | / | Nb3Sn
Nb3Sn | Jc>1500 A/mm2@12T | 
Cooling Capacity@4.2 K | W | >10.0
Specs. of FECR
FECR (First 4th generation ECR ion source)
H. W. Zhao et al., Review of Scientific Instruments 89, 052301 (2018)
Next Generation ECRIS: 45GHz FECR

## Slide 23
COIL-PACK
SUBASSEMBLY
COLLARS
SEXTUPOLE
COILS
AXIAL-LOAD
END PLATE
SUBASSEMBLYS
SOLENOID
STRUCTURE
SUBASSEMBLY
SHELL-YOKE
SUBASSEMBLY
(Shell is strain gauged)
MASTER-KEY PLATES
BLADDER
SUBASSEMBLY
LOAD-KEYS
YOKES
YOKE-SHELL
ALIGNMENT PINS
AXIAL RODS
(Strain Gauged)
COIL END
BLOCKS
In collaboration with ATAP/LBNL（2016~2017）
Key technologies and tests completed in close collaboration with XSMT in China (since 2016)
Bladder & Keys assembly
M. Juchno, et al., IEEE Trans. Appl. Supercond., 28(4), 2018, Art. 4005506
FECR : Nb3Sn Magnet Cold-Mass Structure
Detailed FECR Nb3Sn magnet design and manufacturing will be presented by Liangting Sun in the afternoon session !
Notes: FECR Nb3Sn magnet mechanical structure was designed by collaboration with ATAP magnet group at LBNL.
This viewgraph shows the detailed and very complicated magnet structure and clamping scheme. We use Bladder and key assembly clamping.

## Slide 24
FECR : Nb3Sn magnet Coldmass to Hybrid
NbTi Sextupole Coils
Nb3Sn Solenoid Coils
NbTi Sextupole Coils
Nb3SnNbTi sextupole coils, Structure unchanged
80% B field of the
Nb3Sn magnet
Notes: Already 8 years magnet development, as a project leader, I got very big pressure, I was asked to finish project as soon as possible. The magnet is not final goal, the final goal is ion source and the beams.
In such situation, we had to change our mind. The full Nb3Sn magnet Coldmass was switched to Hybrid structure, using NbTi sextupole coils replace the Nb3Sn coils, the four solenoids are still Nb3Sn conductor. All the structure and other components are same. But we can only get 80% magnetic fields of the Nb3Sn magnet.

## Slide 25
FECR: Joint Test at LEAF
FECR
0.5 MeV/A
RFQ
FC5
Layout of LEAF Platform
FC1
LEAF: Low Energy high intensity highly-charged heavy ion Accelerator Facility
FECR has been used for routine operation on LEAF for 300 hours

## Slide 26
Bi35+
Bi31+
Production of 600 eμA Bi31+, 360 eμA Bi35+
6.5 kW@45 GHz + 4.5 kW@28 GHz (50% transmission of 9.0 kW )
FECR beam commissioning for Bi31+ and Bi35+

## Slide 27
Production of 320 eμA 238U35+
5 kW@45 GHz + 4.5 kW@28 GHz (50% transmission of 9.0 kW )
O2+
O3+
U35+
FECR beam commissioning for 238U35+
Preliminary results !
3 days beam commissioning.

## Slide 28
56Fe + 18O
  Iq= 0.8 eμA
  Ion validated with Si detector
FECR beam commissioning for fully-stripped 56Fe26+
Production of Fully stripped iron beam 56Fe26+
Preliminary results !

## Slide 29
FECR: Joint Test at LEAF and the First Results
FECR: 1.6 emA O6+
1.016 emA O6+@60 mins
1 hour stability demonstration of CW 1.0 emA O6+ beam
accelerated by the LEAF-RFQ (~90% transmission)
LEAF RFQ – 0.5 MeV/A

## Slide 30
FECR: Joint Test at LEAF and the First Results
FECR: 350 eμA 209Bi35+
Beam Intensity (eμA)
DM1 Current (A)
0.23 emA Bi35+@60 mins
6.5 kW 45GHz+5.5 kW 28GHz
1 hour stability demonstration of CW 230 eμA Bi35+ beam
accelerated by the LEAF-RFQ (~90% transmission)

## Slide 31
Bi35+
Bi31+
Production of 600 eμA Bi31+, 360 eμA Bi35+
6.5 kW@45 GHz + 4.5 kW@28 GHz (50% transmission of 9.0 kW )
FECR double frequency heating (1) 209Bi31+ and 209Bi35+
The magnetic field Bz peak 3.9 T, Br at the wall 2.3 T, 28 GHz B field.
45 GHz power played an significant role for raising the beam intensity.
What is the reason or physics behind ?

## Slide 32
Microwave frequency: 45 GHz +28 GHz. Magnetic fields (T): Br-2.23, Binj-3.88, Bmin-0.58, Bext-2.10
28 GHz magnetic field, higher frequency 45 GHz power could play a significant role ?
FECR double frequency heating (2) 238U35+

## Slide 33
The big challenges for HF ECRIS:
SC magnet, high power RF coupling, long-term stability at high RF power, heating to chamber and cryostat, beam emittance…
Discussion and comments

## Slide 34
Thank you for your attention !