## Slide 1: Production of intense highly charged metallic ion beams for routine operation
L. Sun, W. Lu
IMP
Institute of Modern Physics, CAS, 730000, Lanzhou, China
PIBHI’25, April. 7~9, 2025, Acitrezza, Italy

## Slide 2
Outline
General info on Metallic Ion Beams at IMP
  Metallic Ion Beams Operation at IMP
Operation Status
  Operation for compact ion sources
  Operation for SHE
  Operation with refractory metallic ion beams
  Operation stability
Summary
Notes: Needs: SHE, CEE, HIAF
HCI production: metallic beams with CAFe-2 (LECR5 & SECRAL 3), Uranium beam with HIRFL@SECRAL-I & SECRAL-II
New Techniques towards intense beams: HTO, Vlasov launcher, 2-frequency AG, Biased probe + AG effect
HIAF requirements in long range, FECR

## Slide 3
18 GHz LECR5
28 GHz SECRAL-I
14 GHz LECR3
24 GHz SECRAL-II
14 GHz LAPECR2
HIRFL
CAFE2
320 kV HV Platform
General Info: Facilities
Notes: Needs: SHE, CEE, HIAF
HCI production: metallic beams with CAFe-2 (LECR5 & SECRAL 3), Uranium beam with HIRFL@SECRAL-I & SECRAL-II
New Techniques towards intense beams: HTO, Vlasov launcher, 2-frequency AG, Biased probe + AG effect
HIAF requirements in long range, FECR

## Slide 4
General Info: Ion Beam List
:Sputtering
:OVEN
:MIVOC
:Gas
Ion beams produced at IMP
Notes: Needs: SHE, CEE, HIAF
HCI production: metallic beams with CAFe-2 (LECR5 & SECRAL 3), Uranium beam with HIRFL@SECRAL-I & SECRAL-II
New Techniques towards intense beams: HTO, Vlasov launcher, 2-frequency AG, Biased probe + AG effect
HIAF requirements in long range, FECR

## Slide 5
Status: Operation with Compact Ion Source
Ion current （eμA） | Material used | LAPECR2 （14.5 GHz <0.75 kW） 2006-2022
#Mn11+ | MnO2 | 14
*Fe13+ | C₁₀H₁₀Fe | 18
*Ni13+ | C₁₀H₁₀Ni | 35
*Ni17+ | C₁₀H₁₀Ni | 10
#Au30+ | Au | 5.3
#Au35+ | Au | 3
#Bi28+ | Bi | 45
#Bi33+ | Bi | 12
#Eu23+ | Eu | 17
#Eu33+ | Eu | 5
**U25+ | U | 11
**U31+ | U | 4
* MIVOC
**Sputtering
#Conventional oven
Recently a refined design IHO is applied
Notes: Needs: SHE, CEE, HIAF
HCI production: metallic beams with CAFe-2 (LECR5 & SECRAL 3), Uranium beam with HIRFL@SECRAL-I & SECRAL-II
New Techniques towards intense beams: HTO, Vlasov launcher, 2-frequency AG, Biased probe + AG effect
HIAF requirements in long range, FECR

## Slide 6
Ion current （eμA） | LAPECR3 （14.5 GHz <0.75 kW） 2023
*Fe6+ | ~10
*Fe9+ | ~30
*Fe10+ | ~20
*Fe11+ | ~10
* MIVOC
Limited by the space at source injection
MIVOC
Sputtering
Small resistor oven
Status: Operation with Compact Ion Source
Notes: Needs: SHE, CEE, HIAF
HCI production: metallic beams with CAFe-2 (LECR5 & SECRAL 3), Uranium beam with HIRFL@SECRAL-I & SECRAL-II
New Techniques towards intense beams: HTO, Vlasov launcher, 2-frequency AG, Biased probe + AG effect
HIAF requirements in long range, FECR

## Slide 7
Status: Operation for SHE
Stable neutron rich projectile
119
54Cr+243Am297119*294119+3n
55Mn+244Pu299119*296119+3n
51V+248Cm299119*296119+3n
50Ti+249Bk299119*296119+3n
45Sc+249Cf294119*291119+3n
120
55Mn+243Am298120*295120+3n
58Fe+244Pu302120*299120+3n
54Cr+248Cm302120*299120+3n
50Ti+249Cf  299120*296120+3n
A worldwide Research Campaign

## Slide 8
Status: Operation for SHE
Ion current （eμA） | 18+14 GHz/2 kW 2023
Ca11+ | 235
Ca12+ | 225
Ca13+ | 173
Ca14+ | 115
Ca16+ | 65
Ca18+ | 18
Ca19+ | 1.5
[1]. W. Lu, H. Y. Ma, C. Qian, et.al. Nuclear Instruments and Methods in Physics Research A 1062 (2024) 169207

## Slide 9
Target ion: 55Mn17+
M/q= 3.235
Supporting gas: 4He
very difficult to get high charge state!
Status: Operation for SHE

## Slide 10
Supporting gas: 20Ne
even difficult to get medium charge state!
Status: Operation for SHE

## Slide 11
Supporting gas: 14N
stable Mn17+ produced
Status: Operation for SHE

## Slide 12
Target ion: 54Cr17+
M/q= 3.176
Supporting gas: 18O
difficult to avoid the influence of 16O5+
Status: Operation for SHE

## Slide 13
Supporting gas: 14N2
stable Cr17+ produced
Status: Operation for SHE

## Slide 14
Status: Operation with Refractory Metal Ion Beams

## Slide 15
RF: 24+ 18 GHz
Total rf Power: 2-3 kW
Extraction voltage: 12-20 kV
Drain current: 4-6 emA
Slit-x= 16 mm, Slit-y= 40 mm
Bias Voltage: -3~-6 kV
Ta31/35/38+= 30-50 euA
Consumption rate: 5-8 mg/h
Ionization rate: 5-7 %
2018-present
Ta rod
Status: Operation with Refractory Metal Ion Beams

## Slide 16
Material: ZrF4
Rf: 18 GHz
Pw= 0.5-0.6 kW
HV= 12.74 kV, Io= 3-4 emA
Slit-x= 12 mm
94Zr19+= 50-100 euA
Oven temp.: ~460 ℃
Consumption rate: 3-4 mg/h
2023-5
Cartridge heating oven
Status: Operation with Refractory Metal Ion Beams

## Slide 17
Status: Operation Long-term Stability
Chart: 181Ta35+ stability for about one month
| 44577 | 44578 | 44579 | 44580 | 44581 | 44582 | 44583 | 44584 | 44585 | 44586 | 44587 | 44588 | 44589 | 44590 | 44591 | 44592 | 44593 | 44594 | 44595 | 44596 | 44597 | 44598 | 44599 | 44600 | 44601 | 44602 | 44603 | 44604 | 44605 | 44606
Beamcurrent | 25 | 22 | 22 | 21.6 | 22.8 | 21 | 26 | 26.8 | 25 | 21 | 24 | 22 | 22 | 20 | 19 | 18 | 19 | 19 | 19 | 17 | 18 | 18.5 | 18 | 19 | 19.37 | 20.5 | 19 | 21 | 17 | 17
rfpower | 2 | 2 | 2 | 2.15 | 2.15 | 2.15 | 2.15 | 2.15 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.15 | 2.2 | 2.15 | 2.15 | 2.15 | 2.15 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95
2022-18+18 GHz-Ta35+

## Slide 18
Chart: 56Fe17+ stability for near 2 months
| 45549 | 45550 | 45551 | 45552 | 45553 | 45554 | 45555 | 45556 | 45557 | 45558 | 45559 | 45560 | 45561 | 45562 | 45563 | 45564 | 45565 | 45566 | 45567 | 45568 | 45569 | 45570 | 45571 | 45572 | 45573 | 45574 | 45575 | 45576 | 45577 | 45578 | 45579 | 45580 | 45581 | 45582 | 45583 | 45584 | 45585 | 45586 | 45587 | 45588 | 45589 | 45590 | 45591 | 45592 | 45593 | 45594 | 45595 | 45596 | 45597 | 45598
Beamcurrent | 30 | 44 | 45 | 48 | 49 | 48 | 40 | 34 | 33 | 35 | 35 | 35 | 38 | 38 | 36 | 35 | 35 | 32 | 34 | 32 | 34 | 34 | 33 | 31 | 32 | 31 | 40 | 39 | 37 | 37 | 38 | 32 | 25 | 30 | 30 | 30 | 29 | 30 | 28 | 26 | 26 | 27 | 26 | 26 | 26 | 34 | 32 | 30 | 30 | 29
rfpower | 1 | 1.17 | 1.17 | 1.16 | 1.25 | 1.22 | 1.25 | 1.26 | 1.27 | 1.27 | 1.26 | 1.26 | 1.28 | 1.27 | 1.23 | 1.28 | 1.3 | 1.3 | 1.3 | 1.3 | 1.33 | 1.33 | 1.34 | 1.34 | 1.34 | 1.3 | 1.38 | 1.37 | 1.37 | 1.36 | 1.36 | 1.29 | 1.29 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.36 | 1.36 | 1.36 | 1.36 | 1.36 | 1.35 | 1.35 | 1.35 | 1.35 | 1.35
2024-Single 18 GHz-Fe17+
Status: Operation Long-term Stability

## Slide 19
Summary
Metallic ion beams production is a special topic for ECRIS
Diverse methods employed for routine operation
These remain challenging
  High intensity routine operation
    Reasonable consumption rate
    Long-term stability
    Rare/expensive isotope ion beam
  Refractory metallic ion beam reliable operation