## Slide 1: VENUS operation and HCI beams for superheavy element production at LBNL
Damon Todd and Janilee Benitez
Lawrence Berkeley National Laboratory
09 April 2025

## Slide 2: Recent superheavy element discoveries
beam
target
immediately lose a few neutrons and later decay
Notes: ^{48}_{20}\mathrm{Ca}
A short history of recent superheavy element discoveries.
High current 48Ca on heavy targets
If you have a hammer, all problems look like a nail

## Slide 3: Recent superheavy element discoveries
beam
Notes: ^{48}_{20}\mathrm{Ca}
A short history of recent superheavy element discoveries.
High current 48Ca on heavy targets
If you have a hammer, all problems look like a nail

## Slide 4: Recent superheavy element discoveries
beam
Typical beam needs:
Current: as close to ∞ as possible (typically 1-2 pμA is satisfactory)
Energy: 5-6 MeV/u
Notes: ^{48}_{20}\mathrm{Ca}
A short history of recent superheavy element discoveries.
High current 48Ca on heavy targets
If you have a hammer, all problems look like a nail

## Slide 5: Limit in target atomic number
115
116
117
118
119???
120???
proton number
Notes: Es, next, has <mg produced per year in 253 (21 day half life). Things get worse as you c

## Slide 6: Increasing atomic number of projectiles
Increase
beam proton number
Notes: Es, next, has <mg produced per year in 253 (21 day half life). Things get worse as you c

## Slide 7: Limit in target atomic number
RIKEN: 51V on Cm → 119
LBNL: 50Ti on Cf → 120
Dubna: ??Cr on ?? → ??
Increase
beam proton number
(expectation to continue with heavier beams after)
Notes: Es, next, has <mg produced per year in 253 (21 day half life). Things get worse as you c

## Slide 8: One way to get metal into an ECR ion source: ovens
metal
oven crucible
ECR plasma
metal gas
add heat

## Slide 9: One way to get metal into an ECR ion source: ovens
metal
oven crucible
ECR plasma
metal gas
Improve by aiming
add heat

## Slide 10: One way to get metal into an ECR ion source: ovens
metal
oven crucible
ECR plasma
add heat
metal gas
Improve by aiming
Improve more by aiming better

## Slide 11: Side question: what are we measuring when using metal in ovens??
oven
ECR plasma
Ion
gauge
source chamber
extraction
biased disk

## Slide 12: Low-temperature oven used for 48Ca beams from VENUS
Conductively heated
Operating temperature for calcium: ~600°C
Maximum operating temperature: ~700°C
Results:
Delivery of continuous, 1-2 pμA 48Ca11+ by cyclotron
Consumption: ~0.5 mg/hr (>$300k/g)
Stainless insert:
8.5 mm long
5.6 mm diameter

## Slide 13: Reaching higher temperatures: resistive oven
I
Resistive ovens:
Custom-made (Ta, W, and Re)
Thickness ~0.25 mm
Volume ~0.3 cm3
T > 2000 °C

## Slide 14: Reaching higher temperatures: resistive oven
I
Resistive ovens:
Custom-made (Ta, W, and Re)
Thickness ~0.25 mm
Volume ~0.3 cm3
T > 2000 °C
B
F

## Slide 15: Reaching higher temperatures: resistive oven
I
Resistive ovens:
Custom-made (Ta, W, and Re)
Thickness ~0.25 mm
Volume ~0.3 cm3
T > 2000 °C
B
F
Inside VENUS, reliable temperatures reached are typically ≲ 1500 °C, dictated largely by hot metal chemistry

## Slide 16: Vertical inductive oven concept
20.7 mm
24 mm
must fit through 38.1-mm-diameter port
Supported by insulating rod

## Slide 17: Oven exploded view
Insulator
Support ring
Support ring
Lid
Susceptor
Insulator
Susceptor
Point-like contact

## Slide 18: Inductive oven
Bottom view
Front view

## Slide 19: Current inductive oven inner parts
Susceptor:
1.1-mm-thick molybdenum (skin depth = 0.26 mm @ 200 kHz)
Finally replaced first susceptor after >75 days running 50Ti
Insulators:
Yttria-stabilized zirconia
Must be replaced after each run (typically 10 days)

## Slide 20: Typical operation
Operation for >100 μA 50Ti12+ beams::
Inductive power: 800-1000 W of ~175 MHz
Consumption: 2.5 – 5.0 mg/hr
Capacity: ~1.2 g, or 11-20 days
Run time: Up to 10 days straight (so far)
Refill time: ~4 hours to back on target
Sources settings:
  ~10-7 mbar injection pressure
  ~700 W of 18 GHz RF (no 28 GHz)
  Standard 18 GHz fields::
    BECR = 0.64 T
    Bext ~ Bradial ~ 1.2 T
    Binj ~ 1.8 T
    Bmin ~ 0.39 T
Notes:
No temperature diagnostics in VENUS
Oven reached >2000 ℃ in test stand

## Slide 21: Two primary superheavy element projectile beams
50Ti12+
From VENUS inductive oven:
Typically 100-150 μA
Consumption: 2.5-5.0 mg/hr (~0.07% to experimenters)
From Cyclotron:
Typically 15-24 μA (1.25-2 pμA)
48Ca11+
From VENUS low-temperature oven:
Typically 60-100 μA
Consumption: ~0.5 mg/hr (~0.7% to experimenters)
From Cyclotron:
Typically 16-22 μA (1.45-2 pμA)

## Slide 22: Success: Two atoms of element 116 from 22 days of running

## Slide 23: Two primary superheavy element projectile beams
50Ti12+
From VENUS inductive oven:
Typically 100-150 μA
Consumption: 2.5-5.0 mg/hr
From Cyclotron:
Typically 15-24 μA (1.25-2 pμA)
48Ca11+
From VENUS low-temperature oven:
Typically 60-100 μA
Consumption: ~0.5 mg/hr
From Cyclotron:
Typically 16-22 μA (1.45-2 pμA)

## Slide 24: Two primary superheavy element projectile beams
50Ti12+
From VENUS inductive oven:
Typically 100-150 μA
Consumption: 2.5-5.0 mg/hr
From Cyclotron:
Typically 15-24 μA (1.25-2 pμA)
48Ca11+
From VENUS low-temperature oven:
Typically 60-100 μA
Consumption: ~0.5 mg/hr
From Cyclotron:
Typically 16-22 μA (1.45-2 pμA)

## Slide 25: An aiming inductive oven, proof of concept
Produced over 100 eμA 48Ti12+
Clearly not aligned correctly
New design will lead to better alignment

## Slide 26: Precision and accuracy
precision
accuracy
boat oven

## Slide 27
Thank you!

## Slide 28: 3D printed fixture for 4-mm-diameter/0.4-mm-wall-thickness copper tubing
Design
3D printed form

## Slide 29: Safety catch

## Slide 30: Early problems: rotations → clogs
Insulator relative to coil
Susceptor relative to insulator

## Slide 31: Susceptor after runs
Titanium solidifies on ends -> ends are cooler than body (potential problem for “aiming” solution for horizontal ovens??)
Higher temperature body prevents clogging!
Same susceptor and lid have been used for all cyclotron runs (>40 days)

## Slide 32: 50Ti pellets

## Slide 33: Susceptor after runs
Yosemite’s Half Dome

## Slide 34: Solutions to rotations
Insulator relative to coil
Susceptor relative to insulator
Original
New
Solution: slotted insulator body preserves
alignment using support post
Solution: thin molybdenum strips jammed
between insulator and susceptor