## Slide 1
Biagioni, L.Crincoli,
R. Demitra,
G. Costa, M. Anania
Laboratori Nazionali di Frascati
INFN
Angelo.Biagioni@lnf.infn.it
Plasma diagnostics for plamsa-based accelerators
Plasma_lab

## Slide 2
Outline
Motivations
    Plasma-based accelerators
    Plasma lenses
Plasma sources
    Gas-filled discharge capillary
Experimental setup
Plasma sources characterization
Angelo.Biagioni@lnf.infn.it

## Slide 3
Driver bunch
Witness bunch
Plasma-based accelerators
Angelo.Biagioni@lnf.infn.it
Driver bunch
Witness bunch
RF-based accelerators MV/m
Plasma-based accelerators GV/m

## Slide 4
Plasma-based accelerators
Driver bunch
Witness bunch
λp
Plasma density measurement
represents a crucial point to
implement plasma-based
devices:
  Accelerators
  Plasma lens
Linear regime (nb < np)
Weakly NL regime (nb = np)
Non-linear regime (nb>>np)

## Slide 5
First results
Witness
Driver
No Plasma
Plasma obtained at 12kV-310 A
Electron density 1015 cm-3
λp ~ 1050 um
Witness
Driver
3 MeV
7 MeV
By using a 3cm long capillary, an accelerating gradient of 800 MV/m has been obtained, which should be compared to 20-30 MeV of conventional accelerating system
3 cm
Plasma capillary
With Plasma

## Slide 6
Experimental set-up
Angelo.Biagioni@lnf.infn.it
Capillary shapes:
Length (Energy)
Radius (Density)
Spectrometer:
Grating
Optical alignment
Camera timing:
Delay time
Gate time
Timing:
Valve opening time
Voltage delay time
Trigger of ICCD camera

## Slide 7
Plasma sources: gas-filled discharge capillary
10cmx1mm
single inlet
3cmx1mm
20cmx1mm
two inlets
Plasma source characterization means to study the plasma behaviour as a fuction of many parameters: discharge voltage, position and number of the gas inlets, plasma channel shape and so on, that in turn will affect the quality of the accelerated beam

## Slide 8
Plasma characterization: density measurements
Angelo.Biagioni@lnf.infn.it
Stark broadening method
Electrode shadow
Plasma
plume
Plasma channel
By using the Stark broadening method to measure
the plasma density, we obtain the below result:
the larger is the Balmer line (Δλ), the higher is the
electron density of plasma
Balmer Beta line Bβ due to transitions from the
outer orbit n=4 to the orbit n=2

## Slide 9
Plasma density inside and outside the capillary will change during the current pulse: such a behaviour it is very important to select when inject the electron bunch
Density measurements
Angelo.Biagioni@lnf.infn.it
Position (mm)
λ (nm)
Electrode
Plasma
channel
Plasma plume
Δλ
Balmer β line
Capillary

## Slide 10
800 ns
1200 ns
inlets
30 mm
Capillary 3cmx1mm 2 inlet NO SPACERS
13 kV - 300 A
Pressure 300 mbar
Uniformity
50%
20 mm
Stability 5-7%
Plumes
10-15mm

## Slide 11
Laser
100 mJ
11 ns
100 um
Lens to change
the focal spot
Spectrometer
ICCD
Gas injection
Plasma light
Capillary 5cmx1mm Minimum breakdown voltage depends on the neutral gas pressure
By using a laser beam to trigger the discharge :
  Minimum voltage
  Stability shot-to-shot
  Plasma current
  Timing jitter
Vacuum chamber Plasma_lab
+
Laser triggering

## Slide 12
How to use the experimental setup to produce plasmas inside capillaries with different shapes: length and radius
How to implement the optical system and set ICCD camera parameters to make the spectrographic analysis
How to make the data processing to obtain the plasma densities to characterize our plasma sources
Plasma_lab experience
New Plasma lab
Sparc_lab accelerator

## Slide 13
Thank you
for your attention