## Slide 1: The Archimedes Experiment: a way for exploring the Vacuum-Gravity Interaction
Paola Puppo (INFN Roma) on behalf of the Archimedes collaboration
The Low-Energy Frontiers of Particle Physics
10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 2: Scientific motivations and goal of the experiment
Does vacuum fluctuations interact with gravity?
Does the vacuum stress gravitates?
Does vacuum weighs?
The theoretical understanding and experimental evidences are still not completely satisfactory
We can already put interesting upper limit, for instance:
Dark photon (see E. Calloni talk)
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 3: General Information on Archimedes
Ec :Casimir Energy
The Casimir effect is one of the macroscopic manifestations of vacuum fluctuations.
If the vacuum «weighs» then there is a force, directed upward, equal to the weight of the modes expelled from the cavity. In analogy with the Archimedes force[*].
3
The vacuum weight
Gravitational field
[*] G. Bimonte, E. Calloni, G. Esposito, L. Rosa – Physical Review D 76, 025008 (2007) – DOI: 10.1103/PhysRevD.76.025008
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 4: The Casimir effect is derived considering the zero point e.m. energy contained in a casimir cavity, i.e. in the volume defined by two perfectly reflecting parallel plates
y
z
a
L
If the plates are perfectly reflecting, the modes that can oscillate must have discrete wavenumbers on horizontal axes ky = np/a while all values are allowed for kx e kz
4
x
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 5
Casimir Energy
CASIMIR PRESSURE
First prediction: Casimir 1948
First measure (force): Sparnay 1956
Presently tested (force) with an accuracy of 0.5% (Mohideen: 2005)
The Casimir Energy is the change in energy when the plates
are at distance “a” with respect to the plates having a
EC = E(a) – E()
5
P. Puppo - Vacuum Fluctuations at Nanoscale and Gravitation: theory and experiments – Orosei – May 2019

## Slide 6: How to measure the vacuum weigth? The idea is to modulate the vacuum energy of a rigid Casimir cavity by changing the reflectivity of the plates with time
Expected upward force 5 10-16 N
6
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)
Use high Tc layered superconductors as natural multi Casimir-cavities.
YBCO, BSCO, GdBCO… behave as natural multi-layer Casimir cavities.
A transition from normal to superconducting state and vice versa can be induced by the modulation of the temperature of a superconductor.
Profit of the fact that in normal state the plane that will become superconducting is a very poor conductor.
 high variation of Casimir energy at the transition

## Slide 7: The measurement Strategy
7
High Sensitivity Balance: arm center of mass and suspension point must be well positioned (within 4mm)
Temperature modulation around Tc
Quiet environment: low human activity(Newtonian noise) and low seismic noise
Interferometric Readout
T
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 8: Expected signal and sensitivity
Limited by : thermal noise and seismic noise
High Sensitivity Balance
Temperature modulation around Tc
Seismically quiet place for the experiment site
The modulation frequency value is chosen where the sensitivity is the best.
8
P. Puppo - Vacuum Fluctuations at Nanoscale and Gravitation: theory and experiments – Orosei – May 2019

## Slide 9
The balance is suspended with very soft flexural joints
 High frequency noise lowered and hence locking on the interferometer is possible
9
Joints
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)
Temperature modulation system
Arm tilt readout with a Michelson Interferometer
The ITF output on the photodiode and converted in digital signal
The BALANCE

## Slide 10
https://doi.org/10.1140/epjp/s13360-021-01993-w
Tilt measurement comparison between Virgo gravitational wave interferometer (Cascina, Pisa) and Sos Enattos (Sardinia) sites. Most sensitive tiltmeter in the world in the frequency band from 2 Hz to 20 Hz.
A prototype of balance was built to test every component and find the best optic-mechanical configuration for the final balance.
See E. Calloni presentation
for details
Prototype sensitivity in torque is limited by thermal noise.
Preliminary
5

## Slide 11: The data acquisition system and storage
Sampling at 25 kHz;
ITF Control loop with a feedback bandwidth of 200mHz performed with a system hardware of National Instruments;
Data storage in definition;

## Slide 12: THERMAL MODULATION
The experimental chamber is kept at the liquid nitrogen temperature and act as thermal bath.
The thermal modulation must be performed by radiative exchange between sample and an oven which surrounds it. Requirements: Frequency modulation 10mHz
Temperature modulation 2K
YBCo, GdBCO, BSCO sample 20cm diam
Tc (90K-100K)
Modulation frequency and its amplitude around Tc depend on the thermal properties of the materials.
A finite element study is important for the geometry definition and the material choice.
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)
Wires
Arm
Oven
Sample
Example
of FEM result

## Slide 13
Small scale test
Oven and Heater
YBCo sample (4cmX4cmX2mm), 40g
Oven: OFHC copper – thin walls
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 14
liquid nitrogen cryostat
vacuum system
experimental chamber
Cooling Setup
In the oven support there is the liquid
nitrogen direct contact with thermal bath
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 15: Cooling Tests Example
Oven
Sample
P=1 W
P=10 W
Comparison with
FEM (--)
without optimization
K
K
s
Cooling cycles with different heating powers
on the Oven.
Example with 1W heating power performed
on middle 2024
Heated Oven
Oven
Sample
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 16: Data analysis
Two Temp sensors on the Sample (negligible gradient) - Red
Four Temp sensors on the Oven (Black curves – see the gradient)
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)

## Slide 17
Heating TauOven=2201 s (heating and cooling phases)
 Residual Thermal Resistance (kc)
23 W\m2\K
Conduction
kc
Residual Thermal Resistance
Kc included in the FEM
Good agreement obtained
Oven measured temperature
FEM estimation with thermal resistance
P. Puppo - The Low-Energy Frontiers of Particle Physics 10–12 Feb 2025 INFN-LNF Frascati (RM)
Cooling
Heating

## Slide 18
Emissivity estimation (e=1)
Psample
Prad
The agreement between Psample and Prad indicates that the data interpretation is correct

## Slide 19: Sample
Sample thermal properties and radiative exchange
in agreement with the simulation

## Slide 20: Comments
Agreement between data and FEM simulation (model validation)
The modulation frequency is <10 mHz, so some improvements are
implemented:
Use of a radiator
Change of sample geometry

## Slide 21
With a radiator (thin OFHC foil)
from 0.5 to 1.5 mHz
Sample tau=680s
Radiator
NO Radiator
With Radiator

## Slide 22
Oven
cold finger
radiator
ring sample
BSCCO ring sample Graphite radiator
Rin = 92 mm 400x400 mm 500x100 mm P = 10 W
Rout = 100 mm thickness = 0.1 mm thickness = 0.1 mm
V = 20·103 mm3
Modulation of temperature between 107 K and 110 K of a few hundreds of s.

## Slide 23: SAMPLES
R
ΔTC
TC T
Requirements:
TC > 80 K and ΔTC 2 K
Large mass > 200 g → samples with a 10 cm diameter
From the electrical resistance as a function of temperature plot it is possible to obtain information on the first requirement. Also, these plots will let us understand the quality of a sample and if a certain degree of dis-uniformity exits in it.
R
TC T
Ideal superconductor
real superconductor

## Slide 24
 | FRAGMENTS OF A DISC | ENTIRE DISC
Sintered YBCO Sintered YBCO discs were prepared in different sintering conditions (temperature, oxidation) in order to maximise TC and reduce ΔTC (CAN Superconductors). |  | 
crystalline GdBCO/Ag Single-domain melt-textured bulk pieces (CAN Superconductors). |  | 
work in progress
diameter: 100mm
thickness: 3 mm mass: ~ 124 g
(like sample#3)
diameter: 100mm
thickness: 4 mm
mass: ~ 213 g
’’double’’ transition
courtesy of Dr Daniela Stornaiuolo
courtesy of Dr Daniela Stornaiuolo
Tc : 89.5 K
ΔTc: 4.0 K

## Slide 25: CRYOSTAT
Vacuum/Insulation Chamber company: Fantini Sud S.p.A. (Italy) material: steel height , diameter: 3240 mm , 2730 mm mass: 8100 kg
Nitrogen Chamber company: Fantini Sud S.p.A. (Italy) material: steel height , diameter: 2003 mm , 2400 mm mass: 6100 kg
Experimental Chamber company: L.M.P. Amicuzi (Italy) material: steel height , diameter: 1780 mm , 2000 mm mass: 3500 kg
The cryostat consists of three chambers.
The Experimental Chamber, that will hosts
the balance, will be completely submerged
in liquid Nitrogen inside the Nitrogen Chamber.
The volume of liquid Nitrogen in the tank is
approximately 4000 l.
An Aluminium screen around the Experimental Chamber ensures good thermal uniformity even with low liquid Nitrogen level.
Given a thermal input of about 2W/m2, the evaporation time of liquid Nitrogen is estimated
to be about 5 months. In the Insulation Chamber a vacuum (~10-6 mbar) will be created to isolate the system from the outside.

## Slide 26
Superinsulation system of the Second Chamber
Cryotest of the first and second chamber
Third and second chamber

## Slide 27: ARCHIMEDES
Archimedes is an INFN-funded fundamental physics experiment that searches for small weight variations induced by quantum vacuum fluctuations.
It is the first experiment to be installed in the Sar-Grav laboratory, in the area of the disused Sos Enattos mine near Lula (Nu, Sardinia). The SarGrav laboratory has both surface and underground facility, and is dedicated to the research on gravitational waves, gravitational physics and geophysics.
Archimedes will work in the frequency range from 5 mHz to 10 mHz and the signal will be limited by seismic and thermal noise.
Thanks to the unique geological properties of Sardinia and the low population density, Sos Enattos area is an excellent site to host experiments that require very low seismic noise levels. Working at cryogenic temperatures (cryostat) reduces the thermal noise.

## Slide 28: CONCLUSIONS
Archimedes is an experiment conceived to shed light on the discussed interaction between the gravitational field and the vacuum fluctuations.
The measurement must be performed using an extremely sensitive balance and modulating the temperature of superconductors at very low frequencies (about tens of mHz) and with amplitude of a few K. The experiment will work at cryogenic temperature and in a seismically quiet site
An upgraded thermal modulation system have been set up and first promising results were obtained
The results of the simulations support the mechanically isolated system, composed of a ring sample (GdBCO or BSCCO) in thermal contact with a radiator, that exchanges heat only with its thermal bath whose temperature is modulated by the screen that surrounded this system.

## Slide 29: SOME REFERENCES
https://www.facebook.com/archimedes.experiment/
Physics 2020, 2, 1–13; doi:10.3390/physics2010001
doi: 10.1103/PhysRevB.106.134502
https://www.scientificamerican.com/article/how-much-does-nothing-weigh/
doi: 10.1103/PhysRevD.90.022002

## Slide 30
The Low-Energy Frontiers of Particle Physics
10–12 Feb 2025 INFN-LNF Frascati (RM)