## Slide 2: Measuring Ion Dynamics in the Core of European DEMO: A Design Space Exploration for Collective Thomson Scattering
J. Flocken, S. B. Korsholm, J. Rasmussen
Technical University of Denmark, Dept. of Physics, Lyngby, Denmark
e-mail: jlafl@dtu.dk
Notes: Few words about yourself

## Slide 3: Collective Thomson Scattering (CTS)
Probe radiation scatters off electron fluctuations
Collective effects for ion properties define scattered spectrum
Sensitive to:
  ion temperature
  (projected) bulk velocity
  relative ion abundance
  fast ion velocity distribution
Local measurement
Probe
Receiver
Notes: current study:
P ~ 1MW
X-mode, sub-harmonic , ,
, , ,
current study:
P ~ 1MW 𝑇_𝑖, 𝑣_𝑖, 𝑛_𝛼
𝑓_𝑃, 𝛽_𝑅, 𝒓_𝑀, 𝑁_frq

## Slide 4: Optimisation framework
Repeat for different values of parameter of interest
Input parameters
Measurement quality
Ray tracing: Find scattering geometry
Adding noise & Inverting synthetic data
Repeat Nfit times
Forward modelling: Calculate scattered spectrum
New parameter of interest
Update value of parameter of interest to the one with best measurement quality
Reference configuration
Notes: Parameters of interest:
, , ,
Parameters of interest:
𝑓_𝑃, 𝛽_𝑅, 𝒓_𝑀, 𝑁_frq

## Slide 5: Preliminary results
Relative measurement errors weighted by prior uncertainties to get
Key trade-offs:
Lower frequencies mean less ECE noise, but also more refraction
More parallel view means better sensitivity, but also more ECE noise
Notes: Tint = 0.5s

## Slide 6: Conclusions
CTS is viable as a core diagnostic for DEMO
Proof of principle for optimisation procedure
Current optimal setup uses probe frequency of ~58.5 GHz and slightly oblique receiver achieves accuracies of , and
Next steps:
  Improve realism (edge turbulence, variable scenario, ...)
  Consider machine integration
  Beyond DEMO: Apply optimisation procedure to other machines

## Slide 7: Questions?
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.

## Slide 10: EU DEMO: Fusion Reactor Conditions
Large tokamak, ITER-like
4.4 T magnetic field on axis
30 keV core temperature
Designed for single operational scenario little variation between discharges
Extreme neutron irradiation
Limited diagnostics access (breeding blanket)
M. Kannamüller et al., DEMO LAR – Transforming the
2D design point in 3D CAD models (12/11/2024)
Notes: mention new baseline