## Slide 1: SWRIPS MEETING 2024 December 10 WP2 Activities

## Slide 2: WP 2 ACTIVITIES (updated to the internal WP2 meeting held on November 19)
UNIPA:
About 40 days ago, we reactivated the two granular sludge reactors that had been stopped during the summer holidays.
Both reactors are operating under the same conditions as before the interruption: one in anaerobic feeding conditions and the other in fully aerobic conditions. Currently, the systems are operating under a medium organic load, consistent with the conditions prior to the summer break.
After the Christmas holidays, once the reactors have reached steady-state conditions, we plan to increase the organic load to test its maximum value. So, with this step we will complete our study of the three operational conditions forseen in the project, thus low load before the summer break, medium load between late summer and autumn, and high load after January.
With this data we are able to complete the deliverable due at the end of January. We are confident to obtain mature granular sludge by the end of February, or March at the latest. So, we can start the alginate extraction tests.
Regarding the prototype for installation at the Agrumaria Corleone facility, the invitation to tender for its construction has been assigned to a company that is expected to deliver the system by January.
We have already installed the electrical automation and control panel.
We aim to activate the prototype by March.

## Slide 3: WP 2 ACTIVITIES (updated to the internal WP2 meeting held on November 19)
UNIV. MONTPELLIER:
For the project, the works done by our side in Montpellier University are as follows:
1- An overview of citrus industry wastewaters (composition and characterization)
2- Investigating different methods of wastewater treatment that suitable for citrus industry to find new solution for this industry
3- The first phase of the laboratory works: Treated the citrus synthetic wastewater with the help of bubble column bioreactor (working volume 5 L) with granular activated sludge (aerobic granules), which includes the following steps:
A: The stage of adaptation of activated sludge granules with the gradual increase in the organic loading rate (synthetic wastewater: sodium acetate) in this period we studied the performance of granular activated sludge to removal synthetic citrus wastewater in batch mode.
B: Changing the composition of citrus wastewater from acetate to lemon juice (commercially brand) and studied on performance of granular activated sludge to removal of COD, N, P
4- Designing and construction of novel Membrane bioreactor: consisting of airlift bioreactor (membrane system in the riser section part and zeolite chamber in the downcomer section)
5- The second phase of laboratory works: included the following steps:
A: Investigating the real citrus wastewater treatment efficiency with the help of a designed and built bioreactor in the presence of granules activated sludge without the presence of zeolite chamber.
B: Investigating the real citrus wastewater treatment efficiency with the help of a designed bioreactor without the granules activated sludge and in the presence of a zeolite chamber.
6- Now we are working on investigation and analysis of membrane fouling in the presence and absence
of zeolite and investigation of membrane resistances to find the best solution for reducing the fouling of membrane.

## Slide 4: WP 2 ACTIVITIES (updated to the internal WP2 meeting held on November 19)
CNR:
The aim of their research is the development of innovative nanocomposite coating layers for commercial filters with the scope to increase the efficiency of water contaminants removal and to gain antimicrobial and antibiofouling properties.
For this aim, a sulfonated pentablock copolymer was tested for the filtration of bacteria, heavy metals and organic dyes.
Furthermore, this coating layer showed antimicrobial and antibiofouling properties. This coating layers within the addition of graphene oxide flakes will be tested for the filtration of real samples provided from Agrumaria Corleone.
In particular, these samples showed the presence of bacteria and organic matters before and after a biological treatment performed by the group of University of Palermo. Graphene oxide reports high adsorption efficiency and antimicrobial properties that make this material suitable for the removal of organic matter.
The removal efficiency will be estimated by Uv-Visible spectra according to the signals between 250 and 350 nm and antimicrobial and anti-biofouling tests will be performed using standard methods at the joint laboratory “Smart2Sense” (S2S) of CNR & “Regional Reference Laboratory of Clinical and Environmental Surveillance of Legionellosis”, Dept. of Medical and Surgical Sciences and Advanced Technologies “G.F. Ingrassia”, University of Catania.

## Slide 5: WP 2 ACTIVITIES (updated to the internal WP2 meeting held on November 19)
UNIV. UBOUIRA:
The study carried out by the colleagues from the University of Bouira focused on the development of antibacterial filters based on bioactive MgFe₂O₄ photocatalytic nanoparticles.
The nanoparticles were synthesized with varying Mg concentrations (15%, 20%, and 25%) through a systematic process.
These nanoparticles were structurally characterized using X-ray diffraction (XRD) and Fourier-transform infrared spectroscopy (FTIR).
The photocatalytic activity of these nanoparticles was assessed using crystal violet dye as a model pollutant, while antibacterial activity was evaluated against E. coli ATCC 8739 under different treatment conditions, including light exposure and contact with MgFe₂O₄ nanoparticles.
Results demonstrated significant antibacterial efficacy, with reduced bacterial viability in both solid and liquid media.
Additionally, the colleagues developed a novel air filtration system based on these nanoparticles, which exhibited efficiency in removing bacterial load and pollutants.