## Slide 1: SuperB – IFR status of the detector & tooling development

## Slide 2: OUTLINE
Detector
  Status of the design
Tooling
  Status of the development

## Slide 3: STATUS OF THE DETECTOR DESIGN- 1
DETECTOR BASELINE
Grooves in the scintillator accomodating the fibers
The fibers coming from the scintillator are joined to the PM
the signal coming from the PM is collected through a PCB and sent by an electrical wire
GROOVE
FIBER
PM
PCB
WIRE CONNECTOR

## Slide 4: STATUS OF THE DETECTOR DESIGN- 2
DETECTOR LAYOUT
BARREL The longitudinal scintillators are 50 mm in width and 10 mm thick ; the transversal ones are 100 mm in width and 10 mm thick
END CAPS Both the longitudinal and transversal scintillators are 50 mm in width and 10 mm thick
BARREL BEAM AXIS

## Slide 5: STATUS OF THE DETECTOR DESIGN- 3
DETECTOR LAYOUT
Scintillators, fibers & PM are inside a dark box
The PM wires are collected in a bunch coming out from the box
The dark box is made by foils of aluminum 1 mm thick
DARK BOX
BUNCH OF WIRES

## Slide 6: THE BARREL SEXTANT - 1
Since now 9 layers of detector each sextant are foreseen
Absorbers are foreseen into the gaps between the plates
STEEL PLATE
DETECTOR LAYER
EXTERNAL LAYER
GAP

## Slide 7: THE BARREL SEXTANT - 2
Is not yet clear how to accommodate the external layer
EXTERNAL LAYER

## Slide 8: THE ASSEMBLED BARREL
CORNER PLATE

## Slide 9: THE END CAPS - 1
17 detector layers are allowed ; number of layers TBD
The hole of the forward end cap is conical shaped ; the hole of the backward end cap is cylindrical shaped
The layers have to be splitted in three parts and follow the holes shape
DETECTOR LAYERS
SPACERS
DETECTOR LAYERS

## Slide 10: THE END CAPS - 2
The detector layers of the backward end cap have to be shaped also following the cut giving the space for the cooling circuit
COOLING
CYLINDRICAL HOLE
CONICAL HOLE

## Slide 11: Status of the tooling development
The tooling development regards :
  Machine making the grooves housing the fibers
  Machine dispensing the resin fixing the fibers
  A production plan is needed (space, timing, labor, …..) including the quality control ( and the tooling for it )
  The toolings for the installation of the detector in the experimental area are also needed

## Slide 12: Machine making the grooves
The machine consist of :
A plane supporting the scintillator
An head equipped with a cutting disk making the linear groove
An head equipped with a cylindrical milling cutter making the curved grooves for the exit in place of the fibers
The machining time is approximately 8 min each scintillator corresponding to 3,5 weeks/1000 scinti (40 h/week)

## Slide 13: Groove machine sketches (I)
CUTTING DISK
CYLINDRICAL MILLING CUTTER

## Slide 14: Machine dispensing the resin
The machine consist of :
A plane supporting the scintillator
An head equipped with a resin dispenser
The dispensing time has to be checked

## Slide 15: machine machine sketches (I)
RESIN DISPENSER

## Slide 16: Conclusions
The detector design is in a good advanced status of development
The toolings needed for the construction of the detector are under way
The toolings for the assembly in the experimental area have to be developed