## Slide 1: Goals and scope of the Demonstrator
https://agenda.infn.it/event/44387/
R. Losito, CERN
Acknowledging contribution of many colleagues, among which D. Stratakis, D. Schulte,C. Rogers, L. Bottura, L.P. Krzempek

## Slide 2: Outline
Motivation
The ideal Demonstrator
The reality (constraints related to budget, technology, safety etc…)
Propaedeutic R&D
What else can we do with a demonstrator ?

## Slide 3: Motivations and Stakeholders
Picture from this source

## Slide 4: Motivation and Stakeholders: Ideal Demonstrator
What:
  We want to demonstrate 6D reduction of emittance by a factor 2 (C. Rogers)
  We want to benchmark simulations to convince we understand all aspects of the cooling process.
  We want to test the cooling cell technology in an operational environment.
  We also want to have some physics!
How:
  Using the cooling cell technology to be used in the real Muon Collider:
    Magnets: HTS, 20K, cooled by LH2
    RF: Warm, multicell, High Gradient, High Efficiency Klystron
    Absorbers: Hydrogen and LiH
When:
  As soon as possible. If we want to start a MC before 2050, we should confirm the methodology and the technology at least 10÷15 years before

## Slide 5: Demonstrator at CERN
10 kW option
80 kW/4 MW option

## Slide 6: Present layout for the CERN option
Target & Horn
Proton beam dump
Cooling cells
Beam Instrumentation

## Slide 7: Beam Production and Transport (overview)
Beam
dump
TT7 tunnel option adopted as the baseline at CERN
  Proton beam extracted from the PS
  Limited to ~ 10 kW averaged beam power
Design in progress
  Influenced by the constraints of the tunnel
    Target to be placed below the existing shaft
  Preliminary muon bunch intensity estimate: ~ 106 assuming 1013 protons per bunch
Target & Horn capture
Pion decay section
Chicane
Beam preparation system

## Slide 8: Target & Horn
First-pass design optimized for using 14 GeV proton beam to produce ~ 300 MeV/c pions
  Note: does not include engineering constraints
Horn-based pion capture, graphite target (90 cm), current 220 kA
Parabolic and ellipsoidal horn profiles considered
Pion yield (in 210-330 MeV/c range and 2 mm rad transverse acceptance)
  7.9 x 10-4 π+/POT
  Further optimization required
    More ambitious horn currents and target materials
    Refine geometry

## Slide 9: Pion Decay Channel
Need to allow pions to decay, and collect muons
  ~ 40% of pions decay within 8.5 m (at 300 MeV/c)
  Space constraints in TT7
    Civil engineering works required to enlarge the tunnel downstream of the TT7 cavern
Quadrupole-based lattices investigated
  FODO and triplet configurations
  Ongoing work on optimizing for muon capture efficiency
Phase space of muons with 190-210 MeV/c momentum

## Slide 10: Chicane
Selects muons with 190-210 MeV/c momentum and transports them around the beam dump
Beam preparation system (BPS) integrated in the chicane lattice
  To tune the muon beam both transversally and longitudinally
    Transverse emittance ~ 1 - 2.5 mm (collimation)
    In ~ 100 ps bunches (phase rotation)
  Preliminary design done by C. Rogers
To finalise BPS integration within the chicane complex (linear optics matching and tracking studies), after first pass optimization of the pion decay section

## Slide 11: 3D integration model
TT2
TT1
TT7
TT6
(for information)
SPS
Transfer line in TT2
Transfer line in TT7
Demonstrator in TT7
Service building
Junction TT1/TT7
(downstream TT2)
(upstream TT2)
PS

## Slide 12: Integration – demonstrator in TT7
Beam dump
Upstream beam instrumentation
Downstream beam instrumentation
51.8m
29m
6x 5x cooling cells
2m
2m
Imprint of current TT7 (in white)
Part of new service building
(in grey)
Enlargement of TT7 (in red)
Shielded horn with target
Optimization of transfer line components’ position is required or beam dump’s volume to solve interference
4m
14.3m
Ground level
Space envelope for crane
Space envelope for transport
Space envelope for klystrons
Space envelope for lightening
Space envelope for cooling and ventilation
Downstream
Beam dump

## Slide 13: Integration – required service building
Parameters of integrated klystron | Units | CERN specification
RF frequency | MHz | 999.516
Peak RF power | MW | 20
44m
Conclusions
  Conservative approach has been applied in terms of space envelope
  Quantity and space envelope required for klystrons assembly will depend on the final definition of RF frequency and power
  Installation/maintenance scenario gives partial input on transport requirements of service building crane
Modulator
2x control rack
Required lifting range of 3.3m
3.3m
15m
Assembly of 34 klystrons
Circulator
Klystron
Termination load
Integration study is based on CLIC RF L-band klystron (Canon E37503)
Associated components | Type
Modulator | CERN LINAC 4 type has been integrated (final size to be checked)
Circulator | Waveguide junction circulator 704.4 Mhz, 1.5 MW peak, 100kW average (CPR1150) – SPL test place at CERN
RF waveguide | WR1150 Waveguide Components On Microwave Techniques
Termination load | 
3.5m
Transport envelope height

## Slide 14: Integration – proposal of required service building
50m
20m**
(constrain from adjacent 393 - AD/ELENA complex)
10m
2.5m
Personnel and small material access (PAD/MAD)
Material shaft (4x6m)
Buffer zone (3.4x5.7m)
Underground
Surface
20m*
(installation on roof could be considered)
8m*
(installation on roof could be considered)
Proposal of crane
(min 15.1t lifting capacity)
Envelope proposal for power converters (3.8x4.0x40.5m)
Proposal of waveguides routing in dedicated galleries
Ventilation duct cable trays lightening
Transport passage
Required standard services (distinguishers, AUGs, antipanic lightening )
Potential other services and/or shielding
5x5m

## Slide 15: Impact on civil engineering
Access to adjacent 393
(AD/ELENA complex)
Access to new service building
Imprint of new service building
(approximate scale)
TT7
France
Jura side
France
Jura side
View of underground services at CERN
Rainwater
Wastewater
Electricity lines
Cable ducts in use (rerouting)
Cable ducts out of use (reuse or removal)
TT7

## Slide 16: DRAFT R&D Programme
The Ionisation Cooling Demonstrator programme is phased into three main objectives
2026 – 2030
  Build and test a single cooling cell as designed within the EU programme “MuCol”.
  Cost estimated: ~15 MCHF, from 2026 to 2030
  Possibly test it in CTF3, using Dewars or a cryocooler
  Includes: 4 solenoids (2+2), one 3-cell cavity, development of a 704 MHZ, 24 MW klystron.
2028-2033
  Build and Test a “cooling module”, made of 5 cells
  Cost Estimated: ~50 MCHF , decision in 2028, execution from 2030 to 2034
  Possibly test in CTF3 using eventually cryocoolers or a new plant
  Procurement of 6 klystrons

## Slide 17: DRAFT R&D Programme
2030 – 2035
  Construction of an initial Demonstrator Facility (at CERN) .
    Cost estimated: ~50 MCHF, from 2026 to 2030
    Making use of the 5-cell module already tested in CTF3, klystrons and cryogenics
2034-2040
  Use of the facility to test different types of cooling cells.
    Cost: 15 MCHF/year