## Slide 1
Abstract
The NUMEN (NUclear Matrix Elements for Neutrinoless double beta decay) and NURE (NUclear REactions for neutrinoless double beta decay) projects have recently been proposed at the INFN-LNS laboratory to study Heavy-Ion-induced Double Charge Exchange (HI-DCE) reactions to provide data-driven information on the neutrinoless double beta ()-decay nuclear matrix elements. To access the small HI-DCE reaction cross sections (tens of nb), the use of high-intensity beams is a key feature; the MAGNEX facility at INFN-LNS needs a substantial upgrade, requiring a new focal plane detector (a low-pressure gas tracker based on a micropattern gas detector and a telescope array of SiC – CsI(Tl) for particle identification) and a scintillator array of LaBr3(Ce). These new devices must cope with extremely high fluxes of reaction products (up to MHz of ions) and should be sufficiently radiation-hard (up to fluencies of 1013 ions/cm2) while guaranteeing the good performance of the previous detection systems (1/300, 0.2° and ).
The new gas tracker of the MAGNEX spectrometer for high-rate ion detection: an experimental challenge for the NUMEN project
A. Pitronacia,b*, A. Boianoc, G. Brischettob, D. Calvod, F. Cappuzzelloa,b, M. Cavallarob, I. Ciraldob, K. Pallie,f, D. Pierroutsakuc, D. Sartiranad, O. Sgourosb, V. Soukerasb, D. Torresib for the NUMEN Collaboration
*Corresppnding author: A. Pitronaci - antonino.pitronaci@dfa.unict.it
aDepartment of Physics “E. Majorana”, UniCT, Via S. Sofia, 64, 95123 Catania, Italy
bINFN, Laboratori Nazionali del Sud, via S. Sofia, 62, 95125 Catania, Italy
cINFN – Sezione di Napoli, Via Cintia, 80126, Napoli, Italy
dINFN - Sezione di Torino, Via Pietro Giuria, 1, 10125 Torino, Italy
eDepartment of Physics and HINP, The University of Ioannina, 45110 Ioannina, Greece
fDepartment of Chemistry, National and Kapodistrian University of Athens and HINP, 15771 Athens, Greece
0-decay & HI-DCE reactions
Common properties:
same mother/daughter nuclei;
short-range Fermi, Gamow-Teller and rank-2 tensor operators;
DCE-reactions advantages:
No Qvalue dependence;
higher yield due to the nuclear interaction;
MAGNEX and its Focal Plane Detector: upgrade in progress
Magnetic field mapping: MAGNEX peculiarity;
COSY infinity: algebraic methods-based software that solves the transport equation at high order.
(i) Characterization with -source at INFN-LNS
M-THGEM advantages:
High achievable gain, stability, robustness, ideal for heavy-ions detection;
Gain: electron-amplification factor:
IBF: fraction of ions reaching the cathode:
Centre of gravity method
(ii) First in-beam characterization at IFUSP
Tracker performances as a function of the angle wrt incident ion beam;
-source & Pelletron beams: and ;
Safiira setup: Beam spot: 300 m & Angular divergency: 0.2° FWHM
References
: diffusion-contribution;
: geometrical effect
Conclusions and future perspectives:
Characterization at INFN-LNS: the Gain and the IBF obtained experimentally are consistent with the NUMEN requirements. The - and - distributions return angle compatible with the set geometry;
First in-beam characterization at IFUSP: the experimental charge distribution width follows quite well the predicted trend at both ion species and rate changes;
Future perspectives: single-track analysis to improve the quality of the reconstruction algorithm and subsequent resolution studies;
F. Cappuzzello et al., Shedding light on nuclear aspects of neutrinoless double beta decay by heavy-ion double charge exchange reactions, Prog. Part. Nucl. Phys. 128 (2023) 103999.
H. Lenske, F. Cappuzzello, M. Cavallaro and M. Colonna, Heavy ion charge exchange reactions as probes for nuclear 𝛽-decay, Prog. Part. Nucl. Phys. 109 (2019) 103716.
F. Cappuzzello et al., The NUMEN Technical Design Report, Int. J. Mod. Phys. A 36 (2021) 2130018.
M. Cavallaro et al., NURE: An ERC project to study nuclear reactions for neutrinoless double beta decay, PoS BORMIO2017 (2017) 015 [2002.02761].
I. Ciraldo et al., Characterization of a gas detector prototype based on Thick-GEM for the MAGNEX focal plane detector, Nucl. Instrum. Meth. A 1048 (2023) 167893 [2304.02390].
M. Cortesi, S. Rost, W. Mittig, Y. Ayyad-Limonge, D. Bazin, J. Yurkon et al., Multi-layer thick gas electron multiplier (M-THGEM): A new MPGD structure for high-gain operation at low-pressure, Rev. Sci. Instrum. 88 (2017) 013303 [1606.07314].
E.M. Gandolfo, J.R.B. Oliveira, L. Campajola, D. Pierroutsakou, A. Boiano, C. Agodi et al., Response of g-numen labr3(ce) detectors to high counting rates, Instruments 7 (2023).
Y. Assran, A. Sharma Transport properties of operational gas mixtures used at LHC,
https: // doi. org/ 10. 48550/ arXiv. 1110. 6761.
\
Consistent with NUMEN requirements!
2 contributions:
0.6 mm | 0.3°FWHM | 0.5°FWHM | 1/48 | 1/300
0.6 mm | 0.3°FWHM | 0.5°FWHM | 1/48 | 1/300