## Slide 1
Particle Accelerators:
how they work, applications and frontiers
Accelerator Division, LNF-INFN, Frascati
David Alesini

## Slide 2
WHAT CAN PARTICLE ACCELERATORS DO?
Isotopes production
Radiotherapy and adrotherapy
National security
sterilization
Ion implantation
Material treatment
Controlled fission in nuclear reactors
Production of X and  rays for physics of matter
Material studies for fusion
Neutron sources
High energy physics
>40000 accelerators in operation

## Slide 3
HOW DO PARTICLE ACCELERATORS WORK?
SOURCE
ACCELERATOR
SOURCE
USER
A particle accelerator can be considered as a device that transfers energy to charged particles (electrons, protons, ions, ...) through electro-magnetic fields.
USERS
ACCELERATOR

## Slide 4
ACCELERATION
BENDING AND FOCUSING
Transverse Dynamics
Longitudinal Dynamics
To accelerate, we need a force in the direction of motion
2nd term always perpendicular to motion => no energy gain
BASIC EQUATION FOR particle acceleratorS
Beams of charged particles are accelerated with the use of electric fields and are deflected, curved, and focused with the use of magnetic fields. The basic equation for the description of the acceleration and focusing processes is represented by the Lorentz Force.

## Slide 5
The first historical linear particle accelerator was built by the Nobel prize Wilhelm Conrad Röntgen (1900). It consisted in a vacuum tube containing a cathode connected to the negative pole of a DC voltage generator. Electrons emitted by the heated cathode were accelerated while flowing to another electrode connected to the positive generator pole (anode). Collisions between the energetic electrons and the anode produced X-rays.
The energy gained by the electrons travelling from the cathode to the anode is equal to their charge multiplied the DC voltage between the two electrodes.
ACCELERATION: SIMPLE CASE
+
Electric field
Voltage V
Cathode
Anode
Particle energies are typically expressed in electron-volt [eV], equal to the energy gained by 1 electron accelerated through an electrostatic potential of 1 volt:
1 eV=1.6x10-19 J

## Slide 6
To increase the achievable maximum energy, Van de Graaff invented an electrostatic generator based on a dielectric belt transporting positive charges to an isolated electrode hosting an ion source. The positive ions generated in a large positive potential were accelerated toward ground by the static electric field.
DC voltage as large as 10 MV can be obtained (E10 MeV). The main limit in the achievable voltage is the breakdown due to insulation problems.
APPLICATIONS OF DC ACCELERATORS
ELECTROSTATIC ACCELERATORS
750 kV Cockcroft-Walton
Linac2 injector at CERN from 1978 to 1992
LIMITS OF ELECTROSTATIC ACCELERATORS
DC particle accelerators are in operation worldwide, typically at V<15MV (Emax=15 MeV), I<100mA.
They are used for:
 material analysis
 X-ray production,
 ion implantation for semiconductors
 first stage of acceleration (particle sources)

## Slide 7
RF Accelerators : Wideröe “Drift Tube LINAC” (DTL)
Basic idea: the particles are accelerated by the electric field in the gap between electrodes connected alternatively to the poles of an AC generator. This original idea of Ising (1924) was implemented by Wideroe (1927) who applied a sine-wave voltage to a sequence of drift tubes. The particles do not experience any force while travelling inside the tubes (equipotential regions) and are accelerated across the gaps. This kind of structure is called Drift Tube LINAC (DTL).
109-1010 V
With modern particle accelerators, we can now accelerate particles with energy up to thousands of GeVs.
Equivalent to the voltage of thousands of lightning strikes!

## Slide 9
We consider the acceleration between two electrodes in DC.
Ez
source
rate of energy gain per unit length
z (direction of acceleration)
energy gain per electrode pair
DV
+
-
z
Ez
gap
t
E
W=E-E0
Energy-momentum relation
Lorentz force
ELECTROSTATIC ACCELERATION: CONTINUOUS BEAM

## Slide 10
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: BUNCHED BEAM
tinj
E
Only these particles are accelerated
These particles are not accelerated and basically are lost during the acceleration process
t
charge
DC acceleration
t
charge
RF acceleration
Bunched beam (in order to be synchronous with the external AC field, particles have to be gathered in non-uniform temporal structure)
RF period

## Slide 11
ACCELERATION WITH MULTI-CELL RF CAVITIES
Accelerating fields are confined in cavities that are metallic closed volumes were the e.m fields has a particular spatial configuration (resonant modes) whose components, including the accelerating field Ez, oscillate at some specific frequencies fRF (resonant frequency) characteristic of the mode.
The modes are excited by RF generators that are coupled to the cavities through waveguides, coaxial cables, etc…The working frequencies can go from MHz to ten of GHz depending on the applications
The resonant cavities are usually grouped in multi-cell structures. This choice is motivated by reasons of efficiency and compactness.
There are both cavities that operate at normal conducting (NC, copper, surface resistance m) and superconducting (SC, niobium, surface resistance n) cavities that operate at few K.
SC (more complicated because of the necessity of cryostat) are used for operation in multi bunch/long train/high duty cycle machines
The average accelerating gradients that can typically be obtained are of the order of few 10 MV/m in SC and up to more than 100 MV/m in NC.

## Slide 12
ACCELERATION
BENDING AND FOCUSING
Transverse Dynamics
Longitudinal Dynamics
LORENTZ FORCE: ACCELERATION AND FOCUSING
Particles are accelerated through electric field and are bended and focalized through magnetic field.
The basic equation that describe the acceleration/bending /focusing processes is the Lorentz Force.
To accelerate, we need a force in the direction of motion
2nd term always perpendicular to motion => no energy gain

## Slide 13: MAGNETIC FIELD: DEFLECTION
E. O. Lawrence (1930) had the idea to curve particles on a circular trajectory in order to pass many times in the same accelerating system gaining energy at each passage
Particles traveling in a linear accelerator pass through the accelerating structure only once, while in a circular accelerator they pass into the same cavity several times and at each turn, bunches gain energy thanks to the RF accelerating electric field.
With magnetic fields it is possible to bend charged particles (moving at speed v) and it is possible to focus them keeping the particles confined inside in the vacuum chamber.
magnet
RF Cavity
S
N

B
Super Conducting magnets
(up to 15 T)
Normal Conducting magnets
(up to 1 T)

## Slide 14: MAGNETIC FIELD: FOCUSING
Quadrupoles are used to focalize the beam in the transverse plane. It is a 4 poles magnet:
B=0 in the center of the quadrupole
The B intensity increases linearly with the off-axis displacement.
If the quadrupole is focusing in one plane is defocusing in the other plane
N
N
S
S
z
x
beam
y
x
y
Electromagnetic quadrupoles G <50-100 T/m

## Slide 15
To obtain the overall focus of a particle beam along a transport channel or in a circular accelerator it is necessary to use a sequence of quadrupoles with the alternating sign.
This configuration is able to guarantee stable trajectories.
A quadrupole focus in one plane and de-focus in the other plane.
The transverse trajectory described by each particle is a pseudo-sinusoid.
The envelope of all trajectories is called the β- function.
TRANSVERSE FOCUSING: -FUNCTION
Longitudinal coordinate
s

## Slide 16
m
km
A typical LINAC is, in conclusion, an alternating sequence of accelerating sections, quadrupoles, diagnostic elements (that allow the measurement of the beam position, profile, charge, etc…) and pumping systems. Vacuum in a particle accelerator is typically on the order of 10-8-10-10 mbar. If such pressures were not reached, the particles would be lost due to impacts with the gas molecules. They can be of few m up to km…
By dipoles the beam can also be circulated in a ring. A single accelerating cavity accelerate the particles at each passage. These machines are called synchrotrons.
LINAC AND SYNCHROTRON

## Slide 17
APPLICATIONS

## Slide 18
MEDICAL APPLICATIONS: RADIOISOTOPE PRODUCTION
Production of radioisotopes: protons of 7-100 MeV accelerated with cyclotrons or linacs (50 type of isotopes, used for diagnostics and treatment are produced with accelerators)
PET: Positron Emission Tomography

## Slide 19
One irradiate tumors woth X-rays or electrons
Collimation system
Metallic sheet for X ray production
LINAC
MEDICAL APPLICATIONS: RADIOTHERAPY

## Slide 20
Anti-tumor therapy based on irradiation with protons and heavy ions (C).
It is more effective and more localized (Bragg resonance) than that based on electrons or X-rays
Specialized centers: CNAO in Pavia, PSI in Zurich, Loma Linda in California, Japan, ...
Courtesy M. Pullia
MEDICAL APPLICATIONS: ADROTHERAPY

## Slide 21
EXPLORING MATTER WITH ULTRA BRIGTH X-RAYS
electron
photon
A charged particle at a given energy which is bent by a dipole magnet emits electromagnetic radiation (synchrotron light).

The radiated energy is related to the fourth power of the particle relativistic factor . It follows that only electron machines (light particles) basically emit photons (except LHC!).
X Rays:
0.01-10 nm (10-11-10-8 m)
10-10 m

## Slide 22
Radiation FROM ULTRARELATIVISTIC PARTICLES
Electric Field
Charge at rest

## Slide 23
Moving charge
Linear trajectory
Relativistic contraction of the E field lines
vc
Radiation FROM ULTRARELATIVISTIC PARTICLES
Charge at rest

## Slide 24
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 25
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 26
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 27
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 28
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 29
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 30
Radiation FROM ULTRARELATIVISTIC PARTICLES

## Slide 31
Moving charge
Trajectory from a dipole
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 32
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 33
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 34
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 35
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 36
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 37
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 38
Plane wave
Radiation FROM ULTRARELATIVISTIC PARTICLES: DIPOLE

## Slide 39
Moving charge
Trajectory in an undulator
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 40
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 41
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 42
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 43
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 44
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 45
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 46
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 47
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 48
Radiation FROM ULTRARELATIVISTIC PARTICLES: UNDULATOR

## Slide 49
http://www.isa.au.dk/animations/animations.asp

## Slide 50
BRIGHTNESS OF A PHOTON SOURCE
Electron beam
trajectory
Source area
(Aelectron beam dimension)
Angular divergence of the radiation ()
Photon flux (PF)
The most important parameter for a light source is not (only) the number of emitted photons per second but their “density” called brightness.

## Slide 51
EUROPEAN SYNCHROTRON SOURCES

## Slide 52
FUNDAMENTAL PHYSICS: COLLIDERS
Collision between particles and targets

## Slide 53
Collider ring
Detector
The brilliant idea of Bruno Touschek (1960) was to use colliding particles and antiparticles that, in their annihilation, would release all their energy to create new particles. Furthermore, the collision products would have been relatively "simple" compared to those produced by collisions against a complex target.
Birth of the Modern Colliders: TOUSCHEK

## Slide 54
AdA (Anello di Accumulazione) FRASCATI 1960-1965
AdA is made of a weak focusing magnet able to circulate particles (e+/e-) with an energy of 250 MeV.
Trace of the first electrons accumulated in AdA. The average life was 21 sec, the average number 2.3.

## Slide 55
Number of particles per beam (1010)
Transverse dimensions at the Interaction point (IP): up to few  (or even less)
For gaussian beams
[cm -2 sec -1 ]
y
x
IP
luminosity
The luminosity in a collider is a measure of the collision rate. Is proportional to:
-the amount of colliding particles
-frequency of collision
-the beams dimensions at the interaction point
Collision frequency (up to hundreds of MHz)

## Slide 56
frequency of event of  particle production
Lσ =300 events/s
~2.1010
368.000.000 Hz (120 bunches)
1 mm
10 m
Cross section 
~ 3 ·10-30 cm2
LUMINOSITY: EXAMPLE
Particle  generation @ DAФNE

## Slide 57
LHC (Large Hadron Collider) CERN
LHC main parameters
  Colliding particles proton-proton but also ions (Pb-Pb)
  Max Energy per beam 7 TeV
  Number of bunches 2808
  Crossing angle 300 rad
  Emittance 5x10-10 m
  IP transv. Dim. (x=y) 16 m
  Machine length 27.8 Km
BMAX dipoles 8 T with I= 11700 A @T = 1.9 K
L = 1034 cm-2s-1

## Slide 58: ENERGY AND LUMINOSITY: COLLIDER DEVELOPMENT
Energy densities more and more “near” to the BIG BANG
Increase the number of events per second for high precision measurements
The development of colliders followed two different directions:
-higher and higher energies (discovering machines, LHC,…)
-higher and higher luminosities (to increase the number of events and to perform precise measurements)
Saturation energy of different technologies

## Slide 59
MAIN R&D ACTIVITIES ON PARTICLES ACCELERATORS
There are several R&D lines on particle accelerator physics and technology that we can summarize as follows:
HIGH ACCELERATING FIELD
HIGH BEAM QUALITY/INTENSITIES
SUSTAINABILITY: REDUCTION OF COST, POWER CONSUPTION
Compact machines for fundamental, applied physics and industrial or medical applications
New generation synchrotron radiation sources
HIGH ENERGY MACHINES
High energy colliders for fundamental physics
MI-LASA and LNL activities on supercoducting cavities

## Slide 60
LIMITS OF HIGH ENERGY CIRCULAR MACHINES
Hadron colliders (p,…)
The maximum magnetic fields reachable with superconducting Nb3Sn magnets is 16-17 T (8 T LHC)
Lepton colliders
The limit even more than the maximum radius of curvature is given by the power lost by synchrotron light emission
1
2
Larger radius and/or new magnets (HTS, High Temperature Superconductors?)
Larger radius or linear accelerator (limited luminosity and nm beam at IP)

## Slide 61
HIGH ACCELERATING FIELD NORMAL CONDUCTIONG HIGH FREQUENCY
The basic idea is to concentrate electromagnetic energy in smaller volumes to increase its density and, therefore, the value of the accelerating field.
High frequency metallic structures
Metallic structures working at 12 GHz can reach up to 100-150 MV/m accelerating field gradient with a small number of discharges: vacuum breakdown is a complex phenomena still under investigation.
Cell length ~ 2.5 cm
Cell length ~ 5 cm
Cell length ~ 1 cm
S-band
(3 GHz)
C-band
(6 GHz)
X-band
(12 GHz)
Ka Band
(36 GHz)
Cell length few mm
R&D on NC LINACS @INFN
EuPRAXIA@SPARC_LAB (LNF)
ASTERIX experiment. Funded by INFN CSN5.
MICRON experiment. Funded by INFN CSN5.

## Slide 62
HIGH ACCELERATING FIELD DIELECTRIC STRUCTURES POWERED BY LASERS
Lasers are intense pulsed sources of electromagnetic field and at the working frequencies of lasers (1013-1015Hz) metallic structures cannot be used (dissipation,…)
Dielectric structures can be used
Gradient up to 5 GV/m have been measured
MICRON experiment. Funded by INFN CSN5.
Main problems:
Low charge (university-scale/small lab/medical applications up to now)
Low energy: short devices (<1 mm), to achieve high energies thousands of devices have to be sincronized
Alignment and stabilization problems
Wakefield instabilities

## Slide 63
PLASMA ACCELERATORS
Elettric field 100 MV/m
Field up to 100 GV/m
Laser or beam pulse (driver)
plasma
Plasma wave
km
m
Accelerated beam (witness)
Accelerating bubble

## Slide 64
PLASMA ACCELERATION MECHANISM
The laser or beam pulse creates a moving bubble (with velocity c) in the plasma, which allows continuous acceleration of the electron beam
Eacc40 GV/m in a 20 cm channel with a 850 TW laser

## Slide 65
Sparc-like photo injector
X-band linac
Plasma module
FEL
Users
EUPRAXIA@SPARC_LAB (LNF) PROJECT
Plasma acceleration R&D is focused in several directions:
beam quality improvement, stability
repetition rate
staging for maximum energy improvement
…
European project (ESFRI roadmap) with two pillars (Frascati and ELI-Praga) for implementation of infrastructures based on plasma wakefield acceleration producing high quality beams for different applications (2028-2030)

## Slide 66
CERN FUTURE COLLIDERS OPTIONS
FCC: MAIN OPTION
CIRCULAR COLLIDER 90 km
FCC-ee (phase I), 90 GeV/baam
FCC-hh (phase II), 85 TeV, 14 T dipole magnets
CLIC- LINEAR COLLIDER
LINEAR COLLIDER e+/e-
50 km, 1.5 TeV, 100 MV/m accelerating cavities

## Slide 67
CONCLUSIONS
PARTICLE ACCELERATORS REMAIN ONE OF THE MOST POWERFUL INSTRUMENTS IN FUNDAMENTAL PHYSICS RESEARCH, PHYSICS OF MATTER AND PARTICLES WITH MANY APPLICATIONS IN MEDICAL AND INDUSTRIAL FIELDS.
A JUMP IN TECHNOLOGY IS NECESSARY AND NEW IDEAS AND IMPORTANT RESULTS OPENED NEW AND PROMISING WAYS
THE R&D IN THE PHYSICS AND TECHNOLOGY OF PARTICLE ACCELERATORS REMAINS ONE OF THE MOST EXCITING FIELDS OF RESEARCH IN APPLIED PHYSICS IN WHICH FANTASY AND CREATIVITY ARE THE FUNDAMENTAL INGREDIENTS… AND…
THANK YOU FOR YOUR ATTENTION!
Acknowledgements
M. E. Biagini, A. Biagioni, M. Boscolo, F. Cardelli, A. Cianchi, L. Faillace, M. Ferrario, A. Gallo, S. Guiducci, C. Milardi, A. Mostacci, R. Pompili, R. Pompili, B. Sciascia

## Slide 68
https://acceleratori.infn.it/?lang=en
Serve as a link between the community of accelerator experts within the INFN and the Institute’s top governing bodies (President, Executive Board, and Board of Directors).
Promote the establishment of thematically aligned networks among accelerator specialists on topics of significant interest
Foster the harmonization of expertise and technical infrastructure within the Institute in the field of accelerator science and technology.
Encourage and support participation in regional, national, and international funding calls.
Provide advisory input, upon request by INFN management, on matters related to particle accelerators, including the promotion and participation in projects, as well as strategic guidance in this domain.
I’m coordinating INFN-ACCELERATORI that is a committee, composed of various specialists with extensive experience in accelerators and accelerator-related technologies, which aims to: