## Slide 1: Hands-on Session: Calculation of the Loss Angle from Real Measurements of Free Oscillation Decay
Diana Lumaca
INFN – Sezione di Roma Tor Vergata

## Slide 2: Loss Angle
Essential quantities to characterize the dissipative behaviour of materials:
  Quality factor
    Systems with high dissipations have low and larger off-resonance contribution, and viceversa
  A system is dissipative whenever its response to a step input is characterized by a finite relaxation time phase lag between input and response Loss angle
    At resonance
    Additive quantity
  Any physical system can be composed by many different parts (i), whose stored energies (s) can be dissipated by many different mechanisms (m)
    Dilution factor
GeNS – schematic view
Notes: Maybe you have already seen what is the loss angle first of all for a linear dissipative system it is the inverse of the quality factor at the resonance frequency. High dissipation low Q. Low dissipation high Q. The loss angle is an additive quantity, and any physical system can be composed by many different dissipative mechanisms considering the loss angle the ratio between the dissipated energy wrt the total energy in a cycle, every dissipation mechanism is weighted by a dilution factor that depends on the store energy with respect the total one

## Slide 3: What to do?
Analyse the data: Use your preferred software or computing platform to process the data.
  Calculate damping: Compute the damping characteristic time () of the free oscillations.
  Determine the loss angle: Using the results, compute the loss angle ().
Access the measurements: Download the real measurements of the decay of free oscillations from google drive link
Form groups: Create up to 6 groups and assign each group one of the following files:
  5530, 12641, 21926, 33288, 33673, 46640
Understand the data format: The data files contain two columns: two columns (time, amplitude)
File name | fmeasured
5530 | 5530,0078
12641 | 12641,375
21926 | 21926,609
33288 | 33288,125
33673 | 33673,4375
46640 | 46640,875
modo | frequenza | a | tau | phi
(5,0) | 33288,13 | 0,01481 | 2,222 | 4,31E-06
(2,1) | 33673,44 | 0,001916 | 11,72 | 8,07E-07
(6,0) | 46640,88 | 0,003551 | 1,3 | 5,25E-06
% Parametri fisici del campione (SiO2)
diam. = 25.4e-3; % Diametro in metri
thick. = 0.5e-3; % Spessore in metri
E = 72e9; % Modulo di Young (Pa)
rho = 2200; % Densità (kg/m^3)
nu = 0.17; % Coeff. di Poisson
modo | frequenza | a | tau | phi
(2,0) | 5530,01 | 0,5237 | 43,0225 | 1,34E-06
(3,0) | 12641,38 | 0,0032 | 12,2636 | 2,05E-06
(4,0) | 21926,61 | 0,0363 | 4,209 | 3,45E-06
Top secret
Top secret
…
…
Top secret

## Slide 4: Resonant modes
mode |  | File name | fmeasured | ϕmeasured
m | n |  |  | 
2 | 0 | 5530 | 5530,0078 | 1,37E-06
3 | 0 | 12641 | 12641,375 | 2,47E-06
4 | 0 | 21926 | 21926,609 | 3,60E-06
5 | 0 | 33288 | 33288,125 | 4,44E-06
2 | 1 | 33673 | 33673,4375 | 8,53E-07
6 | 0 | 46640 | 46640,875 | 5,44E-06
Top secret
Top secret
Top secret
Top secret
Top secret
Top secret
Top secret
Top secret
Use ResonantModes.m program to see the deformation shape of your mode!

## Slide 5
Start
Annealing 900°C
44 days in vacuum
CO2 polishing of the edge
20 days ageing
Stability of the substrate’s losses and resonant frequencies is mandatory