## Slide 1: SuperB SVT Z-side Strip Connection Options
Irina Rashevskaya, Luciano Bosisio
INFN-Trieste e Università di Trieste

## Slide 2
Each barrel layer has its own dedicated sensor
even number of sensors in each ladder
254 wafers (150 mm)
8 mask sets
Sensor dimensions

## Slide 3
The number of strips has to be an integer. This brings a small difference in Barrel Length (less than 0.4 mm) with respect to the values given by Filippo.
Barrel Lengths

## Slide 4
Need ganging X2 and X3 for layer 4 and 5.
Strip Ganging Option
A prototype fanout for layer 3 is being produced with this ganging configuration

## Slide 5
Apply:
Pairing x2 if track projection exceeds 4 times the readout_pitch
spans more than 4 strips and
Pairing x3 if it exceeds 6 times the readout_pitch
Strip Pairing Scheme in Layers 1, 2, 3
OK!
A prototype fanout for layer 3 is being produced with this pairing configuration

## Slide 6
The maximum track projection for layer 4 and 5 (663um in Ly 5b) is less than 4 times the readout pitch.
We try to apply Pairing x2 if track projection is more than 2 times the readout pitch and Pairing x3 if it is more than 3 times the readout pitch.
Strip Pairing Scheme in Layers 4, 5
We have 640 readout channels only!
=> We need also
ganging
layer 4a Pairing x2 and ganging x2
layer 4b Pairing x2 and ganging x2, x3 (only 11 ch.)
layer 5a Pairing x2 Paring x3 and ganging x2, x3
layer 4b Pairing x2 Paring x3 and ganging x2, x3
Too complex….