## Slide 1: Physics-driven optimisation of the TRIDENT neutrino telescope
Iwan Morton-Blake
On behalf of the TRIDENT collaboration
Tsung-Dao Lee Institute / Shanghai Jiao Tong University
The Neutrino Telescopes Workshop 2025, Padova, Italy

## Slide 2
Solar
Reactor
Atmospheric
Geoneutrinos
Supernova
1010
1
10-20
10-10
keV GeV PeV
Flux [cm-2 s-1 sr-1 MeV-1]
Homestake (1970)
SNO (2002)
KamLAND (2005)
Borexino (2010)
Reines & Cowan (1957)
Daya Bay (2012), KamLAND +…
Kamiokande (1987)
Super-Kamiokande
(1998)
Active galactic nucleus, cosmological sources
Exotic Searches
KamLAND-Zen (2011) (0vBB)
Neutrino Sources
~70 years experience in neutrino measurement!

## Slide 3
Entering Next-Gen: Liquid Scintillator Detectors
Solar
Reactor
Atmospheric
Geoneutrinos
Supernova
1010
1
10-20
10-10
keV GeV PeV
Flux [cm-2 s-1 sr-1 MeV-1]
Kiloton- LS
Detectors
Active galactic nucleus, cosmological sources
Exotic Searches
JUNO
~20,000 tons
Liquid scintillator

## Slide 4
Entering Next-Gen: Water Cherenkov / LArTPCs
Solar
Reactor
Atmospheric
Geoneutrinos
Supernova
1010
1
10-20
10-10
keV GeV PeV
Flux [cm-2 s-1 sr-1 MeV-1]
Active galactic nucleus, cosmological sources
Exotic Searches
e.g.: Hyper-Kamiokande
~200,000t purified water
DUNE
~70 kT Liquid Argon

## Slide 5
Neutrino Telescope Cherenkov Detectors
Solar
Reactor
Atmospheric
Geoneutrinos
Supernova
1010
1
10-20
10-10
keV GeV PeV
Flux [cm-2 s-1 sr-1 MeV-1]
Under-Ice/Water
Telescopes
Active galactic nucleus, cosmological sources
Exotic Searches

## Slide 6
200
kgs
23 kilotons
1 kiloton
190
kilotons
0.1 km3
1 km3
3 kilotons
1 kiloton
They grow up so fast 🥲
…

## Slide 7: Neutrino Telescopes
(Some) highlights from the last 12 years
Detect extraterrestrial high-energy diffuse neutrino flux
Evidence for neutrino emission from a flaring blazar
Glashow resonance event at 2.3σ
Neutrino emission from active galaxy NGC 1068 reaches 4σ
Galactic plane >TeV neutrinos observed at a 4.5σ
Ultra-high-energy cosmic neutrino
Science. 342 6161 (2013)
Science. 361 6398 (2018)
Nature 591 220-224 (2021)
Science 378 538-543 (2022)
Science 380 1338 (2023)
Nature 638 376–382 (2025)
More, better neutrino telescopes on the way!

## Slide 8: TRIDENT  ~10km3

## Slide 9: Timeline
TRIDENT
Expeditions to Sea
R&D
for Technology + Deployment
Present day
First String Deployment: Phase -1
Full TRIDENT Array
This talk
“Neutrino Telescopes in China”:
Donglian Xu 3rd October 09:00

## Slide 10: TRIDENT  ~10km3
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors

## Slide 11: TRIDENT  ~10km3
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors
Want to optimize for both goals simultaneously
Detector Design:
Bigger is better?

## Slide 12: Event interaction types
decay
(τ decay can also produce muons)
Neutral-Current
Charged-Current
Muon tracks
Cascades
TRIDENT simulation

## Slide 13: All-Flavour Detection
+ Excellent for pointing  point source discovery
+ Detection volume > Detector volume
Partial energy deposition within detector
Atmospheric muons : strong down-going background
+ , detection channels
+ Energy deposition within detector
+ Low atmospheric muon and neutrino background
Poorer pointing
Detection volume Detector volume
Difficult to optimize for all types events of all energies!

## Slide 14: All-Flavour Detection
Track angular resolution
TRIDENT Simulation
TRIDENT Simulation
Cascade angular resolution
Simulated Track-like event in TRIDENT
Simulated Cascade-like event in TRIDENT
~0.1°
~3°

## Slide 15
Experimental goals:
Rapidly discover neutrino sources
Sensitivity to all flavors
Point source sensitivity/
Discovery potential vs declination with tracks
TRIDENT neutrino flavour ratio sensitivity with tracks, cascades and double-pulse identification
Combine both goals into a single figure of merit?
Nature Astronomy 7, 1497–1505 (2023)
“Real-time Optical Calibration Strategy and Astrophysical Tau Neutrino Identification in Water-based Next-generation Neutrino Telescopes” W. Tian, PhD Thesis

## Slide 16
1) Source neutrino flux
Energy + Direction
2) Forced Interaction near the detector
Event weighting  Earth propagation, cross sections, oscillation
3) Deep Inelastic Scattering (CORSIKA8[1,2])
Neutral and Charged Current interactions, Particle production
6) Detector response
Photoelectron generation, 40K + dark noise mixing
4) Lepton, hadron propagation (CORSIKA8/Geant4[3])
5) Cherenkov photon generation + propagation (Geant4/Optix[4])
Scattering, absorption, dispersion
7) Electronics response, Triggering, data cleaning
TRIDENTSim
Signal photons +
noise + radioactivity
time

## Slide 17
Sensitivity
Resolution
$ ¥ €
Detector design
Photocoverage
# PMTs

## Slide 18: Neutrino Telescope Design

## Slide 19: Neutrino Telescope Design
Experiment design must be lead by physics,
limited by engineering and cost
Physics
Cost + Engineering

## Slide 20: Neutrino Telescope Design
Site Location
2) Optical Modules – hDOMs
3) String Layout / Volume

## Slide 21: Detector Design – Location
1:25 scale string models in SJTU Ship-towing tank
South China Sea
Near the equator
3.5 km deep
Large, flat plane
TRIDENT
YongXing Island
180km
480km
540km
Sanya
Hong Kong
TRIDENT sensitive viewing region
Low seacurrents, bioactivity
“MuonSLab: A plastic scintillator based detector for muon measurement in the deep ocean”
Low atmospheric muon rate

## Slide 22: Detector Design – hDOMs
Hybrid Digital Optical Module
Hybrid: PMTs + SiPMs
JINST 19 (2024) 06, P06011
JINST 19 (2024) 05, P05040
SiPMs
 Fine timing resolution
Fills spaces between the PMTs, extra sensitivity
SiPM arrays aids in calibration
PMTs
Fine timing resolution (TTS FWHM ~1.8 ns)
High quantum efficiency >30% at 400nm
Balance design with:
Physics performance
Reduction of backgrounds
e.g. 40K & PMT Dark noise
Cost & Power consumption
Additional low energy physics

## Slide 23: Detector Design – hDOMs
“A Cost Effective Optimization of the hybrid-DOM Design for TRIDENT”
3-inch PMT hDOM design
31 3” PMTs
24 SiPMs
(4x8 array)
4-inch PMT hDOM design
19 4” PMTs
5 SiPMs
(8x8 array)
Check / compare performances for various designs:
e.g. neutrino detection efficiency + angular resolution

## Slide 24: Detector Design – Geometry
Nature Astronomy 4 913–915 (2020)
KM3NeT
Baikal GVD
P-ONE
5th International Symposium on Cosmic Rays and Astrophysics, Zhan-Arys Dzhilkibaev
Lake Louise Winter Institute 2025,
Agustín Sánchez Losa
Nature Astronomy 7, p1497–1505 (2023)

## Slide 25: Detector Geometry : String Spacing
Given N number of strings, how should they be arranged?
(looking top-down on detector)
Quickly alters detector volume
Strongly impacts detection efficiency
Deployment difficulties, strings may tangle if too close!
Increasing string spacing / volume

## Slide 26: Detector Geometry : String Height
Given N number of strings, how should they be arranged?
(looking side-on)
Impacts horizontal event detection cross-section
Deployment/maintenance issues if too tall!
Increasing string height / volume

## Slide 27: Detector Geometry : Clustering
Given N number of strings, how should they be arranged?
Deployment/maintenance benefits
Impacts energy range
Miss events in cluster-cluster gaps
More edge events
Equal volumes,
More severe clustering
(looking top-down on detector)

## Slide 28: Comparing Geometries
“Reference” geometry
Using full-chain detector simulation with site-measured optical conditions, atmospheric backgrounds and hDOM backgrounds:
Figure of Merit:
Neutrino source discovery potential
Designs compared vs “Reference” geometry:
Average string spacing ~ 100m
String height ~ 600m

## Slide 29: Track Performance vs Detector Size
TRIDENT Simulation
TRIDENT Simulation
Relative signal event rate
Rel. pointing resolution
Better
Dense 3km3  Sparse 16km3
Track-like events
Big sparse detector : More (fewer) high- (low-) energy tracks Worse direction resolution

## Slide 30: Cascade Performance vs Detector Size
TRIDENT Simulation
TRIDENT Simulation
Relative Signal Event Rate
Rel. Pointing Resolution
Better
Dense 3km3  Sparse 16km3
Cascade-like events
Big sparse detector : More (fewer) high- (low-) energy cascades Worse direction resolution

## Slide 31: Source Discovery Potential
Assuming the “standard” geometry takes 5 years to discover a given source
How much slower/faster can each geometry discover same source?
Bigger detector is not necessarily better
Worse at low energies tracks and cascades:
Worse at high energies tracks and cascades:
Dense detector favours low energy events
TRIDENT Simulation
“hard” source
“soft” source

## Slide 32: Source Discovery Potential – String Clustering
String clusters show poorer performance for all channels, except for low energy cascades.
However, physics must be weighed against deployment & maintenance cost, safety
TRIDENT Simulation

## Slide 33: Source Discovery Potential – Optical properties
While geometry choice is significant,
water optical properties are essential!
 Attenuation length can have larger impact than geometry choices
TRIDENT Simulation

## Slide 34: Source Discovery Potential – Optical properties
Photon detection efficiency should therefore lead the design of a detector.
Ongoing/future measurements at site and in TRIDENT Phase-1 will influence the final design choice
TRIDENT Simulation

## Slide 35: Conclusion
TRIDENT is an upcoming neutrino telescope aims to reach next-generation size and performance
TRIDENT’s design is optimised directly via its physics goals:
  Rapid source discovery and all-flavour detection
Bigger does not necessarily mean better:
  Event rate must be balanced with reconstruction quality.
Optical properties play a significant role and should lead design
  Phase-1 deployment next year used is input
Aim to add flavour ratio sensitivity into design optimisation

## Slide 36: TRIDENT Analysis and Simulation
When they’re not building the detector, they’re contributing to the work shown here.
TRIDENTSim development
Reconstruction and analysis methods for Phase-1
Developing TRIDENT’s diverse physics programme