## Slide 1: Background Components of the JUNO Liquid Scintillator
Guanda Gong
on behalf of the JUNO Collaboration
Sep 29th - Oct 3th, 2025
Padova (Italy)

## Slide 2: Overview
The JUNO Experiment
LS Background Components’ Impact on Physics
  The impact on Reactor Neutrino () Detection
  The impact on Solar Neutrino () Detection
Background Control Strategy
Commissioning Results
Summary

## Slide 3: Jiangmen Underground Neutrino Observatory
Aim to determine the neutrino mass ordering (sign of ), using reactor neutrinos
Located at Jinji town, Kaiping city, Jiangmen city, Guangdong Province, China
Equal distance (53 km) away from two reactor power plants (26.6 GW), doubling the flux
Yangjiang NPP 17.4 GW
Taishan NPP 9.2 GW
Daya Bay NPP
Huizhou NPP
Lufeng NPP
53 km
53 km
Hong Kong
Macau
Guang Zhou
Shen Zhen
Zhu Hai
2.5 h drive
Previous site candidate
Daya Bay
JUNO
Talk by Y.F. Wang at ICFA seminar 2008, Neutel 2011;
Paper by L. Zhan, Y.F. Wang, J. Cao, L.J. Wen, PRD78:111103,2008; PRD79:073007,2009
3
Double Chooz
RENO

## Slide 4: Jiangmen Underground Neutrino Observatory
Overburden
~650 m (1800 m.w.e.)
Slope tunnel：1265 m @ slope of 42%
Vertical tunnel: 563 m
Civil construction finished in Dec, 2021
Data Taking Started at
Aug 26, 2025
Detector construction finished in Dec, 2024
Prog.Part.Nucl.Phys. 123 (2022) 103927
Reactor
Supernova
Atmosphere
Earth
Solar
~60 IBDs per day
Several IBDs per day
Several per day
Hundreds per day
~5000 IBDs for CCSN @10 kpc
+
New physics
More details of the JUNO experiment status can be found in Monica’s Talk
20kt Liquid Scintillator
Energy resolution ~ 3%@1MeV
Vanessa’s talk
Han’s talk

## Slide 5: Background Components of the LS
The 20kt Liquid Scintillator (LS) in the Center Detector (CD) compose of :
  LAB (solvent)
  2.5 g/L PPO (fluor)
  3 m g/L bis-MSB (wavelength shifter)
  g/g BHT (antioxidant)
Sources of the contamination
  The U, Th, K in the ingredients
  Transportation
  The remaining dusts in the acrylic surface
  The remaining dusts and radioactive gas (222Rn, 85Kr) inside the Central Detector (CD) before filling
Good physics sensitivity requires low contamination
  Strict standard and strategies are proposed, balancing the physics and engineering.
JHEP 11 (2021) 102
ppb = 10−9 g/g
NIM.A 908 (2021) 164823
Notes: Linear Alkyl Benzene 2,5-dyphenyloxazole 1,4-bis(2-methylstyryl) benzene butylated hydroxy toluene

## Slide 6: Overview
The JUNO Experiment
LS Background Components’ Impact on Physics
  The impact on Reactor Neutrino () Detection
  The impact on Solar Neutrino () Detection
Background Control Strategy
Commissioning Results
Summary

## Slide 7: LS Background Components’ Impact on Physics The impact on Reactor Neutrino () Detection
Chin.Phys.C 49 (2025) 3, 033104
arXiv:2503.00968
-
Reactor are detected by inverse beta decay (IBD):
Signal rates after selection (counts per day)
Mis-combine two uncorrelated radioactive decay / spallation neutron events
U, Th chain induce and deexcitation cascade signal
Background rates after selection
arXiv:2503.00968
Accidentals
More details of JUNO’s reactor neutrino measurement can be found in Han’s Talk

## Slide 8
Chin.Phys.C 49 (2025) 3, 033104
arXiv:2503.00968
-
Reactor are detected by inverse beta decay (IBD):
Signal rates after selection (counts per day)
U,Th ~
U,Th ~ , 210Po ~
arXiv:2503.00968
Background rates after selection
U/Th, 80k cpd/kton 210Po’s contribution to the B/S of the reactor neutrino measurement < 2% !
LS Background Components’ Impact on Physics The impact on Reactor Neutrino () Detection
arXiv:2503.00968
More details of JUNO’s reactor neutrino measurement can be found in Han’s Talk
Accidentals

## Slide 9: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
Solar , can be detected by elastic scattering:
A rough estimation for the signal and background rates for low energy region
  pp region will be overwhelmed by the 14C this talk will focus on the region with recoil energy > 0.4 MeV
J.Phys.G 43 (2016) 3, 030401
Nucl.Sci.Tech. 34 (2023) 9, 137
rate (cpd/kton)
~1378
~517
~28
~7.5
~5.4
~0.1

## Slide 10: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
Solar , can be detected by elastic scattering:
A rough estimation for the signal and background rates for low energy region
  pp region will be overwhelmed by the 14C this talk will focus on the region with recoil energy > 0.4 MeV ~ neutrino energy > 0.6 MeV
JCAP 10 (2023) 022

## Slide 11: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
Solar neutrino rate sensitivity in region with neutrinos energy [0.6, 2.0] MeV
  Signal vs Background (6 years data) after selection, under four schemes:
  40K 85Kr 238Th 232U 210Pb
    High background
    Medium background
    Low background
    Very Low background
JCAP 10 (2023) 022
The unit is

## Slide 12: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
Solar neutrino rate sensitivity in region with neutrinos energy [0.6, 2.0] MeV
  Signal vs Background (6 years data) after selection, under four schemes:
  40K 85Kr 238Th 232U 210Pb
    High background
    Medium background
    Low background
    Very Low background
JCAP 10 (2023) 022
The unit is

## Slide 13: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
Solar neutrino rate sensitivity in region with neutrinos energy [0.6, 2.0] MeV
7Be- : Improve the Borexino (BX) result within 2 years. Medium bkg needs only 1 year.
pep- : Improve BX results within 8 years. Medium bkg needs only 1 year.
CNO- : Improve BX results within 6 years, with medium bkg and pep- constraint.
JCAP 10 (2023) 022

## Slide 14: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
rate ~
4.5 cpd/kton
g/g U/Th, after 10 years of data taking, all selection applied
8B solar neutrino sensitivity in region with neutrino energy > 2.0 MeV
  U/Th is important background in recoil energy [2,5] MeV region
  For higher energy region, the cosmogenic background has more influence.
  Under or U/Th, the sensitivities are similar (with well
  Bi-Po/Tl cascade decay tagging efficiency).
sensitivity under g/g U/Th. With g/g U/Th the sensitivity does not have significance improvement. (with well Bi-Po/Tl cascade decay tagging efficiency)
Chin.Phys.C 45 (2021) 2, 023004
Chin.Phys.C 45 (2021) 2, 023004

## Slide 15: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
8B Solar , can also be detected by CC and NC interactions:
  CC :
  prompt : delay : decay, lifetime~863 s 3929 events (10 years)
  NC :
  single energy : 3.685 MeV 3032 events (10 years)
U/Th ~ g/g 40K ~ g/g
210Pb ~ g/g
Astrophys.J. 965 (2024) 2, 122
Astrophys.J. 965 (2024) 2, 122

## Slide 16: LS Background Components’ Impact on Physics The impact on Solar Neutrino () Detection
8B Solar , can also be detected by CC and NC interactions:
  Sensitivities under:
    U/Th ~ g/g
    40K ~ g/g
    210Pb ~ g/g
Astrophys.J. 965 (2024) 2, 122

## Slide 17: Background Control During Installation
Final checks of the acrylic tank inside and outside.
Moisture spray over two days reduced dust levels inside CD air from ~10,000 to ~100.
Two weeks high pressure water jet to remove the protection film and clean the inner acrylic surface by 3D rotating nozzle. Check water cleanness until satisfactory.

## Slide 18: Liquid Scintillator Mixing and Purification
Four purification plants + LS Mixing + QA/QC + high purity N2 and water production plant
to guarantee radio-purity and transparency
JUNO
Distillation to remove radioactive impurities
Al2O3 to remove particles
5000 m3 LAB tank
SS pipes to underground
Add 2.5 g/L PPO, 3 mg/L bis-MSB and 5×10-5 g/g BHT
Water extraction to remove radioactive impurities
Gas stripping to remove Rn and O2
OSIRIS for LS qualification

## Slide 19: Liquid Scintillator Filling
Simultaneous water extraction and LS filling
Comprehensive QC/QA program for LS production, measured for batches:
  Radiopurity by ICP-MS every week: U/Th < 1×10-16 g/g
  222Rn in fresh LS, monitored by CD: <1 mBq/m3
  222Rn leak < 0.5 mBq/h
  Frequent radiopurity monitoring for N2 and water
  Weighted average attenuation length > 20m
Attenuation length Weighted average: 20.6m
2024, Dec 18
Start of Water Filling
2025, Feb 1
End of Water Filling
2025, Feb 8
Start of LS Filling
2025, Aug 22
End of LS Filling
Start of Data Taking
Water Phase
Mixed Phase
Full detector calibration
2025, Aug 26
08:00
2025, Aug 23
Replace 100 t old LS
20
10
Attenuation length (m)
Sampling time
Mar
Apr
May
Jun
Jul
Aug
Feb
More LS optical properties information can be Fatima’s poster

## Slide 20: Commissioning Results
Spatial distribution of the single events near the acrylic inner surface.
The spots corresponds to the anchors.
Anchor
VETO Water :
  U/Th<0.410-15 g/g, 222Rn<10 mBq/m3, 226Ra<1 mBq/m3
Acrylic, water, PMTs, steel and LS are clean and water shielding works :
  Single rate <7 Hz for R<17.2m & E>0.7MeV (design 7.2Hz)
  Good enough for reactor neutrinos

## Slide 21: Commissioning Results
VETO Water :
  U/Th<0.410-15 g/g, 222Rn<10 mBq/m3, 226Ra<1 mBq/m3
Acrylic, water, PMTs, steel and LS are clean and water shielding works :
  Single rate <7 Hz for R<17.2m & E>0.7MeV (design 7.2Hz)
  Good enough for reactor neutrinos
LS cleanness is very close to other solar neutrino experiments
  238U < 3×10-17 g/g (low radon area in a small fiducial volume)
  < 1×10-16 g/g (fitted plateau from full detector radon decay)
  232Th < 1×10-16 g/g (R<13m)
  210Po < 1×105 [cpd/kt]
Recirculation probably impossible, unlike Borexino, KamLAND, SNO+,…
Radiopurity control of raw material:
  Meticulous Monte Carlo Simulation for proper distribution of radioactivity budget
  Careful material screening
  Accurate detector production handling
Better than spec. by 15% !
JHEP 11 (2021) 102
Radiopurity control during installation :
Leak check of all joints (each < 10-8 mbarL/s) for 222Rn and 85Kr 
Cleaning and washing of all pipes & vessels to remove dust (by check water/LAB cleanness) 
Clean room environment during installation 
Acrylic Surface treatment and protection(Rn daughters) 
LS filling scheme: water replacement and water washing 

## Slide 22: Summary
JUNO is a large multiple-purpose neutrino observatory, with 20 kton high transparency and high radio-purity liquid scintillator.
Background status of the liquid scintillator physic sensitivities
  g/gU/Th, 80k cpd/kton 210Po’s contribution to the B/S of the reactor neutrino measurement < 2%.
  With g/g U/Th, g/g40K, g/g85Kr, g/g210Pb, JUNO can improve Borexino’s 7Be and pep solar neutrino rate results whitin one year of data taking.
  With similar background level, JUNO will also has good sensitivities on the CNO and 8B solar neutrinos.
The background control is carefully planned and implemented.
Commissioning result :
  Single rate <7 Hz for R<17.2m & E>0.7MeV (design 7.2Hz)
  238U < 3×10-17 g/g (small fiducial volume), 238U < 1×10-16 g/g (full detector)
  232Th < 1×10-16 g/g (R<13m)
  210Po < 1×105 [cpd/kt]
Data taking started in the end of Aug, 2025. Physics results coming soon.