## Slide 1: Results from the NOvA Experiment
Martin J. Frank University of South Alabama on behalf of the NOvA Collaboration
September 30th, 2025 Padua, Italy

## Slide 2: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant

## Slide 3: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant

## Slide 4: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant

## Slide 5: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant

## Slide 6: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant
𝜈e
𝜈𝜇
𝜈𝜏
𝜈e
𝜈𝜇
𝜈𝜏
𝜈3
?

## Slide 7: Introduction
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  measure θ13, θ23, Δm232
  measure δCP CP-violating phase angle
  resolve mass hierarchy
  resolve θ23 octant
Beyond Oscillation Physics
Non-Standard Interactions
Neutrino Cross Sections
Sterile Neutrinos
Dark Matter
Magnetic Monopoles
Supernova
And More!

## Slide 8: Introduction
Beyond Oscillation Physics
Non-Standard Interactions
Neutrino Cross Sections
Sterile Neutrinos
Dark Matter
Magnetic Monopoles
Supernova
And More!
NOνA:
  NuMI: Neutrinos at the Main Injector (νμ)
  Off-Axis: monoenergetic beam (2 GeV)
  νe Appearance (and νμ Disappearance)
Physics Goals:
  Search for magnetic monopoles
  New results hot off the press today!
New

## Slide 9: Neutrino Oscillation Results

## Slide 10: Extracting Nature’s Parameters
normal
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.

## Slide 11: Extracting Nature’s Parameters
normal
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.

## Slide 12: Extracting Nature’s Parameters
normal
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.

## Slide 13: Extracting Nature’s Parameters
normal
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.

## Slide 14: Extracting Nature’s Parameters
normal
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.

## Slide 15: Extracting Nature’s Parameters
θ23 = 45°
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.
normal
inverted

## Slide 16: Extracting Nature’s Parameters
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.
Here is an example measurement NOvA might make.
θ23 = 45°
normal
inverted
+σ
-σ

## Slide 17: Extracting Nature’s Parameters
Using the oscillation equations, we can calculate the neutrino and anti-neutrino appearance probabilities.
Here is an example measurement NOvA might make.
θ23 = 45°
normal
inverted
+σ
-σ
+σ
-σ

## Slide 18: Neutrino Beam
Baseline (L = 810 km)
  The neutrino beam travels from Fermilab to Ash River, MN through the earth’s crust.
Energy (Eν = 2 GeV)
  We can achieve a narrowly distributed neutrino energy by placing the detectors 14.6 mrad off the beam axis.
  This is also the νμ → νe oscillation peak.
Protons on Target (POT)
  13.6 x 1020 POT: neutrino mode
  12.5 x 1020 POT: antineutrino mode

## Slide 19: Neutrino Beam
Baseline (L = 810 km)
  The neutrino beam travels from Fermilab to Ash River, MN through the earth’s crust.
Energy (Eν = 2 GeV)
  We can achieve a narrowly distributed neutrino energy by placing the detectors 14.6 mrad off the beam axis.
  This is also the νμ → νe oscillation peak.
Protons on Target (POT)
  13.6 x 1020 POT: neutrino mode
  12.5 x 1020 POT: antineutrino mode

## Slide 20: Neutrino Beam
Baseline (L = 810 km)
  The neutrino beam travels from Fermilab to Ash River, MN through the earth’s crust.
Energy (Eν = 2 GeV)
  We can achieve a narrowly distributed neutrino energy by placing the detectors 14.6 mrad off the beam axis.
  This is also the νμ → νe oscillation peak.
Protons on Target (POT)
  13.6 x 1020 POT: neutrino mode
  12.5 x 1020 POT: antineutrino mode

## Slide 21: Neutrino Beam
Baseline (L = 810 km)
  The neutrino beam travels from Fermilab to Ash River, MN through the earth’s crust.
Energy (Eν = 2 GeV)
  We can achieve a narrowly distributed neutrino energy by placing the detectors 14.6 mrad off the beam axis.
  This is also the νμ → νe oscillation peak.
Protons on Target (POT)
  26.6 x 1020 POT: neutrino mode
  12.5 x 1020 POT: antineutrino mode

## Slide 22: Neutrino Beam
Baseline (L = 810 km)
  The neutrino beam travels from Fermilab to Ash River, MN through the earth’s crust.
Energy (Eν = 2 GeV)
  We can achieve a narrowly distributed neutrino energy by placing the detectors 14.6 mrad off the beam axis.
  This is also the νμ → νe oscillation peak.
Protons on Target (POT)
  26.6 x 1020 POT: neutrino mode
  12.5 x 1020 POT: antineutrino mode
10 years of beam!
2014 - 2024

## Slide 23: Neutrino Detection
We want to detect electron neutrinos (νe):
  This requires a large detector mass and good electron identification.
NOvA is a rectangular tracking calorimeter.
  low Z materials: PVC extrusions filled with liquid scintillator
    radiation length ~ 40 cm, Molière radius ~ 11 cm
    provides many samples per radiation length (differentiate e− and π0)
  each extrusion contains one wavelength-shifting fiber
  ends of fiber read out by avalanche photo-diode (APD)
APD 32 Channels
charged-current (CC) interaction
1 Channel
x
y
z
PVC extrusions
Detector

## Slide 24: Neutrino Detection
We want to detect electron neutrinos (νe):
  This requires a large detector mass and good electron identification.
NOvA is a rectangular tracking calorimeter.
  low Z materials: PVC extrusions filled with liquid scintillator
    radiation length ~ 40 cm, Molière radius ~ 11 cm
    provides many samples per radiation length (differentiate e− and π0)
  each extrusion contains one wavelength-shifting fiber
  ends of fiber read out by avalanche photo-diode (APD)
APD 32 Channels
charged-current (CC) interaction
1 Channel
x
y
z
PVC extrusions
Detector

## Slide 25: Neutrino Detection
We want to detect electron neutrinos (νe):
  This requires a large detector mass and good electron identification.
NOvA is a rectangular tracking calorimeter.
  low Z materials: PVC extrusions filled with liquid scintillator
    radiation length ~ 40 cm, Molière radius ~ 11 cm
    provides many samples per radiation length (differentiate e− and π0)
  each extrusion contains one wavelength-shifting fiber
  ends of fiber read out by avalanche photo-diode (APD)
APD 32 Channels
charged-current (CC) interaction
1 Channel
Detector
x
y
z
PVC extrusions

## Slide 26: Simulated Event Display

## Slide 27: Near Detector at Fermilab
1 km downstream from NuMI target
105 m underground
300 tons
4 m × 4 m × 15 m
Instrumented with 20k channels
Several neutrino interactions per second
Few cosmic ray muons per second
Top View
Muon Catcher
Beam

## Slide 28: Far Detector in Ash River, MN
810 km downstream from NuMI target
On the surface
14,000 tons
15 m × 15 m × 60 m
Instrumented with 344k channels
Few neutrino interactions per year
~130,000 cosmic ray muons per second

## Slide 29: Neutrino Detection
xz-view
yz-view
x
y
z

## Slide 30: Near Detector Event Display

## Slide 31: Far Detector Event Display
550 μs Exposure

## Slide 32: Time Zoom on NuMI Beam Pulse

## Slide 33: Close-Up of Neutrino Interaction

## Slide 34: Far Detector Neutrino Prediction
We use a data-driven technique to extrapolate the neutrino events in the near detector to the far detector:
  Estimate true energy distribution of near detector events
  Multiply by expected far/near event ratio and oscillation probability
  Convert far detector true energy into reconstructed energy

## Slide 35: Muon Neutrino Events
Muon neutrino event counts:
  384 νμ candidates (beam: 26.6 x 1020 POT)
  106 anti-νμ candidates (beam: 12.5 x 1020 POT)
Note the dip in the energy spectra indicating the disappearance of muon neutrinos

## Slide 36: Muon Neutrino Events
Muon neutrino event counts:
  384 νμ candidates (beam: 26.6 x 1020 POT)
  106 anti-νμ candidates (beam: 12.5 x 1020 POT)
Note the dip in the energy spectra indicating the disappearance of muon neutrinos

## Slide 37: Muon Neutrino Events
Muon neutrino event counts:
  384 νμ candidates (beam: 26.6 x 1020 POT)
  106 anti-νμ candidates (beam: 12.5 x 1020 POT)
Note the dip in the energy spectra indicating the disappearance of muon neutrinos

## Slide 38: Electron Neutrino Events
Electron neutrino event counts
  181 νe candidates (beam: 26.6 x 1020 POT)
  32 anti-νe candidates (beam: 12.5 x 1020 POT)
Samples divided into four selections:
  Low-Energy, Low Particle ID (PID), High PID and Peripheral

## Slide 39: Electron Neutrino Events
Electron neutrino event counts
  181 νe candidates (beam: 26.6 x 1020 POT)
  32 anti-νe candidates (beam: 12.5 x 1020 POT)
Samples divided into four selections:
  Low-Energy, Low Particle ID (PID), High PID and Peripheral

## Slide 40: Extract Nature’s Parameters

## Slide 41: Extract Nature’s Parameters

## Slide 42: Extract Nature’s Parameters

## Slide 43: Extract Nature’s Parameters

## Slide 44: Extract Nature’s Parameters
Mild preference for normal ordering
Mild preference for upper octant of θ23

## Slide 45: Extract Nature’s Parameters
Mild preference for normal ordering
Mild preference for upper octant of θ23

## Slide 46: Extract Nature’s Parameters
Mild preference for normal ordering
Mild preference for upper octant of θ23

## Slide 47: Extract Nature’s Parameters
Mild preference for normal ordering
Mild preference for upper octant of θ23

## Slide 48: Extract Nature’s Parameters
Mild preference for normal ordering
Mild preference for upper octant of θ23

## Slide 49: Extract Nature’s Parameters

## Slide 50: Neutrino Oscillation Results
We measured the most precise single-experiment constraint on the atmospheric neutrino mass-splitting!

## Slide 51: Magnetic Monopole Search

## Slide 52: Magnetic Monopole Search
“The magnetic monopole is the most venerable member of the mythological bestiary of physics.” – Don Groom
We search for magnetic monopoles.
If they exist, they will deposit energy in our detector.
NOvA has the unique potential to probe a new region of phase space:
  due to our large surface area
  and our location on the surface.
NOvA has dedicated triggers to write out monopole-like events.
First search published in 2021.
D.E. Groom, Physics Reports 140, 6, pg. 323 (1986)
10 ⨉ MIP
100 ⨉ MIP
1000 ⨉ MIP
β = 10-3
β = 10-2
β = 10-1

## Slide 53: Magnetic Monopole Search
“The magnetic monopole is the most venerable member of the mythological bestiary of physics.” – Don Groom
We search for magnetic monopoles.
If they exist, they will deposit energy in our detector.
NOvA has the unique potential to probe a new region of phase space:
  due to our large surface area
  and our location on the surface.
NOvA has dedicated triggers to write out monopole-like events.
First search published in 2021.
D.E. Groom, Physics Reports 140, 6, pg. 323 (1986)
10 ⨉ MIP
100 ⨉ MIP
1000 ⨉ MIP
β = 10-3
β = 10-2
β = 10-1

## Slide 54: Magnetic Monopole Search
“The magnetic monopole is the most venerable member of the mythological bestiary of physics.” – Don Groom
We search for magnetic monopoles.
If they exist, they will deposit energy in our detector.
NOvA has the unique potential to probe a new region of phase space:
  due to our large surface area
  and our location on the surface.
NOvA has dedicated triggers to write out monopole-like events.
First search published in 2021.
D.E. Groom, Physics Reports 140, 6, pg. 323 (1986)
10 ⨉ MIP
100 ⨉ MIP
1000 ⨉ MIP
β = 10-3
β = 10-2
β = 10-1

## Slide 55: Magnetic Monopole Energy Deposition
Groom’s summary of the magnetic monopole energy deposition as calculated from EM.
Monopole interaction is similar to particle with charge Z = 69 at high β.
1000 ⨉ MIP
β = 10-1
100 ⨉ MIP
β = 10-2
10 ⨉ MIP
β = 10-3

## Slide 56: Analysis Strategy
We divide the magnetic monopole searches into two broad categories based on:
  Ionization
  Timing
IONIZATION
TIMING

## Slide 57: Analysis Strategy
Large energy deposition is suppressed through Birks effect.
A lot of work went into verifying that these effects were properly accounted for in our simulation.
IONIZATION

## Slide 58: Analysis Strategy
Large energy deposition is suppressed through Birks effect.
Fast monopoles (β ≳ 0.7) produce Cherenkov light.
A lot of work went into verifying that these effects were properly accounted for in our simulation.
IONIZATION

## Slide 59: Analysis Strategy
A lot of work went into verifying that these effects were properly accounted for in our simulation.
Fast monopoles (β ≳ 0.7) produce Cherenkov light.
Large energy deposition is suppressed through Birks effect.
IONIZATION

## Slide 60: Acceptance Region
monopole
monopole

## Slide 61: Data Samples
Ionization Search:
  October 2015 – February 2025
  2,904 days (2,713 days marked as good)
Timing Search:
  February 2016 – October 2024
  2,985 days (2,743 days marked as good)
2012
2014
2016
2018
2020
2024
2022
Build
Data
Detector Gain Settings Changed
October 13, 2015
Analyzed Data
Now
Data

## Slide 62: Ionization Magnetic Monopole Search

## Slide 63: Raw Data with Simulated Monopole
50 μs Exposure
Simulated Monopole
Large Energy Deposition

## Slide 64: Analysis Strategy
Trigger on monopole-like patterns with high energy depositions in live data stream.
Reconstruct event kinematics offline.
  ~100% track purity for β > 10−3
  ~90% track completeness for β > 10−2

## Slide 65: Offline Analysis Strategy
Data:
  Triggered by ionizing monopole algorithm
MC:
  Simulated monopole overlaid with cosmic data
Select events with high energy deposition
Select narrow events:
  Removes energetic showering muons that tend to be wider
Monopole
Showering Muon
Track Width
Energy Deposition

## Slide 66: Offline Analysis Strategy
Data:
  Triggered by ionizing monopole algorithm
MC:
  Simulated monopole overlaid with cosmic data
Select events with high energy deposition
Select narrow events:
  Removes energetic showering muons that tend to be wider
Monopole
Showering Muon
Track Width
Energy Deposition

## Slide 67: Signal Search
Track Width
Energy Deposition
Triggered Data
Simulated Monopoles

## Slide 68: Signal Search
Track Width
Energy Deposition
Triggered Data
Simulated Monopoles
No Magnetic Monopole Event Found!

## Slide 69: Magnetic Monopole Flux Limits

## Slide 70: Timing Magnetic Monopole Search

## Slide 71: Monopole Simulation
We used simulation to determine the efficiency of selecting monopole tracks for 10−4 < β < 10−2.
The monopoles were simulated using an isotropic flux.
Each simulated monopole was combined with 5 ms of zero bias data (i.e. data with typical running conditions).
5 ms of zero bias data

## Slide 72: Monopole Simulation
We used simulation to determine the efficiency of selecting monopole tracks for 10−4 < β < 10−2.
The monopoles were simulated using an isotropic flux.
Each simulated monopole was combined with 5 ms of zero bias data (i.e. data with typical running conditions).
5 ms of zero bias data

## Slide 73: Monopole Simulation
We used simulation to determine the efficiency of selecting monopole tracks for 10−4 < β < 10−2.
The monopoles were simulated using an isotropic flux.
Each simulated monopole was combined with 5 ms of zero bias data (i.e. data with typical running conditions).
5 ms of zero bias data
+ simulated monopole

## Slide 74: Analysis Strategy – Trigger
The NOvA detectors are equipped with a data-driven trigger (DDT) system that continuously examines the live data stream on over 100 computing nodes.
The monopole trigger algorithm examines pairs of hits on the surface of the detector for each event (5 ms).

## Slide 75: Analysis Strategy – Trigger
The NOvA detectors are equipped with a data-driven trigger (DDT) system that continuously examines the live data stream on over 100 computing nodes.
The monopole trigger algorithm examines pairs of hits on the surface of the detector for each event (5 ms).

## Slide 76: Analysis Strategy – Trigger
The NOvA detectors are equipped with a data-driven trigger (DDT) system that continuously examines the live data stream on over 100 computing nodes.
The monopole trigger algorithm examines pairs of hits on the surface of the detector for each event (5 ms).

## Slide 77: Trigger and Reconstruction Efficiencies
Efficiency constant:
  from β ~ 5x10−4
  to β ~ 5x10−3
Some efficiency lost due to tracks parallel to the detector planes.
  |θ| ~ 90°
Improvements in the trigger and offline reconstruction algorithms have increased efficiency since the 2021 result!
θ
z
x
2021

## Slide 78: Trigger and Reconstruction Efficiencies
Efficiency constant:
  from β ~ 5x10−4
  to β ~ 5x10−3
Some efficiency lost due to tracks parallel to the detector planes.
  |θ| ~ 90°
Improvements in the trigger and offline reconstruction algorithms have increased efficiency since the 2021 result!
θ
z
x
2021

## Slide 79: Trigger and Reconstruction Efficiencies
Efficiency constant:
  from β ~ 5x10−4
  to β ~ 5x10−3
Some efficiency lost due to tracks parallel to the detector planes.
  |θ| ~ 90°
Improvements in the trigger and offline reconstruction algorithms have increased efficiency since the 2021 result!
2021
Now
θ
z
x

## Slide 80: Offline Reconstruction
5 ms Exposure

## Slide 81: Remove Low Energy Hits
5 ms Exposure

## Slide 82: Identify Cosmic Rays
5 ms Exposure

## Slide 83: Remove Cosmic Rays
5 ms Exposure

## Slide 84: Identify Groups of Correlated Hits
5 ms Exposure

## Slide 85: Time Zoom on Monopole Group of Hits
Zoom in to 4.8 ms – 4.9 ms

## Slide 86: Identify Straight Line Features (Hough Tracking)
Zoom in to 4.8 ms – 4.9 ms

## Slide 87: Identify Monopole Track
Zoom in to 4.8 ms – 4.9 ms

## Slide 88: Analysis Strategy – Offline
t
x
t
x
t
x
We want to identify straight line tracks.
Two powerful discriminators:
  Correlation coefficient: r2
  Time gap fraction: f
r2 = 1
f ≈ 0
r2 ≈ 0
f ≈ 1
bad
bad
good
Selection Cuts
r2 > 0.95

## Slide 89: Analysis Strategy – Offline
t
x
t
x
t
x
We want to identify straight line tracks.
Two powerful discriminators:
  Correlation coefficient: r2
  Time gap fraction: f
r2 = 1
f ≈ 0
r2 ≈ 0
f ≈ 1
bad
bad
good
Selection Cuts
r2 > 0.95
f < 0.2

## Slide 90: Correlation Coefficient
Signal Region

## Slide 91: Signal Search
Signal Region

## Slide 92: Signal Search
Signal Region
No Magnetic Monopole Event Found!

## Slide 93: Signal Search
Signal Region
No Magnetic Monopole Event Found!
Interesting Events
(far from signal region)

## Slide 94: Interesting Event 1 – Timing Search
No slow activity
High energy activity
FEB flash

## Slide 95: Interesting Event 2 – Timing Search
No slow activity
High energy activity
FEB flash
Beautiful event!

## Slide 96: Magnetic Monopole Flux Limits

## Slide 97: Magnetic Monopole Flux Limits

## Slide 98: Summary
We continue to untangle the oscillation parameter phase space.
  Stay tuned for our combined results with T2K (up next)!
We searched for magnetic monopoles. In the absence of any signal, we set limits as low as 2×10−16 cm−2s−1sr−1.
Thanks to the NOvA Collaboration!
Thanks to our funding agencies for supporting the NOvA experiment (see next slide) and my work (NSF-2412236).
>266 scientists and engineers from 51 institutions from 8 countries

## Slide 99: Acknowledgements
This document was prepared by the NOvA collaboration using the resources of the Fermi National Accelerator Laboratory (Fermilab), a U.S. Department of Energy, Office of Science, HEP User Facility. Fermilab is managed by Fermi Forward Discovery Group, LLC, acting under Contract No. 89243024CSC000002. This work was supported by the U.S. Department of Energy; the U.S. National Science Foundation; the Department of Science and Technology, India; the European Research Council; the MSMT CR, GA UK, Czech Republic; the RAS, the Ministry of Science and Higher Education, and RFBR, Russia; CNPq and FAPEG, Brazil; UKRI, STFC and the Royal Society, United Kingdom; and the state and University of Minnesota. We are grateful for the contributions of the staffs of the University of Minnesota at the Ash River Laboratory, and of Fermilab. For the purpose of open access, the author has applied a Creative Commons Attribution (CC BY) license to any Author Accepted Manuscript version arising.

## Slide 100: Signal Search – L > 20 m