## Slide 1
Peripheral Electronics
Some updates
Mauro Citterio
--------
INFN Milano

## Slide 2: DAQ reading chain for L0-L5
2
High rad area 15Mrad/year
Off detector
low rad area
Optical Link
2.5 Gbit/s to ROM
Counting room
Std electronics
FEB
Optical 1 Gbit/s
< 1 m
LV1
fibers
Detector
HDIs
C
Front-end chips
Copper bus
UPILEX+Cu (?)
Transition card
Serdes
or FPGA
ROM
Work concentrated on  fanout (layer0)
 Copper bus vs Bundle of magnet wires
 Data transmission on Copper bus
- specifications
 better estimate of “power lines” on Copper bus

## Slide 3
Fanout (layer 0)
 Design progressing on Aluminum/Kapton 2 layer fanout
  Fanout min. pitch is 80 um
  Bonding always toward detector side (Stefano/Filippo concern resolved)
    Fanout resistance first estimate ~ 0.8 ohm/cm (assuming Aluminum resistivity ~ 33 ohm x metro x 10-9)
    Narrow pitch needed over a length of ~ 40 mm
      Cern suggestions:
          minimize the area where the pitch is 80 um
            Perform a test on one layer to verify reliability/consistency of pitch
            Concern about bending such a fine lines (perform resistance test before and after bending) on first sample
          Spread lines before reaching bonding
    Overall fanout width about 36 mm  To be verified in model

## Slide 4
The layout of the fanout requires
~ 36 mm. It looks possible from the mechanical point of view, but we need to verify that carefully.
If not, than we need to decrease the pitch. The real minimum pitch need to tested on first CERN sample.
Mimimum pitch ~ 80 um
Simple geometry requested by CERN
Output connector (originally 64 pins reduced to 50 pins. Should carry all copper lines (up to 11 LVDS + power LV and HV maybe).
Pins will increase in outer layers !!!
29 mm
Not clear why hybrid sides are not parrallel
Larger pitch used near IC (~ 100 um)
Serializer

## Slide 5
Output connector (originally 64 pins reduced to 50 pins.
To be able to fit in the transition card
Increasing pins, means increased connector size  we will need to make space not only for the connector, but also for the cable itself !!

## Slide 6
HDI
Layer 0 HDI dimensions
  We should “freeze” the dimensions
  I have started to draw a real “schematic and layout”.
  I am planning to have it completed by Frascati meeting
    In the coming days we should agree on some “tentative” pad layout
  No show-stopper up to now
    Still need to understand if we need to “shielding between LVDS lines close to the connector
    Clock routing not yet addressed
  Number of layers seems similar to Babar HDI
  Summary of LVDS lines
          3 clocks (System clock, Time Stamp clock, readout clock)
          1 REG In
          1 REG out
          1 Reset
          1 Trigger
          4 Data lines
Analog channels
Digital backend
Periph.
blocks
Periph.
blocks
Periph.
blocks
Periph.
blocks
DATA
OUT

## Slide 7
LVDS test in preparation
IC acquired from CERN (8 receivers and 8 transmitters, 6x1.5 mm)
  Extract of info from CERN:
    IBL loads 5.6m of twisted pair cable with this LVDS (FE-I4).
    Baud rate is 160Mb/s, transmission quality is marginal. Eye-plot is small mostly due to NO pre-empjasis
    nSPQ uses the same LVDS over a cable lenght (bunch of magnet wires) of 6.3m with a baud rate of 80Mb/s. Bit error rate is < 10E-14.
    With only one magnet wires baud rate could increase up to 120-130Mb/s, but if a bunch is used «mutual impedance» creates a problem
    We are bonding the IC to a board
    We will retest performance with multiple magnet wires
      we would need to interpose shields ?
    In parallel we will test an LVDC driver designed by Bergamo group
    I am also start designing a flat cable (6 mils data lines, 70 um thick, with shield + power lines)