## Slide 1: Detector arrays for indirect experiments with RIBs in Nuclear Astrophysics
G.L. Guardo on behalf of the AsFiN group

## Slide 2
The Trojan Horse Method
The idea of the THM is to extract the cross section of an astrophysically relevant two-body reaction A+xc+C at low energies from a suitable three-body reaction a+Ac+C+s
Quasi free kinematics is selected
only x - A interaction
s = spectator (ps~0)
EA > ECoul 
NO coulomb suppression
NO electron screening
NO centrifugal barrier
THM Review paper Spitaleri C. et al., Prob. of Fund. Mod. Phys., 1991 Tumino A. et al., An. Rev. Nuc. and Part. Sci. 2021

## Slide 3
Preliminary Study
This allows then to determine the experimental apparatus:
14C detection 6°<θC<10°
α detection15°<θα<20°
23°<θα<31°
Black points: kinematic calculations
Red points: kinematic calculations + |ps|<5 MeV/c
17O+2H, Ebeam=43.3 MeV
Deuteron as source of virtual neutrons!!
Study of the 17O(n,α)14C reaction: extension of the Trojan Horse Method to neutron induced reactions

## Slide 4
Experimental Setup
2H
n
17O
p
14C
α
The reaction 17O(n,α)14C was studied via the 2H(17O,α14C)p , Vcoul=2.3 MeV;
The deuteron is the TH nucleus. Strong cluster n+p; B=2.2 MeV, |ps|=0 MeV/c .
Experiments performed at ISNAP at the University of Notre Dame (USA) and LNS of Catania;
Ebeam(17O)= 43.5 MeV;
Target thickness CD2 150 µg/cm2;
IC filled with 50 mbar isobutane gas;
Angular position to cover the QF angular region
Symmetric set-up in order to increase the statistic.

## Slide 5
The BELICOS Experimental Setup
400 μg/cm2 CD2 target;
EXPADES detection system
Pierroutsakou, D. et al. 2016, NIMPA, 834, 46
T2(T3) IC + DSSSD (300 μm) + SPad (300 μm)
T1(T4) IC + DSSSD (300 μm)
100 mbar isobuthane for IC
Calibration with 7Li beam on 12C, 197Au and CH2
Setup symmetrical, respect to the beam line, in the reaction plane
Trigger: coincidence between two telescopes
The 7Be(n,α)α reaction via THM

## Slide 6
THM study of 18F(p,α)15O @ CRIB
 | DSSSD | ASTRHO
Angular range | 2° - 11° | 11° - 31°
Angular resolution | 0.5° (tracking+ detectors) | 0.5° (tracking+ detectors)
Energy resolution | 0.8% | 0.8%
Trigger: total or, off-line multiplicity 2 fixed
CD2 TARGET 150-200 μg/cm^2
ASTRHO  
n. 8 bidimensional position-sensitive detectors (BPSD,
45 x 45 mm2, 500 μm thick
DSSSD  15O
n. 2 Double Sided Silicon Strip Detectors (16 strips x-y)
PPAC 1
PPAC 2
DSSSD
Safety
disk
TARGET
ASTRHO
BEAM
PPAC2
TARGET
ASTRHO
DSSSD

## Slide 7
THM study of 18F(p,α)15O @ TAMU
 | X1-PSD | TECSA
Angular range | 3° - 12° | 15° - 40°
Angular resolution | 0.7° | 1.1°
Energy resolution | 0.8% | 0.8%
18F beam
TECSA

CD2 Target
X1 PSD
15O
Trigger: TECSA X1-PSD coincidence
CD2 TARGET 400-800 μg/cm^2
TECSA  
n. 8 16 arch strip YY1-300 um
B.T. Roeder et al. NIM A634, 71 (2011)
X1-PSD  15O
n. 2 16 strips each, position sensitive

## Slide 8
THM study of 26Al(n,p)26Mg @ TRIUMF
NEFASTA
8 telescopes arranged into two groups:
- group A 60 mm away from the target, made up of two couples of telescopes, set in the vertical (A1) and in the horizontal (A2) planes. Each telescope will be composed of one DSSSD 1000 m thick (32x32 strips, 51.2x51.2 mm2) and one pad detector 1500 m thick
- The second group of detectors (named B) will be placed at about 700 mm from the target position. Two couples of telescopes, set in the vertical (B1) and in the horizontal (B2) planes, each composed of a 20 m SSSSD and a 1000 m DSSSD
A1 group will cover the angular ranges 9.4°-55.6°, while those in A2 will cover 32.9°-79.1°
B1 detectors will cover the 2°-6.1° angular range, while B2 telescopes will cover the 2.9°-7.1° interval
Mechanical drawings by Dr. M. Costa
BEAM DIRECTION

## Slide 9
THM study of 14O(α,p)17F @ FRIB
Requirements:
Large area coverage
Low detection threshold
No PSD or DE techniques are viable for particle ID
High energy and angular resolution for kinematical particle ID

## Slide 10
THM study of 14O(α,p)17F @ FRIB
Technical detail
ANASEN uses a 43-cm long position-sensitive proportional counter surrounding the beam axis to enable an active-target mode. Silicon-strip detectors surround the proportional counter in a barrel configuration with 3 rings of 12 rectangular Super X3 and annular QQQ3 detectors at forward angles form the cap of the barrel. All detectors in the array are backed by trapezoidal-shaped 2-cm thick CsI(TI) crystals.
Technical detail
SuperORRUBA consists of two rings of silicon detectors designed to operate with one ring forward of 90° in the laboratory and the second backward of 90°. The silicon detectors are based on double-sided non-resistive silicon strip technology. The detectors cover an area, 7.5 cm by 4 cm, with the front sides divided into 64 1.2 mm by 4 cm strips, and the back sides segmented into 4 7.5 cm by 1 cm strips. The 1.2-mm strips are oriented perpendicular to the beam direction, while the 1-cm strips were parallel. The angular resolution in polar angle is less than 1-deg. The azimuthal angular resolution is less important, and thus larger strip pitches are used on the backside.

## Slide 11
Large High-resolution Array of Silicon for Astrophysics
Characteristics:
Wide angular range coverage
Low energy threshold
Compactness
High energy resolution
Angular resolution allows for PID

## Slide 12
Extreme Light Infrastructure Silicon Strip Array
Barrel configuration:
3 rings of 12 position sensitive X3 silicon-strip detectors by Micron
2 end cap detectors made up of 4 QQQ3 DSSSD by Micron
>550 channels readout with standard/digital electronics
Characteristics:
Wide angular range coverage
Low energy threshold
Compactness
Angular resolution better than 0.5 cm
Energy resolution better than 1%
Kinematical identification of outgoing particle
Perfectly suited for nuclear astrophysical studies!!
G. L. Guardo et al. EPJ Web of Conf. 165, 01026 (2017)

## Slide 13
Extreme Light Infrastructure Silicon Strip Array

## Slide 14
Asfin Data Acquisition

## Slide 15
Asfin Data Acquisition

## Slide 16
Direct Experiments with ELISSA&LHASA
The 19F(p,α) reaction

## Slide 17
Particle Identification with Pulse Shape Analysis

## Slide 18
Particle Identification with Pulse Shape Analysis

## Slide 19
Particle Identification with Pulse Shape Analysis

## Slide 20
Conclusions
The availability of radioactive ion beams at facilities like FRIB is a unique opportunity for nuclear astrophysics, as a number of reaction of primary astrophysical importance can be measured for the first time
To catch these experimental opportunities, the Asfin group is developing new arrays with peculiar characteristics: high-resolution, low-threshould, high-efficiency, compactness…
Preliminary results on methods and arrays make us confident for the new perspectives and open the way for new experimental campaigns

## Slide 21
Thank you for your attention

## Slide 22
@Catania: A. Bonasera, S. Cherubini, G. D’Agata, A. Di Pietro, P. Figuera, S. Gammino, G.L. Guardo, M. Gulino, M. La Cognata, L. Lamia, D. Lattuada, A.A. Oliva, R.G. Pizzone, G.G. Rapisarda, S. Romano, D. Santonocito, M.L. Sergi, R. Spartà, C. Spitaleri, A. Tumino
@Napoli M. La Commara @Padova M. Mazzocco, S. Pigliapoco, A. Togni
@Perugia S. Palmerini, M. Limongi, A. Chieffi, M.C. Nucci
Collaborations
Cyclotron Institute,Texas A&M,US: R. Tribble, V. Goldber Texas A&M Commerce US: C. Bertulani
Florida State University US: I. Wiedenhofer
Notre Dame University US: M. Wiescher, M. Couder
C.N.S. Riken, Wako, Japan: S. Kubono, H. Yamaguchi, S. Hayaka University of Taskent: B. Irgaziev, R. Yarmukhanmedov
CIAE, Beijing, China: S. Zhou, C. Li, Q. Wen
Nuclear Physics Institute, ASCR, Rez, Czech Rep.: V. Kroha, V. Burjan, J. Mrazek
Nipne IFIN Bucharest: L. Trache
ELI-NP Bucharest: C. Matei, D. Balabanski Atomki, Debrecen, Hungary: G. Kiss
CSNSM, Orsay, France : A. Coc , F. Hammache, N. De Sereville
University of Catalunya: J. Jose
Rudjer Boskovic Institute Zagreb Croatia: N. Soic, M. Milin GIST, Gwangju, South Korea: W. Bang